Fsfix is Copyright (c) 1989 by Howard C Johnson.  It may be freely
distributed as long as this document is attached.

I wrote this first to fix file systems, then to fix up the MS/DOS parameters
in the TOS boot blocks.

It can be invoked as fsfix (or click on fsfix.prg) and it will query for
the information it needs.

You may also use COMMAND.TOS as a shell to invoke fsfix.
Type fsfix x<CR> to see the command summary.

This program is primarily intended to fix hard disk partitions, but it
also works on floppies.

NOTE: Changing the boot block may require reinstalling your favorite
autoboot.  In particular, Supra and ICD will have to have the checksum
recalculated.  If I find the checksum is valid the first time, I assume
that the first 2 bytes are valid and don't change them.  If you want
to make them fully IBM conforming, run fsfix twice.

The 'r' option only SHOWS what will be changed.  It will be changed only
if rewrite is allowed (fsfix -rylc) or Y option.

A Sample printout of my boot block follows:  Note, I have a Supra Autoboot.

Warning, using Physical drive 0, Controller 0 for drive parameters!
llread(0,1,63DB8,2) ret=0
Boot record for lu: C Reference is HD
branch to boot :		0x1C60	 is now: 0x34EB <<<<<<this is change
nop:				90
name|version:			IBM  |3.2
bytes per sector:		0x200
cluster size:			2
reserved sectors:		1
number of fats:			2
directory size:			416(0x1A0)
total sectors:			32766(0x7FFE)
medium descriptor:		0xF8	
fat size:			65
sectors per track:		17
sides on medium:		9
hidden sectors:			1

records:
boot =	0
fat0 =	1
fat1 =	66
dir  =	131
data =	157

Remember, If you screw up, YOU did it.  I'm not responsible.

Howard C Johnson
ATT-BL
lzaz!hcj