1. Eprom writer card I/O address

   The I/O address of Eprom writer card are as shown below:

	model: EW-901	3C0-3C7
	model: EW-901A	3C0-3C7
	model: EW-901B	390-397

	model: EW-904	3C0-3C7
	model: EW-904A	3C0-3C7
	model: EW-904B	390-397

	model: EW-910	3C8-3CF	

2. The Eprom type and programming voltage are as shown below:

*** Advanced Micro Devices *** 
	
	Eprom type / Programming Voltage
	
	2716		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	2732A		Vpp=21V
	--------------------------------
	2764		Vpp=21V	
	--------------------------------
	2764A		Vpp=12.5V
	--------------------------------
	27128		Vpp=21V
	--------------------------------
	27128A		Vpp=12.5V
	--------------------------------
	27256		Vpp=12.5V
	--------------------------------
	27512		Vpp=12.5V
	--------------------------------


*** Fujitsu ***

	Eprom type / Programming Voltage
	
	--------------------------------
	2732A-35	Vpp=21V
	2732A		Vpp=21V
	--------------------------------
	27C32A		Vpp=21V
	--------------------------------
	MBM2764-20	Vpp=21V	
	MBM2764-25	Vpp=21V
	MBM2764-30	Vpp=21V
	--------------------------------
	MBM27C64-20	Vpp=21V
	MBM27C64-25	Vpp=21V
	--------------------------------
	MBM27128-20	Vpp=21V
	MBM27128-25	Vpp=21V
	MBM27128-30	Vpp=21V
	--------------------------------
	MBM27256-25	Vpp=12.5V
	MBM27256-30	Vpp=12.5V
	--------------------------------
	MBM27C256-20	Vpp=21V
	MBM27C256-25	Vpp=21V
	MBM27C256-30	Vpp=21V
	--------------------------------
*** Hitachi ***

	Eprom type / Programming Voltage
	
	HN462716	Vpp=25V
	--------------------------------
	HN462732	Vpp=25V
	HN462732P	Vpp=25V
	--------------------------------
	HN482732A	Vpp=21V
	--------------------------------
	HN27C32		Vpp=25V
	--------------------------------
	HN27C32A	Vpp=21V
	--------------------------------
	HN482764G-2	Vpp=21V	
	HN482764G	Vpp=21V
	HN482764G-3	Vpp=21V
	--------------------------------
	HN482764P	Vpp=21V
	HN482764P-3	Vpp=21V	
	--------------------------------
	HN27C64G-25	Vpp=21V
	HN27C64G-20	Vpp=21V
	--------------------------------
	HN4827128G-25	Vpp=21V
	HN4827128G-30	Vpp=21V
	HN4827128G-45	Vpp=21V
	--------------------------------
	HN4827128P-30	Vpp=21V
	--------------------------------
	HN27128AG-20	Vpp=12.5V
	HN27128AG-30	Vpp=12.5V
	--------------------------------
	HN27256G-25	Vpp=12.5V
	HN27256G-30	Vpp=12.5V
	--------------------------------
	HN27C256G-20	Vpp=12.5V	
	HN27C256G-25	Vpp=12.5V
	HN27C256G-30	Vpp=12.5V
	--------------------------------	
	HN27512G-25	Vpp=12.5V
	HN27512G-30	Vpp=12.5V
	--------------------------------

*** Intel ***
 
	Eprom type / Programming Voltage
	
	2716		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	--------------------------------
	2732A		Vpp=21V
	--------------------------------
	2764A-2		Vpp=21V	
	2764A		Vpp=21V
	2764A-3		Vpp=21V
	--------------------------------
	P2764A		Vpp=12.5V
	P2764A-3	Vpp=12.5V	
	--------------------------------
	27C64		Vpp=21V
	27C64-2		Vpp=21V
	--------------------------------
	27128		Vpp=21V
	27128-3		Vpp=21V
	27128-4		Vpp=21V
	--------------------------------
	27128A-2	Vpp=12.5V
	27128A-3	Vpp=12.5V
	--------------------------------
	27256		Vpp=12.5V
	27256-3		Vpp=12.5V
	--------------------------------
	27512		Vpp=12.5V
	27512-3		Vpp=12.5V
	--------------------------------

*** Mitsubishi ***

	Eprom type / Programming Voltage
	
	2716		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	2732A		Vpp=21V
	--------------------------------
	M5L2764K-2	Vpp=21V	
	M562764K	Vpp=21V
	M5L2764K-3	Vpp=21V
	--------------------------------
	M562764P-3	Vpp=21V
	--------------------------------
	M5L27256K	Vpp=12.5V
	--------------------------------

*** National Semiconductor ***

	2716		Vpp=25V
	27C16		Vpp=25V
	27C16H		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	27C32		Vpp=25V
	27C32H		Vpp=25V
	--------------------------------
	2764		Vpp=21V
	2764H		Vpp=21V
	--------------------------------
	NMC27C256	Vpp=12.5V
	--------------------------------	


*** Nippon Electric Company,Ltd. ***

	Eprom type / Programming Voltage
	
	2716		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	2732A		Vpp=21V
	--------------------------------
	D2764D-2	Vpp=21V	
	D2764D	Vpp=21V
	D2764D-3	Vpp=21V
	--------------------------------
	D2764C	Vpp=21V
	D2764C-3	Vpp=21V	
	--------------------------------
	D27C64D-20	Vpp=21V
	D27C64D-25	Vpp=21V
	--------------------------------
	D27C64C	Vpp=21V
	--------------------------------
	D27128D	Vpp=21V
	D27128D-3	Vpp=21V
	D27128D-4	Vpp=21V
	--------------------------------
	D27128C-3	Vpp=21V
	--------------------------------
	D27256D	Vpp=21V
	D27256D-3	Vpp=21V
	--------------------------------


*** Toshiba ***

	Eprom type / Programming Voltage
	
	2716		Vpp=25V
	--------------------------------
	2732		Vpp=25V
	2732A		Vpp=21V
	--------------------------------
	TMM2764D-2	Vpp=21V	
	TMM2764D	Vpp=21V
	--------------------------------
	TMM27128D-20	Vpp=21V
	TMM27128D-25	Vpp=21V
	--------------------------------
	TC57256D-20	Vpp=21V
	TC57256D-25	Vpp=21V
	--------------------------------
	27C256		Vpp=12.5V
	--------------------------------
Downloaded From P-80 International Information Systems 304-744-2253