RELEASE 1-1-1989 
CURRENT VERSION IS 4.5
PROBLEMS FIXED:
(1) NO LONGER NEED FOR KEFIX CHIP IF HEALTH BITE IS BAD WHEN WRITTING 018X KEYS
    BACK TO U7
(2) CORRECTS PROBLEM IF READER/WRITER SWITCH IN ON POSITION 
    WHEN NOT READING OR WRITTING KEYS
(3) CORRECTS PROBLEMS IN DOC FILE (SWITCH SETTING WERE INCORRECT ON FIRST
    RELEASE)
(4) ADD PATCH LOCATION FOR S/N, KEYS, AND TIER MASK IN CHIP TO DOC FILE

NOTE: ALL OTHER RELEASES OF THIS CHIP SHOULD NOT BE USED 
      CURRENT RELEASE LEVEL 4.5
      "TESTRON POCKET PAL IS RELEASE 1 OF THIS CHIP
      AND DOES NOT INCLUDE THE FIXES TO PROBLEM IN EARLY RELEASES
      OF THIS CHIP"

PATCH LOCATION FOR S/N, KEYS, AND TIER MASK

	        LOCATION IN CHIP STARTING OFFSET=C000
		2.4 IMAGE	3.0
S/N		ED20		F520
KEY0		ED30		F530
KEY1		ED40		F540
KEY2		ED50		F550
KEY3		ED60		F560
EVEN TIER MASK	E900		F100
ODD TIER MASK	E963		F162
SERVICE ID'S    		F266 F268 F26A (SET TO ID "C4" OR "A5")

VCIIIDIG FUCTIONS

MAIN MENU
1 = VIEW SRAM
2 = READ KEYS
3 = RESTORE KEYS
4 = RESTORE U20 SRAM
5 = MOFIFY SRAM
6 = MONTHLY KEYS
7 = REMOVE CHIP
8 = SERIAL PORT


SUB MENU'S
(1 = VIEW SRAM)
ALWAYS STARTS AT ADDRESS 6000
RIGHT > WILL ADVANCE 3F hex LOCATIONS
LEFT < WILL  DECREMENT 3F hex LOCATIONS
CANCEL WILL EXIT TO MAIN MENU
ENTER AND 0-9 = NEW ADDRESS
ENTER IS USED AS X10 KEY (EXAMPLE NEW ADDRESS 6FC2 INPUT AS 6 ENTER 5 ENTER 2 2)

(2 READ KEYS)
1 = READ 010X KEYS
2 = READ 018X-019X KEYS
3 = EXIT TO MAIN

TO READ 018X-019X KEYS KEYREADER BOARD IS NEEDED
DISPLAY FORMAT FOR 010X KEYS:

SERIAL NUM: XXXXXXXX

KEY0: XXXXXXXXXXXXXX

KEY1: XXXXXXXXXXXXXX

KEY2: XXXXXXXXXXXXXX

KEY3: XXXXXXXXXXXXXX

DISPLAY FORMAT FOR 018X-019X KEYS

SERIAL NUM: XXXXXXXX
AA BB CC
KEY0: XXXXXXXXXXXXXX

KEY1: XXXXXXXXXXXXXX

KEY2: XXXXXXXXXXXXXX

KEY3: XXXXXXXXXXXXXX

AA=CHECK SUM STORED IN U7
BB= CAL CHECK SUM OF READ KEYS AND SERIAL NUMBER
CC= HEALTH BITE (SHOULD BE "DF" IS GOOD)
STARTING SETUP FOR SWITCHES ARE S5=0000 S7=0101 S1=1110 S2=1111 S4=0000
IF TIME OUT OCCURS DURING KEY READ ON 018X-019X BOARDS PROGRAM WILL JUMP
TO OPENING MENU AND RESET, THIS IS CAUSED BY INCORRECT SWITCH SETTING
CAUSING U7 TO HALT. SWITCH FORMAT IS FOLLOWS:

HEX VALUE	8 4 2 1
74193 INPUTS	D C B A
S5              0 0 0 0
S7              0 1 0 1
S1              1 1 1 0
S2              1 1 1 1 
S4              0 0 0 0

(3 RESTORE KEYS)
1 = SETUP S/N
2 = SETUP KEY0
3 = SETUP KEY1
4 = SETUP KEY2
5 = SETUP KEY3
6 = VIEW KEY AND SERIAL NUMBER SETUP
7 = RESTORE 010X KEYS
8 = RESTORE 018X-019X KEYS (REQURIES KEY READER/WRITER BOARD)
9 = EXIT TO MAIN
CANEL = EXIT BACK TO NEXT MENU

USE 1-5 TO SETUP NEW SERIAL NUMBER TO BE INSTALLED 
USE 6 TO VIEW KEY AND SERIAL NUMBER SETUP
USE 7 TO RESTORE KEYS TO OLD STYLE BOARDS (010X)
USE 8 TO RESTORE KEYS TO NEW STYLE BOARDS (018X-019X)

STARTING SETUP FOR SWITCHES ARE S7=0000 S5=0101 S1=0110 S2=0101 S4=0000
ALL INPUT ARE 0-9 AND FOR A=ENTER 0, B=ENTER 1, C=ENTER 2, D=ENTER 3
E=ENTER 4, F=ENTER 5
IF TIMEOUT OCCURS DURING RESTORING KEYS ON 018X-019X BOARDS, PROGRAM WILL
RESET AND JUMP TO OPENING MENU, CHECK SWITCH SETTING AND RETRY.

HEX VALUE	8 4 2 1
74193 INPUTS	D C B A
S5              0 0 0 0
S7              0 1 0 1
S1              0 1 1 0
S2              0 1 0 1 
S4              0 0 0 0


(4) (RESTORE U20 WITH GOOD IMAGE)
1 = RESTORE TO VERION 2.4
2 = RESTORE TO VERION >3.0
3 = EXIT TO MAIN

IF RESTORE FOR A5 BOX LOCATION 6266-626A WILL HAVE TO BE CHANGED WITH
FUCTION 5 MODIFY SRAM
6266=2X 6267=A5 6268=2X 6269 A5 626A A5 IN 3.0 IMAGE

(5 MODIFY SRAM )
VALID ADDRESS ARE 0-FFFF
ALL INPUT ARE 0-9 AND A=ENTER 0, B=ENTER 1, C=ENTER 2, D=ENTER 3, E=ENTER 4
F=ENTER 5
DISPLAY ARE AS FOLLOWS:
XXZZ
XX=CURRENT CONTENTS
ZZ=NEW CONTENTS
> = ADVANCES TO NEXT LOCATION WITHOUT CHANGING CURRENT
CANCEL = EXITS TO MAIN
ENTER = x10

(6 MONTHLY MASK)
1 = DISPLAY MONTHLY MASKS FOR VER. 2.4 BOXES
2 = DISPLAY MONTHLY MASKS FOR VER 3.0 AND GREATER
3 = EXIT TO MAIN
CANCEL KEY WILL RETURN TO MAIN MENU

(7 REMOVER CHIP

WARNING USE THIS FUCTION ONLY IF FUCTIONS 3 OR 5 IS USED FOR IT
CLEAR 6500-6600 THAT IS USED AS KEY BOARD BUFFER AND KEY STORAGE BUFFER.

(8 SERIAL PORT)
1 = TURN ON SERIAL PORT
2 = TURN OFF SERAIL PORT
3 = EXIT TO MAIN

USED IF YOU HAVE SERIAL PORT INSTALLED ON VCII BOARD
OUTPUT IS 1200 8 N 1

COMMENTS:
THIS CHIP NEEDS NO VC SIGNAL TO OPERATE
WHEN SRAM IS DISPLAYED THE CURRENT CONTENTS OF U20 REMAIN
CHANGED, THIS ROUTINE ONLY USES U19 REGISTERS ON LEAVES U20
UNCHANGED. 

SWITCH ON READER/WRITER BOARD SHOULD BE ONLY SWITCH TO ON (RUN)
POSITION WHEN DIRECTED BY MENU.

DO NOT CHANGE CODE FOR I HAVE INSTALLED TRAPS THAT CHECK FOR
CODE CHANGES. THE RESULTS WHO KNOWS!!!!
 
THE FOLLOWING PROGRAMS ARE INCLUDED
VCIIIDIG.ROM = VCIII DIAG CHIP
KEFIX.BIN = NOT NEEDED IN THIS RELEASE (FIXED IN RELEASE DATE 1-1-1989)
VCIIIDIG.DOC = DOC FILE FOR THIS CHIP
READER  = ORCAD IMAGE FOR KEY READER/WRITER (SAME BOARD DOES BOTH CONNECTION
          STAY TO SAME ON VC BOARD)
SERIAL = ORCAD LOGIC FOR ADDING SERIAL PORT TO VCII BOARDS (DO NOT INSTALL
         ON IRD'S)

TO INSTALL KEY READER/WRITER IN TO FOLLOWING ORDER
1= +5 TO U9 PIN 14
2= GND TO U9 PIN 7
3= TRIGGER TO U19 PIN 10
4= CLOCK(3.57mhz) TO U19 PIN 2
5= CLOCK(14mhz) TO U31 PIN 3
6= LOAD COUNTER TO DOUBLE 0--0 NEXT TO U9 PIN 8 OR PIN 7 OF EDGE CONNECTOR
7= CLOCK OUT TO U7 PIN 17 OR RIGHT SIDE OF LEG OF 68pf CAP (REMOVE THIS CAP
   TO PULL KEYS)
REMOVE IN REVERSE ORDER
FOR NEWER BOARDS THE TIMING HAS CHANGED, THEIR IS NOW A CRYSTAL(2.4mhz),1MEG 
RESISTOR, AND TWO(2) CAP. 
TO PULL KEY ON THIS BOARD REMOVE THE CRYSTAL AND 2 CAP AND INSTALL 5K ACROSS
1 MEG INSTALL CLOCK OUT TO THE LEFT SIDE OF 5 K RESISTOR

NOTE: 
ON SOME NEW BOARDS THE 68pf CAP AND TRIM POT HAVE BEEN REPLACED WITH
A CRYSTAL, 1MEG RESISTOR AND TWO CAPS, THE FOLLOWING THE NEW LOGIC:
ONE SIDE OF CRYSTAL GO TO U7 PIN 17 THE OTHER TO U7 PIN 18
THE CAP ARE PADS FOR THE CRYSTAL WITH ONE SIDE TO GND THE OTHER
TO THE CRYSTALL.
THE RESISTOR IS ACCROSS U7 PIN 17 AND 18
BE CAREFULL ON TO GND PIN 17 ARE 18 OF U7
THE BEST WAY TO REMOVE THE CRYSTAL AND CAP IS TO CUT
THEM IN HALF LEAVING THE LEG IN PLACE.

BOARD LOCATION FOR NEW BOARDS:


       			     	l	l
			   --	l	l
TO GND	--------[cap]	   * 	l u7	l
TO GND	--------[cap]	   *	l	l
TO U7 PIN 17----[resistor] --	l_______l
                 1meg           
	*
	* = crystal(2.4mhz)
AFTER KEYS ARE PULLED LEAVE 5 K RESISTOR AND INSTALL 68pf FROM LEFTS
SIDE OF 5 K RESISTOR IF ONE TO THE LEFT HAND LEGS OF TWO REMOVED CAPS.

				

HAVE FUN!!!!!!!!!!!!!!


NEXT RELEASE WILL CHANGE THE INPUT FOR A-F FROM ENTER 0-5 TO
ENTER 1-6 

Downloaded From P-80 International Information Systems 304-744-2253