COMPUTER PROGRAM LINELOSS

            The program LINELOSS is a versatile program capable of doing
       a   variety   of  calculations  related  to  power,   VSWR,   and
       transmission  line  losses.   The  program,  and  the   following
       explanatory  and  tutorial  information, is  excerpted  from  The
       Meteor Burst Communications Handbook, by Jacob Z. Schanker.  This
       handbook  was  prepared  under  U.S. Air  Force  Funding.  It  is
       expected  that it will be available through the N.T.I.S. late  in
       1988.

       TRANSMISSION LINES

       Losses  in  coaxial  transmission lines can  have  a  significant
       effect on system performance. The losses negatively affect system
       performance  in  several  ways.  Therefore,  reducing  coax  loss
       provides multiple benefits. In fact, reducing coax loss is one of
       the easiest, and least expensive, ways to improve  communications
       system performance. These are the factors involved:

              1)  Loss in the transmission line between transmitter  and
              the  antenna  reduce the power delivered to  the  antenna,
              thus reducing the effective radiated power.

              2) Loss in the transmission line between receiving antenna
              and  receiver increase the effective noise figure  of  the
              receiver, reducing receiver sensitivity.

              3)  Any  standing  waves on  the  transmission  line  will
              increase  the  losses  on the line. That  is,  the  actual
              transmission line loss will be higher than the rated  line
              loss.  This point is of particular significance  since  it
              further  aggravates the negative effects of the first  two
              factors.

            It's  easy  to understand how line loss  reduces  the  power
       delivered  at the end of a transmission line, but the  effect  of
       standing waves in increasing the loss requires some  explanation.
       Whenever  the  load  at the end of a  transmission  line  is  not
       perfectly  matched  to the line, that is when ZL  is  not  purely
       resistive and equal in magnitude to the characteristic  impedance
       of  the  line  Zo,  standing  waves  will  exist.  The  impedance
       inequality at the load will cause power to be reflected back down
       the  transmission  line towards the source. This  reflected  wave
       undergoes  the  same  amount of attenuation  (in  dB.)  that  the
       forward  wave  experienced intitially in travelling  towards  the
       load.   This   attenuation   increases   the   overall,   actual,
       attenuation. The actual attenuation is always greater than the
       rated  line  attenuation, except when a  line  is  perfectly
       "flat" (no standing waves).

            The  load in a communications system is either the  antenna,
       or  the  receiver  input. In either case, it is  unlikely  to  be
       perfectly  matched  to the line, which will normally  be  coaxial
       cable with     50 ohm nominal characteristic impedance. A  multi-
       element  Yagi  beam antenna carefully tuned to the  frequency  of
       operation  may  have a relatively low VSWR, typically  less  than
       1.5,  and possible as low as 1.1. On the other hand,  a  wideband
       log-periodic  beam antenna may have a VSWR above 2.0.  The  input
       impedance  of a typical receiver is only nominally 50  ohms.  The
       actual impedance will vary quite a bit from the nominal, and  the
       VSWR is often between 1.5 and 2.0.

            The   rated  attenuation  for  coaxial  cable  is   normally
       expressed in terms of dB. per 100 feet or dB. per 100 meters. The
       attenuation  is  a  function of frequency of  operation,  so  the
       rating  must  specify the frequency at which the  attenuation  is
       given.  Manufacturer's  literature, handbooks, or MIL  specs  are
       possible sources of this information. Often the rated attenuation
       will be given at 10 MHz. and at 100 MHz. Unfortunately, important
       communications frequencies lie between these two frequencies, and
       attenuation ratings are unlikely to be specified at the  specific
       frequencies of operation.  Since the attenuation of coaxial cable
       varies  approximately as the square-root of the frequency  ratio,
       it is possible to make a useful estimate of rated attenuation  at
       specific   frequencies  from  the  rated  attenuation  at   other
       frequencies.

            Module  7  of  the MBC Programs, LINELOSS, may  be  used  to
       calculate  the rated line loss at a particular  frequency,  given
       rated line loss at some other frequency. Once the rated line loss
       is  known,  the actual line loss can be calculated  for  whatever
       value of VSWR exists on the line. The program also expresses true
       line   loss  as  an  operating  efficiency   figure.   Additional
       calculations provided in LINELOSS are conversion between  forward
       and reflected power and VSWR.

            It's  useful  to plug some numbers into  LINELOSS  and  play
       around a bit. The importance of low transmission line loss should
       soon  be apparent. Low VSWR is also helpful, but often is not  as
       easily   controllable.  As  an  example  of  the   considerations
       discussed  above,  and of the use of the  program,  consider  the
       following:

            A  meteor burst system operates at 40 MHz. The  remote  site
       operates   in   half-duplex  with  the  meteor   burst   terminal
       (transmitter/receiver)  connected  to a 5  element  Yagi  antenna
       through  150 feet of RG8A/U type coaxial cable. The VSWR  of  the
       antenna is 1.30. Use Module 7 to find the true loss in the  line,
       the  line  operating  efficiency, and the apparent  VSWR  at  the
       terminal end of the line.

            The  rated attenuation of RG8A/U, from manufacturer's  data,
       is  0.56 dB. per 100 feet at 10 MHz. From the Main  Menu,  choose
       selection  2, "FIND RATED LINE LOSS AT OPERATING  FREQUENCY  FROM
       RATED VALUE AT ANOTHER FREQUENCY." The rated line loss, 0.56  dB.
       is  entered  first. The actual line length, 150  (feet)  is  then
       entered  in response to the prompt. Next, the frequency at  which
       the  rating  was  given, 10 (MHz.) is entered,  followed  by  the
       actual  operating  frequency  of  40  (MHz.).  The  program  then
       calculates  the rated attenuation for 150 feet at 40  MHz.  using
       the approximation that attenuation is proportional to the  square
       root  of  the actual frequency divided by the  rating  frequency.
       This  is accurate enough for most purposes. Note that  the  value
       obtained from the program is 1.7 dB. Choose selection 2 to return
       to the Main Menu, we then choose selection 4 "CALCULATIONS, USING
       CONDITIONS AT ANTENNA END", since we know the VSWR at the antenna
       end. The rated line loss for the length of line being used, which
       we  just found to be 1.7 dB. is entered first. The  program  then
       asks us to enter any additional losses in the transmission  path.
       These  could be due to filters, diplexers, or  other  accessories
       which exhibit some insertion loss. In this case, we assume  there
       is no additional loss and so enter 0. Finally, we enter the known
       VSWR at the antenna, 1.3, in response to the prompt.

            The program then calculates that the VSWR at the transmitter
       end  is  1.19.  This  points  up  the  fact  that  for  a   lossy
       transmission line, the VSWR at the transmitter (source) end  will
       always be less than the VSWR at the antenna (load) end. This is a
       result  of:  (1) the forward power delivered to  the  antenna  is
       reduced by the line attenuation, and, (2) the resulting reflected
       power caused by the antenna mismatch is further attenuated on its
       return trip to the transmitter end. Since VSWR is proportional to
       the  ratio of reflected power/forward power, the transmitter  end
       sees a lower reflected power and a higher forward power than  the
       antenna end, hence a lower VSWR.

            Then  program the calculates that the true overall  loss  in
       the  line  (accounting for the effect of VSWR on the  rated  line
       loss)  is  1.74  dB.,  and that  the  overall  transmission  line
       operating  efficiency is 67.0%. Note that, in this  example,  the
       VSWR  on  the line contributed negligible  (.04  dB.)  additional
       loss.  Since  the VSWR was relatively low (1.3) this is  not  too
       surprising. But what if the antenna VSWR was 2.5? This is a value
       which  might be seen with a log-periodic type antenna, or with  a
       field  expedient  antenna.  It is suggested that  the  reader  go
       through  the calculations for this case. The result is  that  the
       true line loss is 2.20 dB., an increase of 0.5 dB. over the rated
       line loss which would be exhibited for unity VSWR.

            As another example, consider that in the previous example we
       did  not  know  the VSWR of the antenna. However,  using  a  BIRD
       wattmeter  or  similar  instrument,  the  forward  power  at  the
       transmitter  end  was measured as 300 watts,  and  the  reflected
       power  as  20  watts. This may seem pretty good,  but  it  isn't.
       Choose  selection 1 "CONVERT BETWEEN VSWR AND  REFLECTED  POWER",
       from the Main Menu. Entering our values, we find that the VSWR is
       1.70.  Returning  to  the  Main Menu  and  choosing  selection  3
       "CALCULATIONS, USING CONDITIONS AT TRANSMITTER END", the  program
       calculates  that  the true VSWR at the antenna end is  2.24,  and
       that  the true overall loss is 2.09 dB. This is 0.39  dB  greater
       loss than the rated line loss of 1.7 dB. The calculated operating
       efficiency  is 61.8%. This means that the actual power  delivered
       to  the  antenna  to  be radiated is 0.618  X  (Forward  Power  -
       Reflected Power) or   0.618 X (300 - 20) = 173 watts.

       Additional reference:

1      "Program Finds True Transmission Line Loss" EDN, February 18, 1981