440 SPOILER USER'S MANUAL
                                 VERSION 1.01

     There is  only one task that you have to undertake to get the 440 Spoiler
working for  your radio-operating  pleasure.   You  must  connect  your  MSDOS
computer to  your TS-440S.  After your transceiver and computer are connected,
you are at your leisure to learn how to use the Spoiler by trial and error, by
reading, or by a most-efficient combination of both activities.

COMPUTER/TRANSCEIVER CONNECTION

     Your simplest  way  to  physically  connect  your  transceiver  and  your
computer is  for you  to obtain an RS-232 interface box and integrated-circuit
chip set marketed by Kenwood.  You will also need a serial cable to connect an
RS-232 output  of your computer to the interface box.  The interface box, chip
set, and cabling will cost you approximately $100 retail.

     Optionally, you  might want  to obtain  a switch so that your RS-232 port
for devices  other than  control of  your TS-440S  at the  flip of  a  switch.
Connectors and  people can  stand only  so much plugging and unplugging, but a
simple switch solves both problems.

     A more-complex,  but much  cheaper, way  is for you to make up the cables
and build  an interface  box.  It is beyond the scope of this manual to detail
how the  equipment should  be constructed, but construction is a simple matter
if you  are familiar with digital technology.  In the do-it-yourself approach,
you can  expect to  save approximately $65 frugal dollars, but you'll probably
spend about 10 hours on construction and testing.

     When you have the box and the cables in hand, plug them up.  Turn on your
transceiver, and run the Spoiler.

     If something  is amiss in the hardware (the transceiver, the cabling, the
interface box, or the computer), the spoiler will tell you upon installation.

INSTALLING THE SPOILER

     The Spoiler provides for installation when you first run it.  It asks you
for the  number of  the serial port (1 or 2) your TS-440S is connected to, and
then then  it reads  all 110  memories in the transceiver.  The Spoiler writes
these memories  to a  disk file  named DEFAULT.MRY  and makes DEFAULT.MRY your
currently open file.

     During installation,  the Spoiler  writes an  initialization  file  named
SPOILER.DEF.   This file  stores your  serial port  number and the name of the
disk file  that is  currently opened.   If  you ever  want  to  reinstall  the
Spoiler, simply delete SPOILER.DEF from your current directory (or diskette).

     You will  quite likely  alter the  contents of  your  TS-440S  memory  by
exploring the  operation of  the Spoiler.  If you want to save the contents of
your transceiver  memories so  that you can restore them to be exactly as they
were before  you used  the Spoiler,  you'll want  to go  through the following
procedure that follows.

     Issue a  Memory Management command by pressing F6.  At the command-option
prompt, enter  the NEW option by pressing the N key or pressing F3.  You'll be
asked to  enter a  file name  (2 through  8 alphanumeric  charcters  with  the
extension ".MRY"  assumed by  the program) for a new disk file for you to work
with.   The new file that the Spoiler produces will initially have exactly the
same contents  as DEFAULT.MRY,  and your can proceed with your installation in
the security  of knowing  that all  changes you  make to  TS-440S  memory  are
affecting only  the transceiver and your new file.  If you want to restore the
memories in the TS-440S to exactly what they were before your exploration, you
should perform the following procedure.

     Open the  DEFAULT file  by pressing F6 and choosing the O (or F1) option.
Enter the file name DEFAULT at the prompt.  The Spoiler will load the original
memory values  into your  TS-440.   If you  don't want  to alter  the original
memory contents, you should then immediately quit the Spoiler by pressing F10.
Your transceiver  memories will  be restored to the same as they were when you
first ran the 440 Spoiler.

     You'll want  to follow this procedure each time you work with the Spoiler
therefore if  you want  to save  your  original  memory  information  in  your
transceiver.   When you  feel comfortable  with your operation of the Spoiler,
you will want to alter the memories often, as the Spoiler permits you to do at
will.

COURSING THROUGH THE SPOILER

     You should  initially consider  the Spoiler  a display  window  into  the
operation of  your TS-440S.  All operating parameters are displayed in the box
to the  upper-left of  your screen, and all memory information is presented in
the J-shaped  (largest) box  to the right and bottom of your screen.  When you
change any  operating parameter  (frequency, mode, split, RIT, XIT, source, or
memory) from  the TS-440S  front panel,  the Spoiler  updates its  display  to
reflect the change.

     Later, you  should work  with the  Spoiler commands that are initiated by
your pressing  the function keys listed at the bottom of the Spoiler operating
screen.  Using the Spoiler, you'll find that you have little use for the front
panel of  your TS-440S  except for such "analog" functions as your controlling
volume, passband  tuning, antenna  tuning (if  your transceiver has an antenna
tuner installed, and the like.

     The 440  Spoiler, combined  with the  operating  power  of  the  TS-440S,
provides you  with a  quantum leap in radio communications ability.  You'll be
able to operate many traffic nets simultaneously, and you'll quickly find your
DX tallies  among only  those possessed  by other  operators who are using the
Spoiler.   If you  are looking  for world  news from  international  shortwave
broadcasts during whatever international crisis the future brings, you'll find
it much  faster with  the Spoiler.   If  you're looking  for  music  broadcast
throughout the  world, you'll  find your  selection to be both wide and quick.
If you  want to  know what the CB citizenry has evolved into, the Spoiler will
help you find out with convenience that rewards your curiosity.

DETAILED OPERATION

     The Spoiler includes features to tremendously aid your operating work and
play with  the TS-440S,  and it  would be  very boring  for you  to read about
features that are of use to someone else.  The 440 Spoiler Technical Reference
Manual provides a description of the features for you to reference as you need
to use  them.  The technical reference manual, though not suitable for bedside
reading for  anyone without  insomnia, is  your informational  friend during a
time that you have needs.

SUPPORT


     As with all shareware, the 440 Spoiler is supported largely for those who
obtain registered  copies of  the software  and documantation.    The  QSO2000
project is  not Microsoft  Corporation, and  nobody in the project wants it to
become more than a cooperative endeavor among the avant garde communicators of
the world so that the world can become better, faster.

     You are  welcome to  write with  comments and  questions to the following
address.

                         Bill Brewer. K5KNC, Coordinator
                         The QSO2000 Project
                         5518 12th Street
                         Lubbock, Texas 79416

     If you are a registered user of the Spoiler, you may also telecommunicate
your comments  and questions  to the project at the home bulletin board of the
Spoiler.  To access the bulletin board, use the following information.

                         Bulletin Board ECHO (Education)
                         Wireless Conference (conference number 4)
                         806-741-1570
                         24 hours, 7 days a week
                         1200-2400 baud and USR/HST 19200 baud

     The latest  shareware release of the 440 Spoiler is always available from
the Wireless Conference of ECHO (Education).