Morse Code Transceiver Version 1.0 MS-DOS


INTRODUCTION 

        Morse Code Transceiver Version 1.0 MS-DOS is an assembly language 
program for use on IBM PC, XT, AT and Compatibles running the MS-DOS Version 2 
or above. Both monochrome and color monitors are supported. This program was 
developed for use by Amateur Radio operators or others who need a program that 
is capable of both sending and receiving morse code over a wide range of code 
speeds and operating conditions. Many powerful convenience features are 
incorporated enhancing station operation in the CW mode together with ease of 
operation. 

        Morse Code Transceiver Version 1.0 MS-DOS is Shareware therefore under 
the conditions that it is not modified and a fee is not charged it may be 
copied and distribution to others is encouraged. 

******* DISCLAIMER:--- No liability assumed. --- No warrenty implied. ******* 

AUTHOR 

Robert R Anderson, K2BJG 69 Page Drive Oakland, New Jersey  07436 

Phone: 201-337-7858 or 337-9644 


STATION INTERFACE 

        Morse Code Transceiver receive input data, transmit output data and a 
transmit control output signal are at RS 232C level via serial port 1 or 2.  
External hardware interface equipment is required to demodulate and translate 
CW audio signals from the station receiver to RS 232C level for input to the 
computer and to translate RS 232C level TX CW keying and TX control signals 
from the computer to that required by the station transmitter. A negative 
level is 'off' and a positive level is 'on' for all signals. 

        Pin  1          Protective Ground 
        Pin  4  (rts)   R/T Transmitter Control 
        Pin  5  (cts)   CW Receive Input 
        Pin  7          Signal Ground 
        Pin 20  (dtr)   CW Transmit Output 

        Commercial computer interfaces such as the MFJ 1224 are currently 
available and will work with this program. For those who want to "roll their 
own" a suitable unit can easily be constructed using parts readily available 
from such retail electronic parts suppliers as Radio Shack. To aid in the 
design of a suitable CW computer interface unit the following guide lines 
should be followed. Detail circuit design information and practical examples 
can be found in the ARRL Radio Amateurs Handbook. 

        The transmit channels of the interface unit consisting of the transmit 
CW data from pin 20 and the transmit control signal from pin 4 should be 
translated from RS 232 level to TTL level by use two sections of a MC1489 RS 
232 Quad Line Receiver. The CW keying TTL signal must then interface to the 
station transmitter. The circuit required to accomplish this depends on the 
requirements of the transmitter. Older transmitters using grid block keying of 
tubes will probably require what is called negative keying where a key up 
relative high negative voltage of as much as 50 to 150 volts is seen and key 
down current of a few miliampers is required. Late model solid state 
transmitters will probably require what is called positive keying where a key 
up relative low positive voltage of about 20 volts is seen and key down 
current of a few miliampers is required. A single transistor of suitable 
voltage rating and polarity will do the job however if your interface needs to 
be universal then a dual transistor circuit to handle both types of keying 
should be used.  

        Interface of the TTL transmit control signal to the transmitter PTT 
line is not required if transmitter VOX circuits will do the job for your 
operating technique. It is however better to use this signal since VOX delays 
can cause problems at low keying speeds or when quick break in is desired. 
Also this control signal is necessary to hold the transmitter on during a 
pause between characters if operating in manual TX to RX program mode. A 
single transistor of suitable voltage rating and polarity and able to handle 
the required current will do the job. 
 
        The receive channel of the interface unit should consist of an audio 
bandpass filter, a demodulator with a low pass filter and a level translator 
to furnish input RS 232 level receive data to pin 5. 

        The band pass filter function can be accomplished with one or more 
operational amplifiers configured as active filters. The center operating 
frequency should match your receivers CW beat frequency offset. This is 
usually about 800 to 1000 Hz for most amateur receivers. The bandwidth should 
be about 100 to 200 Hz. 

         The demodulator can be a simple diode detector followed by a low pass 
active filter with a cutoff frequency of approximately 75 Hz. A better method 
is the use of a phase lock loop decoder tuned to the same frequency as the 
audio filter. 

         Level translation of the signal from the demodulator to RS 232 level 
is best accomplished by using one section of a MC1488 RS 232 Quad Line 
Driver.                   


PROGRAM INITIALIZATION 

        The Morse Code Transceiver program CW.EXE and if they exist it's 
associated configuration or data files CW.CNF, CW_KCS.DAT, CW_MSG and 
CW_FXS.OVL must to be successfully loaded be located in the same directory on 
the default disk drive. 
        The program is started by typing CW at the DOS prompt. Initial checks 
of the DOS version and current video mode are made. The program is terminated 
with an error message if the DOS version is not 2.0 or above or if the video 
mode is other than 80 X 25 TEXT - color mode 2 BW80, color mode 3 CO80 or mode 
7 MONO. 
        At this point only the main program CW.EXE has been loaded. It 
contains all required default configuration data.  Next if it is found the 
configuration file CW.CNF is read from the default disk drive replacing the 
default configuration data. If the configuration file is not found an error 
message is displayed.   

2
        The default or config file configuration data mow in memory includes 
color video attribute data to be used for color display. The current video 
mode is again checked. If it is mode 3 CO80 no action is taken. If it is mode 
2 BW80 or mode 7 MONO then black/white attributes for normal and the reverse 
video used for the status line replace the existing video attribute data.   
Note - The DOS mode command can be used prior to starting CW to select the 
desired video mode. 
        The data files CW_KCS.DAT (key character sequences) and CW_MSG.DAT (10 
messages) are loaded if they are found. If they are not found error messages 
are displayed. 
        The fixed TX speed overlay file if found is loaded replacing default 
fixed TX speed data. A message is displayed indicating that it is or is not 
loaded. 
        At this point the operator is prompted to see if initialization should 
continue. Pressing (ESC) will cause an immediate return to DOS. Any other key 
will cause program initialization to continue. Upon initialization completion 
the operating screen is displayed and the bell will sound indicating ready to 
start. 


DEFAULT CONFIGURATION and THE CONFIGURATION FILE (CW.CNF) 

        The main program CW.EXE contains default configuration data. It can 
operate without reading the configuration file CW.CNF. It has the means to set 
all variables contained in the configuration file which can be created or 
updated as an option during program exit. The configuration file if it exist 
on the default drive is read during program initialization replacing default 
configuration data. 
        The following program variables are included in the configuration file 
CW.CNF and the default values contained in the main program CW.EXE are 
indicated: 

        Variable                        Default 

        I/O Port                        03F8h           #1 
        Auto TX flag                    0               off 
        Auto RX flag                    0               off 
        Speaker flag                    0               off 
        Upper screen color attribute    30              yel/blu
        Lower screen color attribute    31              h-wht/blu
        Review buffer color attribute   31              h-wht/blu
        Window color attribute          112             blk/wht
        Window border color attribute   116             red/wht
        Status line color attribute     79              h-wht/red
        Tx Dot length                   30 
        Tx Dash length                  90 
        Tx Element space                30 
        Tx Character space              90 
        Tx Word space                   120 
        Rx Dot average length           30 
        Rx Dash average length          90 
        Rx Element average length       30 
        Tx Variable dot                 30 
        Tx Variable element space       30 
                                        00


3
COMMAND SUMMARY 

The following commands are available from CW 

F1      Display Help # 1
F2      Toggle Output to Printer - on/off
F3      Toggle Capture function - on/off
F4      Display Disk Directory
F5      Toggle TX Source - Keyboard/Send File
F6      Transfer Selected Message to Xmt Buffer 
F7      Toggle RX speed mode - Track/Manual
F8      Toggle TX speed mode - Manual/Lock RX speed
F9      Toggle Speaker - on/off
F10     Toggle Mode - TX/RX 

Shf-F1  Display Help # 2
Shf-F6  Preview Selected Message on Lower Screen
Shf-F7  Select RX speed LOCK mode
Shf-F8  Toggle TX speed mode - Fixed/Manual 

Alt-F1  Display Help # 3
Alt-F3  Toggle Capture File - open/close
Alt-F4  Change Drive\Path
Alt-F5  Toggle Send File - open/close or restart
Alt-F6  Toggle Selected Message - Load/Finish
Alt-F10 Toggle TX Control auto/manual 

Ctl-F1  Display Help # 4
Ctl-F3  Save Review Buffer
Ctl-F4  Delete Disk File 
Ctl-F5  Clear Keyboard Buffer
Ctl-F6  Save Messages to Disk
Ctl-F8  Create a Fixed Tx Speed Overlay File
Ctl-F10 Toggle RX Control auto/manual 
                
Alt-1   Select Message # 1
Alt-2   Select Message # 2
Alt-3   Select Message # 3
Alt-4   Select Message # 4
Alt-5   Select Message # 5
Alt-6   Select Message # 6
Alt-7   Select Message # 7
Alt-8   Select Message # 8
Alt-9   Select Message # 9
Alt-0   Select Message # 10 
        
Alt-C   Select Color Attributes
Alt-K   Program key sequences
Alt-P   Select CW I/O port
Alt-X   Exit  

Up Arrow        Increase TX speed
Pg Up           Increase RX speed
Left Arrow      Decrease TX weight
Right Arrow     Increase TX weight
Down Arrow      Decrease TX speed
Pg Dn           Decrease RX speed
Insert          Display review buffer
Delete          Exit review buffer display 


4
All characters that are displayed on the upper screen are saved in the 
"review" buffer.  Once the screen is full and data has scrolled off the top of 
the screen this buffer may be displayed by pressing the Insert key then 
scrolling through it by using the Home, Up-Arrow, Pg-Up, End, Down-Arrow or 
Pg-Dn keys. Upon entry the current (newest) page remains on the screen. The 
Up-Arrow key will display the previous line and depending on the data 
available in the buffer the Pg-Up will display all or part of the previous 
page. The Home key will display one page starting with the oldest available 
data in the buffer. The Down-Arrow key will display the next line and 
depending on current position the Pg-Dn key will display all or part of the 
next page. The End key will display one page ending with the newest data in 
the buffer. The console bell will sound and entry will not be allowed if the 
screen is not full or scrolling past buffer ends is attempted. The Del key 
will exit the review mode.  

F1 (Help) Key Functions: F1 will display Help menu # 1 on the lower screen. 
This menu includes Help Subjects, Printer Control and Capture Functions. Shf-
F1 will display Help menu # 2 on the lower screen. This menu includes Disk 
Functions, Send Data Functions and Message Functions. Alt-F1 will display Help 
menu # 3 on the lower screen. This menu includes Rx and Tx Speed Mode and 
Control Functions. Ctl-F1 will display Help menu # 4 on the lower screen. This 
menu includes Speaker Control, Rx and Tx Control Functions and Other 
Functions. 

F2 (Toggle) will turn on data output to the Printer. In this mode all data 
that is displayed on the upper screen will also output to the Printer. A 
carriage return and a line feed ASCII character sequence is inserted in the 
data stream causing printer response at the end of each upper screen line. 
Pressing F2 again will output carriage return and a line feed ASCII character 
sequence and cut off data output to the Printer. 

F3 (Capture) Key Functions: 

F3 (Toggle) will turn on the Capture function. In this mode all data that is 
displayed on the upper screen is saved in the Capture buffer. The contents of 
the Capture buffer will automatically be written to disk whenever the buffer 
is full. Pressing F3 again will turn off the Capture function. 

Alt-F3 (Toggle) will display a file name prompt to open a Capture file. A new 
file name will cause a new file to be created. If the file name exist a prompt 
will be displayed. Available options are: (ESC key) to abort, (E) to erase the 
existing file and start a new file or (A) to append new data to the existing 
file. Once this file is open the Capture function controlled by the F3 key is 
allowed. Pressing Alt-F3 again will turn off the Capture function, write the 
contents of the Capture buffer to the disk and close the Capture file. 

Ctl-F3  will display a file name prompt to specify a file to write the entire 
contents of the review buffer to a disk. A new file name will cause a new file 
to be created. If the file name exist a prompt will be displayed. Available 
options are: (ESC key) to abort, (E) to erase the existing file and start a 
new file or (A) to append new data to the existing file. 

F4 (Disk) Key Functions: 

F4 will cause the current directory file names to be displayed on the lower 
screen. If more are in the directory than can be displayed a prompt is 
displayed indicating that F4 can be used again to display more. Any key will 
return to the normal lower screen. Program operation can continue during 
directory display. 


5
Alt-F4 will cause the current drive and directory to be displayed on the lower 
screen followed by a prompt to change the drive or the directory. To change 
the current drive enter a valid drive letter followed by a colon and return. 
The new drive and directory will be displayed. A non valid drive specification 
will cause an error message. To change the directory on the current drive 
enter a \ followed by the directory path and return. the new drive and 
directory will be displayed. ESC may be used to abort.    

Ctl-F4 will display a file name prompt to specify a file to delete a disk 
file. (ESC) can be used to abort. 

F5 (Send) Key Functions: 

F5 (Toggle) will turn on the Send File function. In this mode data contained 
in the Send buffer is transmitted instead of data from the keyboard buffer. 
The disk will automatically be read as required whenever the buffer is empty 
until the end of file is reached. Pressing F5 again will turn off the Send 
File function returning to transmission from the keyboard buffer. 

Alt-F5 (Toggle) will display a file name prompt to open a file for subsequent 
transmission. Once this file is open the disk will automatically be read to 
transfer initial file data to a buffer and TX source selection controlled by 
the F5 key is allowed. Pressing Alt-F5 again will display a prompt. Options 
are to turn off the end file function and close the send file, reset the send 
file pointer to the beginning of the file for a restart or continue with the 
send file open. 

Ctl-F5 Clears the keyboard buffer. 

F6 (Message) Key Functions: 

F6 will transfer the current selected message (if ready) to the transmit 
buffer. 

Shf-F6  will display a preview of the current selected message (if ready) on 
the lower screen. 

Alt-F6 will allow the operator to enter a new message into the currently 
Selected Message buffer. Upon pressing Alt-F6 a prompt is displayed on the 
lower screen. Options are (ESC) to abort or (Enter) to start loading indicated 
by the selected message status display changing from "Empty" or "Ready" to 
"Load". The message may then be entered from the keyboard. All special 
character sequence keys may be used. The console bell will sound if another 
input character or character sequence causes the buffer to become full. Upon 
completion the Alt-F6 key must be pressed again to end the load process. The 
status display will change from "Load" to "Ready".  If nothing was entered it 
will change to "Empty". 

Ctl-F6 will write all ten message buffers to a disk file named "CW_MSG.DAT". 
This disk file is read and loads all 10 message buffers upon program 
initialization. 

F7 (Rx Speed) Key Functions: 

F7 (Toggle) will change the RX speed control mode from Track to Manual. 
Pressing F7 again will return the Rx speed control mode from Manual to Track. 
In track Rx speed mode Rx speed follows the speed of the received CW signal. 
To prevent received noise from a receiver not tuned to a CW signal from 
driving the track mode Rx speed out of range the mode will switch to manual 
mode if the track Rx speed exceeds approximately 85 WPM. In manual Rx speed 

6
mode Rx speed is controlled from the keyboard. 

Shf-F7 will change the Rx speed control mode from Track or Manual to Lock. 
This Rx speed mode performs Rx speed Lock function by measuring the next 16 CW 
pulses then calculating and setting a new Rx speed. Upon completion of the Rx 
speed Lock process the Rx speed mode is automatically returned to Track.  

F8 (Tx Speed) Key Functions: 

F8 (Toggle) will change the Tx speed control mode from Manual to Lock Receiver 
Tx speed control mode. In this mode the transmit code speed will change to and 
will follow the current receiver code speed. Pressing F8 again will return the 
Tx speed control mode to Manual allowing the transmit code speed to be 
controlled from the keyboard.        

Shf-F8 (Toggle) will change the Tx speed control mode from Manual or Lock 
Receiver to Fixed Tx speed control mode. In this mode the operator is prompted 
to enter the desired fixed transmit code speed. Pressing Alt-F8 again will 
return the Tx speed control mode to Manual allowing the transmit code speed to 
be controlled from the keyboard. The default fixed speeds are: S5, f5, 7.5, 
10, 13, 15, 18, 20, 25, 30, 35, 40, 45, 50, 55, 60, 65 and 70 WPM. Slow fixed 
speeds use expanded spacing. As an example the dot, dash and element space of 
s5 (slow 5) are at a 13 WPM rate with character and word spacing expanded to 
produce an overall 5 WPM rate described as 13e5. Similarly f5 (fast 5) is 
16e5, 7.5 is 16e7.5 and 10 is 16e10. Speeds from 13 to 70 WPM use normal 
spacing.                         

Ctl-F8 will display a prompt on the lower screen. The operator may press ENTER 
to create a fixed tx speed overlay file on the default drive or may abort by 
pressing any other key. Upon initial creation this file, CW_FXS.OVL will 
contain the default fixed tx speed control data used by the program when 
operated in fixed speed mode. Upon CW program initialization a check on the 
default drive is performed to see if CW_FXS.OVL exist. If it does not exist, 
the operator is informed that the  fixed tx speed overlay is not loaded. In 
this case the default fixed tx speed control data are used. If it does exist 
then it is read from the disk replacing the default fixed tx speed control 
data and the operator is informed that fixed tx speed overlay is loaded. This 
program feature allows of the fixed tx speed data to changed by editing the 
overlay file. See further discussion in the file CW_FXS.DOC. 

F9 (Toggle) will toggle the speaker on and off. When the speaker is on both 
receive and transmit morse code elements may be heard. 

F10 Key Functions: 

F10 (Toggle) will toggle the operating mode. In receive mode CW input is 
decoded for display and input to buffers and the transmitter control output 
signal is off. In transmit mode the transmitter control output signal is on 
and data from the transmit buffer is encoded and transmitted until the buffer 
is empty. 

Alt-F10 (Toggle) will toggle the TX control mode. In Automatic the operating 
mode is switched from receive to transmit upon data becoming available in the 
transmit buffer. Manual TX mode allows the operator to pretype TX data prior 
to transmission. 

Ctl-F10 (Toggle) will toggle the RX control mode. In automatic the operating 
mode is switched from transmit to receive upon the the transmit buffer 
becoming empty. Manual RX mode allows the operator to hold the transmitter on 
during pauses of CW data transmission. 


7
Alt-1 thru Alt-9 and Alt-0 keys select the current of ten 256 maximum 
character message buffers. The message status display will indicate the 
selected message number followed by "Ready" if the selected message buffer 
contains data or "Empty" if it has not been loaded.   

Alt-C will display a line on the lower screen indicating the  six current 
color attributes in use. (1) Upper screen, (2) Lower screen, (3) Review Buffer 
screen, (4) Window, (5) Window Border and (6) Status Lines. A prompt is 
displayed to enter changes in the format: N=xx. N is one of the six indicated 
screen areas. The attribute xx can be any number 0 thru 127. Refer to the disk 
file on the distribution disk "coloratt.doc" for a complete listing. The new 
color is displayed on the line upon selection. If it is not the desired select 
again. When finished press ENTER to reinitialize all screen display and return 
to the program. Pressing ESC at any time will abort cause return to the 
program with no changes. Alt-C will not operate in video mode 7 MONO.    

Alt-K will prompt the operator to select a key for the purpose of entering a 
new key sequence. Any of the following may be used. After a key is selected 
pressing return will prompt the operator to enter a character sequence. The 
maximum length of sequences may be up to 23 characters long. Another return 
will prompt the operator for Yes/No to save the new sequence to disk. If Yes 
is selected the sequence is written to a disk file CW_KCS.DAT. This file is 
read to memory upon program initialization. If No is selected the sequence can 
be used during the current session. 

        '&' Ampersand key            =  ES 
        ''' Apostrophe key           =  CQ 
        '(' Open Parenthesis key     =  QTH 
        ')' Close Parenthesis key    =  (STATION LOCATION) 
        '*' Asterisk key             =  DX 
        '+' Plus sign key            = 
        ':' Colon key                =  73 
        ';' Semicolon                = 
        '<' Less than key            =  DE 
        '=' Equal sign key           =  RST 
        '>' Greater than key         =  (CALL SIGN) 
        '@' At sign key              =  TEST 
        '[' Open brackets            = 
        '\' Reverse alash            = 
        ']' Close brackets           = 
        '^' Up Arrow key             =  QSL 
        '_' Underscore               = 
        '`' Grave accent             = 
        '{' Left brace               = 
        '|' Vertical bar             = 
        '}' Right brace              = 
        '~' Tilde                    = 

Alt-P will display the currently selected CW I/O port (1), (2) or (E) and a 
prompt on the lower screen. (E) indicates an error condition. Options are (1) 
to select serial port #1 (3F8h), (2) to select serial port #2 (2F8h) or 
(ENTER) to return to the CW program with the current displayed port selected. 
  
Alt-X will display the "Exit CW Program ?" prompt. Options are (Y) for yes, 
(S) to save the config data first and (N) or any key to return to the CW 
program.