SB-804

TR-7625 Intermittent TX                           2-7-80


When servicing a TR-7625 for mechanically intermittent TX, check the heavy
WHITE DRB lead at the push-on connector directly in front of relay RL1 on
the RX TX unit.  This post may either become seperated from the land, or
the land may crack from vibration.  Resolder the post, plus reinforce the
connection with a small piece of solid wire soldered on the foil side of
the board.



JEB/yn
(c) 2780TKC