SB-947
TS-440S OPERATION WITH THE MC-85			   01/20/89


With some TS-440S transceivers, insufficient modulation may
occur when the MC-85 compression switch is turned on. This
may be caused by too much of a voltage drop across resistor
R172 on the IF unit of the transceiver . If this is found to
be the case, change the resistor from 1K ohm to 100 ohms.


REQUIRED PART

100 OHM, 1/6 WATT RESISTOR.......RD14CB2C101J


PROCEDURE:


1.	Disconnect the power supply and antenna from the
	transceiver.

2.	Using a #2 Phillips screw driver, remove the 9 screws
	from the top cover of the transceiver. Remove the cover
	and unplug the speaker wire.

3.	Locate resistor R172 on the component side of the IF
	board (Figure 1).

4.	Using a #1 Phillips screw driver, remove the 7 screws
	that secure the IF unit to the chassis of the
	transceiver.

5.	Pull the board up and rotate it towards the front of the
	transceiver to expose the foil side of the board.

6.	Desolder and remove resistor R172 from the board.

7.	Install and solder the 100 ohm resistor in place of
	R172.

8.	Assemble the transceiver by reversing steps 1 - 5.
This modification may be covered under warranty.
Time required for this modification is 0.5 hrs or less.
(C) 110888TKC