AROEN


     AROEN is an RTTY/PACKET/MORSE operating environment that integrates
A PC compatible with two serial ports, a PK-232, and a KENWOOD TS-440
into a multi-mode system.  Full control of both the PK-232 and the
TS-440 is provided, and the TS-440 frequency and mode are displayed
on the screen, providing complete remote operation, if desired.

     AROEN.MSG is the configuration file for the system.  Line 1 of this
is the PK-232 port.  Line 2 is the TS-440 port.  Ports COM1, COM2, COM3
or COM4 can be used for either the TS-440 or PK-232.  The program uses
the LITECOMM serial I/O library.

     The F1 key provides minimal help with other function key usage.
     After pressing F1, pressing '1', '2', '3', or '4' brings up function
     key usage for F1 - F10, Shifted F1 - F10, Control F1 - F10 and
     Alt F1 - F10.

Alt F10 exits the program.  F5 initiates logging a qso and initialized
called station's call sign.  The next F5 received will either abort the qso
or complete the log entry before initializing the called station's call to 
blanks.

F6 will call a station, using a single line of RY's followed by a line
containing the called stations's call sign (assuming it has been initialized 
by an F5 log entry), your call sign, and the time in UTC.

F3 will initiate a CQ call.  F4 will initiate a QRZ call.

     Comments are solicited.  I've been working on this for several months,
and just recently ported it from DSMET 'C' to Borland's TURBOC.  I'm using
version 1.5.

     Dave LeJeune (K5WNV)
     9510 Ashbourn Drive
     Burke, Va 22015

     (703) 425-9107
     (703) 425-7030