WR9R - Field Day Logging System


                         WARNING.

     This program is not warranted in any way.  When you use this
program, you accept responsibility for the consequences of it's
use and/or misuse.  The author does not guarantee the
applicability of this program or any of it's outputs to your
situation, or the performance of this program in any way.  The
author is not responsible for any loss, corruption, or
destruction of data, or any real or imagined damage to any
physical equipment.


INTRODUCTION.

      In order to have a successful Field Day operation, you must
not only work a ton of stations, but turn in a completed dupesheet
or a sorted log/list of callsigns and a summary.  This program
will log callsigns, associated reports, and QTHs to support a Field
Day's QSOing. The primary intent is to be a real-time data entry
system, that will aid in avoiding duplications and increase the
QSOs/hour by decreasing the hassle.

      All QSOs are logged into a common data base for easy access.
The system can later split the log up by mode and band, into
separate files, sorted into alpha-numeric order by call, and
generate summary sheets.  Approximately 4000 stations with their
reports can be logged, with any duplicate entries detected and
rejected at a very high rate.
    Automatic dupe checking and partial call checking can be disabled
if you wish, speeding up the process (if your computer is a little
slow and you're commanding a pile-up, for example). Partials are
displayed in the lower-left window and can be detected automatically.
Calls displayed in the "Partials" window only apply to the current
operating mode and band, this helps in the detection of duplicates
before the QSO is actually made.
An audible warning is used to help indicate that an entry has been
rejected, along with a pop-open window.
    If a printer is connected to the system, it can be enabled to print
QSOs as they are being entered into the log.
The program is designed such that one person can very easily handle
both logging and operating at the same time.

      The system is designed to work on IBM PC XT,AT,386,clones and
compatibles with 384K of memory and a MONOCHROME, CGA, EGA, or VGA
adaptor.



OPERATION

    Before starting the system, set the computer's clock to UTC time
using the DOS Time and Date commands. If the ANSI.SYS driver is in
your config.sys file, remove it, or comment it out so that it is
not loaded, and reboot. Make a backup copy of the disk for safe
keeping.
To start the system, type in the application name and the data base
file name for the event being logged.   For example:

      C:> WR9R FD1990

    A window will open up that lets you enter the stats about your
station, once this is filled in, press ESC. If you wish
to make changes the window can be accessed through the 'F9=LOGS'
menu.

    A window will open for you to select your operating class which
is used to calculate the multiplier for the event. Use the arrow keys
to select, hit return to keep, or ESC to leave it the same. (This
selection method is common to all windows of this type that you
will see.)
Other windows will open to select the initial band and mode of
operation.

    The QSOs are entered in the left-middle window. The window has
three fields, the SPACE bar or TAB allows you to move from field to
field.  When all three fields are filled in, an ENTER will log the
call and the log will scroll up on the right. The DEL key wipes the
current field.  RIGHT ARROW, LEFT ARROW and BACKSPACE work as
character edit keys.
If you wish to edit an already logged call, the UP ARROW and DOWN
ARROW keys let you access the last 20 QSOs. As the past QSOs are
highlighted, the data is brought into the QSO entry/edit window
where it can be altered. The ESC key will exit this mode without
changing the log, an ENTER will save the changes back to the log.

The menu at the bottom of the screen allows you to access all the
features of the system.

      F1 - Performs a duplicate check on the call currently
           entered in the Call field.

      F2 - Performs a partial check on the characters currently
           entered in the Call field.

      F3 - Allows you to select a different HF band.

      F4 - Allows you to change modes (CW/PHONE).

      F5 - Allows you to change system features such as enabling
           or disabling automatic partial checking, dupe checking,
           and the printer. If you enable the printing function
           make sure the printer is on-line before trying to log
           another QSO.

      F9 - Allows you to create summary sheets and sorted
           log listings. These files are pretty complete but
           you will always want to make sure that all the
           information YOU THINK SHOULD BE THERE is there.
           Bonus points and bonus proof sheets will have to
           be edited into these files or added to the printouts
           manually.

      F10- Exits to DOS.  If there are several hundred or a
           few thousand calls, it may take a little while to reload.
           You may not want to leave very often.



CONCLUSION

    This system is a new release, if there are bugs that need fixing
or features that need adding please feel free to WRITE and tell me
about them. (Remember, there's no such thing as finished software,
if there was... LOTUS, Borland, and MicroSoft would not be in
business!)

Feel free to share this FREE version of the program with other hams.
If you would like information on the most current version or upcoming
releases please send SASE to:

      Larry D. O'Cull
      ARS - WR9R
      3725 Tara Ct.
      Westfield, IN
                  46074

or call (317)-873-4065.  (From 6:00 PM to 9:30 PM EST , please.)