NN5ILOG

                                 component of the

                                NN5I LOGGING SYSTEM


                                Copyright (c) 1985

                                  Carl B. Hayes

                                All Rights Reserved

































                                        1








        The   NN5I  Logging System is  a  simple-to-use,   lightning-fast 
        contest  logging and duping system for the IBM Personal Computer.  
        Written  entirely  in assembler language,  it has  the  following 
        features:

             *  Records callsign, exchange, time, date, and 
                callsign of the local station operator for up
                to 2999 QSOs per BAND/MODE combination.

             *  Will print the log of QSOs completed so far, while
                simultaneously logging additional QSOs.

             *  Prints QSOs in chronological order or in order
                by callsign, or as a standard dupe sheet.

             *  Can print QSOs as they are made (real-time printing).

             *  Essentially immune to loss of power to the PC.  If
                power is lost while logging, only the QSO currently
                being entered will be lost.  The others will still
                be there when power is restored.

             *  Extremely fast DUPE checking.  If the callsign is a
                duplicate, the program will tell you with a flashing,
                bright yellow message as soon as you type in the 
                callsign and hit ENTER.  Usually the message will
                appear before you can remove your finger from the
                ENTER key.

             *  Gives you the option of logging a DUP or not.

             *  Continuously displays date, time, number of QSOs so
                far, callsign of last station worked, and callsign
                of the operator who is operating at the moment.

             *  Printed log marks each DUPE contact and lists the
                date and time of the original QSO.

             *  Includes a post-editor for use after the contest is
                over, for correcting incorrect entries made during
                the contest.

        FREE DEMONSTRATION VERSION

        In  order to allow you to try out the NN5I Logging System without 
        purchasing it first,  the system exists in a DEMO version as well 
        as in the "production" version.  The only difference between  the 
        two  versions is that the DEMO version runs only fifteen  minutes 
        at  a  time and then automatically terminates,  and will not  run 
        again with the same log file.







                                        2








        REQUIRED EQUIPMENT

        In order to run the NN5I Logging System, you need an IBM Personal 
        Computer  or  close compatible with at least 384K of RAM  storage 
        and one 360K diskette drive.  The system will run on hard disk or 
        on diskette and is not copy-protected.  It will also run on a RAM 
        disk,  but this has no effect upon speed and makes it  vulnerable 
        to power loss.   Also recommended is a printer,  without which it 
        will be difficult to print out the results.

        WHAT YOU GET ON THE DISK

        The distribution diskette (in the case of the DEMO version,  this 
        may  be  an  ARC or LBR file downloaded from  a  bulletin  board) 
        contains  several  files.  One  of  them,  NN5ILOG.DOC,  is  this 
        documentation  file.   Another,  NN5ILOG.COM,  is the  executable 
        program  that you run during the contest.   The document you  are 
        reading  is the documentation for that program.   In addition  to 
        these,  you also get NN5IEDIT.COM,  which is the program you  run 
        AFTER  the  contest to make any corrections in the log,  and  its 
        separate  documentation  file NN5IEDIT.DOC.   Also  included  are 
        several  BAT  files  for  use in  hard  disk  systems  for  rapid 
        BAND/MODE switching (see below).

        HOW (BRIEFLY) THE PROGRAM WORKS 

        When  you  execute the NN5I Logging Program,  the first thing  it 
        does is format in RAM (not RAMdisk) a file (requiring 240K  bytes 
        of  RAM) that will contain the logged QSOs.  Then it looks on the 
        default  drive  (diskette  drive  or  hard  drive)  for  a   file 
        NN5ILOG.LOG.   If it finds one,  it reads from it any QSOs logged 
        in  previous executions of the NN5I Logging Program.   If no such 
        file  is present,  it creates one on the default  drive.  In  the 
        process  of creating the LOG file,  the program asks you for  the 
        BAND and MODE.   You may enter up to three characters for each of 
        these;  for instance, 160 SSB.  After reading or creating the LOG 
        file,  the program invites you to enter callsign and exchange for 
        each QSO. As you enter QSOs, the program records them in RAM and, 
        as  time  permits,  records them on disk.  The disk recording  is 
        typically finished within 1/3 second after the operator  finishes 
        entering  the  exchange when using a hard  disk;  one  second  on 
        diskette.   There is no need to wait,  though; you can be logging 
        the next contact while the disk update takes place!














                                        3








        SETTING UP

        Before  the  contest,   you  should  decide  how  many  BAND/MODE 
        combinations you intend to work.   For instance,  if you intended 
        to  work  CW and SSB on 160 and 40 meters,  you would  have  four 
        BAND/MODE  combinations.   You will need to prepare one  diskette 
        for each combination.   But see below for special instructions on 
        setting up a hard disk for super-fast BAND/MODE switching.

        As mentioned above,  the program will find or create a large file 
        (240K) on the diskette.  Because loading such a file can be  very 
        quick  (often less than ten seconds depending upon how many  QSOs 
        were previously logged in that file), while creating the file can 
        take  several  minutes,  we  recommend  preparing  the  diskettes 
        (executing NN5ILOG to format the file) before the contest begins.  
        To prepare a diskette, first FORMAT it, then copy the NN5ILOG.COM 
        file onto it. Then insert it into the default drive (usually A:), 
        and enter the command NN5ILOG. 

        The  program will produce a logo on your screen and spend several 
        seconds formatting its internal tables in memory.   Then it  will 
        ask:

                  WHAT IS THE NAME OF THE CONTEST?

        You  should reply with the name of the contest (15 characters  or 
        fewer), for example CQ WORLDWIDE 85.

        Then the program will ask:

                  WHAT CALLSIGN ARE YOU OPERATING WITH?

        You  should  enter the station callsign you will use on  the  air 
        during the contest;  for example,  NN5I/CE0 if you were operating 
        using   the  program  author's  callsign  from   Easter   Island.

        The program's next question is:

                  WHAT NAME WILL YOU USE ON YOUR ENTRY?

        Your reply may be your name, as CARL B HAYES, or perhaps the name 
        of  a  club,  as  PODUNK  RADIO CLUB.   You may enter  up  to  20 
        characters.














                                        4








        Then the program asks:

                  DOES CONTEST USE SERIAL NUMBERS?

        This is an important reply, and is the only reply that you cannot 
        later  change.   If you reply YES,  then at each restart  of  the 
        program  (perhaps  with a new BAND/MODE combination) the  program 
        will  ask  the  serial number for  the  next  contact.   It  will 
        thereafter  keep  track  and constantly display the  NEXT  serial 
        number on the screen.   We chose not to have the program remember 
        the  serial  number on disk because,  when you  change  BAND/MODE 
        combination  (and thus move to a different log file)  during  the 
        heat  of contest,  you might forget to change it and thus end  up 
        with  multiple QSOs with the same serial,  which might disqualify 
        your entry in certain contests.   In any case, you should enter Y 
        if the contest requires serial numbers on QSOs (in the  exchange) 
        and N if it does not.  Entering N will eliminate ALL questions on 
        restart  of the program on an existing log file,  which is faster 
        and more convenient when changing BAND/MODE combination.

        If  (and  only if) you entered Y to the  previous  question,  the 
        program will then ask:

                  ENTER SERIAL NUMBER OF THE NEXT QSO.

        You should answer this question with a number from 1 to 5999.

        The program's last request before it takes off is:

                  PLEASE ENTER BAND AND MODE.

        Enter  up to three characters for BAND,  followed by  a  carriage 
        return,  and up to three characters for MODE, followed by another 
        carriage return.  The program will format the file, counting down 
        from 3000 to 0 in the lower right-hand corner of the screen. When 
        the  count  hits 0 and the program displays the  message,  "ENTER 
        CALL SIGN",  hold down the CTRL key and strike the ESCape key  to 
        terminate the program. 

        Repeat this process for each diskette.

        JUST BEFORE THE CONTEST BEGINS

        Immediately before the contest begins, you should get DOS running 
        on  the PC and set the TIME and DATE as accurately  as  possible.  
        Usually  you will want to use GMT.   In any case,  you should use 
        the  TIME  and DATE commands to do this;  some of  the  automatic 
        time-and-date  hardware that does this automatically on some  PCs 
        is  not accurate enough for communications purposes (yours may be 
        an exception; you should experiment to see how accurately you can 
        set  it.   Then  insert the diskette for  the  desired  BAND/MODE 
        combination  into  the  default  drive and  execute  the  NN5ILOG 
        command by typing "NN5ILOG" and striking the ENTER  key.   You're 
        ready to go.



                                        5








        HOW TO LOG A CONTACT

        To  log  a contact,  simply type in the callsign.   You need  not 
        worry  about  upper  and  lower  case;   the  program  translates 
        automatically.  Simply  type it in and enter a  carriage  return.  
        The program will check to see whether the contact is a DUP. If it 
        is,  a flashing,  bright-yellow message will tell you that it is, 
        and the time and date when the station was first worked.   If you 
        don't  want to log that station again,  strike the ESCape key and 
        the QSO will be discarded.  After you have typed in the call sign 
        and hit the carriage return,  the program will replace the "ENTER 
        CALL SIGN" message with one that says,  "ENTER EXCHANGE".  If you 
        want to log the QSO without entering an exchange,  simply enter a 
        carriage  return  and strike the "+" key (or,  to do  it  with  a 
        single  keystroke,  strike the F9 key).   Otherwise,  type in the 
        exchange.  It  is  not necessary but is OK to  enter  a  carriage 
        return after typing in the exchange.   If you make a mistake when 
        typing  in the callsign or exchange,  you can go back to  correct 
        the entry by using a carriage return (ENTER key) to flip back and 
        forth between callsign and exchange.  When you have them both the 
        way you want them, you are ready to log the QSO.

        To log the QSO,  simply hit "+" (there are two "+" keys on the PC 
        keyboard;  use either one, again without worrying about the SHIFT 
        key).

        To discard the QSO (that is, NOT log it), simply hit the ESCape
        key and no trace of the partially-entered QSO will remain.

        HOW TO SPECIFY YOUR STATION OPERATOR'S CALL SIGN

        Many  contest stations operate with several operators.   In these 
        cases  it is desirable to make a record of which  operators  made 
        which  QSOs.   To  tell the NN5I Logging Program your  operator's 
        call sign,  simply strike the F10 key.   The program will ask for 
        your  operator's  call  sign.    Just  type  it  in  (up  to  six 
        characters) and hit ENTER.  QSOs made thereafter will be recorded 
        with that callsign (until you change it again),  and the  printed 
        listings will include that operator's callsign.

        TERMINATING THE PROGRAM

        To  terminate  the program,  simply hold down the CTRL  key  and, 
        while holding it down,  strike the ESCape key.  This will  return 
        you  to DOS.  You can then change diskettes for another BAND/MODE 
        combination and re-enter the NN5ILOG command.  This is not as bad 
        as  it  sounds;  from  the time you hit ESCape to  the  time  the 
        program  is ready to log for another band and mode  is  typically 
        less  than 15 seconds,  unless you are especially fumble-fingered 
        in  changing the diskettes.  If you have more than  one  diskette 
        drive,  you  can even keep a diskette in each one and switch band 
        and mode by switching default drives.   If you have a hard  disk, 
        you can improve considerably upon this; see the next paragraph.




                                        6








        RAPID BAND/MODE SWITCHING ON HARD DISK SYSTEMS

        If  your  IBM PC has a hard disk,  you can take advantage of  the 
        ability  to  have  online at all times a log  file  for  each  of 
        several  BAND/MODE  combinations.   The basic plan of  action  to 
        switch  to a new band and mode is to terminate the program by use 
        of the CTRL-ESCape keysequence,  then enter a BATch command  that 
        switches   to   a  new  DOS  directory  containing  the   desired 
        (preformatted) log file and reinvokes the NN5ILOG  program.   The 
        program's author (NN5I),  whose hard disks are drives E: and  F:, 
        does it this way:

        In the AUTOEXEC.BAT file on the hard disk is a statement:

             PATH E:\BAT,E:\COM

                                  which  assures that the \BAT  directory 
        will  be searched first for all entered commands,  then the  \COM 
        directory.   In  the  \COM  directory  is a single  copy  of  the 
        NN5ILOG.COM executable program file.   This copy is executed  for 
        any BAND/MODE combination.

        For each BAND/MODE combination, there is a separate DOS directory 
        with a name corresponding to the band and mode; for instance, for 
        20 meter CW there is a directory \20CW in the root directory.

        For  each BAND/MODE combination,  there is a BAT file in the \BAT 
        directory that switches to the appropriate directory and  invokes 
        the NN5ILOG program.   For instance, the BAT file for 20 meter CW 
        is called 20CW.BAT and contains the following statements:

             CD \20CW           
             NN5ILOG       

        As  a convenience,  BAT files for CW and SSB on the most commonly 
        used  bands are included with the NN5ILOG programs on  the  disk.  
        You  can set yourself up to operate this way by making your  hard 
        disk the default drive,  inserting the diskette, and entering the 
        command  BUILDDIR  to execute the batch file  BUILDDIR.BAT  which 
        creates the directories.

        When operating on,  say,  15 meter SSB, all one need do to switch 
        to  20 meter CW is enter the CTRL-ESC keysequence (which  returns 
        to DOS), and then type 20CW and strike the ENTER key.  The system 
        searches  the \BAT directory for 20CW.BAT and finds it;  then  it 
        executes  the  commands in 20CW.BAT.   The first of these  is  CD 
        \20CW,  which  changes  to the \20CW  directory,  containing  the 
        appropriate  log  file  for 20 meter  CW  contacts.   The  second 
        command  is NN5ILOG,  which starts up the NN5ILOG  program.   The 
        program starts up,  then looks for the file NN5ILOG.LOG, which is 
        the name of the log file.   If it finds the file, it reads it and 
        continues logging in it from the point at which it had last been.  
        If the file isn't there, the program creates it.




                                        7








        Thus,  all  that  you  need do to  prepare  for  rapid  BAND/MODE 
        switching  during  the  contest  is to  set  up  the  appropriate 
        statements  in  AUTOEXEC.BAT (the  PATH  statement),  create  the 
        directories  you  intend to use (\COM,  \BAT,  and one  for  each 
        BAND/MODE combination),  place NN5ILOG.COM in the \COM directory, 
        and  create an appropriately named BAT file in the \BAT directory 
        for  each BAND/MODE combination (perhaps using the ones  supplied 
        on  the  disk).   Then switch to each  BAND/MODE  combination  in 
        sequence to test the BAT files and preformat the log files.  As a 
        convenience, we have included a BAT file (BUILDDIR.BAT) to create 
        the  necessary  directories and place the BAND/MODE BAT files  in 
        the \BAT directory.













































                                        8








        KEYBOARD REFERENCE

        The following is a complete summary of the use of the keys on the 
        IBM  PC keyboard.  Please note that it is NEVER necessary to  use 
        the  SHIFT  keys.  For instance,  the plus sign is  a  lower-case 
        character  on one key and an upper-case character on another key. 
        The program will always interpret the key correctly,  whether you 
        use the SHIFT key or not.

             LEFT and Right arrow keys:  There are two left-arrow keys 
                                         and one right-arrow key on the
                                         keyboard.  These can be used  
                                         as backspace and forward-space
                                         while you are typing a callsign
                                         to correct entries.    

             +   (plus sign)             There are two of these.  Either
                                         can be used to log a QSO (think
                                         of it as ADDing it to the log)
                                         after you have typed in the 
                                         callsign and exchange.

             ESCape (by itself)          Used to abort (NOT log) a
                                         QSO that you are typing in.

             CTRL-ESCape                 Holding down the CTRL key while
                                         striking the ESCape key ends 
                                         the program.

             F1                          Stops any printing that is
                                         in progress.

             F2                          Starts printing the QSOs already
                                         logged, in order by date & time.
                                         You can continue logging while
                                         the printing takes place.

             F3                          Starts printing the QSOs already
                                         logged, in callsign order.  You
                                         can continue logging while the
                                         printing takes place.

             F4                          Tells the program to print each
                                         subsequent QSO as it is logged.

             F5                          Tells the program to print a 
                                         standard-format dupe sheet.
                                         You can continue logging while
                                         the printing takes place. 

             F6                          Tells the program to eject the
                                         paper to the top of the next 
                                         sheet.  You can continue logging
                                         while this takes place.



                                        9








        KEYBOARD REFERENCE continued


             F9                          QUICK-log.  Used in checking
                                         an old log.  Typing in a 
                                         callsign and hitting F9 will
                                         immediately DUPE-check the QSO
                                         and, if not a DUPE, log it.
                                         If it is a DUPE, you must hit
                                         "+" or ESCape to log or discard
                                         the QSO.  It is not necessary
                                         to enter the exchange or any
                                         carriage returns.
              
             F10                         Specify station operator's call
                                         sign.  When you strike F10, the
                                         program will ask you to enter
                                         the callsign of the station
                                         operator so that it can be
                                         recorded with subsequent QSOs.

             NumLock                     NumLock is used to stop the
                                         updating to disk, temporarily.
                                         This allows you to carry the
                                         diskette to another PC, perhaps
                                         in order to copy the LOG file
                                         to another diskette for printing
                                         on another PC.  While disk up-   
                                         dating is thus suspended, you
                                         can continue to log QSOs.  
                                         After the diskette is back in
                                         the drive, hit NumLock again to
                                         write any accumulated QSOs and
                                         resume normal operation.  Note 
                                         that, while the disk logging is
                                         stopped, printing (if in 
                                         progress) will stop too.


                                         CAUTION:  while you have the
                                         diskette out of the PC that is
                                         working with disk logging thus
                                         suspended, you must not, on
                                         another PC, do anything (such
                                         as logging, deleting, or 
                                         modifying QSOs) that modifies
                                         the NN5ILOG.LOG file.  If you
                                         do, the file may be damaged
                                         and irretrievably destroyed
                                         when you resume disk logging.







                                       10








        OBTAINING A COPY OF THE NN5I LOGGING SYSTEM

        The DEMO version of the NN5I Logging System,  which runs only for 
        fifteen minutes at a time,  is available free on the NN5I BBS and 
        possibly on other BBSs.

        The NN5I BBS is active at

                                 (214) 960-2730
                                 300 or 1200 baud

        The  DEMO version can be obtained for $5.00 by sending a diskette 
        and self-addressed, stamped mailer to:

                                 Carl B. Hayes
                                 Box 5988
                                 Richardson, TX 75083

        The best way to send a 5-1/4" diskette mailer is to enclose it in 
        an  8" diskette mailer,  which can usually be bought at the  same 
        places that sell 5-1/4" mailers. Simply enclose your diskette and 
        the  new,  stamped and addressed 5-1/4" mailer,  along with  your 
        check or cash,  in the larger mailer, along with a NOTE that says 
        WHAT  YOU  ARE  ORDERING!

        The  PRODUCTION version of the NN5I Logging System  is  available 
        for  $75.00.  Please order it from the above address;  it is  not 
        necessary  to  include  a  mailer when  ordering  the  PRODUCTION 
        version.   You  should include a NOTE that says you are  ordering 
        the  PRODUCTION  version of the NN5I  Logging  System.

        Although  extreme  effort has been expended in the  creation  and 
        debugging of the NN5I Logging System, no guarantee or warranty is 
        given.  Prospective purchasers are urged to use the DEMO  version 
        to  determine whether this program is suited to their needs,  and 
        to assume all risks.  Payment for either the DEMO version or  for 
        the PRODUCTION version is not refundable under any circumstances; 
        this is basically a one-man hobby operation.



















                                       11