The BPQ Switch supports a simplified subset of PK232 Hostmode Commands.
This document is intended to give a brief intorduction to Hostmode, and
define the commands supported by the switch. For full details of the 
PK232 implementation, see the appropriate supplier's manuals.


With Hostmode, a single (virtual) TNC Port to the switch may support
several simultaneous conversations. Messages are passed to and from the
switch as character strings, with start and end frame delimiters. The
first byte specifies the type of data (command, status reponse, user 
data, etc), and the channel number. The system allows two basic modes of 
operation, polled or unpolled. With Polled, data is only sent from the
switch to the application on receipt of a poll. With unpolled, the switch
may send stuff to the application whenever it likes. Each method has its
advantages, and indeed the two BBS systems that I know of that use Hostmode
(G8UFQ and AA4RE) have chosen different modes. Unfortunately neither issues
the command which defines which mode to run in, so I have provided two
Hostmode options, PK232/AA4RE (polled), and PK232/UFQ (unpolled). There 
are other minor differences between my options, which will be mentioned
when the commands that they affect are discussed.

The basic frame format is

	SOH (HEX 01)  CONTROL   Data   ETB (HEX 17)


Any 01h, 10h, or 17h bytes appearing in the packet must be preceeded
by a 10h escape char, to avoid confusion with framing charaters.

The CONTROL byte has the following (hex) format:

  Appl - Switch

	2x		Data for channel x
	4x		Command to channel x
	4F		General (non channel specific) command.

  Switch - Appl

	3x		Data from channel x
	4x		Link status (reply to CO)
	4F		General command reply.
	5x		Link status report from channel x
	5F		Status Errors


  3F is used for monitored data (RX), and 29 for Unproto stuff (TX)


The most important message formats are as follows:

TNC Command:

	SOH 4F C C p p..  ETB    Where CC is the command code, and pp... params.

The Switch will respond immediately (ie without waiting for a poll) with

	SOH 4F C C 00 ETB	 If OK

or	SOH 4F X X 01 ETB        If invalid.

Connect:

	SOH 4x C O Callsign ETB

Note that whatever call you specify, you will just be connected to the
switch. Use switch commands from then onwards.


Session Status:

	SOH 4x C O ETB

Returns 

	SOH 4x C O a b c d e  callsign ETB

	Where a - f are hex values in range 0 - f, ORed with 30H

	a = link state-1 (ie state 5 (connected) = 34h)

	b = ax25 version (always 2 (32h))

	c = number of unacked packets outstanding

	d = number of retries (not supported - always 30h)

	e = conperm flag (not supported - always 30h)

	callsign = users callsign (if connected)



Session state changes (connected/disconnected) are reported as

	SOH 5x 'Text string' ETB


When using polled mode the poll command is

	SOH 4F G G ETB

The reply with be either SOH 4F G G 00 ETB, if nothing is available, or
one (any only one) data/monitored data/link status/data ack message.


Data is send on a connected channel as

	SOH 2x (data) ETB

There is no immediate response. The system will reply with a data ack
when it is able to process another frame.

	SOH 5F X X 00 ETB

The application must not send more data until this is received. Note in
polled mode, the data ack is returned in response to a poll.




Only a minimal subset of the full command set is implemented. The
following commands are processed - others are accepted, but ignored.


	GG	POLL

	CO	CONNECT or STATUS Request

	MN	MONITOR - MN0 means monitor off, MN1 monitor on
		MN2 also set MCOM on. Defaults on in UFQ mode, 
		off in AA4RE mode

	ZM	Monitor port mask - as normal tnc MMASK command

	UR	Users - set max concurrent users. In UFQ mode defaults 
		to 9, in AA4RE mode to zero. The maximum is 15, but as 
		the hostmode spec uses channel 9 for UNPROTO stuff, I
		recommend a limit of 9.

	DI	Disconnect. If followed by S (DIS), user is returned to
		the node, instead of being fully disconnected.



John Wiseman G8BPQ
11/3/90