Notes for Voice Digitizer
                                Gordon S. Hlavenka
                                    May 2, 1989



I built Alan D. Jones' voice digitizer and would like to offer a few
comments:

The "PLAY" program can be called from QuickBasic as documented in HOW2USE. 
But it was not noted that regular IBM BASICA also supports the "SHELL"
command from version 3.xx up.

I redrew the schematic (No offense to George Campbell) with one modification. 
The entire circuit can be implemented on a single LM324 IC.  The output
waveform is not as pretty -- the rise and fall times are longer and there's
some crossover distortion -- but the final product (audio out of the PC
speaker) is equal in quality.

NUMBERS.VOI was (I assume) produced with the original circuit.  TEST.VOI was
recorded using the 324 circuit.  I can't tell any difference...

Type "COPY DGTZ.SCH PRN:/B" at the DOS prompt to print the schematic on your
Epson-compatible printer.  If you have an HP-compatible plotter, DGTZ.PLT is
the one to use.  If you have neither of the above but you do have WordPerfect
5.x (A generally good program with a few big flaws) you can import DGTZ.PLT
into a document and print it on whatever you've got.

A note on adjusting the pot:  It helps a LOT if you have access to an
oscilloscope.  If you do, here's a good procedure:

1    Disconnect the microphone and ground the MIC input.

2    Adjust the pot until the output (U1-14) oscillates.

3    Now adjust the pot until the output just stabilizes.

You want the circuit to just sit on the brink of oscillation for the best
quality.  If you're too close, the spurious pulses make a sort of "background
count" on the recording.  But if you're too stable, the speech begins to get
choppy.  Mine seems to sound better if I stabilize it with the output high. 
Your mileage may vary.

If you don't have a scope, you might want to hook up a 555 and LED to the
output and try to adjust it that way.  You'd need the one-shot though,
because the pulses get narrower than you'd be able to see unaided.  As the
supply voltage changes, the pot may need readjusting.

Compatibility notes:
     COM1 on my AT refuses to see the input from the digitizer.  COM2 (an
     aftermarket add-on) does fine.  I suspect this is because the digitizer
     doesn't produce true negative signals.  If this is a problem on your
     system you can add a 1488 RS232 driver IC.  Run the digitizer on 5 volts
     (9V battery and 78L05).  Use the 5V supply (or the battery) to feed the
     1488 positive supply, and use an extra wire to steal -10V from the
     serial port for the 1488 negative supply.  Several of the pins have this
     voltage available.  There are some single-supply RS232 driver ICs on the
     market, too.

     RECORD locks up my Compaq portable.  PLAY works, though.