ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	º                                                         º
	º    DOSGATE _                                            º
	º             \                                           º
	º              \                                          º
	º               \_ Remote operation of MS-DOS             º
	º                                                         º
	ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
	Copyright (c) 1987

	Rich Bono, NM1D
	7 Redfield Circle
	Derry, New Hampshire 03038

	This document describes DOSGATE version 1.6

	DOSGATE is a system which allows an industry standard MS-DOS computer 
	to be controlled via an RS-232 serial port.  The port is considered to 
	be a remote user.  The traditional console of the machine is still in 
	complete control and can supervise and disable/enable the remote user 
	at will.  There is a simple 'Chat' mode that may be entered from the 
	console to allow 'talking' with the remote user to give assistance or 
	instructions.  In addition to chat mode, there is a simple terminal
	emulator to allow control of a modem or other device connected to the
	serial port.

	The remote user may be connected directly with an RS-232 terminal,
	via a modem over telephone lines, or with a TNC for remote operation
	via radio!

	The local console may still be used for any software 
	that normally runs.  The remote user is capable of running any 
	software that calls only MS-DOS (int 21h) system calls.  Any software
	that by-passes MS-DOS and interfaces with the BIOS or directly with the
	hardware for I/O will not be usable by the remote user.

	This version of DOSGATE is being distributed as SHAREWARE.  You are
	allowed to use DOSGATE on a trial basis for a limited period of time.
	After the trial period, you must register your use of DOSGATE with the
	author.   Remember, DOSGATE is NOT in the public domain, and as such it
	is NOT free software.

	If you find DOSGATE helpful in anyway, or you wish to promote 
	further improvements to DOSGATE, please send an apropriate amount 
	to the author at the above address. If you send $20.00 or more, 
	you will be be placed on the update list.

	The author would like to hear from anyone with comments or 
	suggestions concerning DOSGATE or other projects.

	Currently tested with :

	   DOS:

		Versions 3.2, 3.3, 4.00, 4.01

	   Remote user connection devices:

		Kantronix KAM (version 2.82 through 2.85)
		Kantronix KPC-2 (version 2.82 or 2.85)

	DOSGATE is implemented as an MS-DOS installable device driver.

	Also implemented is a simple terminal emulator which allows one
	to communicate with the serial port.

	To use the terminal emulator, execute DOSGATE at the DOS
	prompt.

	    The terminal emulator has one command:

	    ALT-X - exits the terminal emulator and returns to MS-DOS.

	Device driver installation instructions:

	DOSGATE has but four runtime commands:

		ALT-D will toggle the remote user on and offline.  A message
		is sent to the console and the remote user to inform about
		the change.

		ALT-T will toggle the 'terminal' function on/off.  A message
		is output to confirm the change in mode.  This terminal is
		only to be used for simple configuration commands to or from
		the TNC or modem.

		ALT-C will toggle the 'chat' function on/off.  A message is
		output to both the console and the remote user to inform
		about the change.  Use this mode to 'talk' to a remote user
		that is connected to the system.

DOSGATE should be installed as any other MS-DOS device
        driver. It also provides for various options.

	
	CONFIG.SYS should contain the line:

		DEVICE = DOSGATE.EXE

			This causes the following default options:

					Remote user disabled,
					Remote user with echo,
					1200 baud,
					No handshaking,
					DOSGATE on COM1,
					No Carrier Detect logic
					No SET USER= logic

			The following options are available at boot time . . .

			/R - Remote user enabled at boot time

			/E - Disable ECHO of remote users keystrokes
				This is useful if the remote users'
				terminal has local echo.

			/2 - Selects COM2 for DOSGATE else COM1 is used

			/C - Carrier Detect logic, will do the following when

				CD goes TRUE:  - Issue CTRL-C, 'START', CR
				CD goes FALSE: - Issue CTRL-C, 'END', CR


				Be SURE that your interface cable supports
				  the Carrier Detect Line!!!

				Remote user must be enabled!

				This allows the programs 'start' & 'end' to be
				 executed as remote users come and go.

			/U - Sets the environment variable USER to the ID of
				the user from the TNC status message.
				If no TNC status message, user enters CR, and
				then receives a 'Login:' prompt.  The user's
				input is stored in the USER environment.
				Note: FORCES the /C switch on (see above).

			/Bxx - selects baud rate (default is 1200 baud)
				(No parity, 8 bits, 1 stop bit)
				currently supported baud rates:
					/B96 - 9600 baud
					/B12 - 1200 baud
					/B30 - 300 baud
					/B11 - 110 baud

			/H - Enables hardware handshaking - Must have DSR & CTS
				to be able to transmit to remote. Be sure that
				the interface cable supports these lines!

			/A - Absorb LF's that follow CR's to remote.
				this is useful if the remote users terminal
				automatically does a CR/LF upon receiving a CR.

			/P - Enables Packet radio specific options
				ie:
					Remote user enabled at boot time
					Remote user Echo disabled
					Absorb LF's following CR's to remote
					Enable hardware handshaking
					Carrier detect logic enabled
					SET USER= logic enabled


	for example:

		DEVICE=DOSGATE.EXE /R /E   - Start remote user enabled, and
						absorb (disable) ECHO to the
						remote user.
			or

		DEVICE=DOSGATE.EXE /P      - Start DOSGATE for packet radio
		                             operation (see '/P' above).

	DOSGATE should be the only device driver installed for the CON:
	device.  This means DO NOT install an ANSI.SYS device driver when
	the DOSGATE driver is installed!!!

	Note: At this time, DOSGATE does not support ANSI escape sequences
	to the local console.  ANSI escape sequence support may be implemented
	in a later version (Be sure and register if you desire this).  Escape
	sequences will work on a remote terminal if it understands them.

	It is strongly suggested that you install the DOSGATE driver in a
	sub-directory that is hidden from the user, and that does NOT have
	the environment PATH pointing to it.  Or you may rename DOSGATE.EXE to
	DOSGATE.SYS to keep users from executing DOSGATE and invoking the
	terminal emulator function.

	When used as a terminal emulator DOSGATE allows the choice of baud
	rate to be used.

	ie: DOSGATE /b96	- This would start the terminal emulator using 
				  9600 baud over COM1 (default is 1200 baud).


	Environment variables are used to assist MS-DOS programs executing
	in the DOSGATE environment.  The currently defined evironment is:

		USER	- Set by DOSGATE driver to the ID of the user.
			   Used by DOSMAIL functions and START.EXE.

		DRIVES	- Used by END.EXE, must be set by AUTOEXEC.BAT

		Note: The path environment variable should NOT point
			to a directory that the DOSGATE.EXE driver is
			stored, and the remote user should NOT be able
			to stumble across the DOSGATE.EXE file.  If the
			user attempted to execute the DOSGATE driver, he
			would start the terminal emulator feature of the
			DOSGATE.EXE driver, and hang the system!  Keep
			the DOSGATE.EXE driver in a hidden directory!

	The additional programs, "START.EXE", "END.EXE", "DISC.EXE" are
	used for helping with managing the user in DOSGATE.

	With this version:

		START - Can be invoked automatically
			 (see '/C' parameter above).

			START will:

			1: Open the file 'user.log' in the directory
			specified by the environment 'MSG', and write
			the contents of the environment 'USER' to that file.

			2: Look for a file called "WELCOME.DOC" and
			output it to the user.  This can be to give the
			user instructions when he first connects.

			3: Invoke 'READ /c' to report if the user has any mail.

			Note: START.EXE can be replaced by a program of your
			      own that performs any functions that you desire
			      to be done when the user first "connects" (see
			      below).
			      

		END - Can be invoked automatically
			(see '/C' parameter above).

			END will look in the environment for the
			'DRIVES' parameter.  This is used to set each
			drive to its ROOT ('\') directory, and also to
			leave the machine with the default drive set as
			indicated.  This is used to insure that the
			next user will come into DOSGATE at the same
			place each time, and not where the last user
			left off.

			DRIVES should be set in AUTOEXEC.BAT as follows:

				SET DRIVES=C:;A:;B:;D:

			This would set each drive (A:, B:, C:, and D:) to its
			root directory, and also set the default drive to
			C: (the first drive specified will be the default
			drive).


			Note: END.EXE can be replaced by a program that you
				supply to perform any functions that you
				desire to happen when the user 'disconnects'.


		If the 'sysop' desires some other functions to be performed
		when a user first connects to DOSGATE, just create your own
		program (or batch file) to perform the desired actions, it
		must be named START (.EXE, .COM or .BAT).
		The END (.EXE, .COM, or .BAT) program is called when a user
		disconnects.  This may also be replaced.  If the 'sysop'
		desires nothing to be done for connect/disconnect, and will
		not be using mail, then the 'CD' logic may be disabled.  If
		the 'sysop' desires connect action, but nothing upon
		disconnect, then simply replace the END program with one
		that does nothing.


		DISC - Must be invoked manually.

			At this time, DISC will

				wait 3 seconds,
				issue 3 control-C's,
				wait 3 seconds.
				issue 'DISC' [CR],
				issue 'TRANS' [CR]

			This is to place the TNC in command mode, issue
			a disconnect request, then place the TNC back into
			TRANSPARENT mode until the disconnect is complete.
			The user may use this command to have DOSGATE initiate
			the disconnect.


	Compatibility with DOSGATE:

	The general rules for programs that can be run under DOSGATE are
	fairly simple, not keeping to the rules may simply cause confused
	users, or could cause the system to HANG!


	1 - Any program that affects the serial port that DOSGATE is using
	for the remote user will probably cause the computer to hang!
	DOSGATE is using the serial port with interupts ON, and will
	not tolerate other programs touching the serial port hardware.

	2 - Any program that does not do its I/O through DOS (int 21h) calls
	will by-pass the remote user.  This means that the remote user
	will probably be able to start such a program, and all may appear
	normal on the local console, but the computer may appear dead as
	far as the remote user is concerned.

	3 - Any program that issues ANSI escape sequences may work for the
	remote user (if his terminal supports the proper escape sequences),
	but (with the current version of DOSGATE) will not work correctly on
	the local console.

	4 - Programs that output massive amounts of data may run slow.
	Remember that any data that is output to the remote user is limited
	in speed by the serial port, (1200 baud is about 120 characters per
	second, this means that is will probably take more than 16 seconds
	to output 1 screen worth of data).

	5 - At this time, if the remote user sends too much data to DOSGATE
	and the current program cannot keep up with the user, some data may
	be lost.  There is output hardware handshaking (CTS).


	Special notes for TNC users:

	There are various TNC parameters that are very important for
	succesful use of DOSGATE.  DOSGATE is not very smart as far as the
	TNC is concerned.  This is not an accident or an afterthought!
	Since DOSGATE performs NO TNC COMMANDS then is should be compatible
	with virtually ALL TNCs that have a few minor qualifications.

	The TNC MUST:

		1 - Have its RS-232 Data Carrier Detect (DCD, pin 8) go
			true when a user connects, and go false when a
			user disconnects.  This also means the your
			RS-232 cable must include the DCD line.  Most
			cables designed for a modem have all the nessary
			lines (also important is the CTS and DSR line).

		2 - Be set to go into 'TRANSPARENT' mode when the user
			connects, and return to 'command' mode when the
			user disconnects.
				For Kantronix TNCs:
				  NEWMODE ON
				  CONMODE TRANS

			The following settings are also desirable:

				AX25L2V2 ON
				CHECK 10 - Or some other value (not 0)
				PARITY 4
				8BITCONV ON
				CMDTIME 1
				COMMAND $03
				FLOW OFF
				MRPT ON
				NOMODE OFF
				NUCR 0
				NULF 0
				PACTIME 10
				RELINK OFF
				RING OFF
				SENDPAC $0D
				TRFLOW OFF
				TXFLOW OFF
				CSTAMP ON
				DAYTIME xxxxxxxxxxxx (set to correct time)

		3 - Be set to allow only ONE user to connect at a time.
				USERS 1    (note: KAM & KPC4 set 'USERS 0' to
				                  be sure only one user at a
				                  time can connect)

		4 - Issue a '*** CONNECTED to CALL xxx' message terminated with
			a Carriage Return when the user first connects.  Where
			CALL is the id of the user who connects and xxx can
			be other information such as the date/time.  The syntax
			of this message is crutial to the operation of the user
			id logic of DOSGATE.  Every space and the case of the
			characters (up to the CALL) is very important.  If
			DOSGATE does not find this message when a user logs in
			it will prompt the user to input his id.


		5 - Be set for hardware handshaking.  At this time, DOSGATE
			only supports hardware handshaking.  This does not mean
			that DOS's XOFF handshaking will not work.

	DOSGATE hints:

		DOSGATE does not perform any machine protection. This means
	that if a remote user decides to erase a file or format your hard disk
	he WILL be able to do so!!! Unless you take steps to insure that he
	is unable to perform these dasterdly deeds!  If you can trust ALL
	remote users, then you need not be concerned with this.  Although(!),
	if you are allowing the general public access to your machine, then
	you may want to do the following:

		Create 'Hidden' directories which contain programs or data
		that you don't want the casual user to stumble across.  Note:
		this is not a foolproof method and most 'intelligent' DOS
		users may be able to find the hidden directories.

		Set the Read Only attribute on any files that you don't want to
		be easily erased and don't leave any programs on the system to
		allow the remote user to change file attributes.

		Do NOT keep a copy of your format (or any similarly dangerous
		software) ANYWHERE on your machine.

		Aquire a copy of CED (or other similar DOS extention) to
		allow you to remove or rename internal DOS commands so that
		the remote user cannot DELete files, set the PATH, or look
		at environment variables.  I use CED and map commands that
		I don't want the user to perform to a non existant command,
		this way when the user types the command DEL *.*, instead
		of the prompt "are you sure? ", he is greeted with the message
		"Invalid command or file name"!  After trying a few destructive
		commands, the user gives up, thinking that they have all been
		removed!

		Keep only software that ok for remote users to gain access to
		on the machine.  This way, if a user does destroy something,
		it will not be anything important.

		You also may NOT want to leave any compilers around! This
		will keep a *smart* user from connecting to your machine
		and writing a simple program while online to destroy the
		contents of your disks!!!


	Notes:
		MS-DOS is a trademark of Microsoft Corporation