-------------------------------------------------


          P A C K E T   T E R M I N A L   P R O G R A M

                           Version 1.4
        -------------------------------------------------


        Welcome   to the world of Packet Radio.    Say,   all you 
HAMS   will surely appreciate the time and effort we  have  spent 
designing and perfecting  this program.   We certainly don't care 
if  you  pass  a copy of this program  to  a  friend,   relative,  
fiance,   or even an enemy.   It is intended to further the cause 
of Packet Radio  and stir up additional interest.

        Now  for the BAD news.   This program is written in Turbo  
Pascal  and  the  source  code is available for  PURCHASE!    The  
authors  reserve   the  right to limit the  distribution  of  the  
source  code and  DEMAND  that it not be FREELY distributed.   We 
reserve  all rights  to  this program and are not responsible for  
any   damage caused by the use of this program.   Use it at  your 
own risk!

        Copies  of  the source code diskettes are available   for  
$25.00, from:  

              WD0DUD                        KA0DMJ
              Garry Kraemer                 Larry Kraemer
              1631 A South 6th              R 2 Box 190
              Blytheville AFB, AR           Jackson, MO
                          72315                        63755


         This  program  will  send  128  byte  sectors  to  the  
TNC.  Hardware handshake is mandatory to keep extraneous 
characters out of the file being transfered. See TNC SETTINGS for 
expanded settings.


              NOTE:   IF  YOU SELECT ECHO ON,  WHAT IS DISPLAYED  
IN  THE TRANSMIT WINDOW IS ALSO ECHO'D TO THE RECEIVE SCREEN.   
YOU MIGHT LIKE THIS DISPLAY BETTER.











         COMMANDS

        The program is menu driven and should not be difficult to  
figure out.    Use  the  UP & DOWN ARROW keys or the first letter 
of  the desired menu item to select that function.

        INITIAL OPENING MENU.

        The following functions are available:


                              TERMINAL MODE

                              SEND FILE
                        
                              RECEIVE FILE

                              LOG DRIVE and PATH

                              DIRECTORY

                              COMM PORT SETTINGS

                              OPTIONS

                              QUIT



        SEND   FILE  - Transmits any disk file to  another  MSDOS  
machine using  this  program.   If using TNC Protocol, the 
TRANSPARENT mode will be required  to allow transmission of 
control codes.  You will have to manually enter the TRANSPARENT 
Mode.  Use THREE rapid ^C (CONTROL C)  commands  to return to the 
command mode  of  the  TNC.   This program  will  ask  for the 
filename to send and  then  send  the filename to the receiving 
system.  ^X (Control X) will cancel the send function.  If you 
are using the XMODEM Protocol and a telephone modem, you can send 
to any compatible system using XMODEM Protocol.  CRC is the 
default error setting.  If an error is encountered when the 
filename is specified, the procedure will be exited and you will 
have to re-enter the procedure to send a file. 

        RECEIVE  FILE  - Receives any disk file to another  MSDOS  
machine using  this program.   If using the TNC Protocol, the 
TRANSPARENT mode will be  required  to allow reception of control 
codes.  Use THREE rapid ^C (CONTROL C) commands to return to the 
command mode of the TNC.   This program will  receive the 
filename from the sending system and then write the  file to the 
logged disk drive.   ^X (Control X) will  cancel the receive 
function.  If you are using the XMODEM Protocol, this program 
will receive using either CRC or CHECKSUM error checking.  

        TERMINAL  MODE - A SPLIT screen terminal  program.    The 
TOP  screen  section displays the RECEIVED characters  while  the  
BOTTOM section  displays  the  TRANSMITTED  characters.   
       
     TERMINAL COMMANDS:
   
         CONTROL P - Toggle printer output ON/OFF.
A print spooler (BUFFER) needs to be utilized to eliminate  loss 
of characters.   Most printers can not keep ahead of  the  TNC at 
1200 BAUD.   Issuing a second ^P  will terminate output.

         CONTROL B - Toggle buffer ON/OFF.  A Buffer Open/Closed 
message is displayed in the Transmit screen.  The Buffer must be 
CLOSED to SAVE contents to DISK!  Max buffer size is 32 K BYTES.  
If 32 K is received, a BUFFER FULL message is displayed, a beep 
sounds, and a reminder to save contents to disk is displayed.  

         CONTROL T - Send ASCII/TEXT file from the terminal mode.  
CONTROL X will terminate transmission.  A Cancellation message 
will be displayed on the  Transmit screen.  ONLY files that can 
be 'TYPED' from DOS can be sent.
 
          CONTROL W - Save buffer data to disk.  Limited filename 
checking is performed.  Filename must conform to MSDOS standards, 
ie., Filename.Ext.     

         CONTROL C - Return the TNC to COMMAND MODE!  This 
command will allow you to control the TNC!

         CONTROL E - Exit Terminal mode and return to the COMMAND 
MENU.  

NOTE:  This terminal section DOES NOT provide CRC or CHECKSUM 
error checking; since the TNC performs this function.  

        I HIGHLY recommend the JRAM 3 board.   It will support 2 
MEG  and allow  you to set up any size file for a printer buffer.   
I have 128 K set aside in memory disk for a printer spooler.


        LOG DRIVE and PATH - This function will change the 
default drive and path.  Logging a new drive allows the 
SEND/RECEIVE function to access the LOGGED drive via the 
specified path.  If you wish to receive to a specified sub-
directory, it MUST be created before entering the program.


        DIRECTORY  - This  function  will display the  directory  
of the specified drive.  The LOGGED and Logged drive's path 
remains unchanged.





        COMM  PORT SETTINGS - This function will allow you  to  
configure the  comm port.   A submenu is displayed and you can 
use the UP & DOWN  ARROW  keys  or the first letter of the item  
you  wish  to change.  The current selection (default) is 
displayed to the left of the initial COMM Parameter menu.  
Submenus containing new comm parameter  settings  will be 
displayed when individual items  are selected.   These  new 
settings will be implemented when QUIT  is selected on the 
COMMUNICATIONS PARAMETERS menu.


        COMM PORT SETTINGS SUBMENUS 


        BAUD RATE - BAUD RATES of 300,  1200,  2400,  4800 are 
displayed.  Use the arrow keys to highlight the desired setting 
or enter  the first number of the desired BAUD RATE.

        COMM  PORT NUMBER - PORTS 1,  2,  and 3 are displayed.   
Use  the arrow  keys to highlight the desired settings or enter 
the number of the port desired.

        WORD  LENGTH - 8 and 7 BIT WORD options are displayed.   
Use  the arrow keys to highlight the desired settings or enter 
the  number of the port desired.

        PARITY  - EVEN,  ODD,  and NONE options are displayed.   
Use  the arrow  keys to highlight the desired settings or enter 
the number of the port desired.

        STOP  BITS  - 1 and 2 STOP BIT options are  displayed.   
Use  the arrow keys to highlight the desired settings or enter 
the  number of the port desired.

        RTS - HIGH and LOW options are displayed.  REQUEST TO 
SEND should default  to the proper setting.   This signal should 
be PIN 4  of the  RS-232.   RTS  is  used to control TNC 
TRANSMISSION  to  the Computer.   If  RTS  is LOW,  the TNC will 
not  TRANSMIT  to  the Computer.  

        DTR  - HIGH and LOW options are displayed.   DATA 
TERMINAL  READY should default to the proper setting.   This 
signal should be PIN 20 of the RS-232.  If your modem does not 
work,  try changing the DTR state.   DTR HIGH is compatible with 
the PROMODEM 1200 (HAYES compatible).



        OPTIONS

        TNC PROTOCOL - No ERROR checking provided to the TNC.  
RTS/CTS hardware control of the TNC.  The filename and number of 
records are provided to the receiving TNC.  The receivine TNC 
must use this program to send files in the TRANSPARENT Mode.

        XMODEM - Standard Protocol as designed by Ward 
Christensen. The following submenu options are displayed:
 
             CRC - CRC Error checking selected.

             SUM - CHECKSUM Error checking selected.




        ADD LF to CR - The following two options are displayed:

             ADD LF to CR - Selecting this option will cause a 
Line Feed (LF) to be added to all Carriage Returns (CR).  Only 
valid while in the Terminal mode.             

             CR Only - Selecting this option will display 
received data just as received, ie., no  LF will be added.  Only 
vaild while in the Terminal mode.  


        QUIT - EXIT Submenu or EXIT program. 

































         Now,  for  one  BUG in the HEATHKIT TNC.   When the RTS 
line  is toggled to inhibit the TNC transmitting to the Computer,  
the TNC will  immediately  stop transmission and will  SOMETIMES  
lose  a character.  We have verified this with the folks at TAPR 
and they are working on a modification to help us out.  Heathkit 
claims no BUG spray needed!   Boy, are they wrong!  Just try 
using the file send/receive  mode  to  send  a  .com or  .exe  
file  to  another computer.   I'll bet a new Boeing B-52 that the 
program will  not function  properly after several bytes are 
dropped  out.   (LARRY and  I have more hours in the B-52 than 
any other 'TWINS' in  the world!   Larry has approx 750 hours and 
I have 3000+ B-52,  4000+ total,  and  2000+ Instructor Pilot 
hours.   Now,  if that  don't impress  you nothing will!).  Yes,  
we have tested this program  by connecting  RS-232 direct to 
another RS-232 (FULL HANDSHAKE)  and have verified that it is not 
our program.







































                          TNC SETTINGS


         This  program will send ANY disk file from one MSDOS 
machine  to another  MSDOS machine.  (Source code,  Object code,  
ASCII,  any disk  file!!!!).    NOTE:   BOTH  MSDOS  MACHINES 
MUST  RUN  THIS PROGRAM, IF USING THE TNC PROTOCOL !!!!!  


The TNC should be set to:

        ABAUD 1200           ECHO OFF             PARITY 4
        ABIT 1               ESCAPE OFF           PASS $16
        AUTOLF ON            FLOW ON              REDISP $12
        AWLEN 8              FRACK 4              RETRY 8
        AX25 ON              FULLDUP OFF          SCRENL 78
        AXDELAY 0            HBAUD 1200           SENDPAC $0D
        AXHANG 0             LCOK ON              START $11
        BKONDEL ON           LFADD OFF            STOP $13
        CANLINE $18          MONITOR OFF          TRACE $1000
        CANPAC $19           MALL ON              TXDELAY 4
        CMDTIME 1            MAXFRAME 1           TXFLOW 0FF
        COMMAND $03          MCON ON              VDIGIPEA OFF
        CONOK ON             MFROM ALL            VRPT OFF
        CAPTIME OFF          MTO ALL              XFLOW OFF
        CR ON                MYVADR $1F           XMITOK ON
        CWID OFF             NULLS 0              XOFF $13
        DEBUG $05            NUCR ON              XON $11
        DELETE OFF           NULF ON
        DIGIPEAT ON          PACLEN 128
        DWAIT 2              PACTIME AFTER 4



RS-232C WIRING

MFJ  TNC            MSDOS COMPUTER(DTE)    HEATHKIT TNC

FG   1        not req'd1  FG   not req'd1  FG
RX   2<---------------------2  TX------------->2  RX
TX   3--------------------->3  RX<-------------3  TX
CTS 20<---------------------4  RTS  ------------->4  CTS
RTS  5--------------------->5  CTS<-------------5  RTS
DTR  6---- always high ---->6  DSR<-------------6  DTR
GND  7<-------------------->7  GND<------------>7  GND
DCD  8 --------------------->8  DCD------------->8  DCD
       20  DTR-------------> 20  DSR

NOTE:   The above wiring is required for proper hardware
handshake.  This allows the TNC to operate in the
TRANSPARENT Mode.






  8 Sep 86 ver 1.4 - Added Exit routines if error is 
                     encountered in the file send modes.  
                     Added Paths to the Log Disk selection.
                     GGK.

31 Aug 86 ver 1.3  - Added Menu selection of XMODEM Protocol 
                     for XMODEM, CRC and CHECKSUM, Send & 
                     Receive.  GGK.

22 Aug 86 ver 1.2  - Corrected CR/LF Transmission during send from
                     Terminal mode.  Added code to enable LFADD
                     boolean operator.  Tested FULL HANDSHAKE between
                     two computers.  1200 BAUD checks ok. No problems
                     capturing data to buffer and printing when using
                     print buffer.  Added Counter reset when Buffer is
                     saved to disk (Reset Counters).  GGK.

21 Aug 86 ver 1.1  - Added Buffer capture and Transmit file from
                     Terminal mode.  Also corrected ASYNC_SEND(CH)
                     to loop until CTS and THRE.  GGK.

 1 AUG 86 ver 1.0  - Added DTR and RTS options to COMM PARM MENU.
                     Allows program to be used with external/internal
                     modems.  NO ERROR CHECKING!




    Written by GARRY KRAEMER (WD0DUD)  and LARRY KRAEMER (KA0DMJ)

   Dedicated to our loving families.   They have suffered many 
days while we discussed,  corrected,  debugged,  and perfected  
this program.

                  ----------8 SEP 86----------
                          Latest Update