*** Perfect1.doc ***

     I  want  to comment on the BOXDATA records that I  have been
receiving   on  your disks.  First, I think that  many  users are
confusing the  definition  of  the X-max parameter.  The  typical
ranges for X-max range from 0.1 inches to 0.25 inches with 0.5 on
the JBL 18" 2245H being the largest I've seen (Have you ever seen
one,  they  are  huge.)   If  you  don't  know  the  X-max value,
approximate it with 0.1 to 0.15, 0.2 for large suspensions.
      Note  that   X-max   is  NOT  the   total   possible   cone
movement  allowed   by  the suspension, which  on  large  drivers
could   be  at least   an   inch.   I   have  seen  specification
sheets  from  a  few manufacturers (Credence is one) that give an
"X-max" and a "X-lin" (for X-linear?) value. As far as I can tell
from these,  the   X-lin is really the value of X-max as normally
defined.  And the  "X-max"  value  is  the  maximum  cone  travel
possible.     Contact the manufacturer  if you are confused about
their   specifications.    I   hope   that  a  standard  for  "X"
measurements will surface soon.
     The X-max measurement defines the peak (not to be  confused
with  peak-to-peak)  distance  that  the voice  coil  can  travel
without extending beyond the magnetic  field  as  determined   by
the  pole  piece  length.  The voice coil may be longer in length
than  the  pole  piece.    This   is  defined  as   "voice   coil
overhang."    The  PB  program  uses  the  X-max  measurement  in
calculating the Maximum Sound Pressure  Level  (SPLmax), and thus
is a key factor in the Excursion Limit Plot.  Theoretically,  the
driver  is  "linear"  only if the cone travel is within the X-max
limits!  Think  about  this  the next time you watch your low-end
drivers move 3/4 " peak, from the rest position!
     In general, (not always,)  low  Q  drivers  are intended for
4th  order   systems,  and  typically  have  what  is  coined  as
"long-throw  suspension."  Also, remember that PERFECT BOX  model
is valid up to Qts of 0.7, and the Marquis 12G38BPP1H is slightly
over that value at  0.72.  Of course, each individual driver will
vary from the manufacturers published specs, so you might want to
measure them yourself to be sure.
     Good luck  in your new designs, thanks again for all of your
generous support.   If  you  have any specific questions or would
like  chat about loudspeaker topics, drop me a letter, or call my
   BBS, "UCF Health Topics" at (407)-281-5522, 2400 N-8-1.
     You will find the latest release of Perfect Box posted here.
My BBS is an node  in  FidoNet,  (1:363/507), and thus
will  accept  "Electronic Mail" 24 Hours a day.   If  you  are  a
FidoNet  SysOp   or   know   a   friendly   one   with   a  "FIDO
compatible   Mailer",  you  can  file  request  PB with the magic
filename  "PERFECT",   for   the   current  MS-DOS  version,   or
MACPERF    for  Macintosh   (when  available.)   Of  course,  you
could   always   File  Request  by   the   current  archive  name
"PERF410.ARC."    Also,   I  host  a  local  echo-mail   (E-mail)
roundtable called, "Audio Topics".   You  can find many questions
regarding Loudspeakers, etc. answered there.

You now can save the "RAW data" to an ASCII comma-delimited file
for use with other graphics programs.  Press F7 at the Output
Menu, to Create a new file, and F8 to re-load a previously 
saved file.  You can "jump" to the Output Menu from the Opening
Menu by pressing F6.  Thanks to Registered User, Bob Schiers, of
Ames, IA, for this very helpful suggestion.

                                 Warren A. Merkel
                             *** End of Document ***