SPEC525.DOC                Wednesday, August 8, 1990                 Page 1


      
      
      
      
      
      
                          +---------------------+
                          |                     |
                          |    S P E C 5 2 5    |
                          |   (SPECTRUM  525)   |
                          |                     |
                          +---------------------+
      
      
      
                                Version 3.1
      
      
      
                          A Mouse Control Program
                                  for the
                JRC Model NRD-525 General Coverage Receiver
      
                                    by
      
                             James P. Hawkins
      
                              August 8, 1990
      
                      (First Release) April 24, 1990
      
      
                  Copyright (C) 1989-90, James P. Hawkins
                            All Rights Reserved
      
      
                             James P. Hawkins
                               P.O. Box 9146
                         Trenton, New Jersey 08650
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 2

      
      
      
      
      
      
                         * * * S P E C 5 2 5 * * *
                              (SPECTRUM 525)
      
      
     INTRODUCTION
         This program was written by James  P.  Hawkins  WA2WHV  as  a
         visual  means  of  controlling  the JRC NRD-525.  Most of the
         receiver controls  are  available  on  the  PC  screen.   The
         salient   feature  of  this  program  is  the  display  of  a
         multicolored frequency  spectrum  chart,  divided  into  band
         allocations.  Each allocation can be clicked on as if it were
         a menu selection which causes a frequency calibrated expanded
         dial.   In  addition  to  the  frequency  marks, the dial can
         contain station names  or  any  markings  the  user  desires.
         These  markings  are stored in data files.  It requires a VGA
         graphics as the resolution must be high enough to resolve the
         frequency  dial.   The program is actually an ACTIVE spectrum
         chart, broken up into 6 bands.  At this  time,  the  data  is
         based  files  which  represent  the  hour  of the day and one
         common file which contains markings which will appear for any
         time of day.
      
     INSTALLATION
         Before proceeding, make a backup copy of  the  diskette.   To
         install spec525, insert the diskette and type a:install.  The
         installation will leave you in the C:  The program  is  setup
         to  operate on port COM1 at 1200 baud.  If you wish to change
         the  port  to  COM2,  edit  the  SPEC525.INI  file  so   that
         port=COM2.  The same applies for ports COM3 and COM4.  To set
         the baud rate to 1200  on  your  receiver,  hold  the  "memo"
         button  down  and  press  the '8' button repeatedly until the
         number 1200 is observed on the frequency  dial.   You  should
         now be able to start the program by typing spec525.
      
         If you want the program to be universally executable add  the
         following line to the end of your autoexec.bat file.
      
                 path=%PATH%;c:\spec525
      
         The program needs an SPEC525.INI  file  present  in  whatever
         current directory you are in when you invoke it.  If there is
         none present, it will attempt to create one.  The data  files
         used  by  spec525 should reside in whatever path is specified
         by the "path=" line in SPEC525.INI.  Initially it is  set  to




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 3


         C:   If you have the demo, type DEMO525 to start the program.
         If it's the registered version type SPEC525.
      
     CONTROLS
         This section describes the graphics control panel.
      
         Dial Pointer
             On the  top  of  the  screen  is  a  dial  pointer  which
             indicates  the current selected position on the frequency
             spectrum or dial.  It starts up at zero.
      
         Spectrum/Magnified Bandspread
             The area  below  the  dial  displays  a  portion  of  the
             frequency  spectrum  between 100KHz and 34 MHz, depending
             on what the  band  switch  is  set  to  (read  on).   The
             spectrum  display  consists  of  color  coded areas, each
             representing a specific allocation of the band.  The left
             mouse  button  may  be  clicked  on or dragged across the
             spectrum to change the  frequency  in  10KHz  increments.
             The  dial pointer will follow and remain where it is left
             when the mouse button is released.  If  the  right  mouse
             button  is  clicked  on  one  of the allocations, it will
             expand or magnify into a frequency calibrated dial  which
             is  controllable  in  1KHz increments with the left mouse
             button.  On the bandspread dial, is a  horizontal  center
             line,  above  which  are  frequency markings.  Below this
             line are labeled markings which may be added  or  changed
             by the user.
      
         Fine Tune
             The fine tune dial, which is below and to the  center  of
             the  spectrum  dial,  allows  the  user  to tune in 10 Hz
             increments by clicking or dragging in the lower  half  of
             the  box with the left mouse button.  The dial pointer in
             the upper half will follow and  remain  where  the  mouse
             button is released.
      
         Fine Tune Offset Indicator
             This indicator is to the right of the fine tune  bar  and
             indicates  the plus or minus offset which is added to the
             main dial when the fine tuning is changed.
      
         Memory Channel Map - MCM
             MCM is  a  visual  representation  of  the  200  receiver
             channels  numbered every fifth square from 0 to 195.  The
             squares seem small  at  first,  but  are  quite  easy  to
             select.   The  channel  map is in halfway down the screen
             and contains  two  rows  of  squares.   The  top  row  is
             numbered  to 95 and the bottom row is numbered to 195.  A
             channel is addressed by simply moving the cursor  onto  a
             square and clicking the left mouse button.  There are two
             selections which determine whether clicking a channel map
             square  will  store  the  current  receiver  settings  or
             retrieve  those  already  contained  in    the   receiver
             channel.   They  are  labeled RECALL and STORE with "MCM"




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 4


             appearing below them.  The highlighted option is the  one
             in  effect  and  it will remain in effect until the other
             option is chosen by clicking the  mouse  on  the  option.
             Initially  the program starts in a RECALL mode to prevent
             inadvertant destruction of  a  channel.   The  user  must
             deliberately chose STORE.
      
             With this method, the user may easily store large  groups
             of  frequencies  very  quickly by alternately clicking to
             the frequency, then clicking the memory channel while  in
             STORE  mode.   The  user may also type in frequencies and
             channels as will be shown.
      
         Slew control
             This is below and to the left of the Spectrum display and
             consists of a circle and two arrows on either side.  This
             control is only effective when the display  is  magnified
             to  a  bandspread.   Clicking on the right or left arrows
             steps the expanded display to the next allocation without
             having  to  go  back  to  the  spectrum.  Clicking on the
             circle,  simply  redisplays  the  current  band  display.
             Slewing  is  limited  to  either  end of the current band
             selection.
      
     RECEIVER CONTROLS
         In the lower half  of  the  screen  are  other  controls  and
         indicators.  A selection is made by "clicking" the left mouse
         button on your selection.  When a selection is made the  menu
         item  displays  black  lettering  on  white  background  in a
         reverse video fashion.  The NON-MODE  menu  (SET  FREQ,  DIAL
         MARK, SAVE DB, CHAN STO. CHAN REC.)  does not highlight as it
         does not put the receiver into any mode.
      
         Digital Frequency and Time Indicator
             Indicates the time and current frequency setting  of  the
             receiver  PLUS  the value of timeshift in the SPEC525.INI
             file.  The user  may  edit  the  timeshift  parameter  to
             display  any  timezone shifted from his/her PC time.  The
             best choice is probably Universal Time.
      
         Mode Switch
             Allows selection of RTTY, CW, USB, LSB, AM, FM, FAX using
             the  left  mouse  button.   The  black  area  at  the top
             indicates the current setting.
      
         Bandwidth Switch
             Allows selection of receiver  bandwith  to  WIDE,  INTER,
             NARROW,  AUX.   Note  that  the NARROW selection will not
             work without the optional CFL-232 filter mounted.
      
         CHAN STO. and CHAN REC.
             Allows setting of receiver channels.  Clicking on CHANnel
             STOre  will  prompt  the user for a channel number.  Upon
             entering the channel number, the receiver channel will be
             set to the current program parameters.




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 5


      
             Clicking the CHANnel RECall will prompt the  user  for  a
             channel  number.   Upon entering the number, the receiver
             will be set to the parameters contained in  that  channel
             number.
      
             I may remove these menu options to make room for  others,
             as the previously explained channel map method of storing
             and recalling receiver settings  is  a  visual  and  more
             convenient way of setting channels.
      
         DIAL MARK and SAVE DB
             Allows setting of memory and dial labeling.  Clicking  on
             the  DIAL  MARK  causes the program to ask for a typed in
             input at the bottom of the screen.  When the  user  types
             in a label, followed by a carriage return, the bandspread
             dial will display a labeled tick mark at  the  point  the
             the  frequency  was  set when the label was typed in.  If
             the program  is  on  an  expanded  dial,  the  dial  will
             redisplay to show the new mark, however, if the frequency
             is not in range of the current expanded  dial,  the  mark
             will  not show up unless the user goes to the appropriate
             expanded dial.  This might happen in the case of a  typed
             in  frequency.  REMOVAL of a dial mark is accomplished by
             setting  the  dial  to  the  mark  to  be  removed,  then
             following  the  above  procedure,  but  entering  only an
             <ENTER>.   The  SAVE  DB  option  stores  the  dial  mark
             information  in  the  data  base for the particular hour.
             The labels are temporary unless the user clicks the  SAVE
             DB option.
      
         SET FREQ Option
             When this option is "clicked", the prompt will ask for an
             input frequency to be typed in KHz.  This allows the user
             to type in a specific frequency manually.   This  feature
             in conjunction with the DIAL MARK function can be used to
             enter a series of frequencies  and  labels  from  a  list
             without having to view them or move the frequency dial or
             change the bandswitch.  Also by using the  DBASE  option,
             the  entry  can  be  made for the appropriate hour of the
             day.  It is important to remember, however that  SAVE  DB
             must be clicked to store them away.
      
         SEARCH and SRCH NEXT
             This  selection  allows  the  program  to  search  for  a
             specific  station  name  entry when typed in by the user.
             First occurrences of a label will be found  by  selecting
             SEARCH.  Subsequent occurrences of the same label will be
             found by using SRCH NEXT.  If you click the SEARCH option
             it  prompts  you  for a label. So, if you type in wwv, it
             will  look  for  the  first  occurrence  or  lowest   wwv
             frequency.  If you then click SRCH NEXT, it will look for
             the next occurrence of wwv.  Each time  you  select  SRCH
             NEXT it will look for the next occurrence.  So if you had
             entered all the wwv frequencies, it will select  2.5  MHZ




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 6


             first  then as you keep selecting SRCH NEXT it will cycle
             through 5.0, 10.0, 15.0, 20.0 and 25.0 MHZ and then cycle
             back  to  the  first.   So  if  I  want  to find the best
             reception of WWV, I just  type  it  in  once,  then  keep
             searching  for the best.  Input is not sensitive to upper
             or  lower  case  so  it  does  not  matter  whether   the
             characters are upper or lower case.
      
         AGC
             AGC FAST/SLOW/OFF
      
         ATTEN
             Attenuator ON/OFF.
      
         REM
             Remote control ON/OFF.  This frees up the receiver to  be
             controlled  manually,  by  disabling program control.  If
             receiver is turned on after program is started,  you  can
             synchronize  the  receiver  with  the program by clicking
             remote off, then remote on.  Turning on  remote,  outputs
             ALL   of   the  saved  receiver  status.   This  is  also
             convenient  if  you  want  to  turn   the   remote   off,
             temporarily change the actual receiver controls, then put
             it back to the state it was in by turning the remote  on.
             The  idea  being that the receiver should be in the state
             the program is in when the receiver is listening.
      
         DBASE
             Database file 0-23.  Selects which file to use  for  dial
             markings.   The  numbers  represent  the hour of the day.
             The program automatically  selects  the  data  file  that
             represents  the current hour of the day as it is known by
             the PC.  When the hour changes, the  data  file  changes,
             thus changing the dial markings.  The datafiles are named
             dbandN.525 where  N  represents  the  hour  of  the  day.
             Another  file is cmnband.525.  This file contains station
             names and frequencies that are to be displayed regardless
             of  hour such as Citizens band channel numbers, WWV, etc.
             Dbase files are found in the directory path specified  by
             the  path setting in the SPEC525.INI file which exists in
             whatever current directory the user is in at the time  of
             program execution.
      
         ADB
             Automatic database, disables automatic time switching  of
             data file.
      
         Bandswitch
             Selects the frequency range of the spectrum display.
      
         RECEIVER STATUS SAVE
             The uses editable data contained in the SPEC525.INI  file
             to  initialize.   As  previously  stated,  SPEC525.INI is
             located in whatever directory the user is in at the  time
             of  program  invocation.   When  a user exits the program




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 7


             normally by clicking on the exit menu selection,  control
             settings  and frequency settings are saved SPEC525.INI in
             the form of NRD-525 command strings.  The port name, baud
             rate  and  datapath  and  timeshift are also specified in
             this file.  When the program is started, it looks for the
             values in this file to reset controls.  If a value is not
             present, a default setting, hardcoded in the  program  is
             used.
      
             The  "timeshift="  entry  in  SPEC525.INI   allows   time
             adjustment for time conversion to any time zone including
             Universal time.  For example if Universal time is desired
             and  your  PC is set to EDT, then set timeshift=4 for a 4
             hour time difference.   The  program  will  then  display
             Universal  time.  Set timeshift=0 if you want the program
             to display the time set in your PC.
      
             The user may edit these values manually and the order  is
             unimportant.   When  the  program is terminated normally,
             the file will  be  rewritten.   Missing  values  will  be
             entered and modified values will be changed.
      
             If the file does not exist or is empty, the program  will
             create one with the default values.
      
             This editable form makes it  possible  for  the  user  to
             write   another   program  which  can  set  the  receiver
             parameters as they are all documented  with  the  NRD-525
             interface  card.   An example of the contents of the file
             is as follows:
      
                     port=COM1
                     baud=1200
                     datapath=C:\USR\JIM\
                     timeshift=4
                     A0
                     B3
                     C001
                     D0
                     E1
                     F00113000
                     G0
                     I0
      
             The default settings are as follows:
                     port=COM1
                     baud=1200
                     datapath=c:\spec525\
                     timeshift=0
                     A0
                     B0
                     C001
                     D4
                     E1
                     F00113000




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 8


                     G0
                     I0
         FUTURE PLANS
             When time allows, I am planning to add an additional menu
             to  the  program  which  will  allow  the user to LOAD or
             COMBINE station data from other  named  data  files  then
             save  the  file  under  any desired name.  For example, a
             single  file  may  contain  a  set  of  frequencies   for
             HURRICANE  tracking; another might contain stations which
             contain Spanish Speaking Stations.  These can  be  loaded
             separately   or   combined.   Another  could  be  a  file
             containing dipole antenna lengths so  that  when  loaded,
             the  dial  will  be  a rule to calculate antenna lengths.
             Any  ideas  on  ways  to  implement  these  features  are
             welcome.   Send  me  postal  mail  or  contact me through
             CompuServe ID 71760,3362.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      




     SPEC525.DOC                Wednesday, August 8, 1990                 Page 9


      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      
     SHAREWARE and COPYRIGHT NOTICE
      
         Welcome to user supported software (commonly referred  to  as
         "SHAREWARE").   User  supported  software  allows  you to try
         software before you buy, and when you do  buy,  to  pay  much
         less  than for commercially developed software.  This is true
         because there are no costs  for  advertising,  sales  staffs,
         fancy  packaging  and  distribution  costs  bundled  into the
         software. Just good software, not glossy  packaging,  and  no
         hassles.  Pay  only  if  you  like  it.  Your registration of
         SPEC525 will encourage more development of this type software
         and  ultimately  provide  better  software at lower prices to
         everyone.  SPEC525 3.1 and  its  follow  on  products  depend
         entirely upon your support for their existence.  This program
         is a demob, but the only disabled feature is the  ability  to
         save  new  label  entries (SAVE DB) and the number of station
         labels is limited to 200.  If you register  this  program,  I
         will mail you a fully working copy of the program.
      
         SPEC525 V3.1 is protected by U.S. and international copyright
         laws.   SPEC525  was  written  by  me,  James  P.  Hawkins in
         Microsoft C and is Copyright (c) 1988-90 by James P. Hawkins.
         All rights are reserved.
      
         _________________________________________________________________
      
         You  are specifically granted the right to use SPEC525 3.1 on
         a 30 day trial basis.  If you like it and you  want  a  fully
         functional  copy,  you  must  register  your  copy by sending
         $36.50 to
      
                               James P. Hawkins




     SPEC525.DOC                Wednesday, August 8, 1990                Page 10


                                 P.O. Box 9146
                            Trenton, NJ 08650-1146
      
                    Residents of NJ must include sales tax.
                    (Currently 7%, so please send $39.05).
         _________________________________________________________________
      
         You are also encouraged to share SPEC525 V3.1 with others and
         to distribute copies on computerized bulletin board  systems,
         however you may not:
      
         1)  Charge  for,  or  otherwise  sell,  lease  or  rent  this
             program.  This  also  prohibits  bundling of this program
             with some other product or service.
         2) Modify the program or its documentation in any way.
         3) Distribute the program without this .DOC file.
         4) Distribute this program as part of  a  promotion  for  any
             commercial  venture  or as an inducement to purchase some
             product or service.
      
     You MAY, however, charge a fee for  the  actual  distribution  of
     this  program.  In this case, it must be made clear to the person
     receiving SPEC525 that a registration fee is still  required,  if
     the user intends to keep SPEC525.
      
     Warrantee: This program is being provided "AS IS". It  is  up  to
     the  user  to determine the suitability of this program for their
     purposes. The user takes all responsibility  for  any  direct  or
     consequential  damages.   It is written for VGA graphics only.  A
     monochrome version may be made available in the future when I get
     the chance.
      
     Support: Please DO report all bugs, difficulties or  improvements
     desired.   Registered  users will be notified of the availability
     of the updates.
      
     I have not yet determined the price of updates.  It  will  depend
     on  the change.  If an update is only serious bug fixes, the cost
     will be very minimal.   If  major  enhancements  are  added,  the
     update will be more.
      
      
      
      
      
      
      
      
      
      
      
      
      
      
      




     SPEC525.DOC                Wednesday, August 8, 1990                Page 11