6CB





                          Kenwood TS-440 Low Band Computer
                             Interface Control Program.
            
            Required Equipment:
            
                 IBM PC or Compatible with 128K memory (MIN) and a DSDD
                 floppy disk drive.
                 
                 CGA or EGA Color Monitor
            
            Chapter 1.  Description
            
                 Upon  release   of  the   Kenwood   TS-440   low   band
                 transceiver,  Kenwood   also   announced   a   computer
                 interface option.   This  interface allows  control  of
                 most front  panel aspects of the rig.  The only problem
                 was that  no software  to control the rig was ever sold
                 to use the powerful protocol.  That is until now.
            
                 TS440ctl.exe allows  the user  complete remote  control
                 ability from a Personal Computer screen.  The following
                 are the commands and controls available to the user:
                 
                      VFO A Frequency
                      VFO B Frequency
                      Memory Channel Selection
                      Tuning
                      RIT switch, tune, and dial
                      Band selection
                      Scan
                      Split
                      Lock
                      Mode
                 
                 In  addition  to  the  above,  status  of  the  440  is
                 constantly  updated  on  the  PC  screen.    With  this
                 program, the  user may  access almost every function of
                 the 440 from the PC.
            
            Chapter 2,  Setting Up for TS440ctl
                 
                 As mentioned above, TS440ctl contains a real time clock
                 that reflects GMT time.  In order for the GMT time to
                 be correct, you must first make sure that your system
                 clock is set correctly for YOUR time zone.  Also, a new
                 command must me inserted into your autoexec.bat file.
                 If you are not familiar with this file, consult your
                 DOS reference manual for details.
                 
                 TS440ctl needs to know the time zone that it is running
                 in so that it may determine the correct number of hours
                 to correct for Greenwich Mean Time.  The program
                 figures this out by looking for a value called






                 timezone.   You set timezone to one of the following
                 values:
                 
                      EDT  - Eastern Standard Time
                      CDT  - Central Standard Time
                      MDT  - Mountain Standard Time
                      PDT  - Pacific Standard Time
                 
                 Enter the following line into your autoexec.bat file,
                 or just enter at the DOS prompt:
                 
                      set timezone=XXX
                      
                 where XXX is the timezone where you reside.  The
                 advantage to entering this into your autoexec.bat is
                 that is saves the step each time you want to run the
                 program.  The program defaults to MDT time, for that is
                 the time zone I live.
                      
                 The TS-440  communicates with  the PC via an RS-232 EIA
                 connection.   This is  typically connected to your PC's
                 COM1 port.   A  3 wire  RS-232 cable  connects  to  the
                 kenwood   communications    interface.       For   more
                 information, refer  to the installation manual included
                 with the interface unit.
            
            Chapter 3,  Using TS440ctl.exe
            
            Start-Up
                 TS440ctl is started by typing
                 
                      TS440CTL
                 
                 at the DOS command line.  If you have a hard disk, make
                 sure that you are in the directory, or have a path to
                 the directory in which the program resides.  If you
                 wish to use the second COM port (COM2), type
                 
                      TS440CTL 2
                 
                 When the program begins execution, you should hear the
                 radio beep several times.  This is normal.  If the
                 radio does not beep, check to see that all cables are
                 properly connected and you are using the proper serial
                 COM port for your computer.
                 
                 The start up status of the program is VFO A.  What ever
                 frequency was tuned at the time of last use is the
                 current frequency, as well as the mode, scan status,
                 rit status and so on.  This information should
                 immediately be updated on the screen.
                 
                 
                 






            The Screen
                 The  screen   for  TS440CTL  is  divided  into  several
                 sections.   Each section  contains related information.
                 For example, the top of the screen contains the current
                 status of  all the  functions available,  that is VFO A
                 frequency, VFO  B frequency, and current memory channel
                 and channel frequency.  Based on the selected function,
                 the word  above the  function will  be  illuminated  to
                 indicate the  current selection.   The  current mode is
                 also positioned on the first sector of the screen.
            
                 The second  sector contains  a "meter"  indicating  the
                 current band. Based upon the current band, a pointer is
                 placed under  the  band  position  on  the  meter.  The
                 current XIT  and LOCK  status are  on the right side of
                 the screen.
            
                 The center  of the  screen contains the current display
                 frequency, RIT  status,  and  current  RIT  offset.  In
                 addition, another  function indicator  is  provided  so
                 that, by  looking at  this sector  alone, the  user can
                 obtain most  of the  significant information  regarding
                 the status of the radio.
            
                 The next sector contains the current scan status, spilt
                 status, and  a graphic  indication of  the current  RIT
                 offset.  A real time clock is also included.
            
                 An  lastly,   the  bottom  of  the  screen  contains  a
                 reference of  all  the  control  commands  used.    The
                 following sections  describe these  control commands in
                 detail.
            
            Chapter 4, Keyboard Commands
            
                 Several PC  keys are  used to control the various front
                 panel aspects  of  the  TS-440.    These  commands  are
                 described here:
            
                 Function Keys
                      F1   -    Decrements the current frequency by the
                                current step rate.
                      
                      F2   -    Increments the frequency by the current
                                step rate.
                      
                      F3   -    Decrements the RIT offset.
                      
                      F4   -    Increments the RIT offset.
                      
                      F5   -    Toggles the status of the RIT (on/ off).
                      
                      F6   -    Toggles the XIT status.
                      






                      F7   -    Select frequency for VFO A.
                                This command will prompt the user for a
                                frequency to be placed into VFO A.
                           
                      F8   -    Same as above for VFO B.
                      
                      F9   -    Select Memory Channel.  This command     
                                prompts the user for the memory channel
                                desired.
                      
                      F10  -    Exit, quit the program.
                      
                      A    -    Switch to VFO A
                      
                      B    -    Switch to VFO B
                      
                      C    -    Clear current RIT offset.  This command
                                allows you to have the radio ignore the
                                current position of the RIT controller,
                                and use exclusively the remote control.
                                Note that if the control is moved on the
                                rig, the current controller position is
                                restored, and the program is updated as
                                to its status.
                      
                      M    -    Select memory as current function
                      
                      O    -    Select Mode.  This key scrolls through   
                                all the possible modes of the TS440 (AM,
                                FM, CW, ect...).
                      
                      P    -    Toggle split status.
                      
                      S    -    Toggle Scan Status.
                      
                      T    -    Transmit/ Receive toggle.  (Careful!)
                      
                      Alt F7-   Memory to VFO copy.
                                This command prompts for which VFO to    
                                copy to, and the channel you wish        
                                copied.
            
            Other notes
                 While using  ts440ctl, you  may notice  that the screen
                 updates do  not always  track the  status of the radio.
                 In reality, the problem lies with the radios ability to
                 relay information  back  to  the  PC.    The  interface
                 specification states  that  an  update  of  information
                 takes  place   every   1.5   seconds.   This   can   be
                 misunderstood to  mean that at any time, information is
                 updated every  1.5 seconds.   This,  in fact is not the
                 case.   When activity  takes place on the radio, either
                 using the  front panel  controls or  the PC,  an update
                 will not  take place  until the  radio  sits  idle  for






                 approximately 1.5  seconds.   A good example of this is
                 spinning the  dial while watching the PC screen running
                 ts440ctl.   You should  notice an  update taking  place
                 AFTER the  spin has  stopped.  To counter this example,
                 placing the  radio in  scan  mode  updates  the  screen
                 approximately every  1.5 seconds.    From  the  limited
                 information in  the documentation of this interface, it
                 is not  possible to determine the exact pattern or rule
                 chosen for  this, but  the end  result is  a  sometimes
                 sluggish interface to this program.
            
                 During development  of this  program, every  effort was
                 made to  insure that  status of the screen reflects the
                 actual status  of the  radio.   If, at  some time,  you
                 notice that  the screen  does not  reflect that status,
                 perform some  action on  the keyboard, for example tune
                 up and  then down.  This change should prompt the radio
                 to update the status of the PC.
            
                 If you  use one  of the many keyboard speed up programs
                 available, be  warned that if you hold a key down, then
                 every key  will count.   For  example, if  you tune  by
                 holding the  F1 key  down, it  may go  further that you
                 want.
            
                 This program was written in Borland International Turbo
                 C environment.   It  has been  tested on an PC/AT clone
                 and a Tandy 1000.  If your PC is a close compatible, it
                 should run  fine.   If  you  encounter  problems,  have
                 suggestions, or just have questions drop me a line at
            
                                      Kenneth Byers
                                           or
                                   David Byers (W9HXL)
                                 4813 West Greenway Road
                                  Glendale, AZ   85306
            
                 If you find this program useful, please help a starving
                 computer science  student by  mailing a donation to the
                 above address.   In  addition to  the charity value, it
                 will insure  that you  are notified of upgrades to this
                 program.   Some of  the upgrades I am currently working
                 on are:
                 
                      Bulk Memory Transfers which will allow you to keep
                      libraries of  memory channels  on disk, and upload
                      and download them to and from the radio.
                      
                      VFO to  Memory channel  storage which  will  allow
                      you, at  the touch of a key, to store the contents
                      of the current VFO to any memory channel.
                      






                      Utilities that  allow you  to manipulate memories,
                      as well  as selecting  a memory VIA station ID, or
                      any other comment field.
                      
                      Band Tracking,  allowing you  to select only legal
                      HAM bands,  short wave  bands, or  a user  defined
                      band pattern.
                      
                 It took  quite a  while  to  accumulate  the  knowledge
                 required to  write a  program  of  this  type,  so  the
                 recognition would  make it  all seem  worth while.    I
                 would  suggest   a  possible  donation  of  20.00,  but
                 anything helps.
            
                               Thank you, and enjoy.