>>>>>>> DEMO <<<<<<



                 KENWOOD TS940S INTERFACE CONTROLLER

          The enclosed file serves no other purpose than demonstrate the
  functional capabilities of the TS940CTL program available on various
  BBS's.  I have included a copy of the Documentation for TS940CTL and 
  all Copyright conditions apply to this DEMO as well as the TS940CTL
  program.
  
          This DEMO does not require any connection to the transceiver
  and is only a simulation of transceiver response.  I have been able
  to duplicate transceiver response in the software.
  
          Although I have filled all memory channels in the program, you
  may overwrite these frequencies to test the "writing to memory" capability
  of the program.  Of course, your changes will not be saved and when the
  program is re-run, the programmed memory frequencies will reappear.  I had
  thought of writing the memory channels to a file to be loaded on re-run, but
  since this is only a demonstration program, I did not go to that effort.

          The author would appreciate any feedback as to problems that have
  been experienced or suggestions for future changes.  
  

          73  Dick - VE3COO                            March 19, 1989


                     KENWOOD TS940S INTERFACE CONTROLLER     Vers. 1.3


          This program is being distributed as a freeware program for 
   private use only and is Copyright Protected.  You are encouraged to
   distribute these files to other interested amateurs under the 
   following conditions;

          1) All files will be transferred intact without change.
               (TS940CTL.EXE, TS940CTL.DOC and READ-ME.
             May contain files TS940-1.EXE and TS940-2.EXE.)

          2) No financial gain may be obtained through the use, sale 
             or distribution of this software.

                          * * * * * * * * * * * *
  
          The commands are fairly clear in the menu portion of the screen.
   The following is a more explicit description;

   F1 - MEMORY   -  "F1" toggles the MEMORY function on and off.  In this
                    mode, you are capable of writing the memory status to
                    a selected VFO by using "V".

   F2 - SL.TUNE  -  "F2" allows you to set either the low or high side of the
                    IF Slope Tuning.  This function will LOCK UP the
                    associated control on the transceiver.  If the high side 
                    has been engaged using this program, the low side control
                    will remain functional and vice versa.  Of course if both
                    sides have been engaged using this program, then both
                    controls will be locked.   You may return the controls to 
                    normal function by using a control C (^C).  The IF tuning 
                    will be reset to its normal settings as well.

>  F3 - M. CHNL+ -  "F3" increases the MEMORY CHANNEL by one (1).

   F4 - VBT      -  "F4" engages the Variable Band Tuning in the same fashion
                    as F2 for the Slope Tuning.  The same control LOCK UP
                    applies in this function as well.

>  F5 - M. BANK+ -  "F5" increases the MEMORY BANK by one (1).  The left
                    digit above the frequency is the Bank selected.

   F6 - PG. SCAN -  "F6" engages the Program Scan function.  The transceiver
                    will scan between the frequencies in Memory Channels 
                    9 and 0 in the current Memory Bank.  Thus you have the
                    capabilities of 4 scan frequencies by changing the Memory
                    Bank.  Keys are limited to F6 and F8 in this mode.

   F7 - M. SCAN  -  "F7" toggles the MEMORY SCAN off and on.  Only
                    F7 and F8 are functional during this function.

   F8 - S. HOLD  -  "F8" will hold either the Memory Scan or Program Scan
                    functions.  Hitting the key again will disable the function.
                    Disabling the scan function will also disable it.

   F9 - M. WRITE -  "F9" allows  you to write  directly to  the transceivers
                    memory  channels.  You  may select  either  the  current
                    operating status or enter a new frequency and mode without
                    disturbing the current settings.

   F10- SEND     -  "F10"; refer to "*".

">" denotes commands where repetative commands occur with continued key press.

Cont...)              KENWOOD TS940S INTERFACE CONTROLLER      Vers. 1.3

    V - VFO-B    -  "V" will toggle between VFO A and VFO B.

    F - FREQUNCY -  "F" will allow you to enter a frequency directly into 
                    either VFO A or B.  If the frequency is being entered
                    into the current VFO, you will be requested for the
                    MODE as well.  "ESC" will leave the mode unchanged.

    M - MODE     -  "M" allows you to change the mode (LSB, USB, etc) in the
                    current VFO ONLY.

    A - ANT.TUNE -  "A" turns on the Auto Antenna Tuner.  Hitting "A" 
                    again before the timer has ended the function will 
                    terminate this operation.
      SPECIAL NOTE: The Graphics Display does not represent a true indication
                    of the transceiver antenna tuning condition.

    * - SEND     -  "*" will key up the transmitter (PTT).  Using this key a
                    second time will return you to receive mode.  F10 serves
                    the same function.  This was to allow for right or left 
                    handed operators to use this function while holding a 
                    pencil in either hand. (At least on my keyboard)

    R - RIT      -  "R" toggles the RIT on and off.

    X - XIT      -  "X" toggles the XIT on and off.

    L - F.LOCK   -  "L" toggles the F.LOCK on and off.

    S - SPLIT    -  "S" toggles the SPLIT frequency operation on and off.

    Q - QUIT     -  "Q" obviously terminates the program returning control
                    back to the transceiver if any controls have been locked
                    due to this programs operation.

         If you have entered a command which requires information from the 
   operator, you may abort that operation with either the "ESC" or "ENTER"
   key.  If the input expected is one key stroke, the "ESC" may be used.
   The system will reset after a 10 second wait with no key press. If more 
   than one key stroke is expected (eg. frequency, etc), the "ENTER" key with 
   no input will abort the operation.  This input is not controlled by the
   auto-reset.

                                  ARROW KEYS

>  RT  - INC.  -  The right arrow key increases the VFO frequency by 10 cycles.
>  LFT - DEC.  -  The left arrow key decreases the VFO frequency by 10 cycles.
   SHIFT-ARROW KEY will increase or decrease the frequency by 100 cycles.
   CONTROL-ARROW KEY will increase or decrease the frequency by 1 kHz.
>  + and - keys will increase or decrease the frequency by 10 kHz.


                                OFF SET TUNING

>  UP  - INC.    -  The up arrow key increases the off set frequency.
>  DWN - DEC.    -  The down arrow key decreases the off set frequency.
   C   - CLR.    -  Resets the off set frequency to "0.000".

         During the frequency change operation, I have sacrificed screen
   updating for speed.  If an arrow key is held down, the screen will not
   be updated until the key is released.  

Cont...)            KENWOOD TS940S INTERFACE CONTROLLER      Vers. 1.3



                                  Requirements
                               
          This program was written on and for the IBM XT and clones.  It
   requires the installation of the Kenwood Interface Kit IF-10B and a
   TTL-RS232 converter such as Kenwood's IF-232C.

          I might mention that I did experience considerable difficulty getting
   the computer to recognize that the interface was connected.  I received an
   ERROR #24 DEVICE ERROR.  I eventually shorted pins 6,8 and 20 on the
   RS-232 cable at the computer end and that solved the problem.  

                           ******   WARNING  ******

           I have tested this program using DoubleDos using 128K of upper 
   memory.  I feel you should be made aware of the following experience;

        1)  By design, this program locks out the keyboard during times when 
            keyboard input is undesirable.  In Dbl-Dos the keyboard buffer
            remains active and at points where I have stripped the buffer,
            this operation does not appear to be effective in Dbl-Dos. 
            Using the arrow keys in repetative mode will store the keyboard
            activity in the buffer. (i.e. the frequency shift will continue
            long after the key has been released).
        2)  Also, when you terminate the program using the "Q" command, it
            appears Dbl-Dos is leaving the system in a locked up state.  I
            feel the keyboard lockout, as described above, is the root of 
            the problem.  With a little effort (hitting different keys), I
            was able to regain system control.


         I have tested this program using Turbo mode (8Mhz) and normal mode 
   (4.77 Mhz).  It appears to be working correctly in both although the speed
   is conciderably slower in the normal mode.  If anyone has any problems or 
   suggestions for improvement, please let me know so that may use the 
   information in any future updates.  I would appreciate any feed back.  I 
   can be reached;

       via Packet Radio      VE3COO @ VE3NUU 

       or by mail          Richard (Dick) Tunks  VE3COO
                            1220 Falgarwood Dr.
                             Oakville, Ontario
                               L 6 H   2 L 3















  (C) 1989-VE3COO                                              March 19, 1989