440-3  (C) Douglas K. Heller

	Here is another Kenwood TS-440 control program.

	The program is pretty much straight forward, but I will
 	explain how it works in these docs.

	You can copy the files from this disk to you hard drive
 	with the normal DOS command  COPY *.* Next type 440 <enter>.  
        The program will ask which com 	port 1 or 2.  Com 3 or 4 are 
	not supported. The program will try to get a code from the 
	rig, and if successful, you will be told that you are 
	either using a TS-440 or a R-5000.  If the proper code is not
	received. the program will tell you so and PRESS ANY KEY to Terminate 
	the program.  If the program terminates, check your interface 
	and cabling.

	If all has  worked OK, you should be in the main menu. 	Choose 
	ALT D to display most of the functions of the TS-440. As 
	you can see at the bottom of the screen there are a few function 
	keys that you can do some controlling of the TS-440 like input 
	a frequency, mode. Turn the SPLIT on and off. 

	When you rotate your VFO, you will notice that nothing 	
	seems to happen on the display until you stop. This is 	
	because the TS-440 output is rather erratic. Use ALT X to 
	Exit to the main menu.

	Again from the main menu, Choose <ALT M>, This will read 
	all the memories in the Radio. After the program has read 
	all the memories, it will display 0 to 44. Use 	the <Down Arrow> 
	key to display memories 45 to 89, or 	use the <Up Arrow> 
	to display the Split Memories 90 to 99 usually used for 
	10 meter FM repeater use.

	After paging though the memories you can save the contents 
	of the memories to disk by hitting <ALT S> key. After 
	saving the memories to disk use the  <ALT X> 	to get back 
	to the main menu.

	You can use the final feature of this program to restore any 
	or all the memories to the TS-440 in the unlikely event 
	you reset the micro processor in the TS-440 or you loose 
	the contents of the memories and provides a short cut 
	to re programming the memories 	back into the TS-440. 
	You must have the file 	DKH440.MEM on the same disk or 
	in the same directory as this program. You must have saved the 
	contents of the memories to disk before you use this feature.

	Oh yes, to exit the program from the main menu type a 	
	<ALT X> and you will go back to dos.

	One final thing, If you like this program and make use 	of it, 
	I would appreciate it if you would send me 10 	bucks or so. 
	If you don't, that's fine, enjoy the program and thanks anyway. 
	If you do it helps motivate me to do more and add new features 
	to later versions, and will be greatly appreciated!

            Doug Heller  KE7NF
	    1121 W. Obispo
	    Mesa, Arizona  85210