HAMRAD-DSK1
                      Copyright  1986, 1987


                   Robert H. Lieberman  WA9JWN
                     9027 Sleeping Bear Road
                     Skokie, Illinois  60076



                         WHAT IS HAMRAD?



HAMRAD-DSK1,  includes  several programs of specific interest  to 
the Amateur Radio Operator.    

There  are 6 programs available to the user under the master menu 
program, HAMMENU.  The HAMMENU screen looks something like this:



                  A - Beam Heading Locator
            
                  B - Prefix File Maintenance

                  C - Print Bearings from your QTH

                  D - LOG Book Program

                  E - Print QSL Cards

                  F - Change Station Coordinates 


                      Enter Selection  ?


The primary programs (A thru C) are designed to provide the  user 
with a means by which to determine antenna azimuth positioning... 
in  short,  where  to  point your antenna!   With  your  own  QTH 
coordinates on file, the computer can provide beam headings based 
upon  International  Prefixes (ZL4,  1A0,  etc),  Universal  Grid 
Squares  (EN62DA etc) or Latitude and Longitude.   You  can  also 
create  a bearing list,  of all prefixes in the file,  from  your 
QTH.
 
These  programs  are  proprietary  and are  provided  on  a  user 
supported  basis  (Shareware).   If you find  HAMRAD-DSK1  to  be 
useful,  a  registration fee of $25.00 is strongly suggested.   A 
user  manual  and  any current up-dates  will  be  provided  upon 
registration.




                             SET-UP


Before  using  HAMRAD-DSK1 you should customize  the  STATION.DAT 
file  to  meet your needs.   First,  use EDLIN to view the  file, 
STATION.DAT.    Each   line   is  prompted  with   the   required 
information,  followed  by a colon (:),  followed by the  station 
information.   EQUIP #1 will correspond to ANT #1, etc.  The last 
8 information parameters correspond to the codes required by your 
printer  for  the  appropriate  information.    Dual  codes   are 
separated  by a comma.  DO NOT ALTER the relative position of the 
colon (:) !   A typical STATION.DAT file is as follows:



   CALL SIGN:WA9ABC                               [ your call ]
    LICENSEE:Ronald J. Jones               [ and address info ]
  ADDRESS #1:12345 S. Maine Street  
  ADDRESS #2:Anywhere City, Texas 11111   
  ADDRESS #3:U.S.A.
    EQUIP #1:TS-440/AT
    EQUIP #2:Yaesu 726-R, Gasfet Preamp
      ANT #1:3 Ele Beam, Inv V
      ANT #2:KLM 22CX - KLM 40CX
      10 CPI:27,80
      12 CPI:27,77
 ENABLE XPND:14                         [ Code to EXPAND print ]
DISABLE XPNX:20                                 
 ENABLE EMPH:27,71                   [ Code to EMPHASIZE print ]  
DISABLE EMPH:27,72
 ENABLE COMP:15                    [ Code for COMPRESSED print ]
DISABLE COMP:18



Following  set-up of the STATION.DAT file,  you must now  provide 
the computer with your EXACT International Grid Square which will 
be  held  in  a  file  for  all  future  references.    This   is 
accomplished by initiating the master menu,  HAMMENU.   To do so, 
log to the proper disk and type HAMMENU (followed by a C/R).  you 
will  need  to  know  either your correct  Grid  Square  or  your 
Latitude and Longitude.


  
If  you do not have the Grid Square information,  select  program 
'A',  Beam  Heading.   When  the Beam Heading program  comes  up. 
select  option 'C',  Latitude and Longitude.   Enter the required 
information and it will display your exact Grid Square.

Escape  back  to the master menu and select  option  'F',  change 
Station  Coordinates.   Follow the instructions and you  will  be 
ready to use all subsequent programs.




                       SYSTEM REQUIREMENTS



     
A minimum of 256K user memory is recommended.  A color monitor is 
not  required  but will add significantly to the  users  delight.  
All  programs will operate with a single floppy disk but the  LOG 
program will be severly limited.  A second floppy or (preferably) 
a hard disk will provide optimum results.   A printer is required 
for the QSL program as well as the BEARING program.





                     COMMAND & ENTRY SYNTAX

  

ESC   moves the operator backwards towards DOS.   If for example, 
you  are in the Beam Heading program's  sub-program,  Heading  by 
Prefix,  entering  the  ESC  key will return you to  the  Heading 
Programs  menu.   Another ESC will return you to the  main  menu, 
HAMMENU.  Another ESC will exit you to DOS.

In all program entry modes, upper case is required.  The software 
checks for lower case and converts as is necessary.  
.PA
.HE PROGRAM NOTES:


                   PGM-A  Beam Heading Locator


PURPOSE:  Determine Beam Heading and distance from your QTH to
          destination location.

NOTE:     Wait for Initalization.  About 20 seconds from Floppy
          Disk, 5 seconds from Hard Disk.


          OPTION - A     Locate by International Prefix

                         Enter a prefix, (ie. VK3 o VK)
                         Do not enter an entire call!

          OPTION - B     Locate by Universal Grid Square

                         Enter Grid Square (ie. EN62  or    
                         FL95MM).  You must enter no less
                         than 4 valid characters nor more
                         than 6 characters.

          OPTION - C     Locate by Latitude and Longitude

                         Enter appropriate coordinates in
                         Degrees and Minutes (ie. 56.39).
                         NOTE:  Minutes cannot exceed 59.
                                Coordinates South or East
                                are entered as minus  (-)
                                values.



                 PGM-B  Prefix File Maintenance   

 
PURPOSE:  To update, enter, delete or otherwise change the
          PREFIX.DAT file.

NOTE:     Wait for Initalization.  About 20 seconds from Floppy
          Disk, 5 seconds from Hard Disk.
          
          Changes to this file can be FATAL!  Proceed  with 
          caution.  

          If deleting a prefix, enter right brackets (]]]]...)
          in the first and second entry fields of a record.

          When exiting the program, if changes are made, it is
          recommonded that you sort the file.  Make sure that
          you have additional disk space, equal to the size of
          the current PREFIX.DAT file.  Entries cannot exceed
          500 in quantity.

               PGM-C  Print Bearings from your QTH


 
PURPOSE:  Compute Bearings (beam headings) for all known
          prefixes in the PREFIX.DAT file and print a list
          including Country name, Reference, Distance and
          Universal Grid Square for those coordinates.

          This program is self-documenting.





                     PGM-D  Log Book Program



PURPOSE:  Maintain a traditional log on your computer's disk.
          
NOTES:    The default filename is "MASTR" but any syntax-legal
          name can be used.  DO NOT enter a file extension.
          
          Each record in a .LOG  files  occupies 128 bytes, so
          beware... THIS PROGRAM WILL EATS UP DISK SPACE!


          OPTION-1    Entries are reasonably self-prompting.  
                      A field of dots (........etc) will
                      indicate the maximum length allowed for
                      a field entry.

                      TIME and DATE will, upon first time 
                      entered, default to System  DATE  and  
                      TIME if a C/R is  entered.   Thereafter, 
                      default will be the last entry for DATE
                      and the current System TIME.

                      You  MUST  enter Call, Frequency and 
                      Country.  Country will default to USA
                      on C/R.

          
           OPTION-2   Self documenting.

           OPTION-3   Self documenting

           OPTION-4   Self Documenting

           OPTION-5   Prints the entire file to printer.

           OPTION-6   Self documenting

                     PGM-E  Print QSL Cards


PURPOSE:  This program, utilizing the STATION.DAT file and any
          valid .LOG file, will generate QSL cards on 3.5 X 5
          form-feed  stock.   A  typical QSL will look  something 
          like this:

  
                             WA9ABC
                         Ronald J Jones
                      12345 S. Maine Street
                   Anywhere City, Texas 111111  
                             U.S.A.                         
   ___________________________________________________________
   |   STATION   |   DATE & TIME   |  FREQ  |  RPT  |  MODE  |
   |-------------|-----------------|--------|-------|--------|
   | W0XXX       |08/16/84 0214 UTC| 145.05 |  599  |  A3A   |
   |_____________|_________________|________|_______|________|

    TS-440/AT     3 Ele Beam, Inv V
    Yaesu 726-R, Gasfet Preamp     KLM 22CX - KLM 40CX

    Remarks __________________________________________________

    Remarks __________________________________________________

                         PSE   QSL   TNX     
           


NOTES:    All that remains after the QSL's are printed is to
          enter your remarks, sign, address and send.  Takes
          all the drudgery out of QSLing!

          Your CALLSIGN will be printed in Expanded, Emphasized
          type.  Future editions of this program will provide
          an expanded graphic capability for your callsign.  




           
                           CONCLUSION


These programs have been used for some time without any  hitches.  
However,  there's always room for an exception!  If you encounter 
such  a 'hitch' please let me know and I'll see what can be  done 
to  correct it.   It might be noted that some of the Latitude and 
Longitude  coordinates  in  the prefix file may  be  slightly  in 
error.  I have encountered only one during use, but then again, I 
haven't worked all the prefixes yet!  A SUPER PREFIX file will be 
made available to registered users only when finished.   73's and 
good dxing.
 prefixes yet!  A SUPER PREFIX file will be 
made available to registered users only whe