NAME rc85prg - program an RC-85 repeater controller. SYNOPSIS rc85prg [options] prgfile DESCRIPTION RC85PRG will, using a Hayes-compatible modem with a PC running MS-DOS, dial up an A.C.C. RC-85 controller and program it. The modem is capable of sending digits 0 through 9, * and #. RC85PRG has been compiled with default sequences for the owner unlock code, the control operator code, the user autodialer programming codes, and the controller phone number. Each of these sequences can be redefined by command-line options. The input file contains the programming commands. If not specified on the command line, stdin is used. Hence pipes (|) or redirection (<) may be used to provide programming commands. The MBBIOS interrupt-driven I/O package by AA4RE must be loaded prior to invoking RC85PRG. Contact your local packet BBS sysop if you need help in obtaining AA4RE's excellent package. OPTIONS If RC85PRG is invoked improperly, it will display a usage summary, and indicate the current value of all settable options. Options include: -v enable verbose mode. -t enable test mode (simulate operation). -u indicate autodialer is kept unlocked. -w N wait N secs after dialing the RC85, to permit the phone answer message to finish. -p N pause N secs after each command, to permit the response message to finish. -m COMn:baud,8N1 select a modem port and parameters. Any COM port supported by MBBIOS is permitted. -d phonenumber override the default phone number of the con- troller. Include any exchange access and pause for dialtone characters in this string. -o owner_code override the default owner unlock code. -c ctrlop_code override the default control op code. -2 code override the default 2-digit slot programming code. -3 code override the default 3-digit slot programming code. PRGFILE FORMAT This file is an ASCII file containing one command per line. Comments may be placed anywhere, and are indicated by a '#' and continue to the end of the line. Although a '#' can be used in control sequences sent via radio, the '#' must be used to terminate a programming sequence sent via the telephone. Hence its use as a comment delimiter is not ambiguous. Commands consist of two characters beginning in column 2. Case is not significant. Commands are: CU unlock the controller lock, to permit message programming (for example). CL lock the controller (after a CU command). CS string send  to the controller. Permits an arbitrary RC85 command to be issued.  should contain only one controller command. CO string send the control-operator prefix followed by  to the controller.  should contain only one controller command. S n s p program the autodialer slot number , identified by string , to dial the phone number

. string  may be used to record the callsign or any other text; no spaces are permitted, and this information is otherwise ignored. The S command is equivalent to a sequence of CS commands to enter unlocked mode (if slots 0 through 9 are selected), to unlock the autodialer (if needed, see -u), to clear the current slot contents, and to program a new phone number. If the slot number  is negative, the slot is programmed to speak the number being dialed. MP program the previously-sent message. Equivalent to CS *0. MR readback the message being programmed. Equivalent to CS *2. MA abort the message being programmed. Equivalent to CS *4. EXAMPLE PRGFILE # Program phone numbers into three slots S3 Fire 268-5501 S4 LPSO 232-9211 S11 N5KNX 555-1234 # Program emergency msgs cu cs *1113 #slot 3 = Fire cs *634 mp cs *1114 #slot 4 = LPSO cs 53 71 73 63 mp cl co 75 #Select stardust courtesy tone THEORY OF OPERATION Rc85prg first validates its command-line arguments, then dials the RC85 controller. It waits (see -w) a while for the dialing and rc85 greeting message to complete. Rc85prg will then read the input file looking for programming commands. Each line of the input file constitutes one command. Each command is sent to the RC85 (suffixed automatically by the required # tone) and then the program pauses (see -p) for the spoken acknowlegement. Commands should be given in the proper sequence, that is, unlocked-mode commands should not be mixed with control-operator commands. Autodialer slot programming does not require explicit unlocking; the RC85 is unlocked automatically if slots 0 through 9 are selected. After end-of-file is encountered, the appropriate lock and hangup commands are sent to the RC85, and then the modem is told to hang up the phone line. EXAMPLE rc85prg -o 1989082344 -c 654 -d 121,9,5551212 setimers.r85 dials 555-1212 and programs the controller from the file named setimers.r85. grep ^S11 autodial.r85 | rc85prg -o 1989082344 -c 654 -d 121,9,5551212 uses the grep program to find the line beginning with S11 in the file named autodial.r85, and provides this line to rc85prg for programming. AUTHOR James Dugal, N5KNX @ W5DDL (packet) jpd@usl.edu (Internet) P.O. Box 44844, Lafayette, LA 70504