.PL
        WHATS-UP.DOC Release 0.55 Page 1.



                                  _______
                             ____|__     |                  (tm)
                          --|       |    |-------------------
                            |   ____|__  |  Association of
                            |  |       |_|  Shareware
                            |__|   o   |    Professionals
                          -----|   |   |---------------------
                               |___|___|    MEMBER


                      WHATS-UP (c) Joe Kasser, G3ZCZ, 1990

                               Joe Kasser G3ZCZ/W3
                                    POB 3419
                            Silver Spring, Md. 20918
                                 (301) 593 6136

                               G3ZCZ @ N4QQ.MD.USA

        This  version of WHATS-UP allows you to capture, decode,  display 
        and extract for analysis telemetry from the Digital Voice Encoder 
        (DOVE) OSCAR 17, Fuji-OSCAR 20 spacecraft.  It also allows you to 
        process   captured   telemetry  from  the  late   Fuji-OSCAR   12 
        spacecraft.    WHATS-UP  is  a  table  driven  program  via   the 
        configuration  files to allow maximum flexibility.  This  program 
        does  not decode/display the AMSAT/UoSAT Binary  telemetry  data, 
        and should not be used to capture binary telemetry.

        The program is distributed as a Shareware product. You may freely 
        copy  and  share  the product for noncommercial  use,  with  your 
        friends,  associates and other radio hams. If you decide  to  use 
        the  product, you are asked to become a registered user  by  com-
        pleting  the  registration  form and sending it,  and  $35.00  or 
        equivalent in foreign currency to the author.

        Upon  receipt  of your registration, you will  receive  one  free 
        update disk, telephone and mail (electronic and regular) support. 

        This product may not be sold or distributed with another  product 
        without the express written permission of Joe Kasser, G3ZCZ. 

        Joe  Kasser,  G3ZCZ will only support unmodified copies  of  this 
        software.  Your comments and suggestions for changes are  however 
        welcome.  If you are the first to suggest a change that is imple-
        mented,  you will be sent a complimentary copy of the  disk  with 
        the change incorporated.

        Potential  Commercial  and Educational Institution  Users  please 
        contact  Joe Kasser directly for modifications and/or details  of 
        Site licensing.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 2.


                                Table of Contents

        1.0 Introduction

        2.0 Capabilities

        3.0 Things You Should Know
             3.1 TNC State
             3.2 Limit Checking
             3.3 Link Quality Measurements
             3.4 Program Requirements
             3.5 Data Format
             3.6 Display Pages
             3.7 Function Keys
             3.8 Typical Screen Color Combinations 
             3.9 TNCs
             3.10 Obtaining Updates
             3.11 Look Up Tables

        4.0 Bringing Up WHATS-UP For the First Time
              4.1 Editing the Configuration File.
              4.2 Starting the program.

        5.0 Standby Mode
            5.1 Extract From Playback File
            5.2 Interactive Mode
            5.3 Playback Mode
            5.4 AMSAT/OSCAR Menu
            5.5 Real Time Mode
            5.6 Change Directory Path
            5.7 Change Display Page
            5.8 Show Space on Disk
            5.9 Change Playback File
            5.10 Change Microsat
            5.11 Show Defaults
            5.12 View Playback File
            5.13 Exit to Dos
            5.14 Show Files
            5.15 Show Color Chart

        6.0 Playback Mode

        7.0 Interactive Mode

        8.0 Real Time Mode

        9.0 (Data) Extraction Mode

        10.0 Configuration File

        11.0 Spacecraft Parameter Files



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 3.


        12.0 Telemetry Channel Extraction File

        13.0 Extracted Telemetry Data File

        APPENDIX A DOVE Telemetry 
        APPENDIX B Fuji-OSCAR 20 Telemetry
        APPENDIX C Fuji-OSCAR 12 Telemetry
        APPENDIX D Information about AMSAT
        APPENDIX E Amateur Radio Software by Joe Kasser G3ZCZ
        APPENDIX F Shareware












































        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 4.


        1.0 Introduction

        Orbiting  Satellites  Carrying Amateur Radio  (OSCAR)  send  back 
        volumes of Telemetry daily and apart from a few Command  stations 
        no-one seems to be doing anything with it.  We, as Radio Amateurs 
        tend  to  concentrate on the communications capabilities  of  the 
        spacecraft  and  ignore  their telemetry completely.   If  we  do 
        listen  to  a  beacon,   it's usually  just  to  check  that  the 
        transponder is on, heaven forbid - to actually copy any data.

        The  telemetry  can  tell us a story.  It can  tell  us  what  is 
        happening to both the spacecraft and its environment.  As such it 
        has  a tremendous educational potential which has  remained  just 
        that - a potential for at least the last six years.

        Before  every satellite launch the equations and format  for  the 
        spacecraft telemetry are published by AMSAT.  The telemetry tells 
        us  about  the health and welfare of the spacecraft  itself,  and 
        something  about  the  payload.  Spacecraft  health  and  welfare 
        information tells us about the battery, solar cells and on  board 
        computer  status. Payload information can range from  information 
        about  transponder loading/utilization to data  from  instruments 
        that  measure  the  environment of the space in  and  around  the 
        satellite.  Battery Telemetry is used by the command stations  to 
        determine  when  the  spacecraft  can  be  used,  and  when   the 
        transponders should be shut down.  The number of individuals  not 
        associated  with  command stations who  have  decoded  spacecraft 
        telemetry  and published their findings can be counted using  the 
        fingers of one hand.  There's a lot of computing power out  there 
        that  has  the  potential  to  process  telemetry  and   discover 
        something new, but does not have the access to the data.   WHATS-
        UP  is  an  attempt to provide that data  to  the  average  Radio 
        Amateur.

        2.0 Capabilities

        WHATS-UP contains the following features:

        * Real-time, Interactive and Playback modes.

        * Automatic Capture-to-disk of raw telemetry.

        * Extracts  telemetry channel data to a database  or  spreadsheet 
          readable file for further analysis.

        * Link quality measurement.

        * Capability  to  display and print the raw telemetry  as  it  is 
          received.

        * Up to 16 user configurable display pages (screens). You set the 
          position  on  the page (width of engineering  unit  field,  and 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 5.


          number of decimal places) that a parameter is displayed at.

        * Wild card page (parameter shows up on all pages).

        * Selectable  display of Engineering units or Hex byte  for  each 
          display page.

        * Display of raw packets (i.e. STATUS)

        * Color  changes if a parameter value changed between  successive 
          frames.

        * Audio  and  visual alarms if a telemetry value  exceeds,  falls 
          below or falls outside a preset limit value(s).

        * Dumb split screen terminal mode (a la LAN-LINK).

        * Customizable colors, PC to TNC baud rate, data parity and  stop 
          bits.

        * Default spacecraft configuration files.

        * Time of day clock display (in HH:MM:SS format)

        3.0 Things You Should Know

              3.1 TNC State

             WHATS-UP  does not change the TNC state at start up,  unless 
             you command a time change or a configuration. 

             3.2 Limit Checking

             Limits  are only checked for parameters being displayed  (in 
             Engineering  units).  With  this approach, you  can  set  up 
             different  pages for different on-board subsystems, you  can 
             also  set up different display pages of the same  parameters 
             for daylight, darkness and terminator crossing passes,  with 
             different limit values to draw your attention to changes.

             3.3 Link Quality Measurements

             The  link quality part allows the following to be done.  You 
             can  define which of the packets you want  to  display/count 
             (If  you just want to count them and not display  them,  set 
             the  page  value to 99). You can then view  an  incrementing 
             count  counter each time a selected packet is received.  For 
             example,  using  DOVE-OSCAR  17, you can  also  display  the 
             contents  of  the  STATUS, WASH or  BCRXMT  packets  in  any 
             display page.  This feature allows you to get an idea of how 
             good your receiving system is.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 6.


             3.4 Program Requirements

             IBM PC or clone with 256k memory.

             A  Packet TNC with an RS-232 interface is required for  real 
             time data capture.  WHATS-UP has been tested with a TNC2, an 
             MFJ1278, a KAM and a PK-232 so far.

             3.5 Data Format

             The program DOES require that the telemetry be received, and 
             captured-to-disk with the packet header on a different  line 
             to  the  contents  of the packet  (HEADERLINE  ON).  I  also 
             suggest  that  you turn the date/time stamp on so  that  you 
             will  be  able to playback your data  and  extract  selected 
             values  and their corresponding time codes into a file  that 
             can be read into your spreadsheet program for further  trend 
             analysis.
              
             3.6 Display Pages

             This version (the default) is set up to display all  packets 
             as  wild  cards (i.e will show up on all  pages),  and  then 
             display several temperatures and solar cell array currents.

             By  putting  the correct parameters  in  the  SPACECRAFT.SYS 
             file, you can set up any of the pages to display any of  the 
             telemetry channel data in any row and column in that page.

             3.7 Function Keys

             The following function keys are active:

                  FK 1 capture to disk Toggle
                  FK 2 type of display Engineering Units/Raw Byte Toggle
                  FK 3 select display page
                  Alt-B send a 'Break' to the TNC (interactive mode only)
                  Alt-C connect  to another packet  station  (interactive 
                        mode only)
                  Alt-D disconnect    from   another    packet    station 
                        (interactive mode only)
                  Alt-P Printer on/off toggle
                  Alt-S Sound on/off toggle
                  Alt-X Quit Mode
                  left arrow  decreases playback speed
                  right arrow increases playback speed.

             3.8 Typical Screen Color Combinations 

             You  can  view  the colors  associated  with  the  different 
             numbers by choosing the '*' option in the Main Menu.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 7.


             3.9 TNCs

             Version 0.55 is set up to configure the PK-232 in the AMSAT-
             OSCAR  Mode.  You can use other TNCs in the packet modes  if 
             you configure them yourself.

             3.10 Obtaining Updates

             It  is  anticipated  that  WHATS-UP is  going  to  grow  and 
             incorporate  features for decoding and displaying data  from 
             other  spacecraft.   Microsat binary  telemetry  decode  and 
             display  capability will be added when AMSAT  announce  that 
             the  format has stabilized, and sufficient registered  users 
             express interest in having it.  To stay on the mailing  list 
             and receive an update as it is released, register your copy, 
             then  send  in a disk containing at least 300k  of  captured 
             data from the spacecraft of your choice.  If you would  like 
             to  exchange  data with other  educational  institutions  or 
             users so as to be able to analyze more data than you can get 
             on a single pass, indicate that fact and we will try and put 
             you in direct touch with others who are similarly inclined.

             3.11 Look Up tables

             WHATS-UP uses look up tables to determine how the  telemetry 
             is  decoded and where the decoded data are displayed.   This 
             allows  you  as  the user to  customize  display  pages  and 
             configure  new tables when changes are made in the data  the 
             spacecraft sends, or when new spacecraft are launched.   For 
             example,  a  look up table set for Fuji-OSCAR 12  will  also 
             work  with  fuji-OSCAR 20 if the equation  coefficients  and 
             description  text  are changed in  the  configuration  file.  
             Similar  configuration  files can be used for  each  of  the 
             AMSAT  Microsat ASCII telemetry data formats that were  used 
             in the months following the launch.

        4.0 Bringing Up WHATS-UP For the First Time

        WHATS-UP  has four basic modes of operation;  Interactive,  Real-
        time,  Data Extraction and Playback. You must configure  WHATS-UP 
        before you try any Real-time activity.

              4.1 Editing the Configuration File.

             The configuration file is called WHATS-UP.SYS. You must edit 
             it  with an ASCII word processor (in the non document  mode) 
             to set up the correct parameters on the RS-232 link  between 
             your  TNC  and your PC. See Section 10 for details  of  what 
             parameter is on which line of the WHATS-UP.SYS file.





        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 8.


             4.2 Starting the program.

             You may start the program in three ways as follows.

                   4.2.1 Default

                  Type 'whats-up' and return (without the '  characters). 
                  This brings the program up in the default mode. It will 
                  read the whats-up.sys file to determine the  spacecraft 
                  being monitored, and then prompt you for the mode.

                  4.2.2 User Chosen spacecraft
                   
                  Type  'whats-up spacecraft' and return (without  the  ' 
                  characters). The program reads the spacecraft.sys  file 
                  to load the parameters for the Microsat of choice,  and 
                  then prompts you for the mode.

                   Examples of the command are :

                   'WHATS-UP DOVE' or 'WHATS-UP Fuji20'

                  4.2.3 Custom Mode

                  Type 'whats-up spacecraft mode' and return (without the 
                  ' characters). This brings the program up in the custom 
                  mode.  It will read the whats-up.sys file to  determine 
                  the  spacecraft being monitored, and then start  up  in 
                  the  mode  you set. Valid modes are 'p', 'i',  'e'  and 
                  'r'.

                   Examples of the command are :

                   'WHATS-UP DOVE R' or 'WHATS-UP Fuji20 R'

                  If  you  place  a  command  line  like  this  in   your 
                  autoexec.bat  file, should you be copying telemetry  in 
                  an  unattended manner and a power failure  take  place, 
                  the system will boot up into the correct WHATS-UP  mode 
                  when power is restored.

        5.0 Standby Mode

        The  standby Mode presents you with the Main Menu,  organized  in 
        two prompt windows, as shown below.









        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 9.


        The MODES Menu Window

          E Extract From Playback File
          I Interactive Mode
          P Playback Mode
          O AMSAT/OSCAR Menu
          R Real Time Mode

        The SELECTIONS Menu Window

          A Change Directory Path
          C Change Display Page
          D Show Space on Disk
          F Change Playback File
          M Change Microsat
          S Show Defaults
          V View Playback File
          X Exit to Dos
          Z Show Files
          * Show Color Chart

        Type the letter associated with the option to perform it.

        Each of the options are described below.

            5.1 Extract From Playback File

            This option begins up the Extraction mode.

            5.2 Interactive Mode

            This option begins up the Interactive mode.

            5.3 Playback Mode

            This option begins up the Playback mode.

            5.4 AMSAT/OSCAR Menu

            When you exercise this option you will be presented with  the 
            Menu shown below.

                  A UoSAT ASCII Beacon
                  B Phase 3 RTTY Beacon
                  M Fuji/Microsat ASCII Packet
            Each option is described below.

            5.4.1 UoSAT ASCII Beacon

            This option will configure the PK-232 to copy the UoSAT-OSCAR 
            11 telemetry. Note: you require a hardware change in the  PK-
            232 to make sense of the received data.


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 10.



            5.4.2 Phase 3 RTTY Beacon

            This option will configure the PK-232 to copy the UoSAT-OSCAR 
            13 Baudot Beacon.

            5.4.3 Fuji/Microsat ASCII Packet

            This  option will configure the PK-232 to copy the  DOVE  and 
            Fuji  ASCII  format  PACKET telemetry.  You  should  not  use 
            WHATS-UP  to  capture AMSAT/UoSAT  binary  telemetry  because 
            WHATS-UP filters the ^J and ^M (carriage return and line feed 
            characters) from the incoming datastream.

            5.5 Real Time Mode

            This option begins up the Real-time mode.

            5.6 Change Directory Path

            This  option allows you to temporarily change  the  directory 
            path.

            5.7 Change Display Page

            This  option  allows you to change the display page  for  the 
            Real-time,  Playback  and Extraction Modes. It  performs  the 
            same  operation as Function key 3 (F3) when those  modes  are 
            active.

            5.8 Show Space on Disk

            This  option  allows you to see how much space is left  on  a 
            disk with exiting from the program.

            5.9 Change Playback File

            This option allows you to change the playback file. To select 
            a file, move the cursor down to the desired file and push the 
            'Enter' key.  If you have more files than fit in the  window, 
            touch the 'PgDn' key to display another window full.

            5.10 Change Microsat

            This  option  allows  you to choose  another  spacecraft.  To 
            select  a another one, enter the name of  the  spacecraft.sys 
            file.   For example, the default files supplied with  Version 
            0.55  are  DOVE.SYS and FUJI.SYS. To select the DOVE  or  the 
            Fuji-20 spacecraft, type 'DOVE' or 'Fuji'





        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 11.


            5.11 Show Defaults

            This option allows you to display the default settings.

            5.12 View Playback File

            This  option allows you to view the contents of the  playback 
            file. 

            5.13 Exit to Dos

            This  option allows you to terminate WHATS-UP and  return  to 
            DOS. 

            5.15 Show Color Chart

            This  option  allows you to display the  color  combinations.  
            Use  this  to see what how the different  color  combinations 
            appear on your screen, note the numbers associated with  each 
            color,  then exit from the program and edit the  WHATS-UP.SYS 
            file  using  your editor in its ASCII (non  document)mode  to 
            change the colors to those you desire. 

        6.0 Playback Mode

        The Playback mode allows you to play back captured telemetry with 
        4  speeds (speedy, slow, slower and snail's pace).  If you  touch 
        the 'Escape' key you will bring up the following Menu.

        D Show Space on Disk
        R Reset Packet Counters
        Q Quit to Main Menu
        Z Show Spacecraft data Files

        Type the letter associated with the option to perform it.

        Each of the options are described below.

            6.1 Show Space on Disk

            This  option  allows you to see how much space is left  on  a 
            disk with exiting from the program.

            6.2 Reset Packet Counters

            This  option  resets the packet counters to  zero.  use  this 
            before  playing back a data file to see how many  packets  of 
            each type are present in the file.

            6.3 Quit to Main Menu

            This option returns you to the Main menu.


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 12.



            6.4 Show Spacecraft data Files

            This  option  shows  you  the  data  files  for  the   chosen 
            spacecraft in the default directory path.

        7.0 Interactive Mode

        The  Interactive mode is a dumb terminal. You can use it to  give 
        commands  to the TNC. The usual one is to set the TNC  date  from 
        the  computer's  clock.  You  should  also  use  it  to  set  the 
        'HEADERLINE  ON'. In this mode, you will see the raw  packets  on 
        the channel. You can also use this mode as a regular TNC  program 
        (If you do, you ought to get your head examined, because LAN-LINK 
        will  do the job much better).  The capture-to-disk will turn  on 
        when  the first packet is copied, and will turn off  two  minutes 
        after the last.

        If  you  touch the 'Escape' key you will bring up  the  following 
        Menu.


         C Configure PK-232
         D Show Space on Disk
         O AMSAT/OSCAR Menu
         Q Quit to Main Menu
         Z Show Spacecraft data Files

        Type the letter associated with the option to perform it.

        Each of the options are described below.

            7.1 Configure PK-232

            This  option  configures the PK-232 to copy  the  UI  packets 
            transmitted by the Packet spacecraft.

            7.2 Show Space on Disk

            This  option  allows you to see how much space is left  on  a 
            disk with exiting from the program.

            7.3 AMSAT/OSCAR Menu
            
            This  option brings up the AMSAT/OSCAR Menu as  described  in 
            the Main Menu in the Standby mode.

            7.4 Quit to Main Menu

            This option returns you to the Main menu.




        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 13.


            7.5 Show Spacecraft data Files

            This  option  shows  you  the  data  files  for  the   chosen 
            spacecraft in the default directory path.

        8.0 Real Time Mode

        The  Real-time mode converts and displays engineering  data.  You 
        can  display up to 16 (configured by you) pages  of  information. 
        Information that changes between successive frames, is shown in a 
        different color. Information that has exceeded a preset (by  you) 
        limit  is  shown in an alarm color (default: blinking  red).  The 
        capture-to-disk will turn on when the first packet is copied, and 
        will turn off two minutes after the last.

        If  you  touch the 'Escape' key you will bring up  the  following 
        Menu.

         D Show Space on Disk
         R Reset Packet Counters
         Q Quit to Main Menu
         Z Show Spacecraft data Files

        Type the letter associated with the option to perform it.

        Each of the options are described below.

            8.1 Show Space on Disk

            This  option  allows you to see how much space is left  on  a 
            disk with exiting from the program.

            8.2 Reset Packet Counters

            This  option  resets the packet counters to  zero.  use  this 
            before  a  pass  to see how many packets  of  each  type  are 
            received during the pass.

            8.3 Quit to Main Menu

            This option returns you to the Main menu.

            8.4 Show Spacecraft data Files

            This  option  shows  you  the  data  files  for  the   chosen 
            spacecraft in the default directory path.

        9.0 (Data) Extraction Mode

        In this mode, data is extracted from a playback file into a  file 
        that  can be read into a spreadsheet.  If you answer  the  prompt 
        for the default file with a non-existent filename, WHATS-UP  will 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 14.


        prompt  you  for individual channel numbers.   To  terminate  the 
        sequence  and  begin  the extract mode,  touch  the  'Enter'  key 
        without entering a channel number. 

        Note: Start and stop times are text string matches.

        10.0 Configuration File

        The  contents  of the Configuration file  (WHATS-UP.SYS)  are  as 
        follows:
            Your callsign (e.g. G3ZCZ)
            Default configuration file) (e.g. Dove)
            station latitude (e.g. 35.00)
            station longitude (e.g. 74.00)
            station altitude (e.g. 100)
            default directory path (e.g C:)
            default extracted data file (e.g. whats-up.txt)
            default  file  name  with list  of  telemetry  parameters  to 
                 extract file (e.g. ARRAYS)
            TNC Type (e.g. PK-232)
            PC serial port (e.g. 1)
            PC serial baud rate (e.g. 1200)
            data bits (e.g. 8)
            Stop bits (e.g. 1)
            parity (e.g. 0)
            status (top) window color (e.g. 79)
            Telemetry Page color (e.g. 14)
            outgoing window color (e.g. 14)
            incoming window color (e.g. 30)
            prompt window color (e.g. 15)
            alarm window color (e.g. 15)
            bottom window color (e.g. 79)
            Emphasis color (e.g. 14)
            prompt color (e.g. 14)
            option color (e.g. 78)
            parameter changed color (e.g. 95)
            parameter limit exceeded color (e.g. 14)
            *  Comment line 
            remaining  lines  are  commands sent to the  PK232  when  you 
                 configure the TNC. Note to avoid lock ups FLOW and XFLOW 
                 MUST be OFF.
            HEAD ON
            ECHO OFF
            DAYSTAMP ON
            MONITOR 6
            MSTAMP ON
            FLOW OFF
            XFLOW OFF

        The callsign, TNC Type and geographic parameters are not used  in 
        this version.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 15.


        You  must  configure  WHATS-UP  before  you  try  any  Real  Time 
        activity.

        11.0 Spacecraft Parameter Files

        You  will  need a Different spacecraft parameter  file  for  each 
        spacecraft.   Spacecraft  parameter  files  are  named   by   the 
        spacecraft   and  given  the  extension  '.SYS'.   Examples   are 
        'DOVE.SYS'  and  'Fuji20.SYS'.   These files  determine  how  the 
        individual channels are decoded, and where, in which screen page, 
        and  in which color the decoded data are displayed.  Some of  the 
        items  are  unique  to  WHATS-UP  and  some  to  the   particular 
        spacecraft.

        The contents of the SPACECRAFT.SYS file are as described below.

             11.1 Spacecraft ID.

             This is the call sign of the spacecraft. For example, 

                           Spacecraft      ID

                           DOVE-OSCAR 17  DOVE-1
                           Fuji-OSCAR 12  8J1JAS
                           Fuji-OSCAR 20  8J1JBS

             In the case of the Microsats and Fuji-OSCAR 12/20,  WHATS-UP 
             searches the packet headers to detect the spacecraft by  the 
             ID.

             11.2 Spacecraft Suffix

             This becomes the filetype for the capture-to-disk files. The 
             default suggestions are as shown below.

                           Spacecraft       Suffix

                           AMSAT-OSCAR 13     O13
                           UoSAT-OSCAR 11     U11
                           DOVE-OSCAR 17      D17
                           Fuji-OSCAR 12      F12
                           Fuji-OSCAR 20      F20
                           PACSAT-OSCAR 16    P16
                           WEBER-OSCAR 18     W18
                           LU-OSCAR 19        L19

             11.3 Selected or default display page number

             This  is  the  default display page for  the  Real-time  and 
             Playback modes, when WHATS-UP is first loaded.




        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 16.


             11.4 Number of display pages

             This  is the number of display pages that you have  defined. 
             The maximum number is 16.  This number must be correct as it 
             tells WHATS-UP how many page definition lines to read.

             11.5 Page Definitions

             These are the page definitions, with two items on the  line. 
             The  format  is PAGE_TITLE, Page_Color, as  in  the  example 
             below.

             SPACECRAFT HOUSEKEEPING, 30

             11.6 Telemetry Parameter Configuration

             The   next  set  of  items  are  the   Telemetry   parameter 
             configurations (maximum = 99). You must have at least one of 
             these  lines in the file. If you want a value to show up  in 
             more  than one page (other than the wild card [0]) you  must 
             enter it twice (once per page). Typically each row  contains 
             17 items in the format shown below.

             TLM_Channel, TLM_Segment_ID, TLM_Description,  TLM_Eqn_Type, 
             TLM_Ceof_C,  TLM_Ceof_B,  TLM_Ceof_A,  TLM_Units,  TLM_Page, 
             TLM_Row,   TLM_Col,  TLM_Width,  TLM_Dec,   TLM_Limit_Check, 
             TLM_Limit_Low,TLM_Limit_High.

             Each item is described in the following sections.

                  11.6.1 TLM_Channel

                  This is the channel number of the telemetry data in the 
                  frame.  The  DOVE channel number is  hexadecimal  (e.g. 
                  '0F'), Fuji is decimal.  Each entry must be two digits.

                  A special identifying TLM_Channel is defined in  WHATS-
                  UP. If the value is '99 then the segment identifier and 
                  position  of the segment identifier is defined  in  tow 
                  positions in the line.  This special channel identifies 
                  the type of telemetry frame.

                  11.6.2 TLM_Segment_ID

                  This is the segment identifier. 

                  The Fuji frame contains one real time segment  (Segment 
                  1)  in a frame addressed as 8J1JBS>BEACON.   A  typical 
                  frame is shown below.





        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 17.


                  19-Apr-90  17:14:34  8J1JBS*>BEACON:
                  JAS1b RA 90/04/19 17:13:58
                  609 430 687 676 744 837 845 829 498 681
                  617 001 505 516 526 524 526 523 654 000
                  683 675 686 695 999 643 875 471 099 000
                  110 111 000 000 111 100 001 111 111 000

                  The  segment  identifier is in the seventh  and  eighth 
                  characters  of  the first line of the data.  A  segment 
                  identifier  of  that  position  identifies  the  second 
                  segment.  The segment identifier is the 'RA' located on 
                  the  first line of the data just after the JAS1b  where 
                  the 'R' in 'RA' is the seventh character in the line.  
                  Any  telemetry  frame  addressed  to  BEACON   received 
                  without that segment identifier is assumed by  WHATS-UP 
                  to be Segment 2.

                  DOVE  transmits telemetry in two frames each  addressed 
                  as  DOVE-1>TLM. The Microsat ASCII frame thus  contains 
                  two segments.   Two typical segments of DOVE  telemetry 
                  are shown below.

        DOVE-1>TLM [01/29/90  22:08:46]:
        00:59 01:59 02:86 03:30 04:58 05:58 06:6D 07:45 08:6C 09:66 0A:A1
        0B:D9 0C:E8 0D:D8 0E:01 0F:23 10:CC 11:A8 12:00 13:01 14:A8 15:94
        16:96 17:94 18:95 19:96 1A:93 1B:90 1C:9A 1D:98 1E:23 1F:5E 20:BC

        DOVE-1>TLM [01/29/90  22:08:47]:
        21:98 22:7B 23:24 24:21 25:2E 26:00 27:00 28:00 29:00 2A:00 2B:00
        2C:00 2D:29 2E:00 2F:9B 30:C8 31:9C 32:11 33:DA 34:C0 35:95 36:A4
        37:A4 38:B2 39:96 3A:00

                  The  default segment identifier used by WHATS-UP is  in 
                  the  first and second characters of the first  line  of 
                  the  data. A segment identifier of '00' identifies  the 
                  first  segment,  and  anything else  in  that  position 
                  identifies the second segment.

                  11.6.3 TLM_Description

                  This  item  is the text string or  description  of  the 
                  telemetry channel that will be displayed on the  screen 
                  page. (e.g. '+Z Array Temp.')

                  11.6.4 TLM_Eqn_Type

                  This item tells WHATS-UP the type of equation to use to 
                  decode the telemetry.  






        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 18.


                  A type 1 equation is a quadratic of the form  
                           Y = A*N^2 + B*N + C,
                  where: N = raw telemetry data value
                         A, B, C = Equation Coefficients
                         Y = Result (In Specified Units)

                  This is the equation used by AMSAT-NA in the Microsats.

                  Fuji uses two other equations. They are in the  formats 
                  of

                  Y = D*(N+E), and Y = F*(G-N).  If you know some algebra 
                  you can convert both of Fuji's equations to the  Format 
                  used  by AMSAT, but since a computer is  involved,  why 
                  not let it do the job.  You do however have to  convert 
                  an equation of the form Y=(N+a)/b.

                  A  type  2 equation in WHATS-UP has the format  in  the 
                  form of
                              Y = B*(N-A) , C=0
                                             where B, A are coefficients
                                                   Y,   N   are   decimal 
                  values

                  A  type  3 equation in WHATS-UP has the format  in  the 
                  form of
                              Y = B*(A-N) , C=0
                                             where B, A are coefficients
                                             Y, N  are decimal values

                  If the TLM_Channel is '99', then this item contains the 
                  location of the segment identifier in the first line of 
                  the telemetry data.

                  In the case of Fuji-OSCAR 12/20, the segment identifier 
                  is the 'RA' located on the first line of the data  just 
                  after  the  JAS1b  where the 'R' in  'RA'  is  the  7th 
                  character  in  the first line of the  data.   Thus  the 
                  position of the segment identifier in this case is 7.

                  In the case of the AMSAT Microsat ASCII telemetry,  the 
                  segment identifier for the first segment is '00" in the 
                  seventh character of the first line of the data.

                  Note that the segment identifier and position are  user 
                  definable, and appear in the spacecraft.sys file.

                  11.6.5 TLM_Ceof_C
                  
                  This item is the equation Coefficient C.




        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 19.


                  11.6.6 TLM_Ceof_B

                  This item is the equation Coefficient B.

                  11.6.7 TLM_Ceof_A

                  This item is the equation Coefficient A.

                  11.6.8 TLM_Units

                  This  item is the Units text string (e.g. '.C') in  the 
                  screen  display.   However if the Tlm_Channel  is  '99' 
                  then this item is the segment identifier string.

                  11.6.9 TLM_Page

                  This  item is the Display page number. A 0 is  a  'wild 
                  card' which will be displayed on every page.

                  11.6.10 TLM_Row

                  This item is the Display page row.  It identifies which 
                  row in the screen the data element will be displayed.

                  11.6.11 TLM_Col

                  This  item  is the Display page column.  It  identifies 
                  which  column  in  the screen the  data  item  will  be 
                  displayed.

                  11.6.12 TLM_Width

                  This  item is the Display width for Engineering  Units. 
                  It tells WHATS-UP how many characters wide the  display 
                  is  to be.  You can set it to any value you  want.  For 
                  example,  you  can  display  a  voltage  as  '1.3'   or 
                  '1.28567'.   Before  you widen the  display  too  much, 
                  remember the sampling accuracy of the analog-to-digital 
                  converter in the spacecraft.

                  11.6.13 TLM_Dec

                  This  item  defines  the number  of  digits  after  the 
                  decimal point in the display.

                  11.6.14 TLM_Limit_Check

                  This  item tells WHATS-UP to perform limit checking  on 
                  the  telemetry channel. It may have several  values  as 
                  described below.




        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 20.


                  0 = do nothing, 
                  1 = check below low limit,
                  2= check above high limit, 
                  3 = check for [below low limit] or [above high limit]).

                  11.6.15 TLM_Limit_Low

                  This item is the Low limit value (e.g. -4.00).

                  11.6.17 TLM_Limit_High

                  This item is the  High limit value (e.g. +10.6).

             A  line with an '*' as the first character  terminates  this 
             section.

             11.7 Packet/Link Parameters

             The  next  set  of  items  are  the  Packet/Link  Parameters 
             configurations  (maximum =*** ). You must have at least  one 
             of  these lines in the file. If you want a value to show  up 
             in  more  than one page (other than the wild card  [0])  you 
             must  enter  it twice (once per page).  Typically  each  row 
             contains 10 items in the format shown below.

             Packet_title,   Packet_Type,   Packet_Lines,    Packet_Page, 
             Packet_Color,  Packet_Row, Packet_Col, Link_Page,  Link_Row, 
             Link_Col.

             Each item is described in the following sections.

                  11.7.1 Packet_title

                  This  item is the name of UNP address  (e.g.  TLM,WASH, 
                  BCXRT).

                  11.7.2 Packet_Type

                  This  item  is used by WHATS-UP to define the  type  of 
                  packet.  The following assignments may be used.

                  1    AMSAT  Microsat with the format CC:DD where CC  is 
                       the   hexadecimal  channel  number  and   DD   the 
                       hexadecimal data.

                  3    Fuji format of decimal data in which the line  and 
                       the  position  on the line identify  the  channel.  
                       WHATS-UP allows for up to 60 channels.

                  11.7.3 Packet_Lines

                  This item is the number of lines of text in the packet. 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 21.


                       for  example, the AMSAT TLM packets contain  three 
                       lines, the WASH packets contain only one.

                  11.7.4 Packet_Page

                  This item  is  the page that the raw  contents  of  the 
                       packet will be displayed on. A '0' is a wild  card 
                       which will make WHATS-UP display it on every page.  
                       By careful use of this item, you can display  both 
                       raw and decoded packet data on the same page.

                  11.7.5 Packet_Color

                  This item is the color that the raw packet data will be 
                       displayed in.

                  11.7.6 Packet_Row
                  This item is the row position that the raw packet  will 
                       be displayed in, on the selected page.

                  11.7.7 Packet_Col

                  This item  is the column position that the  raw  packet 
                       will be displayed in, on the selected page.

                  11.7.8 Link_Page

                  This item is the Display page for the cumulative  count 
                       of the packet type. The wild card '0' applies.

                  11.7.9 Link_Row

                  This item  is the row position that the  packet  header 
                       will be displayed in, on the selected page.

                  11.7.10 Link_Col

                  This item is the column position that the packet header 
                       will be displayed in, on the selected page.

             These lines also terminate with an '*' character.

        12.0 Telemetry Channel Extraction File

        The  contents of this file are the defaults for  extracting  data 
        from the playback file.  A typical set are shown below.  WHATS-UP 
        does  a  string  match,  and looks for  the  first  time  that  a 
        particular string occurs. You may thus use the contents of a time 
        packet, or the time mark in a header.

             ZCZC (default start time string) {start of file}
             NNNN (default stop time string) {end of file}


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP.DOC Release 0.55 Page 22.


             26 (list of telemetry channels to be extracted)
             27 (This one contains the solar array currents)
             28
             29
             2A
             2B

        13.0 Extracted Telemetry Data File

        This an ASCII string, comma delimited file which can be  imported 
        into your spreadsheet.











































        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 23


        Latest Microsat Telemetry (TLM) Equations 

        By  Jan  King W3GEY  Reprinted from the AMSAT Journal  Volume  13 
        Number 1, March 1990.

        Spacecraft:  PACSAT-1:                            Rev: 1
                                                          Date: 1/7/90  

        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 

                                      N = Telemetry Count (00 - FF) 
                            
                                      A, B, C = Equation Coefficients

                                      Y = Result (In Specified Units)


        HEX   Description:        C:           B:           A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +9.202       -0.08990     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +9.179       -0.09277     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +9.837       -0.08838     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +9.779       -0.09144     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.817      -0.09911     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000250    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.0500      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +101.05      -0.6051      0.000       Deg. C
        15    +X (RX) temp:  +101.05      -0.6051      0.000       Deg. C
        16    Bat 1 V:       +1.8225      -0.0038046   0.000       Volts
        17    Bat 2 V:       +1.9418      -0.0046890   0.000       Volts
        18    Bat 3 V:       +1.8699      -0.0041641   0.000       Volts
        19    Bat 4 V:       +1.7403      -0.0032880   0.000       Volts
        1A    Bat 5 V:       +1.8792      -0.0042492   0.000       Volts
        1B    Bat 6 V:       +2.0499      -0.0054532   0.000       Volts
        1C    Bat 7 V:       +1.9062      -0.0045331   0.000       Volts
        1D    Bat 8 V:       +1.7536      -0.0033192   0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 24


        1E    Array V:       +8.055       +0.06790     0.000       Volts
        1F    +5V Bus:       +2.035       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.464       +0.0184      0.000       Volts
        21    +10V Bus:      +7.650       +0.0250      0.000       Volts
        22    BCR Set Point: -6.1130      +1.1270      0.000       Counts
        23    BCR Load Cur:  -0.0477      +0.00767     0.000       Amps
        24    +8.5V Bus Cur: -0.00179     +0.000894    0.000       Amps
        25    +5V Bus Cur:   -0.00104     +0.00406     0.000       Amps
        26    -X Array Cur:  -0.00995     +0.00243     0.000       Amps
        27    +X Array Cur:  -0.02370     +0.00254     0.000       Amps
        28    -Y Array Cur:  -0.02220     +0.00273     0.000       Amps
        29    +Y Array Cur:  -0.01810     +0.00259     0.000       Amps
        2A    -Z Array Cur:  -0.02230     +0.00221     0.000       Amps
        2B    +Z Array Cur:  -0.02000     +0.00232     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: -0.02345     +0.00355     0.000       Amps
        2E    BCR Output Cur:+0.00869     +0.00303     0.000       Amps
        2F    Bat 1 Temp:    +101.05      -0.6051      0.000       Deg. C
        30    Bat 2 Temp:    +101.05      -0.6051      0.000       Deg. C
        31    Baseplt Temp:  +101.05      -0.6051      0.000       Deg. C
        32    PSK TX RF Out: -0.0291      +0.00361     +0.0000869  Watts
        33    RC PSK TX Out: +0.0055      +0.00172     +0.0001180  Watts
        34    PSK TX HPA Temp+101.05      -0.6051      0.000       Deg. C
        35    +Y Array Temp: +101.05      -0.6051      0.000       Deg. C
        36    RC PSK HPA Temp+101.05      -0.6051      0.000       Deg. C
        37    RC PSK BP Temp:+101.05      -0.6051      0.000       Deg. C
        38    +Z Array Temp: +101.05      -0.6051      0.000       Deg. C 
        39    S band TX Out: -0.0088      +0.00435     0.000       Watts
        3A    S band HPA Temp 0.000       +1.000       0.000       Counts

        ADC Equations: V = 0.01028 N - 0.02055
                       N = 97.31 V +2.000






















        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 25


        Spacecraft:  DOVE-1:                              Rev: 1
                                                          Date: 1/7/90  


        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 

                                      N = Telemetry Count (00 - FF) 
                            
                                      A, B, C = Equation Coefficients

                                      Y = Result (In Specified Units)


        HEX   Description:        C:           B:           A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx E/F Audio(W)+0.000       +0.0246      0.000       V(p-p)
         1    Rx E/F Audio(N)+0.000       +0.0246      0.000       V(p-p)
         2    Mixer Bias V:  +0.000       +0.0102      0.000       Volts
         3    Osc. Bisd V:   +0.000       +0.0102      0.000       Volts 
         4    Rx A Audio (W):+0.000       +0.0246      0.000       V(p-p)
         5    Rx A Audio (N):+0.000       +0.0246      0.000       V(p-p)
         6    Rx A DISC:     +10.427      -0.09274     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +9.6234      -0.09911     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000100    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.05075     0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +101.05      -0.6051      0.000       Deg. C
        15    +X (RX) temp:  +101.05      -0.6051      0.000       Deg. C
        16    Bat 1 V:       +1.7932      -0.0034084   0.000       Volts
        17    Bat 2 V:       +1.7978      -0.0035316   0.000       Volts
        18    Bat 3 V:       +1.8046      -0.0035723   0.000       Volts
        19    Bat 4 V:       +1.7782      -0.0034590   0.000       Volts
        1A    Bat 5 V:       +1.8410      -0.0038355   0.000       Volts
        1B    Bat 6 V:       +1.8381      -0.0038450   0.000       Volts
        1C    Bat 7 V:       +1.8568      -0.0037757   0.000       Volts
        1D    Bat 8 V:       +1.7868      -0.0034068   0.000       Volts
        1E    Array V:       +7.205       +0.07200     0.000       Volts
        1F    +5V Bus:       +1.932       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.265       +0.0173      0.000       Volts
        21    +10V Bus:      +7.469       +0.021765    0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 26


        22    BCR Set Point: -8.762       +1.1590      0.000       Counts
        23    BCR Load Cur:  -0.0871      +0.00698     0.000       Amps
        24    +8.5V Bus Cur: -0.00920     +0.001899    0.000       Amps
        25    +5V Bus Cur:   +0.00502     +0.00431     0.000       Amps
        26    -X Array Cur:  -0.01075     +0.00215     0.000       Amps
        27    +X Array Cur:  -0.01349     +0.00270     0.000       Amps
        28    -Y Array Cur:  -0.01196     +0.00239     0.000       Amps
        29    +Y Array Cur:  -0.01141     +0.00228     0.000       Amps
        2A    -Z Array Cur:  -0.01653     +0.00245     0.000       Amps
        2B    +Z Array Cur:  -0.01137     +0.00228     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: +0.06122     +0.00317     0.000       Amps
        2E    BCR Output Cur:-0.01724     +0.00345     0.000       Amps
        2F    Bat 1 Temp:    +101.05      -0.6051      0.000       Deg. C
        30    Bat 2 Temp:    +101.05      -0.6051      0.000       Deg. C
        31    Baseplt Temp:  +101.05      -0.6051      0.000       Deg. C
        32    FM TX#1 RF OUT:+0.0256      -0.000884    +0.0000836  Watts
        33    FM TX#2 RF OUT:-0.0027      +0.001257    +0.0000730  Watts
        34    PSK TX HPA Temp+101.05      -0.6051      0.000       Deg. C
        35    +Y Array Temp: +101.05      -0.6051      0.000       Deg. C
        36    RC PSK HPA Temp+101.05      -0.6051      0.000       Deg. C
        37    RC PSK BP Temp:+101.05      -0.6051      0.000       Deg. C
        38    +Z Array Temp: +101.05      -0.6051      0.000       Deg. C 
        39    S band TX Out: -0.0451      +0.00403     0.000       Watts
        3A    S band HPA Temp+101.05      -0.6051      0.000       Deg. C


        ADC Equations: V = 0.01028 N - 0.05138
                       N = 97.31 V +5.000

























        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 27


        Spacecraft:  WEBER-1:                            Rev: 1
                                                         Date: 1/7/90  

        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 

                                      N = Telemetry Count (00 - FF) 
                            
                                      A, B, C = Equation Coefficients

                                      Y = Result (In Specified Units)


        HEX   Description:        C:           B:           A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +11.087      -0.08949     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +10.322      -0.09448     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +10.348      -0.09004     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +11.387      -0.09535     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.746      -0.09348     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.03523     0.000       Volts
         B    +5V Rx Current:+0.000       +0.000234    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0133      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0524      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000033    0.000       Amps
        10    +10V Bus:      +0.000       +0.0767      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +100.01      -0.5980      0.000       Deg. C
        15    +X (RX) Temp:  +100.01      -0.5980      0.000       Deg. C
        16    Bat 1 V:       +1.8292      -0.0037196   0.000       Volts
        17    Bat 2 V:       +1.8202      -0.0036943   0.000       Volts
        18    Bat 3 V:       +1.8050      -0.0036721   0.000       Volts
        19    Bat 4 V:       +1.8576      -0.0038979   0.000       Volts
        1A    Bat 5 V:       +1.8095      -0.0037439   0.000       Volts
        1B    Bat 6 V:       +1.8979      -0.0041754   0.000       Volts
        1C    Bat 7 V:       +1.8246      -0.0038126   0.000       Volts
        1D    Bat 8 V:       +1.7486      -0.0030475   0.000       Volts
        1E    Array V:       +7.800       +0.06790     0.000       Volts
        1F    +5V Bus:       +1.838       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.793       +0.0184      0.000       Volts
        21    +10V Bus:      +7.650       +0.0250      0.000       Volts
        22    BCR Set Point: -6.1963      +1.1277      0.000       Counts


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 28


        23    BCR Load Cur:  -0.0405      +0.00620     0.000       Amps
        24    +8.5V Bus Cur: +0.00384     +0.000830    0.000       Amps
        25    +5V Bus Cur:   -0.00763     +0.00394     0.000       Amps
        26    -X Array Cur:  -0.00140     +0.00210     0.000       Amps
        27    +X Array Cur:  +0.00946     +0.00226     0.000       Amps
        28    -Y Array Cur:  -0.01018     +0.00224     0.000       Amps
        29    +Y Array Cur:  -0.01168     +0.00239     0.000       Amps
        2A    -Z Array Cur:  -0.01516     +0.00237     0.000       Amps
        2B    +Z Array Cur:  -0.02111     +0.00239     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: -0.02189     +0.00332     0.000       Amps
        2E    BCR Output Cur:-0.03019     +0.00327     0.000       Amps
        2F    Bat 1 Temp:    +100.01      -0.5980      0.000       Deg. C
        30    Bat 2 Temp:    +100.01      -0.5980      0.000       Deg. C
        31    Baseplate Temp:+100.01      -0.5980      0.000       Deg. C
        32    PSK TX RF Out: +0.2104      -0.01203     +0.0001786  Watts
        33    RC PSK TX Out: +0.0340      -0.00969     +0.0002198  Watts
        34    PSK TX HPA Temp+100.01      -0.5980      0.000       Deg. C
        35    +Y Array Temp: +100.01      -0.5980      0.000       Deg. C
        36    RC PSK HPA Temp+100.01      -0.5980      0.000       Deg. C
        37    RC PSK BP Temp:+100.01      -0.5980      0.000       Deg. C
        38    +Z Array Temp: +0.0000      +1.0000      0.000       Counts 


        ADC Equations: V = 0.01016 N - 0.05080
                       N = 98.43 V +5.000




























        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 29


        Spacecraft:  LUSAT-1:                             Rev: 1
                                                          Date: 1/7/90  


        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 

                                      N = Telemetry Count (00 - FF) 
                            
                                      A, B, C = Equation Coefficients

                                      Y = Result (In Specified Units)


        HEX   Description:        C:           B:           A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +9.802       -0.08779     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +8.429       -0.09102     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +9.291       -0.08317     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +9.752       -0.08310     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.110      -0.08610     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000250    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.0508      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +93.24       -0.5609      0.000       Deg. C
        15    +X (RX) Temp:  +93.24       -0.5609      0.000       Deg. C
        16    Bat 1 V:       +1.7343      -0.0029740   0.000       Volts
        17    Bat 2 V:       +1.7512      -0.0032113   0.000       Volts
        18    Bat 3 V:       +1.7790      -0.0034038   0.000       Volts
        19    Bat 4 V:       +1.7286      -0.0030036   0.000       Volts
        1A    Bat 5 V:       +1.8114      -0.0036960   0.000       Volts
        1B    Bat 6 V:       +1.7547      -0.0032712   0.000       Volts
        1C    Bat 7 V:       +1.7151      -0.0030739   0.000       Volts
        1D    Bat 8 V:       +1.6846      -0.0028534   0.000       Volts
        1E    Array V:       +8.100       +0.06790     0.000       Volts
        1F    +5V Bus:       +2.035       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.614       +0.0184      0.000       Volts
        21    +10V Bus:      +7.650       +0.0250      0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX A AMSAT Microsat ASCII Telemetry  Page 30


        22    BCR Set Point: +3.7928      +1.0616      0.000       Counts
        23    BCR Load Cur:  -0.0244      +0.00628     0.000       Amps
        24    +8.5V Bus Cur: +0.00412     +0.000773    0.000       Amps
        25    +5V Bus Cur:   +0.02461     +0.00438     0.000       Amps
        26    +X Array Cur:  -0.01614     +0.00232     0.000       Amps
        27    -X Array Cur:  -0.01158     +0.00238     0.000       Amps
        28    -Y Array Cur:  +0.00278     +0.00206     0.000       Amps
        29    +Y Array Cur:  +0.00136     +0.00218     0.000       Amps
        2A    -Z Array Cur:  +0.00370     +0.00209     0.000       Amps
        2B    +Z Array Cur:  -0.00793     +0.00216     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: -0.00901     +0.00283     0.000       Amps
        2E    BCR Output Cur:+0.00663     +0.00344     0.000       Amps
        2F    Bat 1 Temp:    +93.24       -0.5609      0.000       Deg. C
        30    Bat 2 Temp:    +93.24       -0.5609      0.000       Deg. C
        31    Baseplt Temp:  +93.24       -0.5609      0.000       Deg. C
        32    PSK TX RF Out: +0.1059      +0.00095     +0.0000834  Watts
        33    RC PSK TX Out: +0.0178      +0.00135     +0.0000833  Watts
        34    PSK TX HPA Temp+93.24       -0.5609      0.000       Deg. C
        35    +Y Array Temp: +93.24       -0.5609      0.000       Deg. C
        36    RC PSK HPA Temp+93.24       -0.5609      0.000       Deg. C
        37    RC PSK BP Temp:+93.24       -0.5609      0.000       Deg. C
        38    +Z Array Temp: +93.24       -0.5609      0.000       Deg. C 
        39    LU Bcn Temp A: +93.24       -0.5609      0.000    *  Deg. C
        3A    LU Bcn Temp D: +93.24       -0.5609      0.000    ** Deg. C
        3B    Coax Rly Stat: +0.000       +1.0000      0.000       Counts
        3C    Coax Rly Stat: +0.000       +1.0000      0.000       Counts  

        ADC Equations: V = 0.00953 N 
                       N = 104.94 V


        * Note 1:  Thermistor located near box center adjacent to LU
                   thermistor channel no. 5.  

        **  Note  2:   Thermistor  located  near -X face of  box  on  the 
                       experiment baseplate.

















        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 31


        Introduction
         
        On  February  7 1990, the National Space  Development  Agency  of 
        Japan (NASDA) put the Marine Observation Satellite (MOS) 1b  into 
        orbit.   The launch vehicle also carried two secondary  payloads, 
        Fuji-Oscar  20 and the Deployable Boom and Umbrella Test  (DEBUT) 
        spacecraft which is similar in shape and weight to Fuji-OSCAR 20. 
         
        MOS-1b  was  placed into a circular polar orbit, then  DEBUT  and 
        Fuji-OSCAR  20 separated from the launch vehicle at  0233,  above 
        Santiago, Chile. First signals from the spacecraft were  received 
        in Tokyo around 0309 UTC. 

        Fuji-OSCAR  20 is similar in construction to Fuji-OSCAR  12.   In 
        fact, it was originally constructed as a backup to Fuji-OSCAR  12 
        and designated as JAS-1B. It has since been modified and improved 
        as  a  result of the lessons learned during the flight  of  Fuji-
        OSCAR  12.  Fuji-OSCAR 12 was known as Fuji-1 in Japan,  so  this 
        spacecraft  is known by the Japanese as Fuji-2 and as  Fuji-OSCAR 
        12 (or FO-12) by the rest of the world.  This article,  describes 
        the spacecraft and its mission.

        The Orbit

        Fuji-OSCAR  20's  planned service life is 5 years.  It  is  in  a 
        sunsynchronous elliptical polar orbit, having a perigee of  about 
        900  km  and  an apogee of about 1740 at  an  inclination  of  99 
        degrees.  The  Period of the orbit is about  105  minutes.   This 
        orbit  is  optimal  for MOS-1b which is  to  study  oceanographic 
        resources and observe agricultural environmental conditions.   In 
        this  orbit, the spacecraft passes over a given line of  latitude 
        at  approximately  the same time each day.  In  this  orbit,  the 
        spacecraft is shielded from the sun by the earth for about 33% of 
        the  time.  This  eclipse means that the  solar  cells  can  only 
        provide power for about 70 minutes in each orbit and that the on-
        board  nickel  cadmium  storage  batteries  have  to  power   the 
        spacecraft for the remaining 35 minutes.

        The Spacecraft

        Fuji-OSCAR  20  weighs about 50 kg. and is  a  polyhedron  shaped 
        spacecraft  440mm  in  diameter and 470mm in  height  covered  by 
        approximately  1500  gallium arsenide solar cells  which  provide 
        about  11  Watts of power to keep the 11  series-connected  NiCad 
        cells  (rectangular) with a capacity of 6 AH charged.  There  are 
        26  sides to the polyhedron which almost makes it  spherical  for 
        all  practical  purposes other than sticking solar cells  to  it. 
        Fuji-OSCAR  12  was  the same shape but only  carried  about  600 
        cells.  This larger number of cells means that Fuji-OSCAR 20  has 
        a positive power budget and should not need to be switched off to 
        recharge. 



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 32



        The  Power  supply converts the raw bus voltage of +11 to  +18  V 
        (+14 V average) to the three regulated voltages (+10 V, +5 V,  -5 
        V)  used by the rest of the satellite with an efficiency  greater 
        than 70%.

        The  attitude of the satellite is maintained by using the  torque 
        generated  by the interaction of two permanent magnets  with  the 
        earth's  magnetic field. This is a fairly conventional  technique 
        used  in the OSCAR series. Temperature stability is  achieved  by 
        using thermal insulation.

        The Payload.

        Fuji-OSCAR 20 carries two Mode J transponders, both of which  may 
        be operational at the same time.  One transponder is analog (Mode 
        JA), the other is digital (Mode JD).

        The  frequencies and capabilities of the analog  transponder  are 
        similar  to those of Fuji-OSCAR 12.  It consists of  an  inverted 
        hetrodyne  linear  translator  with  a  passband  100  kHz  wide, 
        operating  with a mode J Uplink passband of 145.9 to 146.00  MHz, 
        and a corresponding Downlink Passband of 435.9 to 435.8 MHz.  The 
        spacecraft  has a Transmitter Output of approximately 1 watt.   A 
        ground station needs an Uplink EIRP of about 100 W to communicate 
        through  the  transponder.  The JA telemetry  beacon  is  on  the 
        nominal frequency of 435.795 MHz with a power output of about 100 
        mW and can use CW or PSK modulation.  Fuji-OSCAR 20 is using  the 
        callsign  8J1JBS and the beacons transmit telemetry in  the  same 
        manner as Fuji-OSCAR 12.   

        The   digital  transponder  provides   store-and-forward   packet 
        communication  using  the AX.25 link level protocol,  version  2.  
        Stations  who  used Fuji-OSCAR 12 are able to use  Fuji-OSCAR  20 
        without making any modifications to their equipment.  The  uplink 
        requires Bi-phased Manchester code on an FM signal, at a bit rate 
        of  1200 bps. There are 4 Uplink Frequencies: 145.85 MHz,  145.87 
        MHz, 145.89 MHz, 145.91 MHz.  The necessary ground station Uplink 
        EIRP is also about 100 W.  The transponder has an output power of 
        about 1 W on a downlink frequency of 435.91 MHz and uses NRZI PSK 
        at  1200 bps.  The same PSK modem used to copy Fuji-OSCAR  12  or 
        the  Microsats  is needed to copy Fuji-OSCAR  20.   The  downlink 
        channel also carries packet telemetry.

        The 144 MHz receiving antenna is a ring turnstile mounted at  the 
        bottom of the side panels. The 435 MHz transmitting antenna is  a 
        turnstile antenna mounted at the top of satellite.  Both antennas 
        are  circularly  polarized.   Ground tests have  shown  that  the 
        transmitting  antenna is more omnidirectional than that of  Fuji-
        OSCAR  12, however due to the structure of the  hybrid  circuitry 
        which  allow  both transponders to share the  same  antenna,  the 
        sense  of the circular polarization on the downlink is  different 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 33


        for  each  mode.   As  the  apparent  polarization  is  different 
        depending  on  the  geometry  between  the  spacecraft  and   the 
        groundstation, you will probably have to change between left hand 
        and   right  hand  circular  polarization  during  a  pass.   The 
        spacecraft  is designed so that you can usually keep  the  uplink 
        and downlink polarization the same.

        Mode  JA has provided strong trans-Atlantic signals and  many  CW 
        and  SSB QSOs. Mode-JD was switched on for the first time  during 
        Orbit #95.  To Digipeat via Fuji-OSCAR 20 you don't need to use a 
        digipeater  call.  With the present version of the software,  all 
        AX.25  frames  with a valid CRC heard by the spacecraft  will  be 
        digipeated.

        The first claimed QSO on mode JD is by DB0OS when he connected to 
        himself  and  an extract from the information he copied  at  that 
        time is shown in Table 2.

        ----------------------------------------------------------------
        Table  2  First European MODE-JD Self-Contact via  FUJI  OSCAR-20 
        made!

        Telemetry and Self-Connect:
        --------------------------

        fm 8J1JBS to BEACON ctl UI^ pid F0
        JAS1b RA 90/02/14 11:23:30
        551 427 695 699 741 837 841 821 474 638
        617 001 507 517 531 527 533 532 654 000
        681 665 661 686 999 643 874 438 046 000
        110 111 000 000 100 000 001 111 111 000

        fm DB2OS to DB2OS ctl RR1-

        fm DB2OS to DB2OS ctl I11^ pid F0
        DB2OS de DB2OS (14.2.1990 um 11:15 utc)

        fm DB2OS to DB2OS ctl I12^ pid F0
        1st QSO via FUJI OSCAR-20

        fm DB2OS to DB2OS ctl RR3v

        fm 8J1JBS to BEACON ctl UI^ pid F0
        JAS1b M0 90/02/14 11:26:00
        Repeater is at your service from90/02/12 03:05:00
        The JD Transmitter is available in all orbits
        during JD mode.

        ----------------------------------------------------

        The  spacecraft also carries a BBS which is accessed by means  of 
        the same commands used to access a terrestrial WA7MBL/W0RLI/AA4RE 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 34


        type  of BBS.  You access the BBS by connecting to 8J1JBS on  any 
        of the four uplink channels. When you do connect to it, make sure 
        that you disconnect before LOS because Fuji-OSCAR 20 only  allows 
        16  simultaneous connections. Stations that hang in  there  after 
        the  satellite  drops below their local horizon block  access  by 
        other  stations  and have been christened  'Zombies'.    The  BBS 
        program  is  a modified version of the BBS  program  written  for 
        Fuji-OSCAR 12 and allows the use of 4 banks (1Mbyte) of memory. A 
        typical list of messages copied by KI6QE is shown in figure 2.

        ---------------------------------------------------
        Figure 2 Typical Message Listing from the BBS (copied by KI6QE)


        Fuji-OSCAR 20/JAS1b Mailbox ver. 2.00  
        commands [B/F/H/M/R/U/W]
        Use H command for Help
        JAS>JAS>NO.  DATE   UTC    FROM    TO      SUBJECT
        0086 04/13 05:15  WB6GFJ  W6SHP   Welcome
        0085 04/13 05:14  WB6LLO  KI6QE   SOFTWARE
        0084 04/13 05:14  WB6GFJ  W9FMW   Our Chat
        0082 04/13 03:38  W9FMW   WA4EJR  MESSAGE ON CIS
        0080 04/13 03:36  KG6EX   N1GCR   From Ashley
        0078 04/13 03:32  KG6EX   KD8SI   From Ashley
        0077 04/13 03:31  KG6EX   N8AM    From Ashley
        0076 04/13 03:30  KG6EX   DD4YR   From Ashley
        0075 04/13 03:27  KG6EX   DL1CR   From Ashley
        0074 04/13 03:25  KG6EX   G3RUH   From Ashley
        ---------------------------------------------------------

        The Telemetry

        The  spacecraft telemetry is transmitted either as CW or as  PSK.  
        The  CW  telemetry monitors 12 analog data points and  33  status 
        points,  the PSK telemetry monitors 29 analog data points and  33 
        status  points.  A typical set of PSK telemetry packets  captured 
        by  KI6QE is shown in figure 3. The telemetry decoding  equations 
        are  shown in Table 3.  As you can see the format of the data  in 
        the packet and the type of equations used are different to  those 
        used on the Microsats.

        --------------------------------------------------------------
        Figure 3 Fuji-OSCAR 20 PSK telemetry (as copied by KI6QE)
         
        03-Apr-90  17:40:32  8J1JBS*>BEACON:
        JAS1b RA 90/04/03 17:45:18
        554 433 700 686 757 837 841 823 398 666
        617 001 503 516 526 523 526 523 654 000
        683 675 685 684 999 643 875 316 002 000
        110 111 000 000 100 000 001 011 111 000
        03-Apr-90  17:40:34  8J1JBS*>BEACON:
        JAS1b RA 90/04/03 17:45:20


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 35


        566 427 699 705 746 837 841 824 541 659
        617 001 503 516 526 523 526 523 654 000
        683 675 686 683 999 642 874 316 002 000
        110 111 000 000 100 000 001 011 111 000

        The Telemetry Formats of JAS-1b/Fuji-OSCAR 20 
         
        Telemetry data from FO-20 is transmitted on both the mode JA  and 
        JD beacons. Mode JA sends data by Morse code on the beacon signal 
        of  435.795  MHz, repeating one frame every one minute.  Mode  JD 
        sends a telemetry packet every 2 seconds on the digital  downlink 
        channel  of  435.91  MHz when the telemetry  mode  is  operating, 
        otherwise, one frame is downlinked every one minute. This article 
        contains  the information you need to decode the telemetry.   The 
        spacecraft  can downlink up to 30 items of data and 31  items  of 
        status in the telemetry.  The Mode JA beacon however only carries 
        12 data elements and most of status bytes. 
         
        Mode JA Telemetry Data 
         
        The  Mode  JA beacon transmits the telemetry data in  the  format  
        shown below. These data are sent by Morse code with a "HI HI"  at 
        the  beginning  of  each  frame,  with  a  speed  of  about   100 
        characters every minute,  and always in this format repeatedly.  

         HI  HI  1A  1B  1C  1D 
                 2A  2B  2C  2D 
                 3A  3B  3C  3D 
                 4A  4B  4C  4D 
                 5A  5B  5C  5D 
         
        How to Decode Mode JA telemetry 
         
        The  number  identifies the group, the letters A  through  D  are 
        decimal values expressed in two digits. Let this two-digit be  N, 
        for  each item, true value or engineering  value is  obtained  by 
        decoding  N as shown below.  For example, a value of 123  for  1A 
        means   group 1 and 23 is the measured value of the  solar  array  
        current.   Groups  4 and 5 contain status information  about  the 
        bird,   where  A,  B,  C  and  D  represent    octal    two-digit 
        combinations of 00 through 37. This corresponds to a  combination 
        of five binary  digits. Each bit shows status of each  designated 
        item  in the order from MSB (Most Significant Bit) to LSB  (Least 
        Significant Bit). 










        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 36


        Mode JA Telemetry Conversion Equations 
         
        ========================================================= 
        CH  DESCRIPTION                       CALIBRATION 
        ========================================================= 
        1A  total solar array current          19x(N+0.4)   mA 
        1B  battery charge/discharge current  -38x(N-50)    mA 
        1C  battery voltage                   (N+4)x0.22    V 
        1D  center tap voltage of battery     (N+4)x0.1     V 
        2A  bus voltage                       (N+4)x0.2     V 
        2B  +5 V regulator voltage            (N+4)x0.062   V 
        2C  JTA output power                  2.0x(N+4)^1.618mW 
        2D  calibration voltage               (N+4)/50      V 
        3A  battery temperature               1.4x(67-N)  deg. C 
        3B  baseplate temperature #1          1.4x(67-N)  deg. C 
        3C  baseplate temperature #2          1.4x(67-N)  deg. C 
        3D  baseplate temperature #3          1.4x(67-N)  deg. C 


        The  status  byte conversions are  shown  below.  This method  is 
        used because all items whose status is represented in this manner 
        only  have  two possible situations, either ON or OFF, or  binary 
        values  0 or 1. For example, if the first item of status 4A  were 
        423,   the 4 identifies group 4, and the 23 should be thought  of 
        as its equivalent binary  code (10011).  This shows the status in 
        the  order of MSB to LSB, or bit 4 to bit 0. Using  the  decoding 
        data 423 can be decoded as follows.

        1: Beacon is PSK, 
        0: Engineering data #2 is blank, 
        0: Engineering  data  #1 is blank, 
        1: JTD power is ON, 
        1: JTA power is ON.  

        ------------------------------------------------------ 
        Mode JA System Status Bytes
         
        CH BIT  DESCRIPTION     STATE  
                                1     0 
        ========================================================= 
        4A  0   JTA power       ON    OFF 
        4A  1   JTD power       ON    OFF 
        4A  2   Eng. data #1    ---   --- 
        4A  3   Eng. data #3    ---   --- 
        4A  4   Beacon          PSK   CW 
         
        4B  0   UVC             ON    OFF 
        4B  1   UVC level       1     2 
        4B  2   Battery         tric  full 
        4B  3   Battery logic   tric  full 
        4B  4   Main relay      ON    OFF 
         


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 37


        4C  0   PCU             bit 1 (LSB) 
        4C  1   PCU             bit 2 (LSB) 
        4C  2   PCU             manual  auto 
        4C  3   Eng. data #3    ---   --- 
        4C  4   Eng. data #4    ---   --- 
         
        4D  0   Memory bank #0  ON    OFF 
        4D  1   Memory bank #1  ON    OFF 
        4D  2   Memory bank #2  ON    OFF 
        4D  3   Memory bank #3  ON    OFF 
        4D  4   Computer power  ON    OFF 
         
        5A  0   Memory select   bit 1 (LSB) 
        5A  1   Memory select   bit 2 (MSB) 
        5A  2   Eng. data #5    ---   --- 
        5A  3   Eng. data #6    ---   --- 
        5A  4   Eng. data #7    ---   --- 
        5B  0   Solar panel #1  lit   dark 
        5B  1   Solar panel #2  lit   dark 
        5B  2   Solar panel #3  lit   dark 
        5B  3   Solar panel #4  lit   dark 
        5B  4   Solar panel #5  lit   dark 
         
        5C  0   JTA CW beacon   CPU   TLM 
        5C  1   Eng. data #8    ---   --- 
        5C  2   Eng. data #9    ---   --- 
        5C  3   Eng. data #10   ---   --- 
        5C  4   Eng. data #11   ---   --- 
         
        5D  0   Eng. data #12   ---   --- 
        5D  1   Eng. data #13   ---   --- 
        5D  2   Eng. data #14   ---   --- 
        5D  3   Eng. data #15   ---   --- 
        5D  4   Eng. data #16   ---   --- 
         
        Mode JD Telemetry Data 

        Telemetry    data  are  also  sent  on  Mode  JD  by   means   of 
        packets.These  data  are  transmitted the ASCII format  shown  in 
        Table  4.  In the ASCII telemetry  (RA and RB) XXX  is a 3  digit 
        decimal  number  with a a range between 000 to 999.  This  number 
        represents  the value of N in Table 5 for channels denoted #00  - 
        #26.

        Table  5 contains the equations for converting the received  data 
        into  engineering  values.  The YYY bytes are  three  hexadecimal 
        bytes  of  system  status data, denoted #27a - #29c  and  can  be 
        decoded  as  shown in Table 6. The SSS byte in the last  row  are 
        binary  status data, denoted #30a - #39c.  Table  7 provides  the 
        information needed to decode them in a manner similar to the Mode 
        JA status points shown in Table 3.



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 38


        Table 4.  Mode JD PSK telemetry data format
         
         JAS-1b FF YY/MM/DD HH:MM:SS 
         XXX XXX XXX XXX XXX XXX XXX XXX XXX XXX 
         XXX XXX XXX XXX XXX XXX XXX XXX XXX XXX 
         XXX XXX XXX XXX XXX XXX XXX YYY YYY YYY 
         SSS SSS SSS SSS SSS SSS SSS SSS SSS SSS 
         
        where,   FF  is  the  Frame Identifier,  which  may  contain  the 
        following types:
                                            
         RA: Realtime telemetry, - ASCII    
         RB: Realtime telemetry, - Binary   
         SA: Stored telemetry, - ASCII      
         SB: Stored telemetry, - Binary     
         M0: Message #0                     
         M1: Message #1                     
           ...........                      
         M9: Message #9                     
         
        YY/MM/DD is year/month/day, and HH:MM:SS is hour/minute/second, 
        all in UTC. 


        Table 5.  Mode JD Telemetry Decoding Equations 
         
        CH   DESCRIPTION                  CALIBRATION 
        ========================================================= 
        #00  total solar array current     1.91x(N-4)mA 
        #01  battery charge/discharge     -3.81x(N-508)mA 
        #02  battery voltage              Nx0.022V 
        #03  battery center voltage       Nx0.009961V 
        #04  bus voltage                  Nx0.02021 V 
        #05  +5 V regulator voltage       Nx0.00620 V 
        #06  -5 V regulator voltage      -Nx0.00620 V 
        #07  + 10 V regulator voltage     Nx0.0126  V 
        #08  JTA output power             5.1x(N-158)mW 
        #09  JTD output power             5.4x(N-116)mW 
        #10  calibration voltage #2       N/500 V 
        #11  offset voltage #1            N/500 V 
        #12  battery temperature          0.139x(669-N)deg. C
        #13  JTD temperature              0.139x(669-N)deg. C
        #14  Baseplate Temperature #1     0.139x(669-N)deg. C
        #15  Baseplate Temperature #2     0.139x(669-N)deg. C
        #16  Baseplate Temperature #3     0.139x(669-N)deg. C
        #17  Baseplate Temperature #4     0.139x(669-N)deg. C
        #18  temperature calibration #1   N/500 V 
        #19  offset voltage #2            N/500 V 
        #20  Solar Cell Panel Temp   #1   0.38x(N-685)deg. C 
        #21  Solar Cell Panel Temp   #2   0.38x(N-643) 
        #22  Solar Cell Panel Temp   #3   0.38x(N-646) 
        #23  Solar Cell Panel Temp   #4   0.38x(N-647) 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 39


        #24  ------------------------- 
        #25  temperature calibration #2   N/500 V 
        #26  temperature calibration #3   N/500 V 
        ---------------------------------------------------------

        Table 6.  Mode JD HEX System Status Bytes
         
        CH   DESCRIPTION
        ========================================================= 
         
        #27a  Spare (TBD) 
        #27b  Spare (TBD) 
        #27c  Spare (TBD) 
        #28a  Spare (TBD) 
        #28b  Spare (TBD) 
         
        #28c  error count of memory unit #0 
        #29a  error count of memory unit #1 
        #29b  error count of memory unit #2 
        #29c  error count of memory unit #3 
         
         ----------------------------------------------
        Table 7.  Mode JD BINARY System Status Bytes.
         
        CH    DESCRIPTION             STATE
                                    1      0 
        =========================================
        #30a  JTA power             on     off 
        #30b  JTD power             on     off 
        #30c  JTA beacon            PSK    CW 
        #31a  UVC status            on     off 
        #31b  UVC level             1      2 
        #31c  main relay            on     off 
        #32a  engineering data #1     ----- 
        #32b  battery status        tric   full
        #32c  battery logic         tric   full
        #33a  engineering data #2     ----- 
        #33b  PCU status            bit 1 (LSB)
        #33c  PCU status            bit 2 (MSB)
        #34a  memory unit  #0       on    off 
        #34b  memory unit  #1       on    off 
        #34c  memory unit  #2       on    off 
        #35a  memory unit           on     off 
        #35b  memory select         bit 1 (LSB)
        #35c  memory select         bit 2 (MSB)
        #36a  engineering data #3     ------ 
        #36b  engineering data #4     ------ 
        #36c  computer power        on    off 
        #37a  engineering data #5     ------ 
        #37b  solar panel #1        lit  dark 
        #37c  solar panel #2        lit  dark 
        #38a  solar panel #3        lit  dark 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX B The Fuji-OSCAR 20 Spacecraft Page 40


        #38b  solar panel #4        lit  dark 
        #38c  solar panel #5        lit  dark 
        #39a  engineering data #6     ------ 
        #39b  CW beacon source      CPU   TLM 
        #39c  engineering data #7     ------ 
         
         
        Summary

        This  article  has  been  an introduction  to  Fuji-OSCAR  20,  a 
        friendly  little bird which provides strong mode J  signals  both 
        for analog and digital communications as well as telemetry  which 
        can  be  used for educational purposes.  If you can work  mode  B 
        then you ought to be able to work mode J with just a little  more 
        effort.  Tune in one evening and say 'Kon bon wa' as it goes  by. 
        Remember the 'J' in mode 'J' stands for Japan.

        Acknowledgments

        This  article  has been compiled from information  received  from 
        AMSAT-UK,  DB0OS,  KI6QL,  JAMSAT and the JARRL.   It  was  first 
        published in the AMSAT Journal, Volume 13, Numbers 3 and 4,  July 
        and September 1990.































        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 41


        This  Appendix contains information for decoding the data in  the 
        Fuji-OSCAR  12  PSK  Telemetry Data  Format.  It  is  practically 
        identical to the Fuji-OSCAR 20 format.
         
        JAS-1 FF YY/MM/DD HH:MM:SS
        xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx yyy yyy
        sss sss sss sss sss sss sss sss sss sss
         
        FF := Frame Identifier   RA: Realtime Telemetry - ASCII 
                                 RB: Realtime Telemetry - Binary 
                                 SA: Stored Telemetry - ASCII 
                                 SB: Stored Telemetry - Binary 
                                 M0: Message #0
                                 M1: Message #1
                                 .......
                                 M9: Message #9
         
        YY/MM/DD  =  Date 
         
        HH:MM:SS  =  Time (The command station attempts to keep the clock 
        as 
                     close as possible to UTC)
         
        [ Following is valid only for RA and SA frames ]
         
        xxx =  000 - 999  Format: 3 digit decimal (Analog Data)
                          28  samples  in  row 0 column 0   thru   row  2 
        column 7
                          (denoted #00 - #27 below)
         
          y =  0 - F      one byte Hex (System Status Data)
                          9 samples in row 2 column 8  thru  row 2 column 
        9
                          (denoted #28a - #29c below)
         
          s =  0 or 1     Binary Status Data
                          30 samples in row 3  thru  row 3 column 9
                          (denoted #30a - #39c below) 
         
        ***  FO-12 Telemetry Calibration Equations  ***
         
        Ch.     Item                          Equation    
        --------------------------------------------------------------------
        #00     Total Solar Array Current     1.91 * ( N - 4 )    mA
        #01     Battery Charge/Discharge      3.81 * ( N - 528 )  mA
        #02     Battery Voltage               N * 0.0210    V
        #03     Half-Battery Voltage          N * 0.00937   V
        #04     Bus Voltage                   N * 0.0192    V
        #05     + 5 V. Regulator Voltage      N * 0.00572   V
        #06     - 5 V. Regulator Voltage      N * -0.00572  V


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 42


        #07     +10 V. Regulator Voltage      N * 0.0116    V 
        #08     JTA Power Output              5.1 * ( N  - 158 )  mW
        #09     JTD Power Output              5.4 * ( N - 116 )   mW
        #10     Calibration Voltage #2        N / 500  V
        #11     Offset Voltage #1             N / 500  V
        #12     Battery Temperature           0.139 * ( 689 - N )  Deg. C
        #13     JTD Temperature               0.139 * ( 689 - N )  Deg. C
        #14     Baseplate Temperature #1      0.139 * ( 689 - N )  Deg. C
        #15     Baseplate Temperature #2      0.139 * ( 689 - N )  Deg. C
        #16     Baseplate Temperature #3      0.139 * ( 689 - N )  Deg. C
        #17     Baseplate Temperature #4      0.139 * ( 689 - N )  Deg. C
        #18     Temperature Calibration #1    N / 500  V
        #19     Offset Voltage #2             N / 500  V
        #20     Facet Temperature #1          0.38 * ( N - 684 )  Deg. C 
        #21     Facet Temperature #2          0.38 * ( N - 684 )  Deg. C
        #22     Facet Temperature #3          0.38 * ( N - 690 )  Deg. C
        #23     Facet Temperature #4          0.38 * ( N - 683 )  Deg. C
        #24     Facet Temperature #5          0.38 * ( N - 689 )  Deg. C
        #25     Temperature Calibration #2    N / 500  V
        #26     Temperature Calibration #3    N / 500  V
        #27     Depth of Battery discharge    ( N - 500 ) / 189   AH
         
         
        ***  FO-12 System Status Telemetry Bytes ***
         
        Ch.     Item
        --------------------------------------------------
         
        #28a    Spare (TBD)
        #28b    Spare (TBD)
        #28c    Memory Unit #0 error count
         
        #29a    Memory Unit #1 error count
        #29b    Memory Unit #2 error count
        #29c    Memory Unit #3 error count
         
         
        ***  FO-12 Binary Status Data Points ***
         
        Ch.    Item                     1         0
        -----------------------------------------------
        #30a   JTA Power                On        Off
        #30b   JTD Power                On        Off
        #30c   JTA Beacon               PSK       CW
         
        #31a   UVC Status               On        Off
        #31b   UVC Level                1         2
        #31c   Main Relay               On        Off
         
        #32a   Engineering Data #1      ----      ----
        #32b   Battery Status           Tric      Full
        #32c   Battery Logic            Tric      Full


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 43


         
        #33a   Engineering Data #2      ----      ----
        #33b   PCU Status                Bit 1 (LSB)
        #33c   PCU Status                Bit 2 (MSB)
         
        #34a   Memory Unit #0           On        Off
        #34b   Memory Unit #1           On        Off
        #34c   Memory Unit #2           On        Off
         
        #35a   Memory Unit #3           On        Off
        #35b   Memory Select             Bit 1 (LSB)
        #35c   Memory Select             Bit 2 (MSB)
         
        #36a   Engineering Data #3      ----      ----
        #36b   Engineering Data #4      ----      ----
        #36c   Computer Power           On        Off
         
        #37a   Engineering Data #5      ----      ----
        #37b   Solar panel #1           Lit       Dark
        #37c   Solar panel #2           Lit       Dark
         
        #38a   Solar panel #3           Lit       Dark
        #38b   Solar panel #4           Lit       Dark
        #38c   Solar panel #5           Lit       Dark
         
        #39a   Engineering Data #6      ----      ----
        #39b   CW beacon source         CPU       TLM
        #39c   Engineering Data #7      ----      ----
         
         
         
        ***  Example  *** 
         
        JAS-1 RA 86/08/01 09:00:00
        500 xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx 004 yyy
        01s sss sss sss sss sss sss sss sss sss
         
        Real time ASCII frame sent on 86/08/01 at 09:00:00 UTC
         
        Total Solar Array Current  =  947 mA
        Memory Unit #0 error count =  4
        JTA (mode-JA TX) power Off
        JTD (mode-JD TX) power On









        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 44


        APPENDIX D Information about AMSAT

        For  further  information  about  the  Radio  Amateur   Satellite 
        program,  photocopy and mail the following form together  with  a 
        self addressed stamped envelope (SASE) to :-

         To: 
        [ ]       AMSAT-NA,  850 Sligo Avenue, Silver Spring, MD,  20910-
                  4703. Telephone (301) 589 6062.

        [ ]       Project OSCAR Inc. POB 1136, Los Altos, CA. 94023-1136.

        [ ]       AMSAT-UK, 94 Herongate Road, Wanstead Park, London  E12 
                  5EQ.  Telephone (081) 989 6741.

        Please  send  me  further information  about  the  Radio  Amateur 
        Satellite   program,   and   details  of   membership   in   your 
        organization.

         CALL ________________ TODAY'S DATE _____________

         NAME ______________________________________________

         ADDRESS ___________________________________________

         ___________________________________________

         CITY ___________________________________________

         STATE _________ POSTCODE ______________________
























        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 45


        APPENDIX E Amateur Radio Software by Joe Kasser G3ZCZ

         PC-HAM 3.3 

        PC-HAM contains a number of programs some of which are  described 
        below. 

        LOGBOOK
        Full  blown  logging package. With automatic check  of  logs  for 
        awards such as DXCC. Allows you to recall any entry by call  sign 
        within  seconds.  Indexed displays, QSLing, Contest  mode  QSLing 
        (prints the lot) and lots more written in dBASE3, but a  compiled 
        LOGBOOK.EXE file is supplied together with the source code. 

        CONTEST
        Keeps Dupes in memory, logs QSO's to disk in format which can be 
        processed by the LOGBOOK package. 

        CQSS
        Sweepstakes  game.  Work  the ARRL Sweepstakes  contest  on  your 
        computer. You are located just outside Washington DC. A  propaga-
        tion  model is built in to the program. This program is  REQUIRED 
        training  for all sweepstakes operators. Program is based on  the 
        one  described in detail in 'Software for Amateur Radio'  by  Joe 
        Kasser  G3ZCZ,  published by TAB Books, Blue  Ridge  Summit,  PA. 
        17214.

        WHATSON
        Predict HF Propagation. Contest mode with printout to whole world 
        at hourly intervals. Needs BASIC


         LAN-LINK 1.58

        Function  key  and  Menu driven. Automatic  logbook  entries  for 
        Packet  and  Mailbox/Beacon Mode  AMTOR  Connects,  semiautomatic 
        logbook entries for other modes. Log file can be processed by the 
        Logbook Package of PC-HAM.

        Contest  operation,  sends  standard  message  and  automatically 
        increments  QSO count. Automatic optimized configuration  of  the 
        TNC  for each communications mode. All mode Function  key  'OVER' 
        feature (End).

        There  are 10 files with fixed names (LAN-LINK.001  through  LAN-
        LINK.010)  which may be viewed and transmitted by means of  func-
        tion keys. They may also be edited from the Edit Menu.

        Set up of TNC for AMSAT-OSCAR (non packet) Telemetry reception.

        Time display and event scheduler. ASCII Text Editor. Customizable 
        Colors.  Access to the TNC Command Mode is provided in  case  the 


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHAT-UP APPENDIX C Fuji-OSCAR 12 Telemetry Page 46


        user wishes to override any defaults.

        Automatic capture to disk of all packet radio connects. Automatic 
        indication  of the number of Packet connects. Local Area  Network 
        (LAN) message store and Forward capability. 

        Capable  of  automatic connect attempts to download  a  QTC  from 
        another station in the LAN. Capable of automatic connect attempts 
        to  a  packet BBS to download your incoming messages,  when  your 
        callsign  appears on the BBS mail beacon annunciator. Capable  of 
        automatically requesting Bulletins on subjects that interest  you 
        from your local packet BBS.

        Digipeat  monitoring  and capture. Alert signal to let  you  know 
        when  a  predetermined  call  shows up  in  a  packet  header  on 
        frequency. 

        Conference  Mode  in  multiconnect  situations.  Bridge  Mode  in 
        multiconnect  situations.  Path determination to DX  station  via 
        :QMH:.  Indicator  that  a specific  station  designated  as  the 
        'target'  call  connected  in Packet Mode,  or  linked  to  AMTOR 
        Beacon/Mailbox while you were away.

        Automatic  NET/ROM  and  KA Node path set  up  from  LAN-LINK.DIR 
        call/path directory file. Selective answering machine and MAILBOX 
        using  NC/L  command dialogue. Screen indication  of  connect  by 
        desired station (target call).

        Automatic  Beacon Mode CQ caller. Will call CQ  repetitively  and 
        either work the connect and keep going after disconnect or signal 
        you when a reply is received.

        SAREX special features. :QRA: trigger to determine who else is on 
        channel.

        Automatic  AMTOR SELCAL determination. Function key  change  from 
        monitoring AMTOR FEC CQ's to QSO's in progress (chirpcopy).

        NAVY MARS RTTY file transmitting protocols for the PK-232.

        Log files in dBASE 3 format.













        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX F SHAREWARE Page 47


        The  Association of Shareware Professionals (ASP) has established  
        standards for its members and for any organization which has "ASP 
        Approved"  status. The ASP wants to make sure that the  shareware 
        principle  works for you. If you are unable to resolve a  problem 
        with  an  ASP  member  or  organization  (other   than  technical 
        support),  the ASP may be able to help. Please write to  

        The  ASP Ombudsman, P.O. Box 5786, Bellevue, WA  98006, USA.

        You  are encouraged to copy the floppy disk and share  it  freely 
        with  others.  You have the luxury of trying out the  product  at 
        your own pace and in the comfort of your own home or workplace.  

        After  you  have used the material for  a  reasonable  evaluation 
        period  (90  days),  you should either  discontinue  use  of  the 
        material  or register your copy.  Your support is  important  and 
        greatly  appreciated.  With it, Shareware authors are  encouraged 
        to  design and distribute new products. Without it, a great  deal 
        of high quality, low cost software will cease to be available.

        Why pay at all?

           *  You receive support from the author.
           *  You receive a CURRENT copy of the program.
           *  Your input and ideas help shape future products.
           *  A sense of pride and ownership in having honestly
              participated in the Shareware revolution.
           *  You help to keep software prices down by supporting a
              distribution method which doesn't depend on expensive
              advertising campaigns.

        Be  aware of the following restrictions, designed to protect  the 
        community  of Shareware users and to prevent greedy  people  from 
        taking unfair advantage of the trust, hard work and good will  of 
        Shareware authors. 

        1.   No  price or consideration may be charged for the  material.      
             However, a distribution cost may be charged for the cost  of      
             the diskettes, shipping and handling, not to exceed $6.

        2.   The  files and programs on the disks may not be modified  or      
             deleted.

        3.   The  material  cannot  be sold as part of  some  other  more      
             inclusive package.

        4.   The material cannot be "rented" or "leased" to others.

        5.   The end user must be told clearly in writing on the  outside      
             of  the package and in all advertising that the  diskette(s)      
             are "Shareware."



        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX F SHAREWARE Page 48


        6.   The package must contain a written explanation that the disk      
             is   for  evaluation  purposes,  and  that   an   additional      
             "registration  fee"  is  expected  by  the  author,  if  the      
             material is used beyond an initial evaluation period.

        7.   In the case of distribution via any telecommunications link,      
             the following must be done:

             An error checking protocol must be used.

             The individual files must be combined into, and  transferred      
             in a library or archive format.  

        8.   Shareware  distribution  is  permitted only  in  the  United      
             States, Canada, England, and Australia.







































        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP APPENDIX F SHAREWARE Page 49


        WHATS-UP 0.55 Registration Fee $35.00
        LAN-LINK 1.58 Registration Fee $35.00 
        PC-HAM   3.52 Registration Fee $36.50

                 Register them all for $95.00.

        Evaluation Copies free, you pay only for the disk/postage. For an 
        evaluation  copy  (unregistered  full  blown  version)  of   each 
        software  send a formatted disk and SASE to Joe Kasser.  Overseas 
        users,  send  $5.00 ($10.00 covers all three)  instead.  Try  the 
        software  first, and only register your copy if you make  use  of 
        it. 

         To: Joe Kasser G3ZCZ,  P O BOX 3419,  SILVER SPRING,  MD 20918.

         CALL ________________ TODAY'S DATE _____________

         NAME ______________________________________________

         ADDRESS ___________________________________________

         ___________________________________________

         CITY ___________________________________________

         STATE _________ POSTCODE ______________________

         TNC TYPE _____________________ Home BBS __________

        I enclose a check for ______. Please send me the latest version 
        of ______________, and register me as a user.

        I enclose a disk/sase or $5.00. Please send me the latest version 
        of ______________________ to evaluate. If I like it and use it, I 
        plan to become a registered user.

        Disk Size 5.25 _____(360k) 5.25 _____(1.2Mb) 3.5 ______(730k)

        I AM NOT/AM currently using Shareware Version _____

        which I obtained from _________________________________________.

         Signature _______________________

        Radio Club Registrations 10 or more copies, 10% discount.
                                 50 or more copies, 25% discount.

        Designate one contact person to receive club registered  updates, 
        and  supply  a list of names and call signs of club  members  who 
        will be using the Registered Club Copy.




        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP Index Page 50


        Accuracy, 19
        Alarm, 13, 14
        Algebra, 18
        Alt-B, 6
        Alt-C, 6
        Alt-D, 6
        Alt-P, 6
        Alt-S, 6
        Alt-X, 6
        Altitude, 14
        AMSAT, 1, 2, 3, 4, 7, 9, 10, 12, 18, 20, 21, 23, 40, 44
        AMSAT-NA, 18, 44
        AMSAT-OSCAR, 7, 15, 45
        AMSAT-UK, 40, 44
        Analog-to-digital, 19
        Analysis, 1, 4, 6
        Analyze, 7
        Annunciator, 46
        Antenna, 32
        Antennas, 32
        Apogee, 31
        Archive, 48
        Array, 6, 17, 22, 23, 24, 25, 26, 27, 28, 29, 30, 35, 36, 38, 41, 
          43
        ARRAYS, 14

        BCR, 24, 26, 27, 28, 30
        BCRXMT, 5
        BCXRT, 20
        Beacon, 4, 9, 10, 16, 17, 32, 33, 34, 35, 36, 37, 39, 40, 42, 43, 
          45, 46

        Capture-to-disk, 4, 12, 13, 15
        Channel, 3, 4, 6, 12, 14, 16, 17, 18, 19, 20, 21, 30, 32, 35, 46
        Codes, 6
        Coefficients, 7, 18, 23, 25, 27, 29
        Color, 2, 5, 6, 9, 11, 13, 14, 15, 16, 20, 21
        Column, 6, 19, 21, 41
        Combinations, 2, 6, 11, 35
        Configuration, 1, 2, 5, 7, 14, 16, 45
        Contains, 4, 16, 17, 18, 20, 22, 35, 37, 41, 45
        Contents, 2, 5, 6, 11, 14, 15, 21
        Copy, 1, 4, 7, 9, 10, 12, 32, 47, 49
        Correct, 6, 7, 8, 16
        Count, 5, 21, 23, 25, 27, 29, 39, 42, 43, 45
        Current, 23, 25, 27, 29, 35, 36, 38, 41, 43, 47

        Decimal, 5, 16, 18, 19, 20, 35, 37, 41
        Decode, 1, 7, 17, 35, 37
        Default, 5, 6, 8, 10, 11, 12, 13, 14, 15, 17, 21
        Deg, 23, 24, 25, 26, 27, 28, 29, 30, 36, 38, 42
        DOVE, 1, 3, 8, 10, 14, 15, 16, 17, 25


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP Index Page 51


        DOVE-OSCAR, 5, 15

        Engineering, 4, 5, 6, 13, 19, 35, 36, 37, 39, 40, 42, 43
        Envelope, 44
        Equations, 4, 18, 23, 24, 25, 26, 27, 28, 29, 30, 34, 36, 37, 38, 
          41
        Example, 5, 7, 10, 15, 16, 19, 21, 35, 36, 43
        Exercise, 9
        Extract, 1, 2, 6, 9, 14, 33

        File, 2, 3, 4, 6, 7, 8, 9, 10, 11, 13, 14, 15, 16, 18, 20, 21, 22, 
          45, 46
        Files, 1, 2, 5, 7, 9, 10, 11, 12, 13, 15, 45, 46, 47, 48
        First, 1, 2, 7, 12, 13, 15, 17, 18, 20, 21, 31, 33, 36, 40, 49
        Format, 2, 4, 5, 6, 7, 10, 16, 18, 20, 34, 35, 37, 38, 41, 45, 46, 
          48
        Fuji, 8, 9, 10, 15, 16, 18, 20, 31, 33
        Fuji-OSCAR, 1, 3, 7, 15, 18, 31, 32, 33, 34, 35, 40, 41

        Header, 6, 21, 46
        HEADERLINE, 6, 12
        Hexadecimal, 16, 20, 37

        Identifier, 16, 17, 18, 19, 38, 41
        Institution, 1
        Interactive, 2, 4, 6, 7, 9, 12

        LAN-LINK, 5, 12, 45, 46, 49
        Limit, 2, 5, 13, 14, 16, 19, 20
        Lines, 14, 16, 20, 21
        Link, 2, 4, 5, 7, 20, 21, 32, 48

        Menu, 2, 6, 8, 9, 11, 12, 13, 45
        Microsat, 2, 7, 8, 9, 10, 17, 18, 20, 23

        Non-existent, 13

        Options, 9, 11, 12, 13
        OSCAR, 1, 2, 4, 9, 12, 32, 33, 44
        Output, 24, 26, 28, 30, 32, 36, 38, 42

        Packet, 5, 6, 7, 9, 10, 11, 12, 13, 15, 20, 21, 32, 34, 35, 45, 46
        Protocol, 32, 48
        Protocols, 46

        Quadratic, 18

        Real-time, 4, 7, 10, 13, 15

        Satellite, 4, 31, 32, 34, 44
        Self, 44
        Simultaneous, 34


        COPYRIGHT Joe Kasser, G3ZCZ 1990.

        WHATS-UP Index Page 52


        Spreadsheet, 4, 6, 13, 22
        Stamped, 44
        Status, 4, 5, 14, 34, 35, 36, 37, 39, 41, 42, 43, 47

        Telemetry, 1, 3, 4, 5, 6, 7, 8, 9, 10, 11, 14, 16, 17, 18, 19, 21, 
          22, 23, 25, 27, 29, 32, 33, 34, 35, 36, 37, 38, 40, 41, 42, 45

        WHATS-UP, 1, 2, 4, 5, 6, 7, 8, 10, 11, 13, 14, 15, 16, 17, 18, 19, 
          20, 21, 49













































        COPYRIGHT Joe Kasser, G3ZCZ 1990.