CHECK.COM

 syntax:  CHECK keyword parameter1 parameter2 ...

 purpose:  This is an extension of the DOS batch file capabilities.  When
 run, Check returns an error level number to the batch file to report a
 condition.
       keywords and parameters       information returned
       FileSize filespec             Length of file in K
       FileFound filespec            0 - file found
                                     1 - file not found
       FileText filespec `string'    0 - string found
                                     1 - string not found
       DiskSpace [d:]                number of whole 16k blocks free
                                     on indicated or default drive
       Memory                        number of 16k RAM modules
       VideoCard                     0 - monochrome display adapter
                                     1 - color graphics adapter
                                     2 - enhanced graphics adapter
       Model                         machine ID byte
       8087                          0 - 8087 or 80287 installed
                                     1 - 8087 & 80287 not installed
       80287                         0 - 8087 or 80287 installed
                                     1 - 8087 & 80287 not installed
       Time                          current hour (0-23)
       Day                           current day (1-31)
       Month                         current month (1-12)
       VideoMode                     current video mode (0-16)
       Version                       DOS version (major number) in use
       KeyBoard                      0 - keyboard buffer empty
                                     1 - entry awaiting processing
       Keypress                      ASCII code of key pressed

 Operation: Enter the check command on a line in the batch file.  Have the
 next line look at the returned error level number to determine the next
 operation.  Example          check memory
                              if not errorlevel 16 goto short
                              goto end
                              :short
                              echo minimum 256 K required to run
                              :end

 Source:  PC Magazine 10 Feb 1987 volume 6 number 3 page 299