4. Interpreting the Basic Specifications

This section explains what the specifications above mean, and some other
things you'll need to know.  First, some definitions.  Next to each in parens
is the variable name we'll use for it when doing calculations

horizontal sync frequency (HSF)
    Horizontal scans per second (see above).

vertical sync frequency (VSF)
    Vertical scans per second (see above).  Mainly important as the upper
limit on your refresh rate.

dot clock  (DCF)
    More formally, `driving clock frequency'; sometimes loosely called
`bandwidth'.  The frequency of the crystal or VCO on your adaptor --- the
maximum dots-per-second it can emit.

video bandwidth (VB)
    The highest frequency at which your monitor's video signal can change.
This constrains the highest dot clock you can use and the overall sharpness
of fine details in the video image.

frame length (HFL, VFL)
    Horizontal frame length (HFL) is the number of dot-clock ticks needed for
your monitor's electron gun to scan one horizontal line, *including the
inactive left and right borders*.  Vertical frame length (VFL) is the number
of scan lines in the *entire* image, including the inactive top and bottom
borders.

screen refresh rate (RR)
   The number of times per second your screen is repainted.  Higher frequencies
are better, as they reduce flicker.  60Hz is good, VESA-standard 72Hz is
better.  Compute it as 

	RR = DCF / (HFL * VFL)

Note that the product in the denominator is *not* the same as the monitor's
visible resolution, but typically somewhat larger.  We'll get to the details
of this below.

About Bandwidth:

Monitor makers like to advertise high bandwidth because it constrains the
sharpness of intensity and color changes on the screen.  A high bandwidth
means smaller visible details.

Your monitor uses electronic signals to present an image to
your eyes.  Such signals always come in in wave form once they are converted
into analog form from digitized form.  They can be considered as combinations
of many simpler wave forms each one of which has a fixed frequency, many of
them are in the Mhz range, eg, 20Mhz, 40Mhz, or even 70Mhz.  Your monitor
video bandwidth is, effectively, the highest-frequency analog signal it can
handle without distortion.

For our purposes, bandwidth is mainly important as an approximate cutoff point
for the highest dot clock you can use.


Sync Frequencies snd the Refresh Rate:

Each horizontal scan line on the display is just the visible portion of a
frame-length scan.  At any instant there is actually only one dot active on
the screen, but with a fast enough refresh rate your eye's persistence of
vision enables you to "see" the whole image.

Here are some pictures to help:

                    _______________________
                   |                       |     The horizontal frame length
                   |->->->->->->->->->->-> |     is the time in dot clocks
                   |                      )|     required for the
                   |<-----<-----<-----<--- |     electron beam to trace
                   |                       |     a pattern like this
                   |                       |
                   |                       |
                   |                       |
                   |_______________________|    

                    _______________________
                   |        ^              |     The vertical frame length
                   |       ^ |             |     is the time in dot clocks
                   |       | v             |     required for the
                   |       ^ |             |     electron beam to trace
                   |       | |             |     a pattern like this
                   |       ^ |             |
                   |       | v             |
                   |       ^ |             |
                   |_______|_v_____________|    
                
Remember that the actual raster scan is a very tight zigzag pattern; that is,
the beam moves left <-> right and at the same time up <-> down.

Now we can see how the dot clock and frame size relates to refresh rate.  By
definition, one hertz (hz) is one cycle per second.  So, if your horizontal
frame length is HFL and your vertical frame length is VFL, then to cover the
entire screen takes (HFL * VFL) ticks.  Since your card emits DCF ticks per
second by definition, then obviously your monitor's electron gun(s) can sweep
the screen from left to right and back and from bottom to top and back DCF /
(HFL * VFL) times/sec.  This is your screen's refresh rate, because it's how
many times your screen can be updated thus REFRESHED per second!

You need to understand this concept to design a configuration which trades off
resolution against flicker in whatever way suits your needs.

5. Tradeoffs in Configuring your System

Another way to look at the formula we derived above is

	DCF = RR * HFL * VFL

That is, your dot clock is fixed.  You can use those dots per second to buy 
either refresh rate, horizontal resolution, or vertical resolution.  If one
of those increases, one or both of the others must decrease.


Note that your refresh rate cannot be greater than the maximum vertical sync
frequency of your monitor - for any given monitor at a given dot clock, there
is a minimum product of frame lengths below which you can't force it.

So let's say you've picked a minimum acceptable refresh rate.  In choosing
your HFL and VFL, you'll have some room for maneuver.
 
6. Memory Requirements

For 256-color displays, a byte of video memory is required for each visible
dot to be shown.  This byte contains the information that determines what mix
of red, green, and blue is generated for its dot.  To get the amount of memory
required, multiply the number of visible dots per line by the number of
visible lines.  For a display with a resolution of 800x600, this would be 800
x 600 = 480,000, which is the number of visible dots on the display.  This is
also, at one byte per dot, the number of bytes of video memory that are
necessary on your adapter card.

Thus, your memory requirement will typically be (HR * VR)/1024 Kbytes of VRAM,
rounded up.  In the example case, we'd need (936 * 702)/1024 = 642K.  So if
you have one meg, you'll have extra for virtual-screen panning.
                 
However, if you only have 512K on board, then you can't use this resolution.
Even if you have a good monitor, without enough video ram, you can't take
advantage of your monitor's potential.  On the other hand, if your SVGA has one
meg, but your monitor can display at most 800x600, then high resolution is
beyond your reach anyway.

7. Computing Frame Sizes

Start by dividing DCF by your highest available HSF to get the number
of horizontal sweeps per second available.

For example; suppose you have a Sigma Legend SVGA with a 65MHz dot clock, and
your monitor has a 55KHz horizontal scan frequency.  The quantity (DCF / HSF)
is then 1181.

Now for our first bit of black magic.  You need to round this figure to the
nearest multiple of 8.  This has to do with the VGA hardware controller used by
SVGA and S3 cards; it uses an 8-bit register, left-shifted 3 bits, for what's
really an 11-bit quantity.  Other card types such as ATI 8514/A may not have
this requirement, but we don't know and the correction can't hurt.  So round
the usable horizontal scans per second figure to 1176.

This figure (DCF / HSF rounded to a multiple of 8) is the minimum HFL you can
use.  You can get longer HFLs (and thus, possibly, more horizontal dots on the
screen) by setting the sync pulse to produce a lower HSF.  But you'll pay with
a slower and more visible flicker rate.

As a rule of thumb, 80% of the horizontal frame length is available for
horizontal resolution, the visible part of the horizontal scan line (this
allows, roughly, for borders and sweepback time -- that is, the time required
for the beam to move from the right screen edge to the left edge of the next
raster line).  In this example, that's 944 ticks.


To get the normal 4:3 screen aspect ratio, set your vertical resolution to
3/4ths of the horizontal resolution. For this example, that's 708 ticks. To get
your actual VFL, multiply that by 1.05 to get 743 ticks.

About that 4:3 --- a ratio of 4:3 for width to height of the displayed area
approximates the Golden Section, (1 + sqrt(5))/2.  Human beings seem to be
wired to find this kind of rectangle pleasant to look at; accordingly, video
tubes and the standard resolutions such as 800x600, 640x480 and 1024x768 all
approximate it.  Though it's psychologically magic, it's not technically
magic; nothing prevents you from using a non-Golden-Section ratio if that
will get the best use out of your screen real estate.

So, HFL=1176 and VFL=743.  Dividing 65MHz by the product of the two gives
us a nice, healthy 74.4Hz refresh rate.  Excellent!  Better than VESA standard!
And you got 944x708 to boot, more than the 800 by 600 you were probably
expecting.  Not bad at all!

You can even improve the refresh rate further, to almost 76 Hz, by using the
fact that monitors can often sync horizontally at 2khz or so higher than
rated, and by lowering VFL somewhat (that is, taking less than 75% of 944 in
the example above).  But before you try this "overdriving" maneuver, if you
do, make *sure* that your monitor electron guns can sync up to 76 Hz vertical.
(the popular NEC 4D, for instance, cannot.  It goes only up to 75 Hz VSF).

8. Black Magic and Sync Pulses

Horizontal Sync:

By previous definition, it takes HFL ticks to trace the a horizontal scan line.
Let's call the visible tick count (your horizontal screen resolution) HR.  Then
Obviously, HR < HFL by definition.  For concreteness, let's assume both start
at the same instant as shown below:

                  |___ __ __ __ __ __ __ __ __ __ __ __ __
                  |_ _ _ _ _ _ _ _ _ _ _ _                |
                  |_______________________|_______________|_____ 
                  0                       ^               ^     unit: ticks
                                          |   ^       ^   |
                                          HR  |       |  HFL
                                          |   |<----->|   |
                                          |<->|  HSP  |<->|
                                           HGT1         HGT2
                
Now, we would like to place a sync pulse of length HSP as shown above, ie,
between the end of clock ticks for display data and the end of clock ticks for
the entire frame.  Why so?  because if we can achieve this, then your screen
image won't shift to the right or to the left.  It will be where it supposed to
be on the screen, covering squarely the monitor's viewable area.

Furthermore, we want about 30 ticks of "guard time" on either side of the sync
pulse.  This is represented by HGT1 and HGT2.  In a typical configuration HGT1
!= HGT2, but if you're building a configuration from scratch, you want to start
your experimentation with them equal (that is, with the sync pulse centered).

The symptom of a misplaced sync pulse is that the image is displaced on the
screen, with one border excessively wide and the other side of the image
wrapped around the screen edge, producing a white edge line and a band of
"ghost image" on that side.  A way-out-of-place vertical sync pulse can
actually cause the image to roll like a TV with a mis-adjusted vertical hold
(in fact, it's the same phenomenon at work).

If you're lucky, your monitor's sync pulse widths will be documented on its
specification page.  If not, here's where the real black magic starts...

You'll have to do a little trial and error for this part.  But most of the
time, we can safely assume that a sync pulse is about 3.5 to 4.0 microsecond
in length.

For concretness again, let's take HSP to be 3.8 microseconds (which btw, is not
a bad value to start with when experimenting).

Now, using the 65Mhz clock timing above, we know HSP is equivalent to 247 clock
ticks (= 65x10**6 * 3.8 *10**(-6)) [recall M=10**6, micro=10**(-6)]

Vertical Sync:

Going back to the picture above, how do we place the 247 clock ticks as shown
in the picture?

Using our example, HR is 944 and HFL is 1176.  The difference between the two
is 1176-944=232 < 247!  Obviously we have to do some adjustment here.

The first thing is to raise 1176 to 1184, and lower 944 to 936.  Now the
difference = 1184-936= 248. Hmm, closer.

Next, instead using 3.8, we use 3.5 for calculating HSP; then, we have
65*3.5=227.  Looks better.  But 248 is not much higher than 227.  It's normally
necessary to have 30 or so clock ticks between HR and the start of SP, and the
same for the end of SP and HFL.  AND they have to be multiple of eight!  Are we
stuck?

No!  let's do this, 936%8==0, (936+32)%8==0 too.  But 936+32=968, 968+227=1195,
1195+32=1227.  Hmm.. this looks not too bad.  But it's not a multiple of 8, so
lets round it up to 1232.

But now we have potential trouble, the sync pulse is no longer placed right in
the middle between h and H any more.  Happily, using our calculator we find
1232-32=1200 is also a multiple of 8 and (1232-32)-968=232 corresponding using
a sync pulse of 3.57 micro second long, still reasonable.

In addition, 936/1232~0.76 or 76%, still not far from 80%, so it should be all
right.

Furthermore, using the current horizontal frame length, we basically ask our
monitor to sync at 52.7khz(=65Mhz/1232) which is within its capability.  No
problems.
                
Using rules of thumb we mentioned before, 936*75%=702, This is our new vertical
resolution.  702*1.05=737, our new vertical frame length.

Screen refresh rate = 65Mhz/(737*1232)=71.6 Hz.  This is still excellent.


Figuring the vertical sync pulse layout is similar:

                  |___ __ __ __ __ __ __ __ __ __ __ __ __
                  |_ _ _ _ _ _ _ _ _ _ _ _                |
                  |_______________________|_______________|_____ 
                  0                      VR              VFL     unit: ticks
                                          ^   ^       ^
                                          |   |       |
                                          |<->|<----->|
                                           VGT    VSP
                
We start the sync pulse just past the end of the vertical display data ticks.
VGT is the vertical guard time required for the sync pulse.  Most monitors are
comfortable with a VGT of 0 (no guard time) and we'll use that in this
example.  A few need two or three ticks of guard time, and it usually doesn't
hurt to add that.

Returning to the example: since by the defintion of frame length, a vertical
tick is the time for tracing a complete HORIZONTAL frame, therefore in our
example, it is 1232/65Mhz=18.95us.

Experience shows that a vertical sync pulse should be in the range of 50us and
300us.  As an example let's use 150us, which translates into 8 vertical clock
ticks (150us/18.95us~8).

9. Putting it All Together

The name section contains one field, the name of the video mode specified by
the rest of the line.  This name is referred to on the "Modes" line of the
Graphics Driver Setup section of the Xconfig file.  The name field may be
omitted if the name of a previous line is the same as the current line.

The dot clock section contains only the dot clock (what we've called DCF) field
of the video mode line.  The number in this field specifies what dot clock was
used to generate the numbers in the following sections.

The horizontal section consists of four fields which specify how each
horizontal line on the display is to be generated.  The first field of the
section contains the number of dots per line which will be illuminated to form
the picture (what we've called HR).  The second field of the section indicates
at which dot the horizontal sync pulse will begin.  The third field indicates
at which dot the horizontal sync pulse will end.  The fourth field specifies
the toal horzontal frame length (HFL).

The vertical section also contains four fields.  The first field contains the
number of visible lines which will appear on the display (VR).  The second
field indicates the line number at which the vertical sync pulse will begin.
The third field specifies the line number at which the vertical sync pulse will
end.  The fourth field contains the total vertical frame length (VFL).

Example:

#     Modename    clock  horizontal timing  vertical timing
#                     dots hrsyndotb hrsyndotend hfl vsynpbe vsynpend vfl
     "752x564"     40    752 784  944 1088  564 567 569 611
	           44.5  752 792  976 1240  564 567 570 600

from my viper.ini
;              | horizontal timing              | vertical timing
;        |dot- |visible|hrz sync |hrz sync|hrz  |vert-|vert sync|vert sync|vert
;Modename|clock|dots   |dot start|dot end |total|lines|dot start|dot end  |total
; "800x600" 40  800     868       1020     1088  600   603       609       630
;               HR      HS1       HS2      HFL   VR    VS1       VS2       VFL
; so for P9000:
; hrzt  = ( HFL / 4 ) - 1
; hrzsr = ( ( SH2 - SH1 ) / 4 ) - 1
; hrzbr = ( ( HFL - SH1 ) / 4 ) - 1
; hrzbf = ( ( HR + ( HFL - SH1 ) ) / 4 ) - 1
; vrtsr = VS2 - VS1
; vrtbr = ( VS2 - VS1 ) + ( VFL - VS2 ) = VFL - VS1
; vrtbf = vrtbr + VR = VR + VFL - VS1
; vrtt  = VFL

For Xconfig, all of the numbers just mentioned - the number of illuminated dots
on the line, the number of dots separating the illuminated dots from the
beginning of the sync pulse, the number of dots representing the duration of
the pulse, and the number of dots after the end of the sync pulse - are added
to produce the number of dots per line.  The number of horizontal dots must be
evenly divisible by eight.

Example:
	horizontal numbers: 800 864 1024 1088

Note again that all of the horizontal numbers (800, 864, 1024, and 1088) are
divisible by eight!  This is not required of the vertical numbers.

The number of lines from the top of the display to the bottom form the frame.
The basic timing signal for a frame is the line.  A number of lines will
contain the picture.  After the last illuminated line has been displayed, a
delay of a number of lines will occur before the vertical sync pulse is
generated.  Then the sync pulse will last for a few lines, and finally the last
lines in the frame, the delay required after the pulse, will be generated.  The
numbers that specify this mode of operation are entered in a manner similar to
the following example.

Example:

     vertical numbers: 600 603 609 630

     This example indicates that there are 600 visible lines on the display,
     that the vertical sync pulse starts with the 603rd line and ends with the
     609th, and that there are 630 total lines being used.

   Let's return to the example we've been working.  According to the above, all
we need to do from now on is to write our result into Xconfig as follows:

<name>   DCF     HR  SH1 SH2   HFL   VR  SV1 SV2 VFL

SH1 is the start tick of the horizontal sync pulse and SH2 is its end tick; SV1
is the start tick of the vertical sync pulse and SV2 is its end tick.

#name    clock   horizontal timing   vertical timing    flag
936x702  65      936 968 1200 1232   702 702 710 737


11. Two More Example Calculations

Here's another hypothetical:

An adapter card has a 40 MHz clock rate.  A display has a range of horizontal
sync rates from 30 KHz to 37 KHz.  The minimum number of dots per line is
40,000,000/37,000 = 1,081.081, or approximately 1,081 dots per line.

We'll use this number of dots per line in the following calculations.  So each
line on our display must have at least 1081 dots.  We round this up to 1088 to
make it divisible evenly by eight.  Now let's assume that the horizontal sync
pulse should be 3.8 microseconds long.  We need to find out how many dots it
takes to make a 3.8 microsecond pulse.  We do this by first finding out how
many microseconds are in one dot.  Since there are 40,000,000 dots per second,
1/40,000,000 is the number of seconds per dot.

     1/40,000,000 = .000000025 = .025 microseconds per dot

Thus the number of dots for a 3.8 microsecond sync pulse is

     3.8 microseconds = D dots x .025 microseconds/dot

		or

     D dots = (3.8 microseconds) / (.025 microseconds/dot) = 152 dots

So we have 1088 dots per line, 800 of which are the illuminated ones, with 152
for the sync pulse.  (Note that 152 is evenly divisible by eight.  If it
weren't we would round it up until it was evenly divisible.)  This leaves us
the task of calculating the time before and after the sync pulse that is
necessary for the display.

The rule of thumb for this is that we need about 30 ticks of guard time.  In
this particular case, allocating 32 dots is convenient, because all the other
quantities are divisible by 8.  This results in the timing being 800 dots for
the viewable area, 152 dots for the pulse, and 1088 - (800 + 152) = 136 dots
to divide between the two other times.  Half of 136 is 68 dots, so 68 dots are
placed between the illuminated dots and the sync pulse, and 68 dots are placed
after the sync pulse.  The horizontal numbers in the Xconfig line then become

	800 (800+68) (800+68+152) (800+68+152+68)

			or

		800 868 1020 1088

Now we want to calculate the vertical numbers.  To begin, we must remember
that the vertical numbers are not in terms of dots or microseconds per dot,
but are expressed as numbers of lines!  So we have to calculate how much time
it takes to display a single line.  That's easy, because we know each line is
1088 dots and each dot is .025 microsecond.  Each line is, therefore,

     (1088 dots/line) x (.025 microseconds/dot) =
					27.2 microseconds/line

Since we chose 800 visible dots per line, let's choose the number of lines to
be such that the ratio of horizontal to vertical is 4 to 3.  Thus, 800 is 4 x
200, so the number of visible lines should be 3 x 200 = 600.  Our target
resolution is 800x600.

We know that a vertical sync pulse should be in the range of 50 to 300
microseconds. If we chose 150 microseconds as a typical sync pulse, we find how
many lines 150 microseconds is by dividing 150 by 27.2 microseconds per line.

     (150 microseconds/pulse) / (27.2 microseconds/line) =
			5.51 lines/pulse

By rounding up (never down) to 6 lines/pulse we now have the vertical sync
pulse width.

To guess at the total number of lines per frame (illuminated lines plus
nonilluminated lines in the border) we assume (from "Videotiming...") that the
total number of lines will be 5% more than the number of viewable lines.  So
the total number of lines is

     (600 lines) x (1.05) = 630 total lines per frame

So now we must place the pulse in the time between the end of the illuminated
lines and the end of the frame.  Since we have 630 total lines, 600
illuminated lines, and 6 lines for the pulse, we have

		630 - 600 - 6 = 24 lines left

Some displays don't mind if the pulse begins immediately after the illuminated
lines, but others might want a line or two between the last illuminated line
and the beginning of the sync pulse.  Taking the latter course just to be
safe, we add three lines between the last illuminated line and the beginning
of the pulse.  The rest of the lines are added after the pulse ends.  So the
vertical timing numbers become

	     600 (600+3) (600+3+6) (600+3+6+21)

			or

     		  600 603 609 630

Before we do anything else, we must check that the display can handle 630
lines/frame at 27.2 microseconds/line.  We do this by calculating how many
frames per second our configuration will generate, and comparing it to the
display manual's entry for vertical sync rate.  For 630 lines/frame at 27.2
micro- seconds/line, we have 630 x 27.2 = 17,136 microseconds/frame.  17,136
microseconds/frame is 0.017136 seconds/frame, or 1/0.017892 frames/second.

	1 / (0.017136 seconds/frame) = 58.4 frames/second

If the manual says the vertical sync rate is 58.4 Hz, or 58.4 Hz is in the
range of the display's vertical sync rate, we are fine.  If the display cannot
handle this rate, we'll have to change the number of lines per frame by
adjusting all of the timings proportionally.

Now we combine the horizontal and vertical timing numbers together with the
resolution and clock values to produce a test configuration for Xconfig.  Our
line becomes

     "800x600"  40  800 868 1020 1088  600 603 609 630

An actual calculation

My adapter card has a 40 MHz crystal on it so I started with a 40
MHz clock rate.  My display's maximum horizontal sync rate is 37
KHz, so the minimum dots per line are 40,000,000/37,000 = 1081.
My display's vertical sync rate is the range from 50 Hz to 90 Hz.

My display's manual says that the largest horizontal sync pulse is 3.92
microseconds. With 0.025 microseconds per dot, the pulse is

	(3.92 microseconds) / (.025 microseconds/dot) =
						156.8 dots

Rounding this up to the nearest number evenly divisible by eight
gives 160 dots.

The manual also says that the time between the last illuminated
dot and the beginning of the sync pulse must be at least 0.67
microseconds.  The number of dots in 0.67 microseconds at a 40
MHz clock rate - remember 40 MHz is .025 microseconds/dot - is

	D dots = (0.67 microseconds) / (.025 microseconds/dot) =
						26.8 dots

Since 26.8 is not evenly divisible by eight, round it up to 32 dots.

My display's manual says the time after the sync pulse should be
3.56 microseconds or more.  In dots, 3.56 microseconds is

	D dots = (3.56 microseconds) / (.025 microseconds/dot) =
						142.4 dots

Round 142.4 up to 144, so that it's evenly divisible by eight.

So now for a horizontal line we have 800 illuminated dots, 32
dots between the illuminated dots and the sync pulse, 152 dots
for the sync pulse, and 144 dots after the sync pulse.

	800 + 32 + 160 + 144 = 1136

We now have a line that is 1136 dots long. This is greater than the 1088 we
previously calculated, but remember that 1088 was the MINIMUM number of dots
that could be on a line. So 1136 dots per line is okay for starters.

The numbers to enter on the Xconfig line so far are

	"800x?"  40  800 (800+32) (800+32+160) (800+32+160+144)...

				or

	"800x?"  40  800 832 992 1136...

A line of 1136 dots at .025 microsecond/dot means that a line
represents 1136 x .025 = 28.4 microseconds.

Since we chose 800 dots/line horizontal resolution, we choose 600
lines/frame as the vertical resolution.

My display's manual says that the vertical sync pulse must be at least 64
microseconds long. In terms of lines, 64 microseconds is

	(64 microseconds/pulse) / (28.4 microseconds/line) =
					2.25 lines/pulse

We round 2.25 up to 3 lines for the vertical sync pulse.

The manual says the time between the last displayed line and the start of the
sync pulse must be at least 318 microseconds, and the delay after the end of the
pulse must be at least 630 microseconds. We calculate how many lines each of
these time periods represents as follows.

	(318 microseconds) / (28.4 microseconds/line) =
					11.20 lines

	(630 microseconds) / (28.4 microseconds/line) =
					22.18 lines

We round each of the times up to become 12 lines before the sync pulse and 23
lines after the pulse.  This makes our vertical timing numbers

	600 (600+12) (600+12+3) (600+12+3+23)

			or

		600 612 615 638

Checking the frame rate to see if it falls within the rate of the display, we
see that 638 lines/frame at 28.4 microseconds/line is 18,119 microseconds/frame,
which is 55.19 frames/second. My display can handle anything from 50 Hz to 90
Hz, so the timing is all right.