Bridge-router documentation

In the pub/pcroute/exp directory there are three files that implement
a beta test version of a IP bridge router.  These files are called

    bw03w03.exe         A version for two WD8003E cards 
                            card 1:  I/O address 280H
                                     interrupt (unused)

                            card 2:  I/O address 2A0H
                                     interrupt (unused)
                        Note that this version is really not recommended
                        for production use since the small buffer size
                        of the WD8003E card will cause packets to be
                        dropped under high loads and NFS traffic.  Still
                        it is usefull for experimentation and proof of
                        concept demonstrations.

    bw13w13.exe         A version for two WD8013EBT cards 
                            card 1:  I/O address 280H
                                     interrupt (unused)

                            card 2:  I/O address 2A0H
                                     interrupt (unused)

    b3c73c7.exe         a version for two 3c507 cards 
                            card 1:  I/O address 280H
                                     shared memory D0000H
                                     shared memory size 64K
                                     interrupt (unused)

                            card 2:  I/O address 2A0H
                                     shared memory C0000H
                                     shared memory size 64K
                                     interrupt (unused)

These executables look exactly like their non-bridged counterparts
as far as setup and configuration go.  Thus you should rename the 
appropriate one to PCROUTE.EXE and follow the configuration instructions 
in INSTALL.DOC file that comes with the PCroute distribution.

The difference between these executables and regular PCroute is that
in addtion to performing all the normal fucntions that PCroute does,
it also will bridge ethernet packets between the two interfaces.

Note that these bridges will NOT forward IP or ARP broadcasts because
doing so would certainly confuse the IP network, however all other
broadcast types are sent through.

Also, non-broadcast ethernet packets are always bridged even if they
are IP or ARP.  Now normally IP hosts will only try to send packets
to hosts/gateways on the local segment, thus these packets will be
filtered out by the bridge, but initially, the bridge will not know
this and some packets may get though on startup.  This effect should 
be benign.  If it causes problems, let me know.  I can easily change the 
code so that IP and ARP packets are ALWAYS filtered even when they
are non-broadcasts.

Note that at present, only the binaries are available.  This is because
I had to make a hack because of limitations in TASM.  This hack does
not effect the code that is produced, but does complicate how it is 
compiled.  Rather than try to explain this hack, I prefer simply to
distribute the compiled form for now.  Hopefully I will figure out
a better solution to this problem soon.

Vance
morrison@accuvax.nwu.edu