PCbridge Installation Guide
                              Vance Morrison


What you need to install PCbridge:

    The PCbridge distribution comes in two parts, the binary-documentation
    archive, as well as the source code archive.  If you are using PCbridge
    in a 'standard' configuration (for example, with 2 WD8003E ethernet
    cards), then you will only need the binary-documentation archive.  If
    you wish to modify the code, or use non-standard configurations
    (a three interface bridge for example), you will also need to recompile
    the code.  See compile.doc for details on how to do this.

    In addition to the software you will also need

        1) An IBM XT or AT compatatable.   PCbridge uses very little memory
           itself (about 80K) so a machine with 256K of memory is sufficient.
           Additional memory simply will not be used.  

        2) The proper number and type of interface cards.  As stated
           in the readme.doc WD8003E cards are NOT recommended unless
           you have no file serving traffic crossing the bridge.  
           WD8003EBT or WD80013EBT are the recommended cards.  Standard
           COM boards can be used for the serial line if a remote bridge
           is being configured.

-------------------------------------------------------------------------

If you are buying new hardware:

    Because of the 16 bit data path, it is STRONGLY recommended that
    if you are buying new hardware for you PCbridge that you get a
    AT clone and use 3c507 or WD8013EBT cards.   This PC need not have 
    much memory (256K suffices), and does not need a monitor.  PCbridge 
    also does not used the keyboard in any way, but some BIOS boot
    roms REQUIRE the keyboard to be connected for the machine to
    boot.  I have found that many of these BIOS roms will NOT check
    for a keyboard if the DIP switches inside the PC are set for
    no-monitor (or sometimes monitor = EGA).   Machines with this
    type of boot rom are convenient because you need not buy the
    keyboard and bridge is more compact without it.  

    Such stripped down ATs cost about $400-$500 at the time of this
    writing.  WD8013EBT cards cost $250, and 3c507 about $250-$300
    so a VERY nice bridge could be put together for under $1000.  

    With 386 machines coming down in price, people have asked if
    it is worth buying one of these for a high end bridge.  Although
    the cache and higher clock rate may help, I suspect that a 
    fast 286 machine will provide much better cost/performance.
    In short, a 386 machine is overkill.  

    If you are buying COM boards for a remote bridge, buy the
    ones with the 16550AF chip on them.  These boards have a built
    in FIFO buffer on them that will reduce interrupts by a factor
    of 10, and thus leave more time for the CPU to filter/forward
    packets.

-------------------------------------------------------------------------

Installing the standard WD ethernet-ethernet bridge:


The PCbridge distribution comes with a two interface ethernet bridge
for the WD8013EBT, WD8003EBT and WD8003E, cards.   The file for each
of these versions is simply the name (truncated because of DOS), with
a .EXE extension.   To use it simply 

    1) Rename the proper file to 'BRIDGE.EXE'.

    2) Set the I/O address of the first to WD80XX card  to 280H (the 
       default) and the second to 2A0H.  PCbridge does not use interrupts 
       so you can leave the IRQ line on the default of 3.  Also jumper
       each card for the type of ethernet you will use (thick or thin)

    3) Install these cards in the PC that will become the bridge.  This
       PC needs 256K of memory.

    3) Create a bootable Floppy and put BRIDGE.EXE on it.  Create
       and AUTOEXEC.BAT file that executes BRIDGE.EXE.

    4) Hook up the cables and turn on the PC.

That's it. PCbridge does the rest.   If the bridge does not work, see
trouble.doc.

-------------------------------------------------------------------------

Installing the standard 3Com ethernet-ethernet bridge:

The PCbridge distribution comes with a two interface ethernet bridge
for the 3c507 cards.  This file is named 3c73c7.exe. To use it simply

    1) Rename it to 'BRIDGE.EXE'.

    2) Use the 3c507.exe file that came with the 3c507 cards to set
       the  first card to
                I/O address to 280H, 
                Shared memory address to D0000H
                Shared memory length to 64K
                Interupt to some unused IRQ (say 3)
                ROM disabled (length = 0)
                0-wait state to enable if you PC can handle it 
                    (most fast clones can, you may want to disable
                     it at first if you are not sure) 

        and the second card to
                I/O address to 2A0H, 
                Shared memory address to C0000H
                Shared memory length to 64K
                Interupt to some unused IRQ (say 3, (it can be the same)) 
                ROM disabled (length = 0)
                0-wait state to enable if you PC can handle it 
                    (most fast clones can, you may want to disable
                     it at first if you are not sure) 
       
        Note because of the way the 3c507.exe program works, you can 
        only have one 3c507 card in the PC when you are configuring it.
        Thus you have to configure one card, replace it with the other,
        configure that one, and only then place both cards back in the
        PC.  

    3) Install these cards in the PC that will become the bridge.  This
       PC needs 256K of memory.

    3) Create a bootable Floppy and put BRIDGE.EXE on it.  Create
       and AUTOEXEC.BAT file that executes BRIDGE.EXE.

    4) Hook up the cables and turn on the PC.

That's it. PCbridge does the rest.   If the bridge does not work, see
trouble.doc.

-------------------------------------------------------------------------

Installing the Starlan cards with the standard distribution:

The standard WD8003E program can be used for a starlan-starlan or
starlan-ethernet bridge (if WD8003E cards are used for the ethernet
side).   Simply treat a starlan card like an ethernet card in the
instructions above.  Note, however, that it is really recommended that
a WD8003EBT is used for the Ethernet side (if a starlan-ethernet
bridge is desired).  This configuration, however is not supported by the 
standard distribution, PCbridge will have to be recompile.  See
compile.doc for details.

-------------------------------------------------------------------------

Installing the standard ethernet-serial-ethernet bridge:

PCbridge also comes with a file called REMOTE.EXE which is designed 
to do remote bridging.   The  expected configuration is to have 
two PCs with an ethernet and a COM port on each one.  The PCs are
then connected via a serial line.  The PCs will then bridge packets
between the far ethernets.  The standard distribution is designed
to work with the WD8003E card.  Although the other cards (WD8013EBT
and WD8003EBT) will work too, the extra buffer space of these cards
is not used.  Thus it is recommended that you configure and recompile
a special version if you use these cards in the remote bridge.


    1) Rename the proper file to 'BRIDGE.EXE'.

    2) Set the I/O address of both to WD8003E cards to 280H (the default). 
       You can leave the IRQ line on the default of 3 (but make sure it
       is NOT 4, since that is what the COM1 board uses).  

    3) Set each of the serial boards to be COM1.  (I/O = 3F8H, IRQ=4)

    4) Install one serial board and one WD8003E board in each PC.

    5) Create two  bootable Floppies and put BRIDGE.EXE on each.  Create
       on each floppy an AUTOEXEC.BAT file that executes the command
       
            BRIDGE <baud rate>

       where <baud rate> is the baud rate of the serial line (9600, 19200 etc).
       If no baud rate is given, 19200 is the default.
                
    6) Hook up the cables and turn on both PCs.

That's it. PCbridge does the rest.   Note that since EVERY broadcast
and multicast packet on BOTH networks has to be forwarded through the
serial line, the remote bridge will only work well for networks that
have little broadcast traffic (certainly less than 1 broadcast/sec).

Normally PCbridge assumes that it may always send a character down the
serial line (no flow control).  If you are using a compressing modem,
this assumption is no longer correct.  PCbridge can be configured to
understand hardware flow control (that is only send characters when
the RS232 signal CTS is asserted).  To enable this feature, however
the sofware must be recompiled.  See compile.doc for details on how
to do this.