Yamaha DX100 Editor/Librarian



     Features:

     -  Full featured Editor/Librarian for the Yamaha DX100
     -  The Librarian makes it easy to organize and store a bank
        of voices on disk.  Send your customized banks to the DX100
        or receive banks from this instrument.  Easy audition of voices,
        simply click the mouse on a voice name and "play" the Amiga
        keyboard.
     -  The Editor has the power to edit all parameters for DX100 voices.
        It provides graphical display of voice envelopes, an Undo button
        to correct mistakes, and convenient saving of changes made
        during the editing process.  The voice audition feature makes
        it easy to compare the "original" and "modified" voice.  For
        interesting effects use the Randomize feature to create random
        voice envelopes.
     -  Print hardcopy of voice banks.  Print out all DX100 voice
        parameters.
     -  Fully compatible with the Yamaha DX27 and the DX21
     -  AmigaDOS 2.0 compatible


        This is a ShareWare program.  If you like it and find it useful,
     please send me $30.  If you can't afford this, I'll gladly accept
     any contributions you would like to make.
        A hi-res version of this program that uses a 640 by 400 pixel
     screen is available upon request with the $30 contribution.  This
     version looks great on an Amiga 3000.



     James M. Smith
     P.O. Box 6836
     Los Osos, CA
     93402



                              Instructions

     Getting Started
      
         With the power off on the Amiga and the DX100, connect the
     DX100 (DX27 or DX21) to a standard MIDI conversion box that uses
     the Amiga serial port.  Since the DX100, DX27 and DX21 are software
     compatible this instruction booklet will only mention the DX100. 
     The MIDI-out on the conversion box connects to the MIDI-in on the
     back of the DX100.  The MIDI-in on the conversion box connects to
     the MIDI-out on the DX100.  Connect the audio output on the DX100
     to a sound system.  After turning on the power to the DX100 and the
     Amiga, set the DX100 MIDI On/Off switch to On using the front panel
     buttons.  Set the DX100 transmit and receive MIDI channel to one
     and turn On the MIDI System Exclusive Information.  The DX100 is
     now ready to communicate with the Editor/Librarian, which by
     default is set for MIDI channel one for basic MIDI events and
     system exclusive messages.  The MIDI channel used by the
     Editor/Librarian and the DX100 does not have to be channel one. 
     From the "Play Voice" menu section one of four possible MIDI
     channels can be selected.  But it is essential that the DX100 and
     the Editor/Librarian are set to the same MIDI channel.

          When the Editor/Librarian is first started a listing of the files
     on the volume where this program resides will be given.  Change ":"
     to "df1:"to list the files on drive df1: if required.  The following 
     instructions will lead you by your hand through the operation of this
     program.  If you don't like following instructions, go ahead and play
     with this program on your own.  You will probably be able to figure out
     how to use this program by yourself. 


     Opening a Voice Bank

         The directory of the DX100 Program Disk will show the
     subdirectory, Voice_DX100, displayed in red.  A listing of this
     Voice directory is obtained by single clicking on the word
     Voice_DX100.  This directory contains the eight factory voice banks
     that come with the DX100 and a Demo bank.  Open the FactoryN1 bank
     by clicking on it to obtain a listing of its voices.  Try playing
     with the slider gadget on the right of the listing in order to move
     the display through all 32 voices.  Note that only the first 24
     voices contain meaningful data for the DX100.  The DX21 will
     utilize all 32 voice positions in the bank.  
 
         Voice listings can be moved to the right side of the Librarian
     Window by clicking on the "Move > Bank" button.  Try this now.


     Deleting Voices

         Click on the "Parent Dir" button to get back to the listing of
     the factory voice banks.  This button is used to move up the directory
     tree, to obtain a parent directory listing.  This time click on the
     Demo bank to display its voices.  The Voice Librarian Window will
     now show the Demo bank on the left and FactoryN1 on the right.  
 
         Click on a couple of the voices in the Demo bank, and note that
     their names change to red.  Click on the "Delete Voice" button to
     delete these voices.  All voices shown in red will be deleted after
     this button is activated.  Be very CAREFUL using the "Delete Voice"
     button.  Once a voice has been deleted, it cannot be recovered.  Do
     not delete any voices in the Factory banks.  These banks are the
     backbone of a DX100 voice library.  

         The "Delete Voice" button can also be used to totally erase a
     voice bank.  If this button is selected for a bank in which all
     voices have been previously deleted, then the voice bank file
     itself will be erased and will no longer show up in a directory
     listing.  
     
     
     Copying Voices
     
         Now try copying a voice from FactoryN1 over to the Demo bank. 
     First select a voice in FactoryN1 by clicking on a voice name.  Then
     click on the "Copy Voice" button and select with the mouse an empty
     voice location in the Demo bank.  The voice will be copied to the
     empty location selected in the Demo bank.  

         Try clicking on several voices in FactoryN1 before activating
     the "Copy Voice" button.  Then click on an empty voice location in
     the Demo bank and note that all the voices selected will be copied
     to the Demo bank.  The lowest numbered voice selected will be
     copied to the empty location chosen, and all other selected
     voices will be copied to empty locations below this point.

         So far copying voices from one voice bank to another has been
     discussed.  To copy voices within a particular voice bank, place
     the bank of interest on both the left and right side of the
     Librarian Window and copy exactly as previously described.  As an
     example, select the "Move > Bank" button so that the Demo bank is
     displayed on both sides of the Librarian Window.  Select a voice on
     the left display.  Activate the "Copy Voice" button and select an
     empty voice location on the right display.  The voice selected
     will be copied to the empty location within the Demo bank.

         The "Copy Voice" button will work even if the voice banks
     displayed on the left and right side of the Librarian window have
     not come from the same directory or even the same disk.  As an
     example of how this might work, let's assume that the DX100 Program
     Disk resides on drive df1: and that some voice banks have been
     copied to a ram disk.  After opening a voice bank from the DX100
     Program Disk and having moved this bank to the right side of the
     Librarian window using the "Move > Bank" button, a directory of the
     ram disk is obtained by entering ram: into the Disk box.  After
     opening a voice bank on the ram disk, it is then possible to copy
     voices back and forth between the two banks even though the voice
     banks come from two different disks.

     
     Auditioning Voices
  
         In order to audition voices the MIDI Port must be activated by
     selecting "MIDI Port Active" from the "Play Voice" Menu section. 
     Do this now.     

         The selection of "Auto Send Active" or "Auto Send Off" from the
     "Play Voice" Menu section will have an important effect on the way
     voices are auditioned.  "Auto Send Active" is the default mode and
     probably will be used by most people nearly all the time.  In this
     mode, individual voice data is sent to the DX100 immediately after
     the mouse clicks on a particular voice.  With "Auto Send Off"
     selected, voice data is not sent to the DX100 until the ENTER key
     is pressed or "Send Voice" is selected from the "Play Voice" Menu
     section.  The "Auto Send Active" mode is more convenient to use for
     auditioning voices.  But when copying and deleting voices is the
     main focus of activity, sending voice data to the DX100 whenever a
     voice is selected can be a nuisance.  On these occasions use the
     "Auto Send Off" mode.  

         After selecting a DX100 voice with the mouse, use the Amiga
     keyboard or the DX100 keyboard to audition its sound.  The Amiga
     keyboard will produce "white key" notes over a five octave range,
     with middle C produced by hitting the keyboard key, Q.  The notes
     from the "black keys" on a piano keyboard are not produced.  Eight
     notes may be played simultaneously.  
     

         Using an External Keyboard
 
             When editing voices it is sometimes useful to use an
         external keyboard with touch sensitivity.  To use an external
         MIDI keyboard with the Editor/Librarian, disconnect the end of
         the MIDI cable at the MIDI-out on the DX100 and reconnect to
         the MIDI-out on the external MIDI keyboard.  The other MIDI
         cable remains unchanged.  Turn off the power on the Amiga, the
         DX100, and the external keyboard before making this change. 
         With this new hookup it will not be possible to receive voice
         banks from the DX100.  After following the above instructions
         for auditioning voices, select "Status Connected" from the "Ext
         Keyboard" Menu section to inform the Editor/Librarian of this
         change.  Activate the external keyboard by selecting Activate
         from the "Ext Keyboard" Menu section or by pressing the arrow
         up key on the Amiga keyboard.  The external MIDI keyboard will
         now send MIDI data to the DX100.  Turn off the external
         keyboard by hitting any key on the Amiga keyboard.  
     
     
     Sending and Receiving Voice Banks

         Sending a Voice Bank to the DX100 is accomplished by selecting 
     "Send Bank" from the Transfers Menu section.  The active voice
     bank, which is the opened bank with its title displayed in red, is
     sent to the DX100.  All data previously stored in the DX100 in the
     Internal Bank will be lost.  Therefore be CAREFUL when sending
     voice banks to the DX100.  

         Receiving the Internal Voice Bank is accomplished by selecting
     "Receive Bank" from the Transfers Menu section.  At least one voice
     bank must be opened to establish which voice bank directory is
     being used so that the received data will be filed in the proper
     directory.  The user is free to create as many directories as
     needed for storing voice banks.  If the right side of the Voice
     Librarian is displaying a voice bank, the Librarian will use the
     directory from this bank.  Otherwise the directory that holds the
     left bank of voices will be used.  The received voice bank is
     displayed on the right side of the Voice Librarian Window with the
     bank name given by the string entered in the Bank box.  If no
     string was entered into the Bank box, the name of the received bank
     file becomes NoName.  Be very CAREFUL about naming the received
     bank so that another bank with the same name in the same directory
     will not be lost.  

         If a number of other programs are running concurrently with the
     DX100 Editor/Librarian, the Amiga may not be able to keep up with
     the high speed data sent out from the DX100 during a Voice Receive
     Transfer.  An error message will indicate if a problem has occurred.
     Remember also that receiving voice banks is not possible when an
     external MIDI keyboard is connected.  


     Select All and Create Bank buttons

         The "Select All" button selects all voices in a bank, and
     displays the names of these voices in red.  To delete all voices in
     a bank, select the "Select All" button before activating the
     "Delete Voice" button.  
 
         The "Create Bank" button creates an empty bank file with the
     name given by the string entered in the Bank box.  At least one
     voice bank must be opened so that the created bank will be filed in
     the proper directory.  If no name has been entered into the Bank
     box, a bank called NoName is created.  The empty bank will be
     displayed on the right side of the Librarian Window.  Be very
     CAREFUL about choosing a name for a created bank, because any other
     existing bank with the same name in the same directory will be
     lost.  


     Editing Voices

         Before editing a voice make sure that the "MIDI Port Active"
     menu has been selected so that voice changes can be auditioned. 
     The Voice Editor Window is opened by first clicking on a voice and
     then selecting the "Edit Voice" button.  All the parameters that
     define the characteristics of the selected voice are shown in the
     Voice Editor Window.  These parameters are changed by clicking on
     the displayed values.  Some values will change immediately.  Others
     will require the user to enter the new numeric value into a string
     gadget.  Since all the string gadgets are empty except for the Name
     gadget, simply enter the new value using the number pad on the
     keyboard and hit the ENTER or RETURN key.  Use the DEL and "BACK
     SPACE" keys as needed to correct a mistake before the ENTER key has
     been pressed.  
   
         A good description of the function of all the DX100 voice
     parameters is given in the DX100 instruction manual.  For additional
     information consult the Yamaha publication, "AfterTouch".
     Write to AFTERTOUCH, P.O. Box 7938, Northridge, CA 91327-7938.  
     The layout of the Voice Editor Window will now be discussed.  

         The Voice Editor Window is divided into four main sections and
     the three color coded blocks on the far left define the parameters
     used by the four operators in the DX100.  The red block lists the
     following operator parameters:  on/off, output level, frequency,
     frequency ratio and detuning.  The numbers in the red block
     represent the maximum values that particular parameters are allowed
     to take.  The green block lists the five segments of the operator
     envelope which are the attack rate, the first decay rate, the decay
     level, the second decay rate, and the release rate.  The blue block
     lists the scaling and sensitivity parameters which are the rate
     scaling, level scaling, AMS on/off, EG bias sensitivity, and
     velocity sensitivity.  The values for all these parameters are
     changed by clicking on the numbers in the four operator columns
     next to these blocks.  If the CTRL key is held down while the mouse
     clicks on an operator value, any changes made to a particular
     operator will apply to all four operators.  For the string gadgets,
     release the CTRL key before entering a new number.  This is a fast
     way to change all operators to the same value.  
  
         On the upper right side of the Voice Editor Window is an orange
     block that contains the name of the voice, the algorithm used by
     the four operators, and the feedback employed in the fourth
     operator.  The LFO settings are given in the blue block.  They are
     the LFO delay, the LFO sync on/off, the waveform select (sawtooth,
     square, triangle and sample/hold), the LFO speed, the amplitude
     modulation sensitivity and depth, and the pitch modulation
     sensitivity and depth.  The yellow block lists a number of
     functional parameters.  They are the playing mode (poly or mono),
     the portamento mode, the portamento time, the foot switch setting,
     the modulation wheel controller amplitude and pitch, the amount of
     transpose, the pitch bender range, and the breath controller
     amplitude, pitch, EG bias and pitch bias.  
     
     
          Displaying Voice Envelopes
     
              To graphically display the envelope for each operator for
          a note at middle C, select Display from the Envelopes Menu
          section.  The envelopes are displayed such that the Off Point,
          when the key is released, represents approximately three
          seconds after the key was initially activated to play the
          note.   
                       
              To close the envelope display window, click on any part of
          this window.
     
     
          Auditioning Edited Voices
             
              In the orange block click on the number after the word
          "Algor" to change algorithms.  If "Auto Send Active" was
          selected before entering the Voice Editor Window, the modified
          voice data is automatically sent to the DX100.  Simply "play"
          the DX100 keyboard or the Amiga keyboard to audition the new
          voice.  If "Auto Send Off" had been chosen, send the modified
          voice data to the DX100 by selecting "Send Voice" from the
          "Play Voice" Menu section or by pressing the ENTER key on the
          keyboard.  

              To audition the original unmodified voice again, select
          "Select Original" from the "Play Voice" Menu section or press
          the left pointing arrow key on the keyboard.  The keyboard
          will now play the unmodified voice.  To audition the modified
          voice select the "Select Modified" Menu or press the right
          pointing arrow key.  Toggling back and forth between the
          modified and original voice is especially easy using the arrow
          keys as described. 
         

          Undo Mistakes
          
              Select Undo from the Project Menu section to cancel the
          last change made to the voice parameters.  Pressing the HELP
          key will accomplish the same result.
          
 
          Randomize Envelopes
         
              Select Randomize from the Envelopes Menu section to
          randomize the five parameter envelope for the four operators. 
          The rate scaling parameter is also randomized.  This is
          sometimes an interesting way to create new voices.  The new
          voice parameters are automatically sent to the DX100 if "Auto
          Send Active" had been selected before entering the Voice
          Editor.  Just "play" the keyboard to audition the randomized
          voice.  If "Auto Send Off" had been activated, the menu "Send
          Voice" must be selected or the ENTER key pressed before the
          randomized voice data is sent to the DX100.  Another way to
          select the Randomize feature is to press the ALT key on the
          right side of the keyboard.  


          Saving Voice Data
   
              Select Save from the Project Menu to save the changes
          made to the selected voice that is currently being edited. 
          The new parameters will replace all the old values for this
          voice.  The new voice will now become the "original" voice
          that will be sent to the DX100 when the "Select Original" Menu
          is selected.  

              The "Save Fwd" Menu selection, which stands for Save
          Forward, works quite differently than Save.  This selection
          will copy the new voice parameters to the first empty place in
          the voice bank immediately following the selected voice.  The
          original selected voice will not be modified in any way.  If
          there are no empty locations after the selected voice, the
          "Save Fwd" feature will not work and the user will be notified
          of this.  The "Save Fwd" selection provides a convenient means
          of saving various changes made to the original voice without
          changing the selected voice itself.  
          
          
          Printing Voice Data
          
              Selecting Print from the Project Menu will print all of
          the voice parameters that have been saved with the Save menu
          selection.  The printer will follow the settings in
          Preferences which must be present on the user's Workbench
          Disk.  

 
          Special Keyboard Key, the CTRL key
     
              Use the CTRL key to change all four operator parameters
          simultaneously.  See the section "Editing Voices" for more
          information.  

               
          Alternate Keyboard Keys

             There are six keys that can be used in place of menu
          selections.  These keys have already been discussed but will
          be summarized here.  
   
                  Keyboard Key                 Menu Selection
          
                  ALT (on right side)          Randomize
                  Left Pointing Arrow          Select Original
                  Right Pointing Arrow         Select Modified
                  Up Pointing Arrow            Activate Ext Keyboard
                  ENTER                        Send Voice
                  HELP                         Undo 
               

          Exiting the Voice Editor Window
   
              Select Exit from the Project Menu.  The Voice Librarian
          Window will again open.  
   
   
     
     Printing from the Voice Librarian
     
         Selecting Print from the Project Menu will print all of the
     names of the voices in the active voice bank, which is the opened
     bank with its title displayed in red.  
         
     
     Quitting the Voice Librarian

         Select Quit from the Project Menu section to quit the DX100
     Editor/Librarian.
     
     

     JAMES M. SMITH MAKES NO WARRANTIES, EITHER EXPRESS OR IMPLIED, WITH
     RESPECT TO THIS MANUAL OR WITH RESPECT TO THE SOFTWARE DESCRIBED IN
     THIS MANUAL, ITS QUALITY, PERFORMANCE, MERCHANTABILITY OR FITNESS
     FOR ANY PARTICULAR PURPOSE.