***********************************************************************
*                                                                     *  
*             Welcome to the the digital world of MIDI                *
*                                                                     *     
*                                                                     *  
*                 Roland_S-220 is a freeware program                  *
*                                                                     *  
*                   Copyright (c) 1989 Dieter Bruns                   *
*                                                                     *
*                                                                     *  
*  ( NO commercial use without written permission of the author )     *
*                                                                     *  
***********************************************************************


What's the reason for this software ?
-------------------------------------

The built-in 2.8'' drive of Roland S-220.



What does this software ?
-------------------------

Samples of Roland S-220 are transfered to and from AMIGA.
So you can use 3.5'' disks for saving samples.


Hardware connections :
----------------------

This program works in handshake mode.

Therefore it's necessary to 

- connect MIDI-IN (Roland) with MIDI-OUT (Amiga-MIDI-interface)

- connect MIDI-OUT (Roland) with MIDI-IN (Amiga-MIDI-interface)


Environment of ROLAND :
-----------------------

- switch EXLUSIVE = ON !!!!


Usage of Sample-Dump :
--------------------

serial.device must be in drawer devs !

Set MIDI-channel !!!!!

Sample-Dump switches automatical in BULK-DUMP-MODE,

if samples are requested or transmitted.


If Roland and AMIGA are working on different MIDI-channel

press F1 MIDI at Roland to cancel BULK-DUMP.  


address :

Dieter Bruns                  Dieter Bruns
Lilienweg 131        or       Rebenring 63/0521
2725 Hemsbünde                3300 Braunschweig
WEST-GERMANY                  WEST-GERMANY