THE SYNTHETIC SOUND EDITOR
		*==========================*


This  is the editor, which is used to design simple pieces of waveforms and
to  "program"  the  volume  and pitch altering sequences.  Synthetic sounds
don't  take  much memory (that's the main advantage of them).  They can use
the  whole  5-octave  range.   Although they are quite simple, they usually
sound quite "cool" (and remind me of the good old C-64).

Getting started
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
First load MED, select the Instr-panel, click the Synth-gadget to initialize
a  new synthsound.  Then click the Synth-display selection gadget to display
the  synthsound  editor.  Please turn editing off.  You can play the current
sound with keyboard, like ordinary samples.

Waveform editing
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
There  are  two  waveform  displays,  the  left one is the "master waveform
display" and the right one is for intermediate editing (it also serves as a
copy  buffer).   Between  the  waveform displays are some gadgets, that are
used for transferring waveforms between displays.

First  there  are two copy gadgets.  If you press the left copy gadget, the
right waveform will be copied to the left one (and vice versa).  Gadget "<-
EXCHANGE ->" exchanges the waveforms on the left and right.  "<- MIX" mixes
the left waveform to the right waveform.  It is a powerful tool that can be
needed  quite often.  "<-ADD" is similar to the mix, but it doesn't produce
any  average between the wforms (= waveforms, from now on).  The wforms are
simply  added together.  It's possible, that the waveforms exceed the upper
and  lower  limits  (in  that  case,  they  are  truncated).  Two "<- EDIT"
"EDIT->"  gadgets  allow  you to select either of the displayed wforms as a
current  waveform, which is then used in some editing functions.  Sometimes
they're  automatically  set  (when  you  draw  the  wform  with  mouse, for
example).   "UNDO"  undoes  your  last  editing operation.  It can be quite
useful.   "RANGE  ALL"  selects  the  current  wform,  so  that any editing
operations affect the whole wform.

Freehand drawing
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
A  very  simple way to create wforms is to draw them from scratch.  This is
easily  done.   Just press the left mouse button and draw...  There are two
drawing  modes.  The default is "pixel".  The other is "line".  This can be
used  for  drawing  straight lines.  There's also a mix-mode, that works in
both  "line"  and  "pixel" -mode.  It mixes the drawed pixels or lines with
the already existing data.  Mode-selection gadgets are located below "RANGE
ALL".

Waveform length
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
Each  waveform  in  synthsound  can be 2 - 128 bytes long (it must be even,
though).   The  shorter the waveform, the higher the pitch (it also depends
on  the  wform itself).  Usually, to make the pitches compatible with other
instruments,  you should use length 2, 4, 8, 16, 32, 64 or 128.  The length
can be changed with "LEN:" gadgets below the left wform, by typing in a new
value or by clicking the single-step gadgets.

Multiple waveforms
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
Each synthsound can consist of more than one wform (the maximum is actually
64). On the left, below the left wform, there's a set of gadgets:

curr. wform #
   |
   0  < > / 00
      |/    \|
next/prev    number of the last waveform

The arrow gadgets select the next/previous waveform. As this is a operation
that is needed often, there are keyboard shortcuts:
	Alt-cursor left  = previous
	Alt-cursor right = next

There are two Add gadgets that allow you to increase the number of waveforms.
"Last" adds a new waveform after the last wform.
"Here" inserts a new wform here, and shifts the others.

Del gadgets:
"Last" deletes the last wform.
"Here" deletes the current wform.

Preset waveforms
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
There  are some simple, often needed preset waveforms available at a single
click.   First  make  sure, that the destination wform is the current wform
(selected  with  the  EDIT  <-/->  gadgets).   Then  just  click the preset
waveform icon.  The icons are located at the bottom of the editor.

The available waveforms are: sine, saw up/down, pulse, random and triangle.
The CLR-gadget clears the current wform.
The ALL-gadget clears the whole synthsound (so be careful..)

Range operations
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
These  are  some  basic  operations, that are applied to the selected range
(highlighted  white).   You can select the range by dragging the mouse over
the wform with the right mouse button down.  You can select the whole wform
by  clicking  "RANGE  ALL".  The Range start/Range end gadgets at the lower
right corner of the synthsound editor can be used to make small corrections
to the area.

When  there's  no  range  selected, there's a single horizontal white line.
This  is the cursor.  Some editing operations need it.  The cursor position
can be set by clicking the right mouse button on the wform area.  There are
also  three  narrow  gadgets  (on the left of the preset wform gadgets) for
positioning the cursor:

cursor to     cursor to end
start   |     |
	<  +  >
           |
      cursor to the middle (of the wform)

On the middle of the screen, there's a word "RNG", followed by a strip of
gadgets:
	RNG  Cut  Copy  Paste  Clr  Dbl  Rev  <  >

Cut	(works only on left wform). It "cuts" the selected area, which is then
	moved to the right wform display.
Copy	copies the selected range to the right wform, but doesn't cut it away.
Paste	copies the contents of the right wform to the position pointed by
	the cursor.
Clr	clears the range.
Dbl	"doubles" the range, making it play one octave higher.
Rev	reverses the range.
< or >	shift the ranged data to left or right.

There are two other editing operations: stretch and volume change.

Stretch allows you to stretch a point of the wform towards some other point
(understand?? no?? then try this:)
For example, select a sine wave.  Then position the cursor on the middle of
the  waveform (there's a gadget for this purpose, see above).  Now activate
the  "STRETCH:"-gadget  (on  the  left  lower corner of the synthsound ed).
Type  in the amount of moving, e.g.  32.  This should demonstrate it...  If
the number you type in is negative, the point is stretched to left.

Volume change allows you to increase/decrease the volume of selected range:
First  select  a range.  Then activate the "VOL.CHG:"-gadget.  Now you must
enter  the  amount  of  volume  change (in %'s).  For example, to halve the
volume,  you  should  type 50.  If you want to double the volume, type 200.
The volume will be changed when you press Return.

Transformation
¯¯¯¯¯¯¯¯¯¯¯¯¯¯
This  is  quite  a powerful feature.  It allows you to change a waveform to
another  smoothly (by creating the waveforms between them).  Demonstration:
Allocate 9 new waveforms (click Add/Last 9 times).  Now you have 10 wforms.
Move  to  wform  00,  and select a pulse waveform, for example.  Then click
Transform:   Start  to mark the beginning of transformation range.  Move to
wform 09 (the last one).  Put here a sine wform.  Click Transform:  Do, and
the  magic  is  done.   If  you view the wforms 01 - 08, you'll notice that
there's  now  a  smooth  transition  from  the pulse wave to the sine wave.
-----------------------------------------------------------------------------

THE PROGRAMMING LANGUAGE
========================

Note: please read this section carefully before experimenting, because you
      can lock up your machine with the synthsound programming language (as
      with any other language)

The  programming language is used for controlling the volume/pitch/vibrato/
waveforms/arpeggio/etc...    of  the  synthsound.   It  consist  of  simple
keywords, of which some have an argument.

The  programming  is done using two lists of commands/numbers.  These lists
are  displayed  through  a  small  window below the right waveform display.
First  there  are  line  numbers in decimal and hex (two leftmost columns).
The  middle column contains the volume sequence, while the rightmost is the
waveform/pitch sequence.

       volume ctrl seq
          |
line      |    waveform ctrl seq
  |       |    |
  00 00   40   00
  01 01  END  END

These  lists  are  both  max.   127 ($7F) entries long.  The list is always
terminated  with  "END"  instruction (it's automatically there so you don't
have  to do that).  You can scroll the list with cursor up/down -keys.  The
cursor  can be moved horizontally using the cursor left/right -keys.  There
are  six  possible  cursor  locations  (3  for  both lists).  When entering
commands,  the  cursor  should  be  on  the leftmost position of that list.
Values  are entered by pointing the cursor over the value to be changed and
entering a new value.  Commands and numbers are entered with keyboard.  You
can   insert   entries  to  the  list  with  the  Return-key  (or  clicking
Ins-gadget),  and  delete using Del (or clicking Del-gadget).  JMP commands
are renumbered when entries are inserted or deleted.

ALL NUMBERS IN THE SEQUENCE LISTS ARE HEXADECIMAL.
Just remember this, and you have no problems (fingers crossed :^)
Also, the editing (Esc) must be on before the lists can be changed.

First, let's examine some example sequences:

This is a volume sequence:
	
	00  40 <= set initial volume to 64 (hex $40, did you already forget?)
	01 CHD <= command, that means "Set volume change down speed"
	02  03 <= argument (speed = 3)
	03 END

Here's another:

	00  00 <= initial volume = 0
	01 CHU <= Command: Set volume change up
	02  07 <= speed = 7
	03 WAI <= Command: Wait
	04  10 <= wait 10 pulses
	05 CHU <= Set volume change up
	06  00 <= speed = 0 -> stop changing volume
	07 WAI <= Wait
	08  70 <= 70 pulses
	09 CHD <= Cmd: Set volume change down
	0A  01 <= speed = 1 (slow)
	0B END

Third:

	00  40 <= vol = $40
        01  30 <= vol = $30 (without command, the values are volume changes)
	02  20 <= vol = $20
	03 END

And fourth, finally:

	00  40    <= vol = $40
	01 CHD <+ <= change down speed..
	02  01  | <= ..= 1
	03 WAI  | <= Wait..
	04  20  | <= ..20
	05 CHU  | <= change up
	06  01  | <= ..1
	07 WAI  | <= Wait..
	08  20  | <= ..20 again
	09 JMP  | <= Jump (= goto)
	0A  01 -+ <= to line number 01
	0B END

Now some wform/pitch sequences. Wform/pitch sequence is the "mastersequence"
while the volume sequence is a kind of "slave sequence".

First: (the simplest case)
	00  00 <= set waveform #00
	01 END

A bit more complex:
	00 VBS <= set vibrato speed
	01  40 <= speed = $40
	02 VBD <= set vibrato depth
	03  02 <= depth = 2
	04  00 <= waveform #00
	05 END

And very complex:
	00 ARP <= start arpeggio sequence
	01  00 \
	02  03  arpeggio values 0, 3, 7 (minor chord)
	03  07 /
	04 ARE <= end arpeggio sequence
	05 VBD <= vibrato depth
	06  06 <= 6
	07 VBS <= vibrato speed
	08  40 <= $40
	09  00 <= set waveform #0
	0A  01 <= set waveforms 01 - 0A (one timing pulse/waveform)
	0B  02    | |
	0C  03   \   /
	0D  04    \_/
	0E  05
	0F  06
	10  07
	11  08
	12  09
	13  0A and back to #01...
	14  08
	15  07
	16  06
	17  05
	18  04
	19  03
	1A  02
	1B  01
	1C JMP <= jump
	1D  09 <= to position 09 (restart waveform changing)
	1E END

-----------------------------------------------------------------------------
You can learn a lot by examining the example synthsounds and by
experimenting.

Now, some reference...

About timing
¯¯¯¯¯¯¯¯¯¯¯¯
For  both  sequence  lists, most of the commands are fetched, executed, and
the next command is immediately fetched.  There are also some commands that
wait  for  the  next  timing  pulse, this is important because the computer
would  otherwise  send all its time executing the sequence lists (and would
hang  up).   You  should  take  care that all loops contain a command, that
waits  for  the  next timing pulse.  These commands are WAI (Wait), vol chg
(plain  number  in  the  volume  list)  and  set  waveform (plain number in
pitch/wform list).

For example, the following loops will hang up your computer:

	00 JMP		00  CHU <-+ command CHU doesn't wait
	01  00		01   02   |
        ...		02  JMP   |
			03   00 --+

While the following would not:

	00  20		00  WAI
	01 JMP		01   02
	02  00		02  JMP
			03   00

Execution speed
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
The synthsound handling routine is called once every interrupt.  This means
that  the  handling  is  usually  done  6  times/note  (can be changed with
secondary  tempo, see main docs).  Both lists have an execution speed, that
is  the  speed  of the operation.  When the speed is 1, the next command is
fetched/pitch  changed  etc.   on  every interrupt.  If the speed was 2, it
would  happen  every second interrupt (runs two times slower).  The initial
execution  speed  can be set with the two speed gadgets.  During executing,
the speed can be changed with command SPD.


VOLUME SEQUENCE LIST COMMANDS
=============================

1.	Set volume
	Command: ---
	Keyboard: --- (key needed to enter the command)

	This is the default command (no command identifier). It sets the
	absolute volume of the synthsound. It should be 00 - 40. Note that
	the relative track volumes are not used in synthsounds (mostly
	because of performance reasons).

	Example:
	00  30 ;volume = $30
	01  10 ;volume = $10
	...

2.	End sequence
	Command: END
	Keyboard: ---

	This command terminates the volume sequence list. It's always there
	and automatically inserted. You can't insert commands past this one.

3.	Set volume change down speed
	Command: CHD
	Keyboard: D

	This command sets the speed, in which volume is decreased each timing
	pulse. The volume starts changing automatically after this command.
	To stop automatic volume sliding, issue this command with speed 00.

	Example:
	00  CHD
	01   05 ;speed = 5
	...
	10  CHD
	11   00 ;speed = 0 -> stop sliding

4.	Set volume change up speed
	Command: CHU
	Keyboard: U

	This command is like CHD, except it sets the volume change up.

5.	Wait
	Command: WAI
	Keyboard: W

	This command waits for specified amount of timing pulses (pause).

	Example:
	03  WAI
	04   10 ;wait for 16 ($10) pulses to occur

6.	Jump
	Command: JMP
	Keyboard: J

	Causes an immediate jump to another position of the volume list.

	Example:
	05  JMP
	06   0A ;jump forward to line 0A

7.	Jump waveform sequence
	Command: JWS
	Keyboard: Shift-J

	This command causes a jump in the waveform sequence. This can be used
	for example, to trigger a pitch change at the end of the vol seq
	list. Note that this DOESN'T cause a jump TO waveform sequence.

	Example:
	04  JWS
	05   0F	;Cause jump in waveform sequence list


8.	Halt
	Command: HLT
	Keyboard: H

	This has the same effect with command END (halt execution), but it
	can be inserted in the middle of the sequence list.

	Example:
	03  HLT
	04   04 ;some other code (can be accessed with JMP instruction, for
	...	 example)

9.	Set speed
	Command: SPD
	Keyboard: S

	Sets the execution speed.

	Example:
	0A  SPD
	0B   01 ;speed = 1 (fastest)
	...

(The following commands require OctaMED V2.00 / MED V3.20 or later.)

10.	One-shot envelope
	Command: EN1
	Keyboard: E

	This command allows you to draw the shape of the envelope with the
	mouse. When the end of the envelope is reached, nothing occurs.
	02   40
	03  EN1
	04   05
	Waveform 05 is used as an envelope. Note that the envelope execution
	starts on next interrupt, so the volume is initialized to $40.
	The envelope waveform must always be 128 bytes long!!

11.	Looping envelope
	Command: EN2
	Keyboard: Shift-E

	This works like command EN1, except that when the end is reached,
	execution will start again from the beginning.


WAVEFORM/PITCH SEQUENCE LIST COMMANDS
=====================================

1.	Set waveform
	Command: ---
	Keyboard: ---

	This command is used to indicate the waveform number (starting from
	00). After this instruction, the execution stops until next timing
	pulse occurs. Don't use waveform numbers that are higher than the
	actual number of the last wform.

	Example:
	00  00 ;wform 00
	01  01 ;wform 01
	...

2.	End sequence
	Command: END
	Keyboard: ---

	This command terminates the wform/pitch sequence list. It's always
	there and automatically inserted. You can't insert commands past this
	one.

3.	Set pitch change down speed
	Command: CHD
	Keyboard: D

	This command sets the sliding speed for sliding pitch down. The
	sliding automatically starts after this command and stops, when
	speed is set to zero.

	Example:
	00 CHD
	01  03 ;set speed to 3
	...

4.	Set pitch change up speed
	Command: CHU
	Keyboard: U

	Just like previous, but slides pitch up.

5.	Wait
	Command: WAI
	Keyboard: W

	This command waits for specified amount of timing pulses (pause).

	Example:
	03  WAI
	04   02 ;wait for 2 pulses to occur

6.	Jump
	Command: JMP
	Keyboard: J

	Causes an immediate jump to another position of the wform/pitch list.

	Example:
	05  JMP
	06   0A ;jump forward to line 0A

7.	Jump volume sequence
	Command: JVS
	Keyboard: Shift-J

	This command causes a jump to happen in the volume sequence. Can be
	used e.g. for triggering volume changes after some wform event.

	Example:
	09  JVS
	0A   00 ;start volume sequence from the beginning

8.	Halt
	Command: HLT
	Keyboard: H

	This has the same effect with command END (halt execution), but it
	can be inserted in the middle of the sequence list.

	Example:
	03  HLT
	04   04 ;some other code (can be accessed with JMP instruction, for
	...	 example)

9.	Set speed
	Command: SPD
	Keyboard: S

	Sets the execution speed.

	Example:
	0A  SPD
	0B   01 ;speed = 1 (fastest)
	...

10.	Begin arpeggio definition
	Command: ARP
	Keyboard: A

	This command starts the arpeggio sequence. The following values are
	the arpeggio offsets from the base note. The arpeggio sequence
	is terminated with ARE-command. The arpeggio starts automatically
	after the sequence is defined.

	Example:
	03  ARP ;start arpeggio
	04   00 ;offset values
	05   04
	06   07
	07   0A
	08  ARE ;end arpeggio definition

11.	End arpeggio definition
	Command: ARE
	Keyboard: E

	Ends an arpeggio definition. See above.

12.	Set vibrato depth
	Command: VBD
	Keyboard: V

	This command is used to set the vibrato depth (00 - 7F).

	Example:
	02  VBD
	03   04 ;set depth to 4

13.	Set vibrato speed
	Command: VBS
	Keyboard: Shift-V

	This command sets the vibrato speed (00 - 7F). Both speed and depth
	must be nonzero for vibrato to occur.

	Example:
	02  VBD
	03   04 ;depth = 4
	04  VBS
	05   30 ;speed = 30

14.	Reset pitch
	Command: RES
	Keyboard: R

	This command resets the pitch of the note to its initial pitch.

(The following command requires OctaMED V2.00 / MED V3.20 or later.)

15.	Set vibrato waveform
	Command: VWF
	Keyboard: Shift-W

	Sets the vibrato waveform. The argument is the number of wform.
	The waveform should always be 32 bytes long!! Note that it's
	actually played reversed (use the Rev gadget to reverse it).
	By default, sine wave is used.

	Example:
	00  VBD
	01   06
	02  VBS
	03   40
	04  VWF
	05   04 ;use wform number 04 as vibrato waveform

=============================================================================

Synthsound handling commands in the songs:

Command  E  in the songs controls the MIDI pan, if used with MIDI, but with
synthsounds, it is used to trigger a jump in the wform/pitch sequence list.

For  example,  if  you  wanted  to  decrease the pitch of the sound after a
certain point, your wform/pitch sequence could look like this:

	00  VBS
	01   40
	02  VBD
	03   06
	04   00	;play wform 00
	05  HLT
	06  CHD	;pitch changing entry point
	07   02
	08  END

Now you could compose a track like this:

	C-2 3000  ;this is the previous synthsound
	--- 0000
	--- 0000
	--- 0E06  ;cause a jump to position 06 (pitch starts to slide down)
	--- 0000
	...

With command JVS, you could make the command affect volume sequence too.

Hold/Decay:
===========
Hold/Decay  work well with synthsounds too.  The decay value in synthsounds
is,  however,  a  jump address in the volume sequence list.  When the decay
should  start,  the  execution will jump to this entry in the vol seq list.
This means that you can handle the decay on any way you want.  You can also
make it affect the pitch/wforms using the command JWS.

Example volume sequence list:

	00  40	;volume
	01 HLT  ;end
	02 CHD	;decay handling (entry point) -> cause decay
	03  03
	04 END

The decay value for this synthsound should be 2. When you save/load
synthsounds, the decay values are saved/loaded with the instrument.

=============================================================================

Saving/loading synthsounds
¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯¯
Synthsounds  are  saved  using the filerequester panel, "save instr".  They
usually  take  very little disk space.  Synthsounds can be loaded just like
normal samples (filerequester, sample list, typing sample name).

=============================================================================

HYBRID SOUNDS
¯¯¯¯¯¯¯¯¯¯¯¯¯
Hybrid  sounds are much like synthsounds, except that there are no waveform
pieces.   Instead, there's a normal sample.  All commands of the synthsound
handling programming language can be used with hybrid sounds.  There's only
one thing you should know:  Don't use "Set waveform".  Because there's only
a single waveform, there's no need for that (and it wouldn't work anyway).

=============================================================================

	Final note:

Don't  be afraid if you didn't understand everything described in this file
(I  hardly  understand  it myself ;-) All this information is not necessary
for using the synthsounds (only for designing them).