CHAPTER 8   COMMONLY ASKED QUESTIONS                          8-1

Setting Registers
   
Q: Why isn't there a debugger command to modify register settings?

A: You can do so with an immediate assembly language command.  
   For example, to set the AX register to 100 type MOV AX,100 . 
   You can now also set segment registers this way: MOV DS,0  .  
   REMEMBER that if there isn't a leading zero, all constants fed 
   to D86 are assumed to be decimal.  If you want hex constants, 
   supply a leading zero. 


Q: How do you reset the CS register?  MOV CS,value doesn't work.

A: You issue a far JMP instruction to be executed immediately.  
   For example, to set CS to 0 and IP to 400 hex, type JMP 0:0400
   


Modifying Memory
                
Q: Why aren't there commands for changing memory to different hex 
   values, or for filling memory with a given value?
   
A: You can do this very effectively with D86's patch memory mode.
   Just issue an immediate JMP to the location you want modified, 
   press the F7 key to enter patch-memory mode, and then issue 
   any A86 directive to initialize memory: DB for bytes, DW for 
   words, DD for doublewords, etc.  Remember, you have the full 
   power of the A86 language at your disposal.  You can provide 
   lists of values on a single line: 
   
   DW 0100,0101,MY_SYMBOL

   You can make ASCII initializations with strings on DB lines: 
   
   DB 'This is a string',0D,0A,0

   You can use the DUP construct to fill memory with a given 
   value or sequence of values:
   
   DB 100 DUP 0, 10 DUP (1,2,3)           

                                                             8-2
Screen Problems

Q: My debugger screen gets corrupted whenever the program being 
   debugged outputs to the console.  What can I do about it?

A: This problem exists because D86 cannot quickly refresh the 
   screen on computers using the CGA (Color Graphics Adaptor) 
   video interface, without filling the screen with annoying 
   "snow".  So on a CGA computer D86 tries to keep track of what 
   it has output, and refresh only the parts of the screen that 
   have changed.  The strategy fails if the program itself 
   changes the screen.  You can restore a trashed screen by 
   pressing the Alt-F9 key.

   I haven't had the chance yet to implement a more sophisticated 
   screen interface, allowing you to switch between the program's 
   and the debugger's screen.  Until I do, you have these 
   options:

   * You can keep pressing Alt-F9 a lot.

   * If your program is making simple, teletype-style outputs 
     using MS-DOS function calls, you can redirect standard 
     output to your printer for the debugging session.

   * If you're really doing serious development of a heavily-
     video program, you should consider getting a second, 
     monochrome-interface monitor for your computer.  Starting 
     from your CGA display, invoke D86 with the +V option.  D86 
     will come up on your monochrome monitor, but the program's 
     cursor will remain on the CGA monitor.

                                                             8-3
Debugging ROM

Q: I tried stepping into a ROM BIOS routine.  It worked for a 
   while, but when I got to a certain instruction and stepped, 
   the computer crashed.  What's wrong? 

A: My official policy on stepping into ROM is, "all bets are 
   off".  D86 does better than many debuggers at stepping into 
   ROM, but there are still some fairly insurmountable problems.  
   First, D86 itself calls the BIOS.  Not all BIOS routines are 
   reentrant; you could get unfortunate interactions between the 
   call being stepped and calls made by D86 while you are 
   stepping.  Second, ROM cannot be modified and hence traps 
   cannot be set within ROM.  D86 doesn't try to detect failed 
   trap-setting, so the program may be set loose in situations 
   where D86 thinks (and you think) it will retain control.

   This will always happen if you try the F2 key in ROM.  It will 
   also happen if you try to use the F1 key on an instruction that 
   loads a segment register.  For arcane reasons, the single-
   stepping feature built into the 8088 doesn't work on such 
   instructions, so D86 must single-step them with a trap.  Thus, 
   F1 on a segment-loading instruction in ROM will set the 
   program loose.