CDBENCH version 2.4 (C) 1992 Profit Press

CDBENCH reports CD-ROM interface performance information. It will only
operate on the Profit Press MegaDEMO CD-ROM. By operating on only this
CD-ROM (pressed by a single company) more reliable results can be
obtained. The run time of this program can be up to 5 minutes and is
neccessary to produce results that can be measured accurately by the
system timer.

Information on benchmarks

1/3 stroke seek:        The standard for determining the "average" seek
                        time of a drive. This test performs 60 seeks back
                        and forth across the disc.

Random seek:            Performs 60 seeks to a "random" areas of the CD-ROM
                        under the 350 megabyte mark. The seeks are always
                        the same every time CDBENCH is run. (allows for
                        relatively short seek comparisons between drives)

1/3 stroke seek & read: Performs 60 staggered seeks (to defeat caching)
                        over 1/3 of the CD-ROM. After each seek a single
                        2k sector is read. This test will defeat some
                        CD-ROM drives and caching programs that ignore
                        seek commands.

Sustained long read:    Reads 2 megabytes of consecutive sectors off
                        the CD-ROM in 32k blocks. This represents the
                        maximum data rate. Multimedia compatible drives
                        should read more than 150,000 bytes per second.

Sustained short read:   Reads 512k of consecutive sectors in single
                        sector (2k) blocks. This will show how well
                        the buffer or cache in the CD-ROM drive handles
                        small but frequent accesses.

MegaSearch benchmark:   A simulation of common file handling operations
                        used by MegaSearch Retrieval Software and MegaDOOR.
                        This should provide a good indication of relative
                        DOS random access speeds to the CD-ROM.


A database of CD-ROM results will be maintained on the Profit Press BBS.
The phone number is (602)770-0008 and we support 2400-14400 with v.32bis.
If you'd like an ASCII output of your results type CDBENCH <filename>
(preferably a filename that doesn't output to the CD-ROM!). Blanks will
be left in your output file to add information about your CD-ROM and
system configuration. Please upload your results to our BBS!

The table below reflects benchmark results attained from the CDBENCH utility
included on the Profit Press MegaDEMO CD-ROM disc. If a drive is repeated
more than once it's because we received more than one response for it, and
ASCII files are tiny - so we included it.

Results as of 1/26/93 include:

Drive                 1/3 seek  Rseek  Seek/read  Longread   Shortread  MS
------------------------------------------------------------------------------
 0 Toshiba 3201B (8/89)   N/A      N/A    407.5    153903.9   153903.9   32.6
 1 Panasonic CR-501-C   630.95   473.44   501.83   154526.9    89177.9   31.65
 2 Genstar 2000         475.3    310.4    761.0     69020.2     7466.4   N/A
 3 NEC CDR-80             N/A      N/A    865.38    54139.24    5059.41  82.80
 4 Amdek Laserdrive-1     N/A      N/A   1202.38    53909.84    4985.39 121.43
 5 Texel DM3021/5021      N/A      N/A    392.9    154527.0   156426.9   41.8
 6 DAK/BSR $199 ext.    802.2    614.5   1046.7     68279.4    14199.5  115.3
 7 Chinon ?             280.0    204.0    427.0    153903.0   144576.0   N/A
 8 DAK/BSR $399 ext.    257.3    183.2    399.3     95420.4    14157.3   37.5
 9 DAK/BSR $199 ext.    793.04   620.88  1076.01    66034.89   14011.81 111.98
10 Sony CDU-531         298.53   206.96   438.64    92193.64   13289.75  39.18
11 Mitsumi              789.38   616.30   940.48   153903.90  144576.39  76.98
12 Toshiba 3201B        379.12   337.00   398.35   154526.99  156426.91  33.46
13 Magnavox CDD461 ext.   N/A      N/A    933.15    30485.76    7261.83  80.82
14 Hitachi CDR3500 ext.   N/A      N/A    418.5     94710.1    25929.5   56.6
15 Texel 3024/5024      301.28   297.62   347.99   310310.30  183500.80  21.81
16 Texel 5024             N/A      N/A    315.93   310310.30  221907.94  26.21
17 MITSUMI #CRMC-LU     758.24   571.43  1011.90    94945.69   56797.87  94.34
18 Texel 3024             N/A      N/A    342.49   310310.30  272629.76  22.64
19 NEC CDR 84             N/A      N/A    390.11   310310.30  156426.91  32.75
20 Sony CDU-6101-11     351.65   267.40   531.14     7655.07   14094.60  54.40
21 Magnavox CDD461        N/A      N/A    935.90    25859.19    7340.03  71.81
22 DAK/BSR $199 ext.    783.8    660.26   916.67    94945.69   26359.23  91.04
        N/A = NOT AVAILABLE

Information on drives:
  0 Toshiba 3201B (8/89)
        - 486/33 system with a WD-7000FAST 16 bit SCSI controller
  1 Panasonic CR-501-C
        - 486/50 system with a CSM 8 bit SCSI controller
  2 Genstar 2000
        - 386/20 system with proprietary 8 bit controller
  3 NEC CDR-80
        - 386/40 system with Trantor 8 bit SCSI
  4 Amdek Laserdrive-1
        - 386/40 system with proprietary 8 bit controller
  5 Texel DM3021
        - 386/25 system with Always IN-2000 16 bit SCSI
  6 DAK/BSR $199 ext.
        - 386/20 system with proprietary 8 bit controller
  7 Chinon
        - Unknown model number in CompuAd computer
  8 DAK/BSR $399 ext.
        - 386/40 system with proprietary 8 bit controller
          This is an older OEM Sony CD-ROM drive.
  9 DAK/BSR $199 ext.
        - 386SX/20 system with proprietary 8 bit controller
 10 Sony CDU-531
        - i486/33 with Sony CDB-241 interface
 11 Mitsumi (internal)
        - 386DX/40 with Mitsumi interface card
 12 Toshiba 3201B
        - 386DX/33 with Adaptec 16bit SCSI controller
 13 Magnavox CDD 461 External
        - 386DX/25 with Philips CDD163/00 controller
 14 Hitachi CDR-3500 external
        - system and interface unknown
 15 Texel 3024 internal doublespeed SCSI
        - 486/50 system with a CSM 8 bit controller
 16 Texel 5024 external doublespeed SCSI
        - 386/33 Gateway with Trantor 130b 8-bit controller
 17 MITSUMI #CRMC-LU (StorQuest STQ500CD)
        - 386/25 DX with proprietary 8 bit interface
 18 Texel 3024 internal doublespeed SCSI
        - 486/33 with Trantor 130
 19 NEC Intersect Model CDR 84
        - 386/33 with MediaVision ProAudio16 SCSI
 20 Sony CDU-6101-11
        - 386DX/25 with Sony CDB-231 Nov, 1988
 21 Magnavox CDD 461
        - 486/33
 22 DAK-$199-EXT
        - 386DX/40 using 8-bit proprietary interface