MSCMOUSE Version 8.00
For Mouse Systems' 2- and 3-button input devices.
Copyright (C) 1984-1992  Mouse Systems Corporation.

                             INSTALLATION NOTE:

If you already have a copy of MSCMOUSE.COM and/or MSCMOUSE.SYS, just copy
the files accompanying this diskette into the same subdirectory where your
copies already exist.  Then reboot your computer to activate the version
8.00.

                         VALID COMMAND LINE OPTIONS:

/!ccc - Button assignment.  c can be L, M, or R.
/1    - Use serial port COM1.
/2    - Use serial port COM2.
/A0   - Turn off mouse acceleration.
/A#   - Set sensitivity of dynamic accelerator (# = 1 - 9).
/C    - Use Bus Card.
/Dnnn - Double speed threshold.  nnn can be from 0 to 100.
/E    - Enable/Disable resolution doubling (for 3 button PC Mouse).
/Hnnn - Horizontal sensitivity.  nnn can be from 0 to 100.
/I    - Ignore/Listen to application's acceleration commands.
/Np,i - Use hexadecimal I/O port (p) and IRQ level (i).
/P    - Use PS2-compatible Mouse on Pointing Device Port.
/Q    - Suppress driver screen text.
/R    - Remove COM port from system configuration (for BASIC programs).
/Snnn - Horizontal and vertical sensitivity.  nnn can be from 0 to 100.
/Vnnn - Vertical sensitivity.  nnn can be from 0 to 100.
/U    - Unload mouse and pop-up driver and release memory.
/?    - The help display.

The command line options are used on the same line as the MSCMOUSE command.
The usage is as follows:

        MSCMOUSE /C/A5/E/I
   or
        DEVICE=\MOUSE\MSCMOUSE.SYS /C/A5/E/I

MICROSOFT WINDOWS
-----------------------------------------------------------------------------

This diskette contains another document file, WINDOWS.DOC.  This text file 
includes instructions for the installation of your Mouse Systems mouse with
Microsoft Windows version 3.0 and 3.1.