MODPLAY  *********                            (C) Mark J Cox
             MODPLAY  **                                        1990/1991
             MODPLAY  *******                              
             MODPLAY  **************   

             Amiga fourÄchannel sound module player for PC's
             Hardware devices for great sound output!


    I. CONTENTS
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    How to make:
                Mono output from a parallel port for about 5 pounds
                Mono output from a parallel port for around 1 pound
                Stereo from one parallel port for about 12 pounds

    This document has been supplied with MODPLAY or MODRES and the
    license agreement attached to the MODPLAY documentation applies
    to this file.



    I. INTRODUCTION
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    MODPLAY will play modules through the PC Speaker as mentioned above, via
    an D to A converter on any of the three possible parallel ports, in stereo
    if you have an D to A converter on both LPT1 and LPT2 (this sounds really
    good) and also through a special board that plays stereo from one
    printer port ("stereoÄonÄ1")

    1. HOW TO MAKE A D/A CONVERTER FOR FIVE POUNDS
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    A simple circuit for HiFi quality sound needs only a few components (and
    this circuit will work with other software).   It even sounds better than
    a Sound Blaster for sampled output!

    You need:

    IC1 a ZN426E (about 3 pounds) (Ferranti or Plessey are UK manufacturers)

    C1 a 10micro-farad electrolytic capacitor (10V or greater)

    C2 a 4.7micro-farad electrolytic capacitor (10V or greater)

    R1 a 380ohm resistor (5%, 1/8W)

    CON1 a phono socket for connecting a lead to your amplifier

    CON2 a 25 way male D-type connector for your parrallel port

    A bit of 10 way cable - or 10 short wires.

    A +5v supply

                               Zn426e    +5V
                              ÚÄÄÄÄÄÄÄÄ¿  ³  
                  (2)  D0  ÄÄÄ´9     14ÃÄÄ´
                  (3)  D1  ÄÄÄ´10      ³ ÚÁ¿ 
                  (4)  D2  ÄÄÄ´11      ³ ³ ³ 390ê
                  (5)  D3  ÄÄÄ´12      ³ ÀÂÙ
                  (6)  D4  ÄÄÄ´13     5ÃÄÄ´
                  (7)  D5  ÄÄÄ´1      6ÃÄÄ´       +
                  (8)  D6  ÄÄÄ´2      4ÃÄÄ³ÄÄÄÄÄÄÄÄ´ÛÄÄÄÄ> TO AMPLIFIER
                  (9)  D7  ÄÄÄ´3   7   ³  ³        10æF  
                              ÀÄÄÄÄÂÄÄÄÙ +Ï        (may not be needed)
                                   ³ 4.7æFÛ  
                                   ³      ³  
                  (25) GND ÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄ GND
                                   



    2. GETTING A +5V POWER SUPPLY
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    Catalogues such as MAPLIN (uk) provide simple circuits for obtaining
    a +5v power supply (it only has to be 100mA maximum).  Alternatively
    you could tap +5v off the keyboard connector or use 3 1.5volt
    batteries (or even 4 1.5volt batteries with two diodes in series to
    drop the voltage).  In fact, anything that produces a voltage in the
    range 4.5 Ä 5.5 volts. (in fact you can even tap +5v from the game
    port).  Don't forget to connect the 0v of your power supply to the GND
    rail shown.



    3. HOW TO MAKE AN EVEN CHEAPER D/A
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    For the price of 20 1% resistors and a plug, with no power supply
    needed you can make a D/A converter that sounds close to the IC
    one above (it seems only the UK can get a Plessey ZN426E)

    You need one plug for your amp, one for your parallel port and
    9 20k and 9 10K resistors
    Use 1% resistors if possible Ä and 20k sound much better than 22k

          Printer Port:

          signal   pin        20k   20k
          D0       2      >ÄÄÄ°°°ÄÂÄ°°°ÄÄ0v
                              20k ° 10k
          D1       3      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D2       4      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D3       5      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D4       6      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D5       7      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D6       8      >ÄÄÄ°°°Ä´
                              20k ° 10k
          D7       9      >ÄÄÄ°°°Ä´
                              20k ° 10k  100nF
                                  ÃÄÄÄÄÄÄ´ÛÄÄÄÄ> TO AMPLIFIER
                                  ° 10k
          GND      20     >ÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄ>
                                  0v
          
     Thanks to Harry Stox for the above circuit.  Again, make sure all
     the 0v lines are connected together.  The 100nF capacitor may not
     be needed, try removing it if this circuit sounds poor.



 
    4. STEREO-ON-1 BOARD
    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    It is possible to play in stereo with only one parallel port (MODPLAY
    version 2.00 onwards) using the circuit below.  MODPLAY will
    automatically detect this circuit if it is present and work out what
    address it is at Ä so you can plug it into any of your parallel ports. 
    MODPLAY needs no further options and will default to playing through
    this device.  The +5v supply can be  anywhere between 4.5 and 5.5 volts
    so it could be run from three 1.5v  batteries. (Or from four
    rechargable batteries as these are only 1.2v) 

    * Stereo-on-1 works from MODPLAY 2.03 onwards where it did not in 2.00 *

    You can use your stereo-on-1 board with other programs that require
    a single D/A on the port as follows:

    Find out what address your port is at (LPT1 = 0378, LPT2 = 0278) and
    add 2 (LPT1 = 037A, LPT2 = 027A).  Go into DEBUG and type
    o 37a,0       (replacing 37a with the port address)
    q
    Then all sound directed to the parallel port will come out of both
    channels. 

                                ZN428
                                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿         390ê
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´11           6ÃÄÂÄÄÄÄÂÄ±±±±±ÄÄ+5v
              ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´12           7ÃÄÙ    ³ 
              ³ ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄ´13           3ÃNC    ³      
              ³ ³ ³ ÚÄÄÄÄÄÄÄÄÄÄÄ´14            ³      ³  + 10æF
              ³ ³ ³ ³ ÚÄÄÄÄÄÄÄÄÄ´15           5ÃÄÄÄÄÄÄ³ÄÄÄ¶ÃÄÄÄÄÄ> Left out
              ³ ³ ³ ³ ³ ÚÄÄÄÄÄÄÄ´16            ³      ³     0vÄÄÄ>
      20 >Ä0v ³ ³ ³ ³ ³ ³ ÚÄÄÄÄÄ´1           10ÃÄÄ+5v ³ 
              ³ ³ ³ ³ ³ ³ ³ ÚÄÄÄ´2            9ÃÄÂÄ0v ³      
      14 >ÄÄÄÄ³Ä³Ä³Ä³Ä³Ä³Ä³Ä³ÄÄÄ´4            8ÃÄÙ    ³    
              ³ ³ ³ ³ ³ ³ ³ ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ      ³    
      11 >ÄÄÄÄ´ ³ ³ ³ ³ ³ ³ ³   ZN428                 ³  + 1æF    
              ³ ³ ³ ³ ³ ³ ³ ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿      ÃÄÄÄ¶ÃÄ0v
       9 >ÄÄÄÄÁÄ³Ä³Ä³Ä³Ä³Ä³Ä³ÄÄÄ´11 D7   VRIN 6ÃÄÄÄÄÄÄÙ
       8 >ÄÄÄÄÄÄÁÄ³Ä³Ä³Ä³Ä³Ä³ÄÄÄ´12 D6  VROUT 7Ã NC
       7 >ÄÄÄÄÄÄÄÄÁÄ³Ä³Ä³Ä³Ä³ÄÄÄ´13 D5     NC 3Ã NC     
       6 >ÄÄÄÄÄÄÄÄÄÄÁÄ³Ä³Ä³Ä³ÄÄÄ´14 D4         ³        + 10æF
       5 >ÄÄÄÄÄÄÄÄÄÄÄÄÁÄ³Ä³Ä³ÄÄÄ´15 D3    OUT 5ÃÄÄÄÄÄÄÄÄÄ¶ÃÄÄÄÄÄ> Right out
       4 >ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄ³Ä³ÄÄÄ´16 D2         ³           0vÄÄÄ>
       3 >ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄ³ÄÄÄ´1 D1     +V 10ÃÄÄ+5v    
       2 >ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄ´2 D0     0v  9ÃÄÂ0v
       1 >ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´4 !EN    0v  8ÃÄÙ
      25 pin male D connector   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


      Notes:

      Make sure all the 0v lines are connected together and connected to the
      0v line of your power source.  Also, make sure the +5v lines are 
      connected together.  The lines marked 'NC' do not need to be connected.  

      If a ZN428 is not available, any D/A with input latches will work -
      the D/A should latch the data bus when pin 4 (!EN) is low.

      Ä³Ä = No connection, ÄÅÄ = joined

      The above circuit (Stereo-on-1) is (C) Mark J Cox 1991, 29 Lundie Close
      Stenson Fields, Derby DE2 3AN; and is supplied for personal use only.  
      For any other use, please contact the author at the address above. If 
      this circuit is abstracted or incorporated into any other document or
      circuit then that document or documentation supplied with that circuit
      must contain this paragraph of text.  Any commercial use where not 
      agreed by written contract with the author (Mark J Cox) is prohibited.



     13. UK SUPPLIERS
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     A lot of people have been having difficulty obtaining the ZN426/ZN428
     IC's.  If you cannot find an alternative, there is a company in the
     UK that will do overseas orders.   Carriage charges vary from 10%
     of the total order value (Ireland) to 25% (Fiji) and payment can be
     by Eurocheques, bank drafts, credit cards etc. Maplin: +44 702 554161
     

     14. CONTACT/SUPPORT
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     Before June 1992:
     -----------------
     Mark J Cox                 Electronic Mail: 
     17 Kirkburn Place           (JANET) m.j.h.cox@uk.ac.bradford (UK)
     Bradford                            m.j.h.cox@bradford.ac.uk (other)
     W. Yorks, UK              (NETMAIL) Post a message in PLAY SUPPORT on
     BD7 2BZ                             Kingdom of Greyhawk BBS
                                         (+44 332 756414)
     After June 1992:
     ----------------
     29 Lundie Close           (NETMAIL) Post a message in PLAY SUPPORT on
     Stenson Fields                      Kingdom of Greyhawk BBS
     Derby, UK                           (+44 332 756414)
     DE2 3AN                     

     All comments on PLAY, RESPLAY, MODPLAY or future software are welcomed!
     Please enclose a SSAE to ensure reply.