Page i                                                               
                                                                                
                                                                                
           Introduction to the Backup VAP                                       
                                                                                
                                                                                
                          This manual explains how to use the                   
                          NetWare Backup VAP to back up and restore             
                          data on a file server.  It also explains how to       
                          install the NetWare Backup VAP.                       
                                                                                
                          You can use the NetWare Backup VAP to                 
                          back up and restore data on a NetWare v2.2            
                          file server.  The Backup VAP will back up             
                          and restore both DOS files and Apple File             
                          Protocol (AFP) files.                                 
                                                                                
                          Because the Backup VAP is a process  that             
                          runs on top of the NetWare operating system,          
                          you can use it to back up and restore data            
                          while the file server is up and running.  The         
                          Backup VAP can be operated at the console             
                          of either a file server or a router containing a      
                          tape drive unit.                                      
                                                                                
                                                                                
           Organization of the manual                                           
                                                                                
                          This manual contains the following sections,          
                          each starting on the indicated page.                  
                                                                                
                          Installation                        1                 
                                                                                
                          BACKUP utility                      7                 
                                                                                
                          RESTORE utility                    17                 
                                                                                
                          Error messages                     32                 

           Page ii                                                              
                                                                                
                                                                                
           Who needs to read what?                                              
                                                                                

                  Installation                                                  
                                                                                
                          If the Backup VAP has not been installed on           
                          your file server or router, complete the              
                          instructions in the "Installation" section.  (See     
                          page 1.)  Installation is usually a one-time          
                          process.                                              
                                                                                
                                                                                
                  BACKUP utility                                                
                                                                                
                          To back up network data to a tape cartridge,          
                          complete the instructions in the "BACKUP              
                          Utility" section.  (See page 7.)  You should          
                          back up data as often as necessary to ensure          
                          that losses from accidental file deletions or         
                          network disk problems will be minimal.                
                                                                                
                                                                                
                  RESTORE utility                                               
                                                                                
                          To restore data in one or more files,                 
                          directories, or volumes from a tape cartridge         
                          to a network disk drive, complete the                 
                          instructions in the "RESTORE Utility"                 
                          section.  (See page 17.)                              
                                                                                
                                                                                
                  Error messages                                                
                                                                                
                          This section outlines error messages that can         
                          appear on the console screen during the               
                          Backup or Restore session.  (See page 32.)            
                          These error messages are specific to the              
                          Backup VAP and are in addition to the error           
                          messages listed in the NetWare System                 
                          Messages manual.                                      

           Page iii                                                             
                                                                                
                                                                                
           NetWare command format conventions                                   
                                                                                
                          The command format displays the appropriate           
                          syntax for entering commands at the console           
                          prompts.  The example below shows a typical           
                          command format used in this manual:                   
                                                                                
                             BACKUP [path [filename] [option...]]               
                                                                                
                          The conventions for this command format are           
                          explained below.                                      
                                                                                
                          BACKUP      Words that appear in all                  
                                      capital letters must be spelled           
                                      exactly as shown.   Although              
                                      they appear in capital letters,           
                                      they can be typed in either               
                                      upper or lower case.                      
                                                                                
                          path        Words that appear in italics              
                                      are variables.  They should be            
                                      replaced with the information             
                                      pertinent to your task.  In               
                                      this case, path would be                  
                                      replaced with the directory               
                                      path of the directory you want            
                                      to back up.                               
                                                                                
                          [ ]         Square brackets indicate that             
                                      the enclosed item is optional:            
                                      you can enter a command with              
                                      or without the enclosed item.             
                                      In the example above, path,               
                                      filename, and option are                  
                                      optional.                                 
                                                                                
                          ...         Ellipses indicate that more               
                                      than one variable can be used             
                                      with the command.  In this                
                                      case, more than one option can            
                                      be entered.                               
                                                                                
                          <Enter>     Angle brackets indicate that              
                                      you should press the key that             
                                      appears between them.  In                 
                                      this case, you should press the           
                                      Enter key.                                

             Page 1                                                             
                                                                                
                                                                                
             Installation                                                       
                                                                                
                                                                                
                               This section explains how to install the         
                               Backup VAP in a file server or router.           
                               Installation is a one-time process that must     
                               be completed before you run BACKUP or            
                               RESTORE for the first time.                      
                                                                                
                                                                                
                                                                                
             Install hardware                                                   
                                                                                
                               You can run the Backup VAP from one of the       
                               following:                                       
                                                                                
                               o   A file server running NetWare v2.2.          
                                                                                
                               o   A router running NetWare v2.2.  This         
                                   could be a workstation booted as a router    
                                   (using an alternate boot diskette).          
                                                                                
                               Whether you run the Backup VAP from a            
                               server or a router, you can back up or restore   
                               to any server on your internetwork running       
                               NetWare v2.2.  The only restriction is that      
                               you must be able to log in as SUPERVISOR         
                               or as another user with Read and File Scan       
                               rights in the directories to be backed up and    
                               restored to.                                     
                                                                                
                               Install the tape drive and tape controller       
                               board in the file server or router according to  
                               the instructions furnished by the computer       
                               and tape drive manufacturers.  You make          
                               hardware configuration settings (interrupt       
                               line, I/O base, and DMA channel) on the tape     
                               controller board.                                

             Page 2                                                             
                                                                                
                                                                                
                               Select one of the 19 configuration options       
                               listed in the chart below.  If possible, use     
                               configuration option 0.                          
                                                                                
                                  Configuration  Interrupt     I/O    DMA           
                                     Option        Line        Base  Channel        
                                                                                
                                        0            5         280h   3           
                                        1            3         200h   1           
                                        2            3         330h   1           
                                        3            4         200h   1           
                                        4            4         300h   1           
                                        5            4         330h   1           
                                        6            5         200h   1           
                                        7            5         300h   1           
                                        8            3         330h   1           
                                        9            7         200h   1           
                                       10            7         300h   1           
                                       11            3         330h   1           
                                       12            3         300h   1           
                                       13            5         280h   1           
                                       14            7         280h   3           
                                       15            3         200h   3           
                                       16            3         300h   3           
                                       17            5         200h   3           
                                       18            5         300h   3

                               Make the hardware settings according to the      
                               board manufacturer's instructions.  Make a       
                               note of the configuration option you select.     
                                                                                
                                                                                
                       Note:   Follow the tape drive manufacturer's             
                               instructions concerning the types of tape        
                               cartridges that you can use with your            
                               particular tape drive.                 


             Page 3                                                             
                                                                                
                                                                                
             Install the Backup VAP                                             
                                                                                
                               To install the Backup VAP on a file server or    
                               router, complete the following steps:            
                                                                                
                                                                                
             1.   Configure the Backup VAP.                                     
                                                                                
                               The Backup VAP software must be configured       
                               for the same hardware configuration option       
                               you used when you installed the tape drive       
                               hardware.  If the hardware and software          
                               configurations do not match, the Backup VAP      
                               will not run, and other hardware or software     
                               in the file server or router may fail as well.   
                                                                                
                               The Backup VAP software is shipped               
                               configured for option 0.  If you select any      
                               configuration option other than option 0, you    
                               must configure the software to match the         
                               hardware configuration using BUCONFIG            
                               (see Step 1a).  (If you select option 0 and      
                               have not previously configured the software      
                               for a different configuration option, skip to    
                               Step 2.)                                         
                                                                                
                         1a.   To configure the Backup VAP, use the             
                               diskette labeled NetWare Backup VAP v1.0.        
                               Do one of the following:                         
                                                                                
                               þ   Use the Backup VAP diskette in the           
                                   floppy disk drive of any workstation or      
                                                                                
                               þ   Copy the contents of the Backup VAP          
                                   diskette to a network drive.                 
                                                                                
                         1b.   To view the configuration of the Backup VAP      
                               (without reconfiguring the file), type           
                                                                                
                                   BUSHOW  <Enter>                              
                                                                                
                               All configuration options appear on the screen   
                               with an asterisk by the option the VAP is        
                               configured for.                                  

             Page 4                                                             
                                                                                
                                                                                
                               BUCONFIG uses DCONFIG (Device                    
                               CONFIGuration) to configure the Backup           
                               VAP.  As it does, all configuration options are  
                               listed on the screen, with an asterisk ( * ) by  
                               the option you selected.                         
                                                                                
                         1c.   At the DOS prompt for the appropriate local      
                               or network drive, use the following command      
                               format:                                          
                                                                                
                                   BUCONFIG option                              
                                                                                
                               Replace option with the configuration option     
                               number (0 through 18) you selected during        
                               the tape drive installation.                     
                                                                                
                                                                                
                               Example.  To configure the Backup VAP for        
                               configuration option 1, type                     
                                                                                
                                   BUCONFIG 1  <Enter>                          
                                                                                
                                                                                
                       Note:   Below the last option, you will probably see a   
                               message similar to "WARNING:  Specified          
                               disk not found.  C1: 4,0."  This message can     
                               be ignored.                                      

                                                                                
             2.   Copy the Backup VAP.                                          
                                                                                
                               The Backup VAP file, BACKUP.VP0 (the last        
                               character is a zero), must be copied to a        
                               directory or diskette from which it can be       
                               loaded as a VAP.                                 
                                                                                
                               o   For a file server, the Backup VAP must       
                                   be copied to the SYS:SYSTEM directory.       
                                   This must be done by a user with             
                                   supervisory privileges.                      
                                                                                
                               o   For a router, the Backup VAP must be         
                                   copied to the router's boot diskette.        
                                                                                
                               Use COPY or NCOPY to copy the                    
                               BACKUP.VP0 file.                                 

             Page 5                                                             
                                                                                
                                                                                
                       Note:   If your file server or router uses more than     
                               one VAP, whenever you boot the file server       
                               or router, the Backup VAP (BACKUP.VP0)           
                               must load first, before any other VAP.           
                                                                                
                               The VAP loading sequence is controlled by        
                               the last number in the VAP filename              
                               extension, which for the Backup VAP is a 0       
                               (zero).  If your SYS:SYSTEM directory (or        
                               router boot diskette) contains another VAP       
                               file with the .VP0 extension, the other VAP      
                               file must be renamed with a .VP1 extension.      
                               In turn, any higher-number VAPs must be          
                               incremented by one (.VP1 becomes .VP2, and       
                               so forth).  (For VAP files with the .VAP         
                               extension, no change is required.)               


             3.   Load the Backup VAP.                                          
                                                                                
                               Once the BACKUP.VP0 file has been copied         
                               to SYS:SYSTEM or the router boot diskette,       
                               whenever you boot the file server or router,     
                               you see the following:                           
                                                                                
                                   Value Added Processes have been defined.  Do 
                                   you wish to load them?                       
                                                                                
                               Answer "Yes."  As the Backup VAP is loaded,      
                               messages similar to the following appear:        
                                                                                
                                   Loading VAP BACKUP.VP0                       
                                                                                
                                   BACKUP & RESTORE VAP.                        
                                                                                
                                   Server ADMIN  version 2.2                    
                                                                                
                                   BACKUP/RESTORE VAP Version 1.01.  DCONFIG    
                                   Option 0                                     
                                   (c) Copyright 1991 Novell, Inc. All Rights   
                                   Reserved.                                    

             Page 6                                                             
                                                                                
                                                                                
                               Before you type anything further at the          
                               console, wait for all VAPs to load and for the   
                               console prompt ( : ) to appear.  (Do not         
                               confuse the console prompt with other colons     
                               that may appear on the screen while the          
                               VAPs are loading.)                               
                                                                                
                               If you type anything before the console          
                               prompt appears, you may cause the console to     
                               "hang."                                          
                                                                                
                               You can then run BACKUP or RESTORE.              

           Page 7                                                               
                                                                                
                                                                                
           BACKUP Utility                                                       
                                                                                
                                                                                
                          This section explains how to back up network          
                          files with the BACKUP utility (which is part          
                          of the Backup VAP).  You can run BACKUP               
                          if you have supervisor privileges or if you           
                          have Read and File Scan rights in the                 
                          volumes and directories you want to back up.          
                                                                                
                          After you back up files, you can restore              
                          damaged or deleted files to their status at           
                          the last back up using RESTORE.  (See page            
                          17.)                                                  
                                                                                
                                                                                
                  Note:   Before you follow these instructions for the          
                          first time, make sure the Backup VAP has              
                          been installed and loaded in the file server or       
                          router, explained in the "Installation" section.      
                          (See page 1.)                                         
                                                                                
                                                                                
                                                                                
                                                                                
           Plan the backup session                                              
                                                                                
                          You need to know the following before you             
                          start BACKUP.                                         
                                                                                
                          o  Whether to back up from the file                   
                             server console or a router console.                
                             This depends on where the Backup VAP               
                             was installed.  (See page 1.)                      
                                                                                
                          o  Which file server you are backing up.              
                             If you have more than one file server, you         
                             specify which file server to back up.              

           Page 8                                                               
                                                                                
                                                                                
                          o  The username and password to log in                
                             with.  You must have Read and File                 
                             Scan rights in the directories to be               
                             backed up.                                         
                                                                                
                                                                                
                  Note:   References in this manual to the supervisor           
                          will generally include the user SUPERVISOR            
                          and other users with supervisor equivalence.          
                                                                                
                                                                                
                          o  Whether to disable logins and log                  
                             users out (supervisor only).  BACKUP               
                             uses a large percentage of the file server's       
                             processing capacity and may slow the               
                             network to an undesirable speed.  Also,            
                             BACKUP does not back up files that are             
                             in use.  (Logins are re-enabled after              
                             BACKUP is complete.)                               
                                                                                
                          o  Which volumes, directories, or files to            
                             back up.  You can back up one or more              
                             volumes or directories.  Or you can back           
                             up one or more files that follow a                 
                             filename pattern (using DOS wildcard               
                             characters).                                       
                                                                                
                          o  Whether to back up bindery files                   
                             (supervisor only).  If you back up                 
                             specific directories or files, you can also        
                             back up the bindery files.  (In full-volume        
                             backups by the supervisor, bindery files           
                             are automatically backed up.)  Although            
                             the bindery files are in volume SYS, they          
                             will be backed up (if specified) regardless        
                             of the volume you back up.                         
                                                                                
                          o  Whether to back up trustee rights.  If             
                             you back up specific directories or files,         
                             you can back up the directories' trustee           
                             rights as part of the backup.  (Trustee            
                             rights are automatically backed up in full-        
                             volume backups.)                                   

           Page 9                                                               
                                                                                

           Run the BACKUP utility                                               
                                                                                
                          This section explains how to back up network          
                          files using the BACKUP utility.  You can run          
                          BACKUP if you are the network supervisor              
                          or equivalent or if you have Read and File            
                          Scan rights in the volumes and directories to         
                          be backed up.                                         
                                                                                
                          Before you run BACKUP, complete the                   
                          following steps:                                      
                                                                                
           1.  Select the file server to back up.                               
                                                                                
                          To back up your default server at the server          
                          console, skip to Step 2.                              
                                                                                
                          To select the server, at the server or router         
                          console prompt ( : ), use the following               
                          command format:                                       
                                                                                
                             SELECTSERVER [server]                              
                                                                                
                          Use SELECTSERVER if you are running                   
                          BACKUP from a router or a file server other           
                          than the target server.                               
                                                                                
                          Replace server with the name of the file              
                          server you want to back up.  (Server is               
                          optional; if you do not specify a server, you         
                          are prompted to enter one.)                           
                                                                                
                          Example.  To specify server ADMIN, type               
                                                                                
                             SELECTSERVER ADMIN  <Enter>                        
                                                                                
                          or                                                    
                                                                                
                             SELECTSERVER  <Enter>                              
                                                                                
                          You are prompted to enter the target file             
                          server name.                                          

           Page 10                                                              
                                                                                
                                                                                
           2.  Start BACKUP and specify variables.                              

                     2a.  To start BACKUP, at the file server or router         
                          console prompt ( : ), use the following               
                          command format:                                       
                                                                                
                             BACKUP [path [filename] [option...]]               
                                                                                
                          Replace path with the path for the directory          
                          you want to back up.  If you do not specify a         
                          path, BACKUP backs up one or more                     
                          complete volumes (which you specify later).           
                                                                                
                          Replace filename with the names or filename           
                          pattern of the files you are backing up.              
                          Filename patterns use DOS wildcard                    
                          characters (* and ?).                                 
                                                                                
                          Example.  You can specify *.EXE to back up            
                          files with the .EXE extension.  Specify a             
                          filename only with its path; the filename             
                          must be separated from the path by a space,           
                          not a slash or a backslash.                           
                                                                                
                          Replace option with one or more of the                
                          options listed below.  Specify options only if        
                          you specify a path.                                   
                                                                                
                          /S          Use to back up files in                   
                                      subdirectories of the specified           
                                      directory path.                           
                                                                                
                          /B          Use to back up bindery files              
                                      from volume SYS (supervisor               
                                      only).  You can back up the               
                                      bindery files no matter which             
                                      volume or directory you are               
                                      backing up.                               
                                                                                
                          /T          Use to back up trustee rights             
                                      associated with the directories           
                                      that are backed up.                       

           Page 11                                                              
                                                                                
                                                                                
                          Examples.  To back up one or more volumes,            
                          type                                                  
                                                                                
                             BACKUP  <Enter>                                    
                                                                                
                          (You specify volumes later.)                          
                                                                                
                          To back up all files in SYS:HOME/MARIO,               
                          type                                                  
                                                                                
                             BACKUP SYS:HOME/MARIO  <Enter>                     
                                                                                
                          To back up all files in SYS:HOME/MARIO                
                          and its subdirectories, type                          
                                                                                
                             BACKUP SYS:HOME/MARIO /S  <Enter>                  
                                                                                
                          To back up all files with the extension .BAT          
                          in SYS:HOME/MARIO and its subdirectories,             
                          and to back up all trustee rights associated          
                          with these directories, type                          
                                                                                
                             BACKUP SYS:HOME/MARIO *.BAT /S /T                  
                             <Enter>                                            
                                                                                
                          (Note the space between SYS:HOME/MARIO                
                          and *.BAT.)                                           
                                                                                
                     2b.  When prompted, type your username and                 
                          press <Enter>.                                        
                                                                                
                     2c.  When prompted, type your password and                 
                          press <Enter>.  (If your username has no              
                          password, press <Enter>.)                             
                                                                                
                                                                                
                  Note:   If you make a mistake while typing your               
                          password, use the Delete key, not the                 
                          Backspace key, to erase your mistake.                 

           Page 12                                                              
                                                                                
                                                                                
                     2d.  If you did not log in as SUPERVISOR or                
                          equivalent, complete one of the following:            
                                                                                
                          o  If you specified a directory path in your          
                             BACKUP command (in Step 2a), skip to               
                             Step 3.                                            
                                                                                
                          o  If you are doing a full-volume backup and          
                             did not specify a directory path in your           
                             BACKUP command, skip to Step 2h.                   
                                                                                
                          If you logged in as SUPERVISOR, when                  
                          prompted to disable logins, type Y or N.              
                          (Logins are re-enabled after BACKUP is                
                          complete.)                                            
                                                                                
                          If you answer "No," complete one of the               
                          following:                                            
                                                                                
                          o  If you specified a directory path in your          
                             BACKUP command (in Step 2a), skip to               
                             Step 3.                                            
                                                                                
                          o  If you are doing a full-volume backup and          
                             did not specify a directory path in your           
                             BACKUP command, skip to Step 2h.                   
                                                                                
                     2e.  If you disabled logins, you now have the              
                          option to force existing users to log out.  The       
                          current users are listed on the screen, along         
                          with the following prompt:                            
                                                                                
                             Do you want to FORCE users to log out? (y/n) >     
                                                                                
                          If you answer "Yes" users are not logged out          
                          at this point.                                        
                                                                                
                          If you answer "No," complete one of the               
                          following:                                            
                                                                                
                          o  If you specified a directory path in your          
                             BACKUP command (in Step 2a), skip to               
                             Step 3.                                            
                                                                                
                          o  If you are doing a full-volume backup              
                             (and did not specify a directory path in           
                             your BACKUP command), skip to Step                 
                             2h.                                                
                                                                                
                          Each user is notified to log out.  Wait a few         
                          moments to give users a chance to logout.             

           Page 13                                                              


                     2f.  When prompted to clear remaining user                 
                          connections, type Y or N.                             
                                                                                
                          If you answer "Yes," the remaining users              
                          (except the Backup VAP user) are logged out.          
                          Complete one of the following:                        
                                                                                
                          o  If you specified a directory path in your          
                             BACKUP command (in Step 2a), skip to               
                             Step 3.                                            
                                                                                
                          o  If you are doing a full-volume backup              
                             (and did not specify a directory path in           
                             your BACKUP command), skip to Step                 
                             2h.                                                
                                                                                
                          If you answer "No," the remaining users are           
                          not cleared.  You can continue the backup             
                          (with users still connected) or go back and           
                          force them to log out.                                
                                                                                
                     2g.  When prompted to proceed, type Y or N.                
                                                                                
                          o  If you answer "No," return to Step 2e.             
                                                                                
                          o  If you answer "Yes" and you specified a            
                             directory path in your BACKUP command              
                             (in Step 2a), skip to Step 3.                      
                                                                                
                          o  If you answer "Yes" and you did not                
                             specify a directory path in your BACKUP            
                             command, continue with Step 2h.                    

           Page 14                                                              
                                                                                
                                                                                
                     2h.  If you are doing a full-volume backup, a list         
                          of the file server's volumes appears:                 
                                                                                
                             Volume:         Kilobytes used:                    
                                                                                
                                SYS:           137464 Kbytes                    
                               BOOM:           143000 Kbytes                    
                                BAH:            65796 Kbytes                    
                                                                                
                                      Total    346260 Kbytes                    

                          In addition, for each volume you are                  
                          prompted:                                             
                                                                                
                             Back up volume          SYS:    137464 Kbytes ?    
                                                                                
                          For each volume, type Y or N.                         
                                                                                
                     2i.  After you specify which volumes to back up,           
                          you are prompted:                                     
                                                                                
                             Do you wish to make any changes? (y/n) >           
                                                                                
                          Type Y or N.  If you answer "Yes," return to          
                          Step 2h.  If you answer "No," continue with           
                          Step 3.                                               
                                                                                
                                                                                
           3.  Back up network files.                                           
                                                                                
                     3a.  After you specify the BACKUP variables, you           
                          are prompted:                                         
                                                                                
                             Insert cartridge No. 1 and press Enter.            
                                                                                
                          Insert the tape cartridge into the tape drive         
                          and press <Enter>.  If necessary, refer to the        
                          tape insertion instructions furnished with the        
                          tape drive.                                           
                                                                                
                          A message appears, indicating that the tape           
                          cartridge is being mounted (wound to the              
                          starting position on the tape).                       
                                                                                
                          Novell has added a timed release program to           
                          the BACKUP utility.  This program allows              
                          you to delay a backup for up to 24 hours.             

           Page 15                                                              
                                                                                
                                                                                
                          After the tape cartridge is mounted, a prompt         
                          similar to the following appears:                     
                                                                                
                             Would you like to delay the backup for up to 24    
                             hours (y/n)?                                       
                                                                                
                          Answer "no" to begin the backup now.                  
                          Answer "yes" to select a time for the backup          
                          to begin.  If you answer "yes," a prompt              
                          similar to the following appears:                     
                                                                                
                             The current time is 3:35 pm                        
                                                                                
                             Enter desired starting time in the format          
                             "hh:mm am/pm.">                                    
                                                                                
                          Enter a starting time for BACKUP.  The                
                          following screen appears:                             
                                                                                
                             Backup will begin at 2:55pm.                       
                             The current time is 1:30pm.                        
                                                                                
                          The specified files are backed up at the time         
                          you specified.                                        
                                                                                
                     3b.  As the files are backed up, they are listed on        
                          the screen:                                           
                                                                                
                               1 SYS:HOME/                                      
                               2 SYS:HOME/MARIO/                                
                                 :                                              
                                                                                
                             SYS:HOME/MARIO/                                    
                               0 SYS:HOME/MARIO/APRIL_1.COM                     
                               1 SYS:HOME/MARIO/LOGIN                           
                             SYS:HOME/MARIO/BU/                                 
                             SYS:HOME/MARIO/BU/161/                             
                               2 SYS:HOME/MARIO/BU/161/GEO.161                  
                               3 SYS:HOME/MARIO/BU/161/ALPHA.161                
                             SYS:HOME/MARIO/BU/YUBIN/                           
                             SYS:HOME/MARIO/BU/DRIVE-C/                         
                               4 SYS:HOME/MARIO/BU/DRIVE-C/CONFIG.SYS           
                               5 SYS:HOME/MARIO/BU/DRIVE-C/AUTOEXEC.BAT         
                                                                                
                          The unnumbered lines are directories.  The            
                          numbered lines are files.                             

           Page 16                                                              
                                                                                
                          The information on the screen is also stored          
                          in two files:                                         
                                                                                
                          o  VAP_FILE.LOG records the backup date               
                             and time, the files that are backed up,            
                             and the cartridge number and tape                  
                             locator information for each file.                 
                                                                                
                          o  VAP_ERR.LOG also records the backup                
                             date and time, along with error messages           
                             that appear during BACKUP.                         
                                                                                
                          In a full-volume backup, these files are              
                          created in the root directory of each volume          
                          backed up.  In a specific-directory backup,           
                          these files are created in the directory you          
                          specified in Step 2a.                                 
                                                                                
                                                                                
                  Note:   The VAP_FILE.LOG and VAP_ERR.LOG files                
                          are created only for the supervisor or a user         
                          with Create rights in the applicable directory.       
                                                                                
                                                                                
                     3c.  If the tape cartridge reaches the end during          
                          backup, the tape is rewound and you are               
                          prompted to insert another tape cartridge.            

                          After specified files have been backed up, the        
                          following messages appears:                           
                                                                                
                             Finished Backup Session.                           
                                                                                
                             Rewinding Tape.                                    
                                                                                
                          After the tape cartridge is rewound, the              
                          console prompt ( : ) reappears on the screen,         
                          and BACKUP is complete.                               
                                                                                
                          Label your backup tapes and store them in a           
                          safe place.                                           
                                                                                
                                                                                
                  Note:   If you booted a workstation as a temporary            
                          router to run BACKUP, bring down the                  
                          router (using the DOWN console command)               
                          before rebooting the computer as a                    
                          workstation.                                          

         Page 17                                                                
                                                                                
                                                                                
         RESTORE Utility                                                        
                                                                                
                             This section explains how to restore               
                             previously backed up network files with the        
                             RESTORE utility (part of the Backup VAP).          
                             You can run RESTORE if you are the                 
                             network supervisor or if you have Read and         
                             File Scan rights in the volumes and                
                             directories you restore files to.                  
                                                                                
                             If a user deletes a file or if a network disk      
                             has problems, you can restore files to their       
                             status at the last back up.  (See page 7.)         
                                                                                
                                                                                
                    Note:    Before you follow these instructions for the       
                             first time, make sure the Backup VAP has           
                             been installed and loaded in the file server or    
                             router, as explained in the "Installation"         
                             section.  (See page 1.)                            
                                                                                

         Plan the restore session                                               
                                                                                
                             You must know the following before you start       
                             RESTORE.                                           
                                                                                
                             o   Whether to restore from the file               
                                 server console or a router console.            
                                 This depends on where the Backup VAP           
                                 was installed.  (See page 1.)                  
                                                                                
                             o   Which file server you are restoring            
                                 to.  If you have more than one file            
                                 server, you specify which file server to       
                                 restore to.                                    

         Page 18                                                                
                                                                                
                                                                                
                             o   The username and password to log in            
                                 with.  You must log in as a user with          
                                 Read and File Scan rights in the               
                                 directories to be restored.                    

                                 In some cases, it may be important to          
                                 run RESTORE as supervisor.  For                
                                 example, if you are restoring directories      
                                 that have been deleted, users other than       
                                 the supervisor may not be able to              
                                 recreate the subdirectories (and               
                                 consequently cannot restore files to those     
                                 subdirectories).  If you do not want to run    
                                 RESTORE as supervisor,  make sure the          
                                 user has Create rights in the directories      
                                 that do exist.                                 
                                                                                
                                                                                
                    Note:    References in this manual to the supervisor        
                             will generally include the user SUPERVISOR         
                             and other users with supervisor equivalence.       
                                                                                
                                                                                
                             o   Whether to disable logins and log              
                                 users out (supervisor only).                   
                                 RESTORE uses a large percentage of the         
                                 file server's processing capacity and may      
                                 slow the network to an undesirable speed.      
                                 Also, RESTORE does not write over files        
                                 that are in use.  (Logins are re-enabled       
                                 after RESTORE is complete.)                    
                                                                                
                             o   Which volumes, directories, or files to        
                                 restore.  You can restore one or more          
                                 volumes or directories.  Or you can            
                                 restore one or more files that follow a        
                                 filename pattern (using DOS wildcard           
                                 characters).                                   

         Page 19                                                                
                                                                                
                                                                                
                             o   Whether to restore bindery files               
                                 (supervisor only).  If you backed up the       
                                 bindery files with BACKUP, you can             
                                 restore them as part of the restore            
                                 session.  Although the bindery files are in    
                                 volume SYS, they will be restored (if          
                                 specified) regardless of the volume you        
                                 are restoring.                                 
                                                                                
                             o   Whether to restore trustee rights.  If         
                                 you backed up trustee rights during            
                                 BACKUP, you can restore the directories'       
                                 trustee rights as part of the restore          
                                 session.                                       
                                                                                
                                                                                
                                                                                
         Run the RESTORE utility                                                
                                                                                
                             This section explains how to restore network       
                             files using the RESTORE utility.  You can          
                             run RESTORE if you are the network                 
                             supervisor or equivalent or if you have Read       
                             and File Scan rights in the volumes and            
                             directories to be restored.                        
                                                                                
                             Before you run RESTORE, complete the               
                             following steps:                                   
                                                                                
         1.    Select the file server to restore to.                            
                                                                                
                             To restore to your default server at the           
                             server console, skip to Step 2.                    

                             To select the server, at the server or router      
                             console prompt ( : ), use the following            
                             command format:                                    
                                                                                
                                 SELECTSERVER [server]                          
                                                                                
                             Use SELECTSERVER if you are running                
                             RESTORE from a router or a file server             
                             other than the target server.                      
                                                                                
                             Replace server with the name of the file           
                             server you want to restore to.  (Server is         
                             optional; if you do not specify a server, you      
                             are prompted to enter one.)                        

         Page 20                                                                
                                                                                
                                                                                
                             Example.  To specify server ADMIN, type            
                                                                                
                                 SELECTSERVER ADMIN  <Enter>                    
                                                                                
                             or                                                 

                                 SELECTSERVER  <Enter>                          
                                                                                
                             You are prompted to enter the target file          
                             server name.                                       
                                                                                
                                                                                
         2.    Start RESTORE and specify variables.                             
                                                                                
                      2a.    To start RESTORE, at the file server or            
                             router console prompt ( : ), use the following     
                             command format:                                    
                                                                                
                                 RESTORE [path [filename] [option...]]          
                                                                                
                             Replace path with the path for the directory       
                             you want to restore.  If you do not specify a      
                             path, RESTORE prompts you for the path             
                             and additional options later.                      
                                                                                
                             Replace filename with the name or filename         
                             pattern of the files you are restoring.            
                             Filename patterns use DOS wildcard                 
                             characters (* and ?).                              
                                                                                
                             Example.  Specify *.EXE to restore files with      
                             the .EXE extension.  Specify a filename only       
                             with its path; the filename must be separated      
                             from the path by a space, not a slash or a         
                             backslash.                                         

         Page 21                                                                
                                                                                
                                                                                
                             Replace option with one or more of the             
                             options listed below.  You can specify options     
                             only if you specify a path.                        
                                                                                
                             /C             Use to confirm whether or not       
                                            to restore a specific directory     
                                            or file.                            
                                                                                
                             /S             Use to restore files in             
                                            subdirectories of the specified     
                                            directory path.  (Only the          
                                            specified files that were           
                                            backed up are restored.)            

                             /B             Use to restore the bindery          
                                            files to volume SYS (no matter      
                                            which volume or directory you       
                                            are restoring).  (The bindery       
                                            files are restored only if you      
                                            backed them up.)                    
                                                                                
                             /T             Use to restore the trustee          
                                            rights associated with the          
                                            directories that are restored.      
                                            (The trustee rights are             
                                            restored only if you backed         
                                            them up.)                           
                                                                                
                             /R=path        Use to restore directories and      
                                            files to a different directory      
                                            path than they were backed          
                                            up from.  Replace path with         
                                            the directory path where you        
                                            want to restore the directory       
                                            (and its subdirectories, if         
                                            applicable).                        
                                                                                
                             Examples.  To start RESTORE (and be                
                             prompted later for the restore variables), type    
                                                                                
                                 RESTORE  <Enter>                               
                                                                                
                             To restore all files in SYS:HOME/MARIO,            
                             type                                               
                                                                                
                                 RESTORE SYS:HOME/MARIO  <Enter>                

         Page 22                                                                
                                                                                
                                                                                
                             To set the confirmation feature, type              
                                                                                
                                 RESTORE [path [filename] /C]  <Enter>          
                                                                                
                             If you specify the confirm option, each time a     
                             directory or file meeting your specifications is   
                             listed, you are prompted to restore the            
                             directory or file:                                 
                                                                                
                                 SYS:HOME/MARIO/APRIL_1.COM?                    
                                    (y)es  (n)o  (r)estore_the_rest             
                                    (s)kip_the_rest                             
                                                                                
                             Respond to this prompt in one of the               
                             following ways:                                    
                                                                                
                             o   Type Y to restore or N to not restore the      
                                 directory or file.                             
                                                                                
                             o   Type R to turn off confirmation and            
                                 restore all the rest of the directories and    
                                 files that meet your restore specification     
                                 within the current directory.                  
                                                                                
                             o   Type S to skip (not restore) the rest of       
                                 the directories and files that meet your       
                                 restore specification within the current       
                                 directory.                                     
                                                                                
                             To restore all files in SYS:HOME/MARIO and         
                             its subdirectories, type                           
                                                                                
                                 RESTORE SYS:HOME/MARIO /S  <Enter>             
                                                                                
                             To restore all files with the .BAT extension       
                             in SYS:HOME/MARIO and its subdirectories,          
                             and to restore all trustee rights associated       
                             with these directories, type                       
                                                                                
                                 RESTORE SYS:HOME/MARIO *.BAT /S /T             
                                 <Enter>                                        
                                                                                
                             (Note the space between SYS:HOME/MARIO             
                             and *.BAT.)                                        

         Page 23                                                                
                                                                                
                                                                                
                             To restore files backed up from SYS:HOME/          
                             MARIO and its subdirectories, and to place         
                             the restored files (and subsequent                 
                             subdirectories) in the directory SYS:HOME/         
                             MARIO/BACKUP, type                                 
                                                                                
                                 RESTORE SYS:HOME/MARIO /S                      
                                    /R=SYS:HOME/MARIO/BACKUP  <Enter>           

                             RESTORE creates subdirectories as necessary        
                             to restore files to the new directory path.        
                                                                                
                      2b.    When prompted, type your username and              
                             press <Enter>.                                     
                                                                                
                      2c.    When prompted, type your password and              
                             press <Enter>.  (If your username has no           
                             password, press <Enter>.)                          
                                                                                
                                                                                
                    Note:    If you make a mistake while typing your            
                             password, use the Delete key, not the              
                             Backspace key, to erase your mistake.              
                                                                                
                                                                                
                      2d.    If you did not log in as SUPERVISOR or             
                             equivalent, skip to Step 2h.                       
                                                                                
                             If you logged in as SUPERVISOR, when               
                             prompted to disable logins, type Y or N.           
                             (Logins are re-enabled after RESTORE is            
                             complete.)                                         
                                                                                
                             If you answer "No," skip to Step 2h.               

         Page 24                                                                
                                                                                
                                                                                
                      2e.    If you disabled logins, you now have the           
                             option to force existing users to log out.  The    
                             current users are listed on the screen, along      
                             with the following prompt:                         
                                                                                
                                 Do you want to FORCE users to log out? (y/n) > 
                                                                                
                             If you answer "Yes," users are not logged out      
                             at this point.                                     
                                                                                
                             If you answer "No," skip to Step 2h.               
                                                                                
                             Each user is notified to log out.  Wait a few      
                             moments to give users a chance to logout.          
                                                                                
                      2f.    When prompted to clear remaining user              
                             connections, type Y or N.                          

                             If you answer "Yes," all remaining users           
                             (except the Backup VAP user) will                  
                             immediately be logged out. Skip to Step 2h.        
                                                                                
                             If you answer "No," the remaining users are        
                             not cleared.  You can continue the restore         
                             (with the users still connected) or go back        
                             and force them to log out.                         
                                                                                
                      2g.    When prompted to proceed, type Y or N.             
                                                                                
                             If you answer "No," return to Step 2e.             

         Page 25                                                                
                                                                                
                                                                                
                      2h.    When prompted, insert the tape cartridge into      
                             the tape drive and press <Enter>.  If your         
                             backup is on more than one tape, be sure to        
                             insert the first tape cartridge.  If necessary,    
                             refer to the tape insertion instructions           
                             furnished with the tape drive.                     
                                                                                
                             A message appears, indicating that the tape        
                             cartridge is being mounted (wound to the           
                             starting position on the tape).                    
                                                                                
                             Backup information stamped on the tape             
                             cartridge during BACKUP is then displayed:         
                                                                                
                                            Server: ADMIN                       
                                                                                
                                     NetWare Version:  2.2                      
                                                                                
                                 Backed up: April 11, 1991   12:05 p.m.         
                                                                                
                                            Cartridge No. 1                     
                                                                                
                      2i.    When prompted, examine the backup                  
                             information on the screen and type Y or N.         
                             (If you answer "No," either insert a different     
                             cartridge or terminate the restore session.)       
                                                                                
                             If you specified a path or filename in your        
                             RESTORE command (in Step 2a), skip to              
                             Step 3.                                            
                                                                                
                             Backup information from the tape then              
                             appears:                                           
                                                                                
                                      VOLUME SYS:                               
                                                                                
                                 Backup began at directory:                     
                                      SYS:HOME\MARIO                            
                                                                                
                                 Do you wish to restore from this volume?       
                                 (y/n) >                                        
                                                                                
                      2j.    When prompted to restore from the volume,          
                             type Y or N and press <Enter>.                     
                                                                                
                             o   If you answer "No," the volume is              
                                 skipped, and you are given the option to       
                                 terminate the restore session.                 
                                                                                
                             o   If you answer "Yes," continue with the         
                                 next step.                                     

         Page 26                                                                
                                                                                
                                                                                
                             The highest directory level on the backup          
                             tape appears:                                      
                                                                                
                                 Source Path:                                   
                                      SYS:HOME\MARIO                            
                                                                                
                                 Limit the restoration to some subdirectory of  
                                 the above Source Path? (y/n) >                 
                                                                                
                      2k.    When prompted to limit the restoration, type       
                             Y or N.                                            
                                                                                
                             o   If you answer "No," the entire source path     
                                 shown is restored (subject to restrictions     
                                 you specify in subsequent prompts).            
                                                                                
                             o   If you answer "Yes," you are prompted to       
                                 enter the name of the subdirectory             
                                 (relative to the source path) from which       
                                 restoration should begin.  For example, to     
                                 restore only the directory                     
                                 SYS:HOME/MARIO/SCHEDULE to                     
                                 SYS:HOME/MARIO, you would specify              
                                 SCHEDULE.                                      
                                                                                
                      2l.    When prompted to limit the restore using a         
                             file name or pattern, type Y or N.                 
                                                                                
                             o   If you answer "No," all files in the           
                                 specified directories are restored (subject    
                                 to restrictions you specify in subsequent      
                                 prompts).                                      
                                                                                
                             o   If you answer "Yes," you are prompted to       
                                 enter the filename or pattern, using DOS       
                                 wildcards (* and ?).  For example, to          
                                 restore all files with the .EXE extension,     
                                 specify the pattern *.EXE.                     

         Page 27                                                                
                                                                                

                      2m.    When prompted to include subdirectories,           
                             type Y or N.                                       
                                                                                
                             o   If you answer "Yes," files are restored to     
                                 the specified root directory and its           
                                 subdirectories.                                
                                                                                
                             o   If you answer "No," files are only restored    
                                 to the specified root directory.               
                                                                                
                      2n.    When prompted to confirm each file, type Y         
                             or N.                                              
                                                                                
                             o   If you answer "Yes," each time a directory     
                                 or a file matching your restore                
                                 specification is listed, you are prompted to   
                                 restore the directory or file.  (If you        
                                 specify not to restore a directory, all files  
                                 in the directory are skipped.)                 
                                                                                
                                 The confirmation prompt allows you to          
                                 turn off confirmation (and restore all         
                                 remaining applicable files) or to not          
                                 restore any more files.                        

                             o   If you answer "No," the specified              
                                 directories and files are restored without     
                                 confirmation.                                  
                                                                                
                      2o.    When prompted to restore the bindery, type         
                             Y or N.                                            
                                                                                
                             o   If you answer "Yes," the bindery files in      
                                 volume SYS are restored (no matter             
                                 which volume you are restoring to).            
                                 However, the bindery files are restored        
                                 only if they were backed up on the tape        
                                 you are restoring from (and only if you        
                                 are logged in as SUPERVISOR).                  
                                                                                
                             o   If you answer "No," the bindery files are      
                                 not restored.                                  

         Page 28                                                                
                                                                                
                                                                                
                      2p.    When prompted to restore trustees, type Y or       
                             N.                                                 
                                                                                
                             o   If you answer "Yes," the trustee rights        
                                 associated with the directory and its files    
                                 are restored.  However, the trustee rights     
                                 are restored only if they were backed up       
                                 on the tape you are restoring from.            
                                                                                
                             o   If you answer "No," the trustee rights are     
                                 not restored.                                  
                                                                                
                             You then see a prompt similar to the               
                             following:                                         
                                                                                
                                 Files and subdirectories will be restored to   
                                 the following path:                            
                                                                                
                                      SYS:HOME/MARIO                            
                                                                                
                      2q.    When prompted to restore to a different            
                             volume or directory, type Y or N.                  
                                                                                
                             o   If you answer "No," the files are restored     
                                 to the same directory they were backed         
                                 up from.  Skip to Step 2r.                     
                                                                                
                             o   If you answer "Yes," you can specify a         
                                 different destination volume and directory     
                                 to restore the files to.  The directory path   
                                 for the restored files consists of the         
                                 destination volume name and directory          
                                 you specify, plus the subdirectories (if       
                                 applicable) and files of the original path     
                                 shown in the prompt.                           
                                                                                
                                 When prompted, specify the destination         
                                 volume name and directory.  (You can           
                                 retain the default volume name and             
                                 directory by pressing <Enter>.)                
                                                                                
                             Example.  Consider files and subdirectories        
                             backed up from SYS:HOME/MARIO.  If you             
                             specified volume BOOM and directory                
                             RESTORE/FILES, the files and subdirectories        
                             would be restored to BOOM:RESTORE/FILES.           
                             The file backed up as SYS:HOME/MARIO/              
                             SCHEDULE/APRIL.91 would be restored as             
                             BOOM:RESTORE/FILES/SCHEDULE/                       
                             APRIL.91.                                          

         Page 29                                                                
                                                                                
                                                                                
                                                                                
                    Note:    If you restore AFP (Macintosh) files, you          
                             must rebuild the Macintosh desktop file after      
                             running RESTORE if both of the following           
                             are true:                                          
                                                                                
                             o   You have restored AFP files to a different     
                                 volume than they were backed up from.          
                                                                                
                             o   The volume to which the files were             
                                 restored does not contain the application      
                                 that uses the restored files.                  
                                                                                
                             If this is the case, as you rebuild the            
                             Macintosh desktop file (as instructed in your      
                             Macintosh documentation), you also need to         
                             re-enter file information comments for the         
                             restored files.                                    

                      2r.    When prompted, examine the restore                 
                             specifications as they appear on the screen,       
                             and type Y or N.                                   
                                                                                
                             o   If you answer "No," return to Step 2j.         
                                                                                
                             o   If you answer "Yes," continue with Step        
                                 3.                                             

         Page 30                                                                
                                                                                
                                                                                
         3.    Restore network files.                                           
                                                                                
                      3a.    The restore session now proceeds, according        
                             to specifications made in Step 2.  The files       
                             that were backed up on the tape are listed         
                             on the screen as they are either restored or       
                             skipped over (according to your restore            
                             specifications), in a format similar to the        
                             following:                                         

                                 SYS:HOME/MARIO/                                
                                 Restoring SYS:HOME/MARIO/APRIL_1.COM           
                                 Restoring SYS:HOME/MARIO/LOGIN                 
                                 SYS:HOME/MARIO/BU/                             
                                 SYS:HOME/MARIO/BU/161/                         
                                 Restoring SYS:HOME/MARIO/BU/161/GEO.161        
                                 Restoring SYS:HOME/MARIO/BU/161/ALPHA.161      
                                 SYS:HOME/MARIO/BU/YUBIN/                       
                                 SYS:HOME/MARIO/BU/DRIVE-C/                     
                                 Skipping SYS:HOME/MARIO/BU/DRIVE-C/CONFIG.SYS  

                                 Skipping SYS:HOME/MARIO/BU/DRIVE-C/AUTOEXEC.BAT

                                                                                
                             Error messages that appear on the screen are       
                             recorded, along with the restore date and          
                             time, in the VAP_ERR.LOG file.  This file is       
                             created in the directory from which the            
                             restore session originated, as you specified in    
                             either Step 2a or Step 2j.                         
                                                                                
                                                                                
                    Note:    The VAP_ERR.LOG file is only created for           
                             the supervisor or a user with Create rights in     
                             the applicable directory.                          

                             If you restore Apple File Protocol (AFP) files,    
                             particularly those with multiple revision          
                             numbers, these files may be renamed as they        
                             are restored.  This applies only to the DOS        
                             versions of the filenames and not to the           
                             Apple versions.  Renamed files are listed in       
                             the VAP_ERR.LOG file.                              
                                                                                
                                                                                
                      3b.    If you answered "Yes" to the "Confirm each         
                             file" prompt in Step 2n, each directory and        
                             file matching your restore specification is        
                             listed on the screen, along with a                 
                             confirmation prompt:                               
                                                                                
                                 SYS:HOME/MARIO/APRIL_1.COM?                    
                                 (y)es  (n)o  (r)estore_the_rest                
                                 (s)kip_the_rest >                              

         Page 31                                                                
                                                                                
                                                                                
                             Respond to this prompt as follows:                 

                             o   Type Y to restore or N to not restore the      
                                 directory or file.  (Remember, if you          
                                 specify not to restore a directory, all files  
                                 in the directory are skipped.)                 
                                                                                
                             o   Type R to turn off confirmation and            
                                 restore the remaining directories and files    
                                 that match your restore specification.         
                                                                                
                             o   Type S to skip (not restore) the remaining     
                                 directories and files that match your          
                                 restore specification.                         
                                                                                
                      3c.    If the tape cartridge reaches the end during       
                             the restore session, the tape is rewound, and      
                             you are prompted to insert another tape            
                             cartridge.                                         
                                                                                
                             After files have been viewed and the specified     
                             files restored, the following messages appear:     
                                                                                
                                 Reached End of Session Marker.                 
                                                                                
                                 Rewinding Tape.                                

                      3c.    If the tape cartridge reaches the end during       
                             the restore session, the tape is rewound, and      
                             you are prompted to insert another tape            
                             cartridge.                                         
                                                                                
                             After files have been viewed and the specified     
                             files restored, the following messages appear:     
                                                                                
                                 Reached End of Session Marker.                 
                                                                                
                                 Rewinding Tape.                                
                                                                                
                             After the tape cartridge has finished              
                             rewinding, the file server or router console       
                             prompt ( : ) reappears on the screen, and          
                             RESTORE is complete.                               
                                                                                
                                                                                
                    Note:    If you booted a workstation as a temporary         
                             router to run RESTORE, bring down the              
                             router (using the DOWN console command)            
                             before rebooting the computer as a                 
                             workstation.                                       

           Page 32                                                              
                                                                                
                                                                                
           Error Messages                                                       
                                                                                
                                                                                
                          The following is a list of error messages that        
                          can appear while running the Backup VAP.              
                          Other error messages are listed in the                
                          NetWare System Messages manual.                       
                                                                                
                          Use this section as a reference guide rather          
                          than as a diagnostics or troubleshooting              
                          guide.  It suggests possible causes for errors        
                          and explains steps you can take to correct            
                          the errors.                                           
                                                                                
                          Some error messages include a <value>.  Use           
                          the Extended Error Code section of the DOS            
                          Technical Reference manual to trace the error         
                          using <value>.                                        

                                                                                
                  Attachment to <server> has been lost.                         
                                                                                
                          Explanation:                                          
                                                                                
                          The connection to the file server being backed        
                          up or restored to has been lost.  This                
                          message can appear when you run BACKUP                
                          or RESTORE from a router or from a file               
                          server other than the server being backed up          
                          or restored to.                                       
                                                                                
                          Action:                                               
                                                                                
                          Restart BACKUP or RESTORE.  If this does              
                          not work, make sure the target file server is         
                          online and that you have a reliable physical          
                          connection.                                           

           Page 33                                                              
                                                                                
                                                                                
                  Bindery file <filename> not restored.                         

                          Explanation:                                          
                                                                                
                          The bindery files were not restored properly.         
                          This can be caused by a file creation error or        
                          a physical tape error.  A file server's existing      
                          bindery files are not deleted until both new          
                          bindery files are successfully restored from          
                          the backup tape, so the server should still           
                          have usable bindery files.                            
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Bindery files were not restored properly.                     
                                                                                
                          Explanation:                                          
                                                                                
                          The bindery files were not restored properly.         
                          This can be caused by a file creation error or        
                          a physical tape error.  A file server's existing      
                          bindery files are not deleted until both new          
                          bindery files are successfully restored from          
                          the backup tape, so the server should still           
                          have usable bindery files.                            
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Cannot continue restoring Bindery files.                      
                                                                                
                          Explanation:                                          
                                                                                
                          The bindery files were not restored properly.         
                          This can occur because the disk or directory          
                          table is full, or because one of the bindery          
                          files being restored from the tape is damaged.        
                          A file server's existing bindery files are not        
                          deleted until both new bindery files are              
                          successfully restored from the backup tape, so        
                          the server should still have usable bindery           
                          files.                                                
                                                                                
                          Action:                                               

                          No action is necessary.                               

           Page 34                                                              
                                                                                
                                                                                
                  Cartridge has no valid header stamp.                          
                                                                                
                          Explanation:                                          
                                                                                
                          The tape you inserted during the restore              
                          session does not have a valid header stamp            
                          (containing tape cartridge number, date and           
                          time, and so on).  This can occur if the tape         
                          header is unreadable for some reason or if            
                          you have inserted the wrong tape (that does           
                          not have a valid header).                             
                                                                                
                          Action:                                               
                                                                                
                          Insert the correct tape cartridge into the tape       
                          drive.                                                
                                                                                
                                                                                
                  Cartridge is write-protected.                                 
                                                                                
                          Explanation:                                          

                          The tape cartridge is set in the write-               
                          protected ("safe") position.                          
                                                                                
                          Action:                                               
                                                                                
                          Reset the tape cartridge so that it is not            
                          write-protected, so that backed-up data can           
                          be written to it.  (If necessary, refer to the        
                          instructions supplied with the tape cartridge.)       
                                                                                
                                                                                
                  Cartridge not properly inserted.                              
                                                                                
                          Explanation:                                          
                                                                                
                          During the tape mounting sequence, the tape           
                          cartridge was not securely seated in the tape         
                          drive.                                                
                                                                                
                          Action:                                               
                                                                                
                          Insert the tape correctly into the tape drive.        
                          (If necessary, refer to the instructions              
                          supplied with the tape drive.)                        

           Page 35                                                              
                                                                                
                                                                                
                  Encountered header <headertype> for <file2> before <file1>    
                          was done.                                             
                                                                                
                          Explanation:                                          
                                                                                
                          While a file or a directory (file1) was being         
                          restored, the header for another file or              
                          directory (file2) was encountered on the tape         
                          before the first file was completely restored.        
                          When a file or a directory is backed up, it is        
                          preceded on the tape by a header that gives           
                          the number of 4KB file blocks that the file or        
                          the directory is stored in.  This error occurs        
                          when the next header is encountered before            
                          the expected number of blocks has been                
                          restored.  If this error occurs, the first file is    
                          not restored, but the second file is.                 
                          (Headertype identifies either a file or a             
                          directory header.)                                    
                                                                                
                          Action:                                               

                          No action is necessary.                               
                                                                                
                                                                                
                  Error <value> attempting to open data fork of <filename>.     
                                                                                
                          Explanation:                                          
                                                                                
                          BACKUP or RESTORE could not open the                  
                          data fork of an Apple File Protocol (AFP) file.       
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               

           Page 36                                                              
                                                                                
                                                                                
                  Error <value> attempting to open resource fork of             
                          <filename>.                                           
                                                                                
                          Explanation:                                          

                          BACKUP or RESTORE could not open the                  
                          resource fork of an Apple File Protocol (AFP)         
                          file.                                                 
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Error <value> creating directory <directory>.                 
                                                                                
                          Explanation:                                          
                                                                                
                          RESTORE attempted unsuccessfully to create            
                          a directory on the file server.  This error           
                          happens most frequently because the disk or           
                          the volume is full, or because the user               
                          running RESTORE has insufficient rights to            
                          create a directory in the given path.                 
                                                                                
                          Action:                                               
                                                                                
                          Check whether the disk or the volume is full,         
                          and make sure you have sufficient rights to           
                          create a directory at the specified location.         
                                                                                
                                                                                
                  Error writing to Bindery file <filename>.                     
                                                                                
                          Explanation:                                          
                                                                                
                          The bindery files were not restored properly.         
                          A file server's existing bindery files are not        
                          deleted until both new bindery files are              
                          successfully restored from the backup tape, so        
                          the server should still have usable bindery           
                          files.                                                
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               

           Page 37                                                              
                                                                                
                                                                                
                  Fatal Tape Error.  Aborting Backup Session.                   

                          Explanation:                                          
                                                                                
                          The tape has been removed prematurely                 
                          during the backup session.                            
                                                                                
                          Action:                                               
                                                                                
                          Run BACKUP again, making sure the tape                
                          remains securely inserted until completion or         
                          until you are prompted to remove it.                  
                                                                                
                                                                                
                  Fatal Tape Error.  Aborting Restore Session.                  
                                                                                
                          Explanation:                                          
                                                                                
                          The tape has been removed prematurely                 
                          during the restore session.                           
                                                                                
                          Action:                                               
                                                                                
                          Run RESTORE again, making sure the tape               
                          cartridge remains securely inserted until             
                          completion or until you are prompted to               
                          insert another tape cartridge.                        
                                                                                
                                                                                
                  File <filename> is not a Bindery file.                        
                                                                                
                          Explanation:                                          
                                                                                
                          While the bindery files were being restored, a        
                          file found in the bindery area of the tape did        
                          not have a valid bindery filename.  The               
                          misnamed bindery file is not restored.                
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               

           Page 38                                                              
                                                                                
                                                                                
                  Insufficient RIGHTS to back up this path.                     
                                                                                
                          Explanation:                                          

                          You do not have sufficient rights to back up          
                          the specified volume or directory path.  You          
                          must have Read and File Scan rights in the            
                          root of the volume or directory you are               
                          backing up.                                           
                                                                                
                          Action:                                               
                                                                                
                          Run BACKUP as user SUPERVISOR, or as a                
                          user with Read and File Scan rights in the            
                          root of the volume or directory you are               
                          backing up.  Or, get the network supervisor           
                          to grant you additional rights to run                 
                          BACKUP.                                               
                                                                                
                                                                                
                  Invalid Backup option switch.                                 
                                                                                
                          Explanation:                                          
                                                                                
                          When starting BACKUP, you specified an                
                          option other than the valid options (/B, /S,          
                          and /T).                                              
                                                                                
                          Action:                                               
                                                                                
                          Type the BACKUP command using valid                   
                          options.                                              
                                                                                
                                                                                
                  Invalid Path specification.                                   
                                                                                
                          Explanation:                                          
                                                                                
                          You used an invalid format when specifying a          
                          path in the BACKUP or RESTORE command.                
                                                                                
                          Action:                                               
                                                                                
                          Specify the path using the correct format.            

           Page 39                                                              
                                                                                
                                                                                
                  Specified destination path <path> is not valid.               

                          Explanation:                                          
                                                                                
                          The path you specified in your RESTORE                
                          command using the /R option is not a valid            
                          directory path.                                       
                                                                                
                          Action:                                               
                                                                                
                          When you use the /R option, specify a valid           
                          directory path.                                       
                                                                                
                                                                                
                  Supervisor access level is required to back up the Bindery.   
                                                                                
                          Explanation:                                          
                                                                                
                          You specified (with the /B option) to back up         
                          the bindery files.  However, to back up the           
                          bindery files, you must run BACKUP as                 
                          SUPERVISOR (or supervisor equivalent).                
                                                                                
                          Action:                                               
                                                                                
                          Log in as SUPERVISOR or equivalent.                   


                  Supervisor access level is required to restore the Bindery.   
                                                                                
                          Explanation:                                          
                                                                                
                          You specified (with the /B option) to restore         
                          the bindery files.  However, to restore the           
                          bindery files, you must run RESTORE as                
                          SUPERVISOR (or supervisor equivalent).                
                                                                                
                          Action:                                               
                                                                                
                          Log in as SUPERVISOR or equivalent.                   

           Page 40                                                              
                                                                                
                                                                                
                  The Bindery was not backed up with this volume.               
                                                                                
                          Explanation:                                          
                                                                                
                          You are attempting to restore the bindery             
                          files from a tape to which the bindery files          
                          were not backed up.                                   
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  The directory table on volume <volume> is full.               
                                                                                
                          Explanation:                                          
                                                                                
                          While you were restoring to the specified             
                          volume, the volume ran out of available               
                          directory entries.                                    
                                                                                
                          Action:                                               
                                                                                
                          Increase the number of directory entries on           
                          the volume or delete unneeded files.  (You            
                          can run VOLINFO to view the number of                 
                          available directory entries.)                         

           Page 41                                                              
                                                                                
                                                                                
                  The existing Bindery has been damaged.                        
                                                                                
                          Explanation:                                          
                                                                                
                          While the bindery was being restored there            
                          was a problem with the restored bindery file          
                          (from the tape).  However, the system could           
                          not rename the original bindery back to its           
                          correct name.                                         
                                                                                
                          Whenever bindery files are restored, backup           
                          copies (with modified filenames) of the               
                          original bindery files are kept until new             
                          bindery files are successfully restored from          
                          the tape.  If the new bindery files are not           
                          successfully restored, the original bindery files     
                          are renamed to their original filename.  This         
                          message indicates that the original files were        
                          not successfully renamed.                             
                                                                                
                          Action:                                               

                          You may need to repair the original bindery           
                          with VREPAIR.                                         
                                                                                
                                                                                
                  The path string contained illegal characters.                 
                                                                                
                          Explanation:                                          
                                                                                
                          The path you specified contained illegal              
                          characters.                                           
                                                                                
                          Action:                                               
                                                                                
                          Retype the path string using only legal path          
                          characters.                                           
                                                                                
                                                                                
                  This is Cartridge No. <number> but Cartridge No. <number>     
                          was requested.                                        
                                                                                
                          Explanation:                                          
                                                                                
                          RESTORE prompted you to insert a certain              
                          tape cartridge and you inserted a different           
                          cartridge.                                            
                                                                                
                          Action:                                               
                          Insert the tape cartridge with the specified          
                          number.                                               

           Page 42                                                              
                                                                                
                                                                                
                  Trustees were not backed up with this volume.                 
                                                                                
                          Explanation:                                          
                                                                                
                          You are attempting to restore trustee rights          
                          from a tape to which trustee rights were not          
                          backed up.                                            
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Unable to create file <filename>.                             
                                                                                
                          Explanation:                                          
                                                                                
                          RESTORE failed to create the specified                
                          filename.  This could occur if you have               
                          insufficient rights or if the hard disk has           
                          insufficient space.                                   
                                                                                
                          Action:                                               
                                                                                
                          Make sure you have sufficient rights to               
                          restore the file and that there is sufficient         
                          disk space.                                           
                                                                                
                                                                                
                  Unable to log in as <username>.  Error = <value>.             
                                                                                
                          Explanation:                                          
                                                                                
                          You were unable to log in because you                 
                          entered an invalid username or an incorrect           
                          password, or for the reason specified by              
                          <value>.                                              
                                                                                
                          Action:                                               

                          Enter a valid username with the correct               
                          password, or correct the condition indicated          
                          by <value>.                                           

           Page 43                                                              
                                                                                
                                                                                
                  Unable to transfer data fork of <filename>.                   
                                                                                
                          Explanation:                                          
                                                                                
                          RESTORE was unable to transfer the data               
                          fork of the specified Apple File Protocol (AFP)       
                          file.                                                 
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Unable to transfer resource fork of <filename>.               

                          Explanation:                                          
                                                                                
                          RESTORE was unable to transfer the                    
                          resource fork of the specified Apple File             
                          Protocol (AFP) file.                                  
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               
                                                                                
                                                                                
                  Unrecoverable data error.                                     
                                                                                
                          Explanation:                                          
                                                                                
                          There is a major problem with the tape                
                          cartridge, tape drive, or tape controller.            
                                                                                
                          Action:                                               
                                                                                
                          Replace the faulty tape cartridge, or have the        
                          tape drive or tape controller serviced.               
                                                                                

                  User <username> does not exist on this server.                
                                                                                
                          Explanation:                                          
                                                                                
                          When starting BACKUP or RESTORE you                   
                          specified an invalid username.                        
                                                                                
                          Action:                                               

                          Restart BACKUP or RESTORE using a valid               
                          username.                                             

           Page 44                                                              
                                                                                
                                                                                
                  Volume <volume> does not exist on this server.                
                                                                                
                          Explanation:                                          
                                                                                
                          You are attempting to restore to a volume             
                          that does not exist on the file server.  This         
                          could happen when you try to restore a                
                          directory path backed up from one server to           
                          the same directory path (on a nonexistent             
                          volume) on another server.                            

                          Action:                                               
                                                                                
                          Specify the correct destination directory path        
                          when starting RESTORE.                                
                                                                                
                                                                                
                  WARNING! Restoring AFP files to a DOS server may lose         
                          information.                                          
                                                                                
                          Explanation:                                          
                                                                                
                          You are attempting to restore Apple File              
                          Protocol (AFP) files (backed up on a file             
                          server that does support AFP files) to a file         
                          server that does not support AFP calls.  In           
                          doing so, you will lose the information from          
                          the resource forks of the AFP files.                  
                                                                                
                          Action:                                               
                                                                                
                          No action is necessary.                               


                  You have entered an invalid Password for user                 
                          <username>.                                           
                                                                                
                          Explanation:                                          
                                                                                
                          While starting BACKUP or RESTORE you                  
                          specified the incorrect password for the              
                          username.                                             
                                                                                
                          Action:                                               
                                                                                
                          Restart BACKUP or RESTORE using the                   
                          correct password for the username.                    

             Index                                                              
                                                                                
                                                                                
                               A                                                
                                                                                
                               AFP (Apple File Protocol) files                  
                                   Macintosh desktop file, rebuilding  29       
                                   renamed by RESTORE utility  30               
                                                                                
                               B                                                
                                                                                
                               BACKUP utility.  See also Backup VAP             
                                   bindery files, backing up  10                
                                   command, entering  10                        
                                   file server, selecting  9                    
                                   logins, disabling  12                        
                                   planning  7                                  
                                   subdirectories, backing up  10               
                                   tape cartridge, inserting  14                
                                   trustee rights, backing up  10               
                                   volumes, specifying  14                      
                               Backup VAP.  See also BACKUP utility; RESTORE    
                                       utility                                  
                                   configuring  3                               
                                   error messages  32                           
                                   installation  1                              
                                   loading  5                                   
                                   SELECTSERVER command  9, 19                  
                               Bindery files                                    
                                   backing up  10                               
                                   restoring  21, 27                            
                                                                                
                                                                                
                               D                                                
                                                                                
                               Directory path                                   
                                   specifying in BACKUP  10                     
                                   specifying in RESTORE  20                    
                                                                                
                               E                                                
                                                                                
                               Error messages  32                               

                              F                                                
                                                                                
                               File server                                      
                                   specifying in BACKUP  9                      
                                   specifying in RESTORE  19                    
                               Filename                                         
                                   selecting in BACKUP  10                      
                                   selecting in RESTORE  20, 25                 
                                                                                
                               I                                                
                                                                                
                               Installation                                     
                                   Backup VAP  3                                
                                   configuration options  2                     
                                   hardware  1                                  
                                   NetWare versions supported  1                
                                   VAPs, renaming  5                            
                                                                                
                               L                                                
                                                                                
                               Logins                                           
                                   disabling in BACKUP  12                      
                                   disabling in RESTORE  24                     
                                   reasons to disable  8, 18                    
                               Logouts                                          
                                   forcing in BACKUP  12                        
                                   forcing in RESTORE  24                       
                                                                                
                               M                                                
                                                                                
                               Macintosh desktop file, rebuilding  29           
                                                                                
                               O                                                
                                                                                
                               Options                                          
                                   specifying in BACKUP  10                     
                                   specifying in RESTORE  21                    
                                                                                
                               P                                                
                                                                                
                               Password                                         
                                   specifying in BACKUP  11                     
                                   specifying in RESTORE  23                    

                               R                                                
                                                                                
                               Restore destination, specifying  21, 28          
                               RESTORE utility                                  
                                   bindery files, restoring  21, 27             
                                   command, entering  20                        
                                   file server, selecting  19                   
                                   files, confirming  27, 30                    
                                   logins, disabling  24                        
                                   Macintosh desktop file, rebuilding  29       
                                   planning  17                                 
                                   restore destination, specifying  21, 28      
                                   subdirectories, restoring  21, 27            
                                   tape cartridge, inserting  25                
                                   trustee rights, restoring  21, 28            
                                   VAP_ERR.LOG, renamed AFP files listed in  30 
                                   volume, specifying  25                       
                               Router                                           
                                   bringing down  16, 31                        
                                   selecting file server from  9, 19            
                                   using workstation as  1                      
                                                                                
                               S                                                
                                                                                
                               SELECTSERVER command                             
                                   selecting the file server to back up  9      
                                   selecting the file server to restore to  19  
                               Server, file                                     
                                   selecting in BACKUP  9                       
                                   selecting in RESTORE  19                     
                               Subdirectories                                   
                                   backing up  10                               
                                   restoring  21, 27                            
                                                                                
                               T                                                
                                                                                
                               Tape cartridge                                   
                                   inserting  14, 25                            
                                   using additional  16, 31                     
                               Trustee rights                                   
                                   backing up  10                               
                                   restoring  21, 28                            

                               U                                                
                                                                                
                               Username                                         
                                   planning which to use  8, 18                 
                                   specifying  11, 23                           
                                                                                
                               V                                                
                                                                                
                               VAP_ERR.LOG file                                 
                                   purpose of  16, 30                           
                                   renamed AFP files listed in  30              
                                   backing up  10                               
                                   restoring  21, 28                            

                               W                                                
                                                                                
                               Workstation, using as router  1