Observer 2.0




(c) 1994 Network Instruments, LLC
    P.O. Box 581156
    Minneapolis, MN  55458-1156
    (612) 822-2025
FAX (612) 825-5647
BBS (612) 822-0902








TABLE OF CONTENTS
TABLE OF CONTENTS					1
INTRODUCTION TO OBSERVER				7
Functional Overview					8
Observer						8
Netware Discoverer					10
Who Should use Observer and Netware Discoverer		12
Limited Warranty					15
Copyright and License					15
System Requirements					16
Technical Support					17
INSTALLATION						19
Licensing						19
Quick overview for experts				21
Putting the files on your PC:				21
Configuring the DOS component of Observer:		22
Configuring the DOS component of Netware Discoverer:	23
Running Observer and Netware Discoverer:		24
Step by Step Installation:				24
Differences between ODI, NDIS and the Packet Driver	25
Step 1: Configuring ODI, NDIS or a Packet Driver.	27
Procedure 1a: Configuring ODI				28
Procedure 1b: Using NDIS				31
Procedure 1c: Using a Packet Driver			31
Step 2: Copy the Observer files onto the PC		34
USING OBSERVER						41
Overview and quick start				41
Filters							43
Saving a Filter						45
Adding and Editing Hardware Addresses			46
Setting hardware address Filters			47
Choosing a Protocol AS A sub-filter			49
Discovery Mode						50
Monitoring your LAN: Network Statistics			52
Bandwidth Utilization mode				52
General Statistics Information				55
Received Packets Statistics				56
Size Distribution Statistics				58
Protocol Statistics					60
Printing Statistics screens				61
Capturing packets on your LAN:  Packet capture mode	61
Viewing Captured Packets				63
Printing captured packets				67
Saving Captured Packets to a File			69
Settings Dialog						70
Program Flags						74
OBSERVER.EXE						74
VPACK and VPACKODI					75
USING NETWARE DISCOVERER				81
Overview and quick start				81
The Main MDI Window					84
File Menu						85
Options Menu						87
The Preferences dialog					88
Discoverer Discovery Mode				92
Server exclusion List					93
Login to Server						94
The Window Menu						96
The MDI Window Button Bar				96
The List of Nodes View					98
Information Windows (general)				99
Server Information Windows				103
Charts							103
Number Connections (server)				104
Open Files (server)					104
IPX Packet Statistics (server)				104
SPX Packet Statistics (server)				105
Total Packet Statistics (server)			105
Bridge Statistics (server)				106
Volume Usage (server)					109
Options							109
Lists							110
IPX Packet Statistics List (server)			110
SPX Packet Statistics List (server)			113
Total Packet Statistics (server)			117
Bridge Statistics List (server)				119
Volume Information List (server)			121
Open Files List (server)				122
Info:							122
Server Version (server)					122
IPX-SPX Versions (server)				122
Bridge Driver Configuration (server)			123
Node Information Windows				124
Charts							125
IPX Packet Statistics chart (node)			125
SPX Packet Statistics chart (node)			126	
Total Node Packets chart (node)				126
Options							127
Lists							127
IPX Packet Statistics List (node)			128
SPX Packet Statistics List (node)			130
Shell Driver Statistics List (node)			134
Shell Statistics List (node)				137
Info							139
OS Version Information (node)				140
IPX-SPX Versions (node)					140
Shell Driver Configuration (node)			140
User Volume Information (node)				142
REFERENCE						145
A Short Overview of TCP/IP for troubleshooting		145
Monitoring TCP/IP Sessions with Observer		148
Ethernet Frame Header					148
Token Ring Frame Header					150
IEEE 802.2 and IEEE 802.2_SNAP subheaders		151
Internet Addresses					152
Address Resolution Protocol (ARP)			153
Internet Protocol (IP)					155
Transport Control Protocol (TCP)			158
User Datagram Protocol (UDP)				162
Internet Control Message Protocol (ICMP)		163
Short Overview of Novell’s IPX and SPX protocols	166
Internetwork Packet Exchange (IPX) packet header	167
Sequential Packet Exchange (SPX) packet header		168
NetWare Core Protocol (NCP).				171
Service Advertising Protocol (SAP).			176
Routing Information Protocol (RIP).			177
Serialization packets.					179
WatchDog Packets					179
APPENDIX						181
Program Descriptions					181
Troubleshooting						183
Observer Troubleshooting				185
Discoverer Troubleshooting				189
Sample Configuration Files:				190
ODI:							190
NDIS:							191
Packet Driver:						192
Packet Driver Installation Information			192
INDEX							199



INTRODUCTION TO OBSERVER
As Local Area Networks (LANs) become part of 
our every day lives, the need to manage and 
troubleshoot these LANs becomes increasingly 
important.  Most network operating systems have 
some ability to diagnose problems but these 
abilities usually fall short as truly useful LAN analysis 
tools.

Observer is a LAN analyzer (packet viewer and 
decoder), network load monitor, Novell network 
statistics gathering tool, and much more.

Observer was designed to be useful to both the 
average LAN user and the computer professional.  
Observer can be used by a system administrator, 
network user, programmer, network application 
developer, network product tester - basically 
anyone who needs to know exactly what 
happens on a network, and/or how to make a 
network run smoothly.

After using Observer, network administrators will 
not be able to imagine how it was possible to 
work without it.   Observer allows you to truly "see" 
your LAN working.

Observer allows you to keep track of your network 
conditions, warns you about a network overload, 
and captures packets from a single computer (or 
multiple computers) on the network.  Observer’s 
Netware Discoverer collects Novell specific 
statistics and displays or graphs them over time.
FUNCTIONAL OVERVIEW
Observer contains two separate programs 
designed to complement each other:

Observer is the network analyzer that captures 
packets into a buffer, and decodes that capture 
buffer.  Observer also includes a number of 
statistical collection processes that display 
different types of LAN activity over time.  By 
design, Observer only "observes" it only listens to 
the network, it does not generate any traffic.

Netware Discoverer is a Netware specific 
statistical collection tool.  Unlike Observer, 
Discoverer continually polls both Novell Servers 
and nodes to collect statistics and information.  
Because Discoverer polls each station, it is quite 
active on your LAN, and (using Observer if you 
like) you will see that Discoverer generates its own 
small amount of LAN traffic.

Observer
Observer has four main modes.  Each mode gives 
you insight into different functions of your LAN in 
real time.  Most modes are affected by the filters 
you set.

DISCOVERY mode allows you to capture all of the 
network addresses on your LAN, store them in the 
filters table, and alias them as names or IP 
addresses.

PACKET CAPTURE mode displays a graph that 
represents your current packet capture state.  This 
graph shows you, in real time, how many and 
what kind of packets are being captured and 
whether packets are being dropped.  Once 
packets have been captured, they can be 
viewed using the packet capture’s view mode.

BANDWIDTH UTILIZATION has two modes:  Standard 
Bandwidth Utilization allows you to graphically 
monitor the amount of your total network 
bandwidth that is currently being used - showing 
the data in a sliding 8-16 minute graph.  Long 
Term Bandwidth Utilization (LTBU) shows 
graphically high, low, and average utilization over 
a tunable time frame (up to 7 days), and allows 
the data to exported to a comma delimited 
spreadsheet format for further analysis and 
charting.

NETWORK STATISTICS includes Received Packet 
Statistics, Size Distribution Statistics, and Protocol 
Statistics.  These statistical modes let you see who 
is using your LAN and who or what is generating 
traffic.  Each modes sheds different light on the 
workings of your LAN.

In each of the four modes, there are many filters 
and sub-filters which can be used.  You can 
choose to trace all protocols on your network, or 
choose only a subset of protocols to filter on.  
Packet capturing and filtering can help you 
localize problems.  Translation of packets into 
function and type gives a record and an 
explanation of the data exchange on a LAN.  If 
you need to thoroughly study packet content 
byte by byte, raw mode allows the packets to be 
viewed without any translation.  Once packets 
are captured, you can filter and print captured 
packets to a printer or to a file.
Netware Discoverer
Netware Discoverer provides detailed information 
and statistics collected from Novell servers, 
stations, bridges and routers.  Discoverer also 
provides a Discovery Mode search similar to 
Observer's Discovery Mode.  Discoverer’s 
Discovery Mode supplements Observer's 
Discovery Mode auto aliasing of IP address to the 
hard network address - in Netware Discoverer's 
Discovery Mode, you can auto alias a users Novell 
login name to the hard network address.

Netware Discoverer supplies information about a 
specific Novell Server, and all of the Novell Servers 
reachable on the network (both LAN and WAN).

For servers, some examples of this kind information 
are: the number of users logged in on a server, 
the nodes that are currently down, free/used disk 
space on all volumes, number of open files - the 
total number and the number used by each user, 
and much more.  For users, it gives information 
about number of files, directories and disk space 
used.

Statistical information from the Server's Bridge 
drivers provides information about the general 
condition of the network and routing activity 
between networks.  IPX and SPX statistics provide 
information about a particular node or server, 
number of packets sent and received, number of 
good and bad packets, ECB availability and 
failures.

Lists provide miscellaneous version information 
about servers, stations and users, which may be 
useful for a network administrator during daily 
operation, and particularly for keeping a network 
up to date. 

Important information that changes over time 
can be monitored as it develops in a graphical 
format (charts).  These include IPX and SPX traffic 
statistics, number of users attached to a server, 
volume usage, and bridge statistics.  All of these 
graphs are auto scrolling, showing your particular 
information graphically, as it develops over time.

Finally, all of this information is provided in a MDI 
(Multiple Document Interface), where a system 
administrator can simultaneously monitor the 
general condition of a network server, and a 
number of servers or users in particular - displaying 
similar information, or completely different 
information, all at the same time in each MDI sub-
window (known as an information window).

Information windows come in two classes; 1) 
NODE information windows that display station 
(node) information and charts, and 2) SERVER 
information windows that display information that 
the server provides.

For example, the initial list on the left of the 
Discoverer main MDI window (The List of Nodes) 
shows a list of servers.  Each Netware server can 
be double clicked on (using the LEFT mouse 
button) to display a list of users currently 
connected to that server (print and other servers 
may or may not have users associated with 
them).  Clicking on the RIGHT mouse button on a 
server or node icon opens the SERVER or NODE 
information window (on the right of the MDI 
window).

On the right part of the MDI window there can be 
a server graphic chart showing network traffic on 
a server, and volume information of another 
server, a number of NODE windows showing 
statistics and charts for different users attached to 
different servers.  In essence, it is like a Windows 
within Windows, where SERVER or NODE 
information windows can be re-sized, placed in 
different order, tiled, cascaded, minimized, etc.  
With all of this power, an administrator can run 
Discoverer and notice very little interruption of the 
other functions of the Windows PC - Discoverer 
takes very little resource to function.
WHO SHOULD USE OBSERVER AND NETWARE DISCOVERER
Any LAN administrator, network programmer, or 
LAN user will find Observer and Netware 
Discoverer helpful.  Observer’s utilities were 
designed to meet the needs of the most technical 
network professional, as well as to provide 
information for an average LAN user.

Observer will be most useful for a network LAN 
administrator who  knows his or her LAN workings 
from a functional view, but wants to see what is 
really going on "on the wire" for troubleshooting 
an existing problem or pre-solving a network 
condition that could spell disaster in the future.

Observer, like all network analyzers "sees" all 
traffic on your LAN segment.  To see and analyze 
traffic on a different segment, you will need to 
load and run Observer from a PC on that 
segment.  If you find this limitation inconvenient or 
impractical (your segments are located on a 
WAN), you may want to consider upgrading (or 
purchasing - if you do not own Observer) to 
Network Instruments Analyst/Probe.

Analyst/Probe provides complete Observer 
functionality over a multi-segment LAN or WAN.  It  
allows you to "see" and analyze up to 253 
segments of a LAN or WAN from an Analyst PC.  
Probes are software modules that are loaded on 
a Windows PC on each segment that the Analyst 
PC communicates with via TCP/IP.  Contact your 
dealer or Network Instruments for more 
information on Analyst/Probe.

Discoverer will be most useful for a Novell Netware 
administrator that manages Netware LANs that 
are either physically far apart or have elusive non-
reproducible problems that happen over the 
course of time and need to be isolated.

Note:  Netware Discoverer is only useful if you 
have a Novell LAN.  If you do not have a Novell 
LAN, do not choose to install Netware Discoverer 
during the installation process.

To set up and use Observer and Netware 
Discoverer, you will need to be familiar with both 
DOS and Windows, including editing files, 
changing  configurations, and have a basic 
knowledge of your LAN setup.

Observer contains both DOS and Windows 
programs.  Observer must be installed on at least 
one PC on each network segment to analyze 
network traffic.  For Observer installation, a 
network card is required for each PC.  No 
additional hardware is required on the Observer 
PC.

Netware Discoverer requires LSL.COM, 
IPXODI.COM and the VLMs (VLM.EXE and any 
other components your VLM is configured to use) 
to be installed and running.  Additionally, you will 
need to have Novell's Windows Network support 
drivers and DLL’s properly (and completely) 
installed on your PC (NETWARE.DRV, NWCALLS.DLL 
and NWIPXSPX.DLL and all of the DLL’s, DRV’s and 
VxD’s and *.386’s that they call need to be 
present in your Windows SYSTEM subdirectory).  If 
you are using Microsoft Windows for Workgroups 
(WFW), you will need to make certain you are 
using WFW over ODI, and make sure that you 
have set up Windows Networking to recognize the 
Netware Shells.

The Netware Windows drivers and DLL's are 
proprietary programs of Novell Inc., and are either 
included with your Novell system or you can 
download the latest versions of the Drivers and 
DLL's from Internet (ftp.novell.com), from 
Compuserve, or ask your Novell dealer for the 
latest VLMUPx, WINDRx and NWDLLx (where "x" is 
the version number).
LIMITED WARRANTY
Network Instruments, LLC will replace defective 
media or documentation for 90 days after the 
shipment of the product from Network 
Instruments, LLC.  Should Network Instruments, LLC 
release a new version of Observer within 60 days 
of shipment of the product, Network Instruments, 
LLC will update the copy of Observer at no 
charge.  This update may consist of disks or a 
manual or both, at the discretion of Network 
Instruments, LLC.

The Observer license does not guarantee the 
usability of Observer, expressed or implied.  In 
cases of loss, destruction, or corruption of data, 
Network Instruments, LLC shall not be liable.

Network Instruments, LLC makes no other 
warranty.

COPYRIGHT AND LICENSE
Observer (including Netware Discoverer) is neither 
shareware nor freeware.  Observer is a 
commercial software package that is subject to 
international copyright laws.

Upon registration of the 1-25 Node LAN version of 
the Observer product you are licensed to use 
Observer at one site on one LAN, if and only if that 
LAN has less than 25 nodes connected in total.  If 
you have a LAN with more than 25 nodes, you will 
need the 25+ Node LAN version of the Observer 
product.  The 25+ Node LAN Observer product is 
also licensed for one site and one LAN.

If you have multiple LANs (LANs which are not 
connected to each other) or multiple physical 
sites (different locations or buildings), you will 
need to purchase additional copies of Observer.

Multiple site licenses and multiple LAN licenses are 
available at a reduced license fee.  Contact 
Network Instruments for more information.

Observer is the property of Network Instruments, 
LLC and may not be copied for purposes other 
than backup.

Depending on how you purchase Observer you 
will either have a RTU (Right To Use) license, or 
upon registration of the DEMO you will receive a 
RTU.  In either case the RTU is your proof of 
purchase.  You will need to produce this 
document for upgrades and you will need to 
provide the RTU activation numbers to receive 
technical support.

This software is licensed as stated above.  The 
license does not constitute ownership of the 
software, only the right to use it.
SYSTEM REQUIREMENTS
Minimum: 486SX/25 w/4MB RAM, Windows 3.1, a 
supported network adapter, and a VGA color 
monitor.  Note:  If you are using Windows for 
Workgroups, the minimum RAM required is 8MB.

Recommended: 486DX/25 (or faster) w/16MB 
RAM, Windows 3.1 (or 3.11), a 16 bit network 
adapter, a fast 16 bit VGA adapter, and a 15" 
VGA color monitor running in at least 800x600 
resolution.

Observer may run on systems with less power and 
RAM than those listed above, but Network 
Instruments does not support configurations with 
less than the minimum stated requirements.
TECHNICAL SUPPORT
Network Instruments provides technical support 
from 9:00 AM to 5:00 PM Central Standard Time.  
Technical support is provided on the phone at 
(612) 822-2025, by fax at (612) 825-5647, or by 
email at support@netinst.com.

Before calling technical support please read the 
troubleshooting section at the end of this manual, 
and the README.WRI on your distribution disk to 
see if your problem has not already been 
answered.






INSTALLATION

LICENSING
Observer is always sold in a DEMO version.  The 
DEMO version can be licensed to become a fully 
functioning product.

Observer will run in DEMO mode until it is licensed.  
The DEMO mode will simulate LAN traffic and 
does not require a LAN or LAN hardware to be 
present.  If you choose to install Observer’s 
Netware Discoverer, it will run in DEMO mode 
"unlicensed" for 5 minutes, and then it will disable 
itself (Note: Netware Discoverer DOES require a 
network adapter and ODI to be loaded even in 
DEMO mode).

The DEMO mode is provided so that a potential 
Observer user can get a feel for the package 
without having to purchase it.  You can turn a 
DEMO version of Observer into a licensed version 
with a key number as described below.

This key number is unique and can only be used 
for one copy of Observer and will only work for 
one site.  The key number will either enable 
Observer for use on a 1-25 node LAN or a 25+ 
node LAN, depending on the license fee paid.  A 
1-25 node license key number will not work on a 
25+ node LAN.

To turn the DEMO version of Observer into a full 
functioning licensed version, you will need to fill 
out the license dialog with your name and your 
company name to generate your unique 
customer registration number.  To bring up the 
license dialog, choose "File" -> "License" from the 
main Observer (or Discoverer) screen.

Once the licensing information has been filled out, 
you will need to fax your company registration 
number (and payment - depending on how you 
purchased Observer) to Network Instruments to 
receive your key number.  The key number will 
turn your DEMO copy of Observer into a fully 
functioning copy of Observer.  Network 
Instruments FAX number is (612) 825-5647.

Depending on where and how you purchased 
Observer, you may have a "Right to Use" (RTU) 
certificate.  If you have purchased such a 
certificate, follow the instructions on the Right to 
Use document to license Observer.  If a Right to 
use certificate came with your copy of Observer, 
follow the instructions on that Right to Use 
document to license Observer.

Once you have licensed Observer, Observer and 
Observer’s Netware Discoverer will automatically 
be licensed.
QUICK OVERVIEW FOR EXPERTS
Putting the files on your PC:
Run the Observer installation program from 
Windows by putting the Observer disk in your 
floppy drive and running the program 
A:\INSTALL.EXE from the Windows "File" -> "Run" 
menu.

Install will ask you which directory you want 
Observer to be installed into.  Unless you have a 
compelling reason to install Observer elsewhere, 
we suggest that you install Observer in the default 
destination.

INSTALL lets you choose between DEMO mode 
(check the DEMO box) or licensed mode (un-
check the DEMO box).  As mentioned above, 
DEMO mode will simulate network traffic so that 
you can see Observer functioning as if it were on 
a real LAN.

When installing in DEMO mode, you will not be 
given the chance to install Netware Discoverer 
(see note below for more information on 
DEMOing Netware Discoverer).

Once the product is licensed, and the key 
number is provided, Observer will capture data 
from your LAN, and work without any of the DEMO 
limitations.

If you install in licensed mode, Observer’s 
installation program will offer to make the required 
changes in your AUTOEXEC.BAT (and other 
required files).  Observer’s install will also ask you if 
you would like to install Netware Discoverer - 
make the appropriate choice.

Note:  If you do not have a Novell LAN, do not 
install Netware Discoverer.  If you are not using 
ODI, you cannot use Netware Discoverer.  See 
note below.

Make sure to check the README.WRI for any late 
breaking installation information.

[NOTE:  Because Netware Discoverer requires ODI, 
including LSL, IPXODI, VLM support and ALL of the 
Netware Windows DRV’s, DLL’s, 386’s and VxD’s, it 
is not automatically installed during DEMO 
installation.  If you would like to DEMO Netware 
Discoverer, and are confident that you have your 
Windows PC properly configured as described 
above, uncheck the DEMO box and install 
Observer in licensed mode, including Netware 
Discoverer.  Both Observer and Netware 
Discoverer will run in DEMO mode if not licensed.  
For Observer this means it will play simulated data, 
for Netware Discoverer this means that it will only 
function for 5 minutes, but it will see real data from 
your LAN.)
Configuring the DOS component of Observer:
If you are installing in licensed mode, Observer’s 
Windows programs require a DOS TSR that 
interfaces with your network driver and makes 
packets available to the various Windows DLL’s 
and programs.  This TSR can take less than 5K of 
RAM.

Observer’s installation program will ask if you 
would like to use ODI, NDIS, or the Packet Driver.

If you choose ODI, INSTALL will install 
VPACKODI.EXE in your AUTOEXEC.BAT for you.

If you choose NDIS, INSTALL will install 
DISPKT10.DOS, modify your PROTOCOL.INI, 
SYSTEM.INI and install VPACK.EXE into your 
AUTOEXEC.BAT.

If you choose the Packet Driver, INSTALL will install 
VPACK.EXE in your AUTOEXEC.BAT for you.

ODI, NDIS, and Packet Driver installation methods 
expect that your network is up and running and 
configured correctly for a protocol analyzer to 
function.  If you run into troubles, see the step by 
step installation for your particular network setup 
for help.

(For ODI, see step 1a below for an example of a 
NET.CFG to use with VPACKODI.EXE.]
Configuring the DOS component of Netware Discoverer:
If you choose to install Netware Discoverer, it 
requires: ODI and the VLM’s to be installed and 
running.  Additionally, you will need to have 
Novell's Windows Network support DRV’s, VxD’s, 
386’s, and DLL’s properly (and completely) 
installed on your PC.  For more information on 
exactly what is required see the  "If you are using 
Netware Discoverer" section under procedure 1a.  
Note: If you are using Microsoft Windows for 
Workgroups (WFW), you will need to make certain 
you are using WFW over ODI.

If installing in licensed mode, install will then ask to 
reboot your PC.
Running Observer and Netware Discoverer:
Once you have rebooted and VPACK.EXE (or 
VPACKODI.EXE) has been loaded, you can start 
Observer by double clicking on the Observer icon 
in the Observer group.  Start Netware Discoverer 
by double clicking the Netware Discoverer icon.

If Observer fails to load with an error indicating 
that you do not have enough DOS memory to 
allocate VPACK (or VPACKODI’s) buffer space, 
see the section on Program Flags later in this 
manual, or the troubleshooting section in the 
Appendix.  This describes the way to lock VPACK 
(or VPACKODI’s) buffer space prior to going into 
Windows before other applications can steal it 
away.
STEP BY STEP INSTALLATION:
The installation of Observer will involve the 
following 4 steps:

1. Decide which network stack you are 
using/going to use.  Prepare that stack if 
necessary.

2. Run INSTALL.EXE from Windows.

3. Decide if you will install Netware Discoverer.

4. Reboot your PC.

If you are installing Observer in DEMO mode, you 
will not need to go through Step 1, you can go 
directly to Step 2.

This installation procedure expects that you have 
your network adapter installed and configured 
properly.  If you are able to connect to your 
network and run your network software, you 
probably have the network adapter installed and 
configured properly.

If you are using ODI to interface with your network 
adapter, you may need to modify your NET.CFG 
ODI configuration file.  If you are using NDIS, make 
sure that your NDIS network is up and running.  If 
you plan to use the Packet Driver, you will need to 
know what kind of network adapter you will be 
using and the various hardware settings of your 
network adapter for step 1.

Note: If you plan on using Netware Discoverer, 
you must use ODI.
Differences between ODI, NDIS and the Packet Driver
If you are using Novell, we recommend that you 
use ODI as your network access method.  This 
includes Windows for Workgroups with Novell.  If 
you plan on using Netware Discoverer you MUST 
use ODI and set up the VLM’s (if you do not know 
what the VLM’s are, see you Novell supplier, or 
contact Network Instrument’s support 
department).

If you are using Windows for Workgroups without 
Novell, we recommend that you use NDIS for your 
network access.

If you are not using either ODI or NDIS we 
recommend that you use the Packet Driver for 
your network access.

ODI is Novell’s method for accessing the network 
from a DOS or Windows PC.  ODI was designed 
with network monitors in mind and provides a 
complete interface for Observer while allowing 
other network traffic to flow.  Because of this, ODI 
is the preferred method for running Observer.

If you use ODI for your network interface, 
VPACKODI.EXE will work in conjunction with 
LSL.COM so that you can concurrently use both 
Observer and your Novell (or any other) network 
software.

NDIS also allows you to use most network shells 
and Observer at the same time.  Some network 
software (specifically some TCP/IP’s that use 
blocking calls may not run concurrently with NDIS 
and Observer).  If you experience trouble with 
Observer and your other network, try not loading 
your other network software while running 
Observer.  Note:  When using NDIS, Observer will 
suspend all packet receives when you switch to a 
full screen DOS prompt.

Packet Drivers are small, efficient network card 
drivers that virtualize the network adapter from 
the network software.  This allows network 
software such as Observer to access the network 
without specific knowledge about the network 
adapter itself.  While it is possible to use a Packet 
Driver with Novell, we suggest that you use ODI if 
you have a Novell network.  It is not possible to 
use a Packet Driver with Windows for Workgroups 
if you are using Windows for Workgroups 
networking.  You can not use Observer with Token 
Ring and a Packet Driver.

If you use the Packet Driver interface (assuming 
you do not have Novell or Windows for 
Workgroups), VPACK.EXE will take all incoming 
packets.  VPACK.EXE can not be run with any 
other network software shells.  This means that you 
will not be able to concurrently use Observer with 
any other network software (i.e. IPX.COM, and 
NETX.EXE) at the Observer workstation.  This will not 
affect the use of network software on any other 
workstations.

For all three methods (ODI, NDIS, and Packet 
Driver) it not recommended to run a full screen 
DOS prompt while Observer is trying to capture 
information.
Step 1: Configuring ODI, NDIS or a Packet Driver.
Note:  If you are installing Observer in DEMO 
mode, go directly to Step 2.

This step is potentially the most complicated part 
of setting up Observer.  Your procedure will 
depend on what kind of a network you have.

If you have ODI, you may need to modify your 
NET.CFG file.  This is explained in Procedure 1a.

If you are using NDIS you will only need to verify 
that your LAN is up and running.  Go to Procedure 
1b

If you decide to use a Packet Driver, you will need 
to select and configure the Packet Driver.  This is 
described in Procedure 1c.  Procedure 1c is for 
people who are using a Novell network pre-3.x/4.x 
(Netware 2.x) or for those of you using a TCP/IP 
product that uses the Packet Driver.
Procedure 1a: Configuring ODI
This procedure assumes that you have a Novell 
LAN and a pre-existing ODI setup.  This procedure 
describes what VPACKODI.EXE (Observers ODI 
interface) needs to have configured in your 
NET.CFG file.  Note:  If you do not have a NET.CFG 
file, you will need to create one.  This file is the 
configuration file for LSL.COM and is usually in the 
same directory as LSL.COM.

If you are not sure whether you have an existing 
ODI configuration or not, check your 
AUTOEXEC.BAT or your STARTNET.BAT file for the 
following files:

LSL.COM
IPXODI.COM
NETX.EXE (or VLM.EXE)

If these files are being loaded on your system, you 
are using ODI. 

ODI uses the configuration file NET.CFG to give its 
programs and drivers information about the 
network protocol settings and network card driver 
settings.  You may need to add to your NET.CFG 
FRAME designations for each of the frame types 
that you will want to capture and examine.  Your 
NET.CFG may have one, some, or all of these 
types already.  For Ethernet add the ones that are 
not in your NET.CFG but are listed below (for 
Token Ring, check the Appendix under "Sample 
Files").

A sample NET.CFG file for a NE2000 network 
adapter might look like this (yours may be 
different):


LINK DRIVER NE2000
	INT 5
	PORT 300
	FRAME ETHERNET_802.3
	FRAME ETHERNET_II
	FRAME ETHERNET_802.2
	FRAME ETHERNET_SNAP

LINK SUPPORT
	BUFFERS 15 4028
	MEMPOOL 4096


Observer’s VPACKODI.EXE (this will automatically 
be installed in step 2) will capture and make 
available to Observer all protocols for each 
FRAME line in your NET.CFG.  VPACKODI.EXE will 
not see any FRAME types that are missing from 
your NET.CFG.  We recommend adding all frame 
types unless you specifically know that you will not 
be using a particular one.  Note: If you are 
planning to monitor TCP/IP, you must have the 
ETHERNET_II frame type listed in your NET.CFG.  
[See the Appendix for a sample NET.CFG for 
Token Ring.)

If you are using Netware Discoverer
For Discoverer to work properly it requires: 
LSL.COM, IPXODI.COM and VLM.EXE to be 
installed and running (this includes any *.VLM’s 
that VLM.EXE may require).  Additionally, you will 
need to have Novell's Windows Network support 
drivers (*.DRV’s,  DLL’s, VxD’s and 386’s) properly 
(and completely) installed on your PC 
(NETWARE.DRV, NWCALLS.DLL and NWIPXSPX.DLL 
and all of the drivers that these files call need to 
be present in your Windows SYSTEM subdirectory).  
You must also configure Windows to recognize 
the Netware shells.  This is done in Setup for 
Windows 3.1, and in the Network dialog in WFW 
(3.11).

The Netware Windows drivers and DLL's are 
proprietary programs of Novell Inc., and are either 
included with your Novell system or you can 
download the latest versions of the Drivers and 
DLL's from Internet (ftp.novell.com), from 
Compuserve, or ask your Novell dealer for the 
latest VLMUPx, WINDRx and NWDLLx (where "x" is 
the version number).

Once you have modified your NET.CFG file (and 
verified the complete VLM installation if you are 
using Discoverer), you can now proceed to Step 
2.
Procedure 1b: Using NDIS
Since Observer’s installation program sets up all of 
the necessary NDIS configuration files for you, the 
only thing you need to do at this point is to verify 
that your NDIS LAN is up, and functioning.

You can verify that your NDIS LAN is running by 
starting Windows, and logging into your LAN.  
Make sure that you can send and receive 
information.

Once you have verified that your LAN is up and 
running, you can now proceed to step 2.
Procedure 1c: Using a Packet Driver
This procedure is for installations with any kind of 
network EXCEPT Novell (using ODI), Novell with 
ODI and Windows for Workgroups, Windows for 
Workgroups with NDIS, or any Token Ring.  In this 
procedure you will use a program called a Packet 
Driver to provide VPACK.EXE with an interface to 
your network adapter.

Packet Drivers are small, fast programs that 
separate your network adapter from your network 
software.  This allows one version of Observer to 
work with all kinds of network adapters.  Packet 
Drivers are freeware and a collection of them are 
included with Observer.  You will find both the 
Packet Driver collection and a detailed installation 
guide (INSTALL.DOC) for Packet Drivers in the 
\DRIVERS directory of the Observer distribution 
disk.  A subset of the INSTALL.DOC is located in the 
Appendix of this manual.

Find the Packet Driver for your network adapter in 
the DRIVERS directory on the Observer distribution 
disk.  Packet Drivers are named in a manner that 
should allow you to determine which  driver to use 
with which card.  For example, the packet driver 
NE2000.COM is for use with a Novell NE2000 
network card (or an NE2000 clone).  For a 
complete list of all the Packet Drivers, see  
INSTALL.DOC located in the \DRIVERS directory.

In this example, we will use the NE2000 Packet 
Driver.  This Packet Driver requires three pieces of 
information about your network card: 1) The 
software interrupt, 2) The IRQ (interrupt), and 3) 
The I/O address (also known as base memory).  A 
typical Packet Driver will have the following 
invocation format:

NE2000  [packet_int_no]  (irq)  (i/o)  
(other_paramiters)

Where:

packet_int_no: (Packet Interrupt Number) Is the 
software vector that the first network program will 
use to connect to the Packet Driver.  This can 
range from 60-79, but it will usually be 61.  Note 
that this flag is represented in hex notation, so 61 
would be represented by 0x61.

irq: (IRQ) Stands for "Interrupt ReQuest" and is 
often just called interrupt.  This must be unique for 
each card in your PC and can not, under any 
circumstances, be shared with any other adapter.  
Some good choices are 5, 10, 11, or 12.  Some 
very bad choices are 2, 3,4,7, or any number 
above 13.  Keep in mind the "right" choice is 
whatever is set on your network adapter card, 
and not used by any other adapter.  To determine 
the IRQ, you may need to open up your PC and 
look at the jumper setting on the adapter itself, or 
run the cards diagnostics to find out what the IRQ 
is set to in the cards setup memory.  This value is 
not represented in hex so an IRQ of 5 would be 
represented by 5.

i/o (I/O) Is the I/O or Port that the card uses.  This is 
also set on the card and can not be used by any 
other adapter in your PC.  The default for the 
NE2000 card is 300 and thus would be represented 
in hex notation by 0x300.

other parameters:  Some network adapters 
(notably the SMC/WD family) use shared memory.  
Check your Packet Driver for any additional 
parameters required and look in the INSTALL.DOC 
in the appendix of this manual for your specific 
card’s requirements.  [Another way identify what 
your specific Packet Driver’s requirements is to run 
the Packet Driver at the DOS prompt without any 
parameters.  This will show you a copyright and a 
help screen that lists all of the required parameters 
for that specific Packet Driver.]

For our example, the NE2000 command line might 
be (this may not match your cards set up exactly):

NE2000 0x61 5 0x300

When executed, this is what you might see:


Packet driver for NE2000, version 11.4.3
Packet driver skeleton copyright 1988-93, Crynwr 
Software.
This program is freely copyable; source must be 
available.


System: 80[345]86 processor, ISA bus, Two 8259s
Packet driver software interrupt is 0x61 (97)
Interrupt number 0x5 (5)
I/O port 0x12C (300)
My Ethernet address is 08:00:00:12:07:50


If you get any errors, (i.e. an Ethernet address of 
all FF’s or all 0’s, or a usage screen), the Packet 
Driver did not load correctly.  Check your settings 
and try again.  If you still have troubles, see the 
troubleshooting section in the Appendix of this 
manual.

Once the Packet Driver has been loaded, you 
can now proceed to step 2.
Step 2: Copy the Observer files onto the PC
Run Windows and click on "File"->"Run".  In the 
"Run" dialog box, fill in the path to the executable 
A:\INSTALL.EXE.

You can now choose to install Observer in DEMO 
mode or in licensed mode.  To install in DEMO 
mode, check the DEMO box at the bottom of the 
install dialog.  To install in licensed 
mode, uncheck the DEMO box.

 
The install dialog box will then ask if you want 
Observer installed in the C:\OBSERVER directory.  
Unless you have a compelling reason to install 
Observer elsewhere, we suggest that you install 
Observer in this default destination.

If you chose to install in DEMO mode, you will not 
be asked about network interfaces or to install 
Netware Discoverer.  You can now go to the 
Using section.

If you are installing in licensed mode, you will be 
asked if you are sure you want to install in licensed 
mode, if so, answer YES.

You will then be queried if you would like to install 
Netware Discoverer.  If you do not have a Novell 
LAN do not install Netware Discoverer (uncheck 
the box at the bottom of the dialog).  If you do 
have a Novell LAN read the dialog carefully, and 
decide if you want to install Discoverer or not, if so 
leave the "Install Netware Discoverer" checkbox 
checked.

Install will now copy the Observer files.  Once this is 
complete, install will ask you whether you want to use 
ODI, NDIS or the Packet Driver Choose whichever method 
you would like to use.

 
All choices (ODI, NDIS, or Packet Driver) expect 
that you have completed Step 1 successfully.

If you choose ODI, Observer’s installation program 
will offer to make the necessary changes in your 
AUTOEXEC.BAT file.  If you tell INSTALL not to 
modify your AUTOEXEC.BAT file, you will need to 
run VPACKODI.EXE or add it to your 
AUTOEXEC.BAT for Observer to function. Sample 
files are given in the Appendix of this manual.  If 
your PC uses DOS 6.x’s multiple boot setup, 
Observer’s installation program will create a file 
called AUTOEXEC.INS in your Observer directory 
with the required load lines to run Observer.  You 
should copy these load lines into the appropriate 
section of your AUTOEXEC.BAT.

If you choose NDIS, Observer’s installation 
program will offer to make the necessary changes 
in your AUTOEXEC.BAT, PROTOCOL.INI, and 
SYSTEM.INI files.  If you tell INSTALL not to modify 
your files, you will need to run VPACK.EXE or add it 
to your AUTOEXEC.BAT for Observer to function.  
You will also need to modify your PROTOCOL.INI 
and SYSTEM.INI files.  Sample files are given in the 
Appendix of this manual.  If your PC uses DOS 6.x’s 
multiple boot setup, Observer’s installation 
program will create a file called AUTOEXEC.INS in 
your Observer directory with the required load 
lines to run Observer.  You should copy these load 
lines into the appropriate section of your 
AUTOEXEC.BAT.

If you choose to use the Packet Driver, INSTALL will 
offer to make the necessary changes to your 
AUTOEXEC.BAT file.  If you tell install not to modify 
your AUTOEXEC.BAT file, you will need to run 
VPACK.EXE or add it to your AUTOEXEC.BAT for 
Observer to function.  If your PC uses DOS 6.x’s 
multiple boot setup, Observer’s installation 
program will create a file called AUTOEXEC.INS in 
your Observer directory with the required load 
lines to run Observer.  You should copy these load 
lines into the appropriate section of your 
AUTOEXEC.BAT.

Once the Observer files have been installed on 
your PC, and network access method 
configuration files modified, INSTALL will ask to 
reboot your system.  Once you reboot your 
system, you will be able to start Windows and run 
Observer by double clicking on the Observer icon 
in the Observer group.

If Observer fails to load with an error indicating 
that you do not have enough DOS memory to 
allocate VPACK (or VPACKODI’s) buffer space, 
see the section on Program Flags later in this 
manual, or the troubleshooting section in the 
Appendix.  This describes the way to lock VPACK 
(or VPACKODI’s) buffer space prior to going into 
Windows before other applications can steal it 
away.






USING OBSERVER
OVERVIEW AND QUICK START
Observer has four modes of operation:

1) DISCOVERY Mode allows you to capture all of 
the network addresses on your LAN, store them 
in the filters table, and alias them as names or 
automatically alias them as IP addresses.

2) PACKET CAPTURE mode allows you to capture 
packets.  Once  packets have been captured, 
you can view the capture buffer contents or 
filter and print the results.  The packets 
captured will depend on the filters you set in 
the "Filters" dialog.

3) BANDWIDTH UTILIZATION has two modes:  Standard 
Bandwidth Utilization allows you to graphically 
monitor the amount of your total network 
bandwidth that is currently being used - 
showing the data in a sliding 8-16 minute 
graph.  Long Term Bandwidth Utilization (LTBU) 
shows graphically high, low, and average 
utilization over a tunable time frame (up to 7 
days), and allows the data to be exported in 
comma delimited spreadsheet format for 
further analysis and charting.

4) NETWORK STATISTICS includes Received Packet 
Statistics, Size Distribution Statistics, and 
Protocol Statistics.  These statistical modes let 
you see who is using your LAN and who or 
what is generating traffic.  Each mode sheds 
different light on the workings of your LAN.

Packet Capture mode and Network Statistics 
mode allow filtering by address or protocol or 
both.  You can set filters from the "Filters" dialog 
from any Observer screen.  Bandwidth Utilization 
mode does not use any filters - it reads and 
records all packets regardless of type or address.  
[Note: if using ODI, Bandwidth Utilization will only 
see registered FRAME types as described by your 
NET.CFG file.]

When using Bandwidth Utilization mode, you must 
set the maximum theoretical network bandwidth 
of your network in the "Modes" -> "Settings" 
dialog box (default is set 10MB/s - the speed of an 
Ethernet network).  For more information about 
the "Modes" -> "Settings" dialog, see the Settings 
section of this manual.

Note:  Windows provides a multitasking-tasking 
environment for applications - sort of.  Windows 
3.x multitasking-tasking is non-preemptive single 
threaded multitasking-tasking.  This means that 
you can choose to run other applications while 
Observer is running, but depending on the speed 
of the PC, the amount of filtering you are doing, 
and the load that the other applications put on 
the PC, Windows may not give Observer the 
processor time it requires and thus Observer may 
drop packets.  This is most likely to be a problem 
on a slow PC, in a heavily trafficked LAN with a 
very large capture taking place.  If you believe 
that you are not seeing all of the packets that you 
should, or if Observer is reporting dropped 
packets, try running Observer without any other 
Windows applications active.

The Network Statistics modes give you an alternative way 
to discover (this is different from Discovery Mode) 
network addresses on your LAN and to copy an address to 
the clipboard for use in the filter and alias dialog 
boxes.  You can do this by double clicking on any 
network address - this will copy it to the Windows 
clipboard. FILTERS Before you use Observer you will need 
to familiarize yourself with the Filters dialog box.  
The setting and use of filters is central to the 
functioning of Observer.  If you do not set a filter, 
Observer will capture all packets and all protocols.  In 
other words, setting no filter is just like setting an 
ANY_ADDRESS to/from ANY_ADDRESS address filter with an 
"All Protocols" sub-filter.  

Since LAN traffic can generate a tremendous 
amount of data, we suggest that you filter out as 
much as possible to make the interpretation of 
the captured data easier.

 
Filtering allows you to choose an address or set of 
addresses (an "address filter") and a protocol or 
set of protocols ("a protocol sub-filter") to filter the 
capture with, and to display packets with.  These 
filters and sub-filters will sort packets and capture 
only those that you wish to capture.

The "Filters" -> "Current Filter" dialog box allows 
you to select one to five specific computers (or 
hosts) by address, for monitoring network traffic or 
statistics.  See "Saving a Filter" later in this section.

You can select "ANY_ADDRESS" and one 
computer’s address to get information from that 
computer to any address or from any address to 
that computer.

You can also select "ANY_ADDRESS" to and from 
(«) "ANY_ADDRESS" to activate a "filter" that 
sees all addresses, and thus all LAN activity. 
(Within the parameters of your protocol sub-filter 
and, if using ODI, your FRAME specifications.)

Filtering can be done by address or protocol or both.  
You can select a specific protocol that you want to 
monitor or choose to monitor all protocols present on 
your network.  Observer currently supports specific 
translation of the IP and IPX/SPX suite of protocols.  
Other protocols are viewed in raw mode.

After you make changes in the Filters dialog box, 
you can either click on the "O.K." button to save 
and enable the changes or "Cancel" to discard 
all changes and preserve previous filter settings.

Filters are stored in the file OBSERVER.FLT in 
Observers installation directory.  This file is a text 
file and can be edited with any text editor.

Saving a Filter Once you have set a filter, it can be 
saved as a named filter that can then be selected at a 
later time using the "Filters" -> "Select Filter" 
dialog. You can save and name up to 5 different filters 
to be recalled at a later time.

 

Filter names can be edited by clicking in the 
name section of the dialog.

Changes are kept in a text file in your Observer 
installation directory called OBSERVER.FLT. Adding and 
Editing Hardware Addresses The hardware address listbox 
shows the addresses (and aliases) you may want to 
monitor.  You can create as many entries as you are 
licensed for, however you can only set a filter to 
monitor up to 5 addresses at a time.  See the section on 
Discovery mode for more information about adding network 
addresses

The format of an address entry is either the six 
numbers of the Ethernet address separated by 
colons or dots, or the Token Ring address.  This 
may be followed by a space then an alias up to 
17 letters long.  An alias is a name that Observer 
will substitute for an address when showing the 
headers of incoming packets (if you tell Observer 
to use aliases).  This can make packets easier to 
recognize and analyze.

For example:

	00:02:8A:49:B2:48    David Jones

To manually add a hardware address, click on the 
edit line at the top of the Filter dialog box and 
enter the hardware address and press <ENTER> or 
click on a down arrow at the end of the edit line.  
The entry will be added to the list.  To edit an 
existing entry, select that entry using your mouse 
and click on the "Edit" button to the right from the 
hardware addresses list or simply double-click on 
the line you want to edit.  The address will appear 
in the edit line and you can make all necessary 
changes and save it as described above.  You 
cannot edit or change the "ANY_ADDRESS" entry.

To remove an address entry, highlight the address 
by a clicking on it and click on the "Remove" 
button.
Setting hardware address Filters
Observer filters allow you to capture packets 
coming from one hardware address to another - 
in one or both directions:  All incoming packets to 
a particular address from any source, all outgoing 
packets from a particular address to any 
destination, or all the traffic on the network - 
subject to the protocol sub-filter.

To set up a filter, select one of the five lines in the 
three boxes below the hardware address with a mouse 
click.  Then click on an address you want to monitor in 
the hardware address box and click on the "Add" button 
over right or left filter sub-box.  Repeat the above 
procedure for the second address.

Once you have added both addresses, you can 
choose the direction to capture.  Choose "->" to 
only see packets from the left address the right 
address on the filter line.  Choose "" to only see 
packets from the right address to the left address 
on the filter line.  Choose the "«" to see packets 
from or to the right and left addresses on the filter 
line.

If you want to capture all packets in one or both 
directions - select the line "ANY_ADDRESS" in the 
hardware addresses box and add it to the filter 
line.

If you want your current filters to be loaded on 
startup of Observer, check the "Enable current 
filters on startup" box, otherwise Observer will start 
up with no filter and thus default to a capture all 
packets state.
Choosing a Protocol AS A sub-filter
Observer allows you to select a protocol that you 
want to monitor as a sub-filter.  The choices in this 
list will depend on whether you are using Ethernet 
or Token Ring.  For Ethernet you have 5 choices of 
protocol sub-filters:

All protocols (no filtering by protocol)
TCP/IP set of protocols (TCP,UDP,ICMP,....)
IPX-SPX ETHERNET II (Novell)
IPX - IEEE 802.3 (Novell)
IPX - ETHERNET II + IEEE 802.3 (Novell)

For Token Ring, the protocol sub-filter list will show:

All protocols (no filtering by protocol)
TOKEN-RING_SNAP - all sub-protocols
TOKEN-RING_SNAP - TCP/IP set of protocols
TOKEN-RING_SNAP - IPX/SPX set of protocols
TOKEN-RING - all sub-protocols
TOKEN-RING - IPX/SPX set of protocols
MAC frames only

To choose a protocol, click the arrow on the right 
of the "Protocol:" line at the bottom of the 
"Filters" dialog box.  Select the option that best 
filters the situation you wish to monitor.  It is best to 
do as much filtering as possible when trying to 
isolate network problems.

Note: Observer can analyze many more protocols 
than it allows you to filter.  If your particular 
protocol is not present in the specific list of 
protocols, just choose the "All Protocols" (no 
filtering by protocol) line.
DISCOVERING HARDWARE ADDRESSES ON YOUR LAN: 
DISCOVERY MODE 
Discovery mode allows you to capture all of the 
network addresses on your LAN, store them in the 
filters table, and alias them as names or IP 
addresses.

Observer allows you to add addresses manually or 
to "discover" addresses on your LAN with the 
Discovery mode dialog.  To start Discovery mode 
choose "Modes" -> "Discovery Mode" from the 
menu.

 
Once you are in Discovery mode, you can have 
Observer "listen" to your LAN and record all of the 
active network addresses.  

By pressing the start button on the right of the 
screen, Observer will begin to collect all of the 
active addresses on your LAN segment.  
Addresses will be added immediately as each 
station accesses the LAN (up to the number of 
addresses you are licensed for).

Once you have collected the addresses you are 
interested in saving, you can save them by 
clicking on "Save All" or highlight just a few 
addresses using your mouse, and save only those.  
The addresses will be saved in the OBSERVER.FLT 
file.  They will then be available for use as an 
address in the Filters dialog.

You can choose to alias addresses at this point, or 
you can wait until you need to use the address 
and alias it in the Filters dialog.

Clicking on the "Load list of addresses at startup" 
loads all of the addresses you have stored in your 
OBSERVER.FLT file when going into the Discovery 
mode dialog.  If you start Discovery mode with 
"Load a list of addresses", then clicking on the 
"Highlight New" button will display all of the 
addresses that are newly discovered in this 
Discovery mode session.

If you are using TCP/IP, Observers Discovery Mode 
allows you to automatically fill the alias of an 
address with the IP address of that station.  To 
activate this feature check the "Fill new address’s 
alias with IP address" checkbox at the bottom of 
the Discovery Mode dialog.
MONITORING YOUR LAN: NETWORK STATISTICS
Observer has four modes which allow you to 
monitor and observe different aspects of your 
LANs movement of data across the wire: 
Bandwidth Utilization (short and long term), 
Received Packets Statistics, Size Distribution 
Statistics, and Protocol Statistics.
Bandwidth Utilization mode
Observer provides two different bandwidth 
utilization modes.

1. Bandwidth Utilization - this displays a graph 
that is an instantaneous "window" of your 
bandwidth utilization.  Information is real time, 
but the graph will only display up to 16 minutes 
of information.  Sampling is once a second.

2. Long Term Bandwidth Utilization (LTBU) - this 
displays (and allows for export) longer term 
information about your bandwidth utilization.  
The graph shows high, low and average over 
time - up to 7 days.  Sampling is still once a 
second, but the display can be configured to 
report at various time intervals.

The Bandwidth Utilization screen can be 
activated from the main window by selecting 
"Modes" -> "Bandwidth Utilization".

 
Once you are in the Bandwidth Utilization screen, 
the graph shows the current utilization.  A 
Maximum Utilization value is kept at the top of the 
graph.  This value is reset each time you start and 
stop Bandwidth Utilization.

This graph shows the amount of data on your 
network segment graphed against the maximum 
theoretical bandwidth for your network topology, 
as set in the "Modes" -> "Settings" dialog box.  For 
Ethernet you should choose "10 Mbps", for Token 
Ring choose either "4 Mbps" or "16 Mbps" 
depending on your LAN.

Note: This graph is not subject to any filters.

The Long Term Bandwidth Utilization screen can be 
activated from the main window by selecting "Modes" -> 
"Long Term Bandwidth Utilization".

 
Once the LTBU graph pops up, it automatically 
begins capturing data.  Three lines will be shown, 
red - maximum, blue - average, and green for 
minimum.  Although data points are only shown 
for the time period set in "Modes" -> "Settings", 
data is collected and processed every second.

The scroll bar at the bottom of the graph will allow 
you to see historical utilization data.  The LTBU 
graph can collect 10,922 data points.  So, for 
example, if you choose a 1 minute averaging 
time, this calculates out to 7.59 days before the 
LTBU graph will reach its data limit.

See the Settings section for more information on 
Averaging Time and Time scales.

Note: Long Term Bandwidth Utilization is not 
subject to any filters.
General Statistics Information
General Statistics screen information (for all 
Network Statistics screens):

To start the statistics capture, click on the "Start" 
button.  To stop the capture, click on the "Stop" 
button.

Once you are in a network statistics screen, you 
have a number of choices to make.

The network statistics screen has three views: 
Received Packets, Size Distribution, Protocol 
Statistics.  You can view LAN traffic by address 
and percentage of captured bandwidth, by 
address and packet size distribution as a percent 
of captured bandwidth, or by protocol.  You can 
choose the view you would like to see from the 
"Modes" menu.  Each of the network statistics 
windows are shown and explained below.

Some screens have additional options that are 
explained in each of the dialogs individual 
sections that follow.

By default, each statistics view will show all traffic 
(subject to your current filter selections) by the 
"Destination Address".  You can press the 
"Direction" button to switch from a "Destination 
Address" listing to "Source Address" listing.

You can press the "-Aliases" button to switch from 
a listing of hard network address to one of aliased 
addresses that you have set up in the "Filters" 
dialog box.  (For more information on how to set 
aliases, see the Filter section.)  When the button 
shows "-Aliases", aliasing is off.  When it shows 
"+Aliases" aliasing is on.

The "Clear" button clears the current screen, 
clears the capture buffer and stops the capture.  
Press the "Start" button to begin a new capture.

Received Packets Statistics
The Received Packets window can be activated 
from the main window by selecting "Modes" -> 
"Received Packets Statistics".

 
To begin a capture press the "Start" button.

The Destination/Source Address field will show 
either the destination or source address.  This can 
be either a hard network address or an alias 
(depending on the state of the alias button).

The "%" field shows the percent of bandwidth 
utilization for that destination/source address.  
Note that this is the % of filtered bandwidth.  If you 
would like to see the percent of total bandwidth 
that that particular address is using, you will need 
to set up an ANY_ADDRESS to and from 
ANY_ADDRESS filter.

The "Packets" field shows the number of packets 
to (or from) the destination/source address, 
subject to the current filter set.

The "Bytes" field shows the bytes to (or from) the 
destination/source address, subject to the current 
filter set.

The "Sort" button activates the sort dialog:

 
The sort dialog allows you to choose the direction 
of the display (with respect to source or 
destination) and the sort order of the window.  
Sorting is useful for determining which stations are 
sending the most data, and which are less active.

Once the capture begins, you can double click 
on any address to copy the hard address into the 
Windows clipboard.  This can provide a 
convenient way to begin building an alias table.  
For example, if you double click on an address 
and then switch to the "Filter" dialog box, you can 
then paste that address into the "Hardware 
Address" edit box using Shift-Ins.  To automatically 
build a complete hard address table, see the 
section on Discovery mode.

Size Distribution Statistics

 
The Destination/Source Address field will show 
either the destination or source address.  This can 
be either a hard network address or an alias 
(depending on the state of the alias button).

The "%" field shows the percent of  bandwidth 
utilization for that destination/source address.  
Note that this is the % of filtered packets.  If you 
would like to see the percent of total packets that 
that particular address is using, you will need to 
set up an ANY_ADDRESS to and from 
ANY_ADDRESS filter.

The "Packets" field shows the number of packets 
to (or from) the destination/source address, 
subject to the current filter set.

The rest of the screen shows the packet size 
distribution divided by packet size in bytes.  This is 
shown as a percentage of the total for that 
address.  This is a good way to determine if a 
particular station is being as efficient as it could 
be by sending mostly large or mostly small 
packets.


Protocol Statistics

 The Protocol Statistics screen shows Ethernet LAN 
traffic divided by network protocol and sub-protocol 
(the Token Ring display will be slightly different).  
Protocols are displayed as a percentage of the total 
filtered traffic.  Sub- protocols are displayed by the 
number of packets received of that type. Printing 
Statistics screens Any of the statistics screens can be 
printed by selecting "File"->"Print Protocol Statistics" 
from the Network Statistics screen. CAPTURING PACKETS ON 
YOUR LAN:  PACKET CAPTURE MODE Observer’s Packet Capture 
screen  consists of a menu bar, monitor graph, 
Start(/Stop), View and Clear buttons.  

Note: To capture packets, you should first select a 
filter set.  This can be done using the "Filters" menu 
choice from Packet Capture (or any Observer) 
screen to bring up the "Filters" dialog box.  See 
the section on "Filters" for more information.

To begin capturing packets, press the "Start" 
button.  You will see three different lines on the 
capture graph.  The red line shows the non-
captured traffic, the blue line shows  the captured 
traffic, and the black line shows the dropped 
packets.

Note the red blinking "Capturing" in the upper 
right hand corner of the graph.  This is your 
"Capture is on" indicator.  Observer will also tell 
you the percent of your capture buffer that is full, 
and will automatically stop capturing when the 
buffer becomes full.  For more information on the 
capture buffer size, see the Observer "Settings" 
dialog section in this manual.

Once you have captured the packets you can 
view the packets with the "View" button, or save 
the capture buffer to a file to view later.  Pressing 
the "View" button will turn capturing off unless you 
disable the "Stop capturing if switched from the 
main window" checkbox from the "Modes" -> 
"Settings" dialog box.

For information on viewing captured packets see 
the "Viewing Captured Packets" section.

To save a capture buffer to a file, capture the 
information you want to save and select "Save 
Packet Buffer" from the "File" menu on the 
Capture Mode graph or from the View screen.  To 
load a previously saved capture buffer, choose 
"Load Packet Buffer" from the "File" menu on the 
Capture Mode graph or from the View screen.

To stop capturing packets, press the "Stop" 
button.

To clear the capture buffer, and stop the capture, 
press the "Clear" button.
 

Viewing Captured Packets

To view the packets in the capture buffer, click on 
the "View" button from the "Receive Packets" 
screen.

Once you are in the view screen, you can click on 
a particular packet (with your LEFT mouse button) 
in the top window to display the packet decoded 
information in the bottom window.  The two 
windows are fully sizable by dragging the middle 
border up or down.  Observer decodes all Novell 
packets and all IP packets.  Other packets are 
shown in raw mode.

You can click on the "Show aliases" box at the 
bottom of the screen to enable aliasing of 
network addresses.

Clicking on the "Raw Packets" box at the bottom 
of the screen will switch from a decoded packet 
view to a raw packet view.

The Settings menu choice has two option:

Select Frame Colors - This brings up the colors 
dialog.  You can also access this dialog by single 
clicking your RIGHT mouse button on any packet 
line on the top part of the View Packets screen.  In 
either case, this allows you to choose the color of 
the packet line you would like to associate with 
the selected frame type.  For example, you could 
set all IP packet types to show with a white 
background and a green foreground, while 
displaying all IEEE 802.3 packet types (Netware 
3.x’s default) as white foreground with a red 
background.  This can help you visually pick out a 
particular packet type, if you are capturing 
multiple types.

View Configuration - This brings up the View 
Configuration dialog where you can control 
Observers post-capture filtering:

 
Probably one of the most powerful features of 
Observers packet capture/decode this allows you 
to filter the packet capture after you have 
captured a buffer.  The post- filters will filter out 
any unwanted data both in the packet decode 
screen and on any print outs of the data capture.

The view configuration dialog options include:


 

This dialog allows you to "post-filter" all or some of 
the IP header information.

 
This dialog allows you to "post-filter" all or some of 
the TCP header information.

Show Differential Packet Times - choosing this 
option (check the checkbox) will allow Observer’s 
View Packets windows to display the differential 
packet times.  Differential packet times can show 
difference in time of arrival (and thus time sent) 
for the current packet and the previous packet.  
This is called the packet delta.

You can also search the data segment of a 
packet capture buffer by using the "File"-> "Find 
Packet" dialog:

 
Multiple instances of the Find Packet dialog can 
be active at one time.  To activate the multiple 
instance search, start one search and choose 
"File"->""Find Packet" again without closing your 
first search - both will remain active.

Printing captured packets
You can print a packet capture buffer (the "View 
Packets" screen content) on a printer attached to 
your computer or (if you are using ODI or NDIS) to 
any printer available on your network.

To set up a printer for Observer select 
"Print"->"Print Setup" from  the View Packets 
dialog box and select either the default printer or 
choose a different printer from the "Specific 
Printer" dialog.

To print out a packet capture, click on the "File" 
-> "Print" to bring up the printer dialog sub-menu.

You will be given options for the set of packets to 
print.  The default is set to print all captured 
packets.

 
You can choose to print commented or raw 
packets, or both (which can be most useful for a 
programmer analyzing packet details in depth).  
You can have Observer print out either Ethernet 
addresses or aliases as the printed headers

Lastly, you can choose whether Observer will print 
packets continuously or print each packet on a 
single page. (Providing that length of a packet 
allows it, every new packet will always start 
printing on a new page). 

Once you have made your print options 
selections, click on the "Print" button.

To exit without saving, press "Cancel".
Saving Captured Packets to a File


To save a packet capture to a file select 
"Print"->"Save to a File" menu in the View Packets 
dialog box.
 

You will be given a choice of packets numbers to 
print.  The default is set for all captured packets.  
However, if after reviewing a packet’s contents in 
the "View Packets" dialog you are interested in 
some particular section of the capture you can 
specify only that section.

Next you can choose to save commented or raw 
packets, or both (which can be most useful for a 
programmer analyzing packet details in depth). 
You can let Observer save either Ethernet 
addresses or aliases as the printed headers.  

When you have made your options choices, click 
on the  "Save" button.  You will be given a choice 
of file name and directory to save the capture.

To exit without saving, press "Cancel".
SETTINGS DIALOG
The settings dialog box allows you to 
set the global variable information in Observer.

 
Windows buffer size is the amount of Windows 
memory that Observer will set aside to store 
captured packets.  Values are in kilobytes, so a 
setting of 132 would represent a .132 megabyte 
(MB) buffer.  A 2048 KB buffer would represent a 
2.048 MB buffer.

You should choose the smallest buffer that will 
capture the event you are interested in looking at.  
Observer will show the buffer percentage full and 
you will get an idea of what is the best buffer for a 
particular situation.  Keep in mind that a full 4 MB 
buffer is a lot of data to sort through.  You will 
want to capture an event in as little time with as 
little buffer space as possible.

It is not recommended (although it is allowed) to 
use a buffer larger than the amount of physical 
RAM in your PC.

On a 16 MB system the maximum recommended 
buffer is 10 MB (a setting of 10,000).  On a 8 MB 
system, the maximum recommended buffer is 4 
MB (a setting of 4,000).  Again, use the smallest 
buffer possible to capture the event of interest.

Lock Windows buffer from paging will tell Windows 
to not page out the Observer packet buffer.  This 
will make Observer more efficient, since its buffers 
will always stay in RAM (as opposed to Windows 
swapping out the buffer).

This is the recommended mode for operation of 
Observer, but be careful.  If you set your buffer 
size too high and lock the buffer from paging, 
Windows may swap out its own programs and 
cause Windows to crash.  

Stop capturing if switched from main window - this 
will turn capturing off when you switch focus from 
the capture graph window.  Switching focus is 
done when you start another Windows 
application, when you choose to view packets, or 
when you move the Windows focus to another 
window.

Observer can capture packets while Windows is 
doing something else.  However, under heavy 
traffic conditions, (or with a slow PC) Observer 
may drop packets if this option is not checked.

Ask confirmation to clear packet buffers - brings 
up a conformation (yes/no) dialog when the 
"Clear" button pressed.

Network Bandwidth - select the network 
bandwidth of your LAN.  This will be used to 
calculate the % of Bandwidth Utilization when in 
Bandwidth utilization mode.  Options are:

4 Mbps	- Used for 4 MB Token Ring
10 Mbps	- Used for all Ethernets
16 Mbps	- Used for 16 MB Token Ring

Long Term Bandwidth Utilization configuration - this 
is where you configure the averaging time and 
stretch scale:

Averaging time - LTBU graph can collect 10,922 
data points.  If you choose a 1 minute averaging 
time, this calculates out to 7.59 days before the 
LTBU graph will reach its data limit.

So, for example, you could choose 30 seconds for 
and averaging time and Observers buffer would 
capture and display for  10,922 (points) / 120 
(points per hour) / 24 (hours per day) = 3.79 days.

Stretch time scale - By default, the LTBU graph will 
plot each data point 10 pixels apart (10x) and fill 
in the distance between with a solid line.  Setting 
this to 1x will plot data points one pixel apart.  
LTBU will plot times on the graph in a manner 
which insures that no time stamps will overwrite 
the previous or the next.  All export files contain all 
time stamps and all data points as described in 
the averaging time above.

Program Flags
This section discusses the optional flags for all 
programs that use flags.  Flags shown in brackets 
[] are optional.  Flags are not case sensitive.
OBSERVER.EXE
OBSEVER.EXE has the following optional flags:


OBSERVER [-i=xx] [-DEMO] [-TOKEN]


where:

-i=xx
The software interrupt you specified in the VPACK 
(or VPACKODI) command line.  This is only 
required if you have specified a flag with VPACK 
or VPACKODI.  Values (xx) are in hex and can be 
from 60-6F.  6F is the default.

This flag can be used in conjunction with any 
other flag.

Example:

OBSERVER -i=63

-DEMO
This starts Observer in DEMO mode.  In this mode, 
Observer will play fake data, and does not require 
a LAN or LAN adapter to function.

Example:

OBSERVER -DEMO

-TOKEN
Only used with the -DEMO flag, this tells the 
Observer DEMO that your would like to look at 
Token Ring data.

When using Observer in licensed mode, it will 
automatically determine whether you are using 
Token Ring or Ethernet.

Example:

OBSERVER  -TOKEN  -DEMO


VPACK and VPACKODI
VPACK and VPACKODI have the following option 
flags.


VPACK or VPACKODI  [-i=xx]  [-m=y]


where:

-i=xx
The software interrupt.  You may want to specify 
this if the default (6F) is conflicting with some other 
program.  If you have specified a software 
interrupt different that the default, you must also 
specify the same interrupt on the OBSERVER.EXE 
command line.  Values (xx) are in hex and can be 
from 60-6F.

-m=y
where y can be:

6	for a 60K buffer
5	for a 50K buffer
4	for a 40K buffer
3	for a 30K buffer
2	for a 20K buffer 

A sample command would look like:

VPACKODI  -m=3

This flag allows you to lock a capture buffer when 
loading VPACK or VPACKODI.  This makes sure 
that a buffer is allocated no matter what is using 
lower DOS memory in Windows.

Since the allocation of the lower DOS memory 
under Windows is dynamic and often very 
inefficiently laid out, locking VPACK or 
VPACKODI’s memory will usually not result in any 
loss of functionality.  In other words, programs 
often take as much RAM as is available, and if 
they get less, it will not hurt them - WFW 
networking is an example of this.

If you see an error indicating that you do not have 
enough contiguous DOS memory to allocate 
VPACK or VPACKODI’s buffer, you will need to use 
the "-m" flag.

This error is VPACK or VPACKODI telling you that 
other applications have taken all of the DOS 
memory available and have not left enough 
room for VPACK or VPACKODI to allocate a 
buffer.

First off, lets explain how Windows handles DOS 
drivers and what happens to your lower DOS RAM 
when you start Windows.

People often think that because when they open 
a DOS window in Windows they may have 500+ K 
of RAM free, that this is how much RAM they 
actually have available in DOS.  This is not true.  
Each time Windows opens a new DOS window it 
allocates an additional 640K of RAM from the 
RAM above 1 MEG.  Your original (lower) DOS 
memory (the memory that is below 1 MEG) is used 
by Windows and Windows programs for all sorts of 
things.  For example, Windows for Workgroups 
drivers can use up to 450K of your original DOS 
memory to load.  If it cannot allocate this Ram 
Windows will not load WFW networking.  (Try and 
load WFW with only 420K free in DOS - you will see 
what we mean).

VPACK and VPACKODI were designed to take 
only 3K of DOS memory while Observer is not 
running and auto allocate up to 60K of DOS buffer 
when you run Observer (the memory is returned 
when you terminate Observer).  VPACK and 
VPACKODI try to allocate 60K if they can find the 
60K contiguous.  If they can not find 60K, they try 
50K, 40K, 30K then 20K.  After that they give up 
and you see the error message.

This can be solved in two ways:

1. Unload some of the offending programs.  
Sound blasters, screen savers, clock utilities, 
and unused network protocols are the usual 
suspects.  And try running VPACK or 
VPACKODI again.

2. Run VPACK or VPACKODI with a locked 
memory buffer - explained above.







USING NETWARE DISCOVERER
OVERVIEW AND QUICK START
To start Discoverer double click on the Discoverer 
icon.

Note:  As mentioned in the install, Discoverer 
REQUIRES Novell Netware, ODI, the VLM’s and all 
of the Netware Windows DRV’s, DLL’s and VxD’s 
installed and running.  If you experience problems 
running Discoverer, see the installation section 
under ODI (section 1a) for things to check.

Additionally, at this time to receive Netware 
statistics you must be using Novell’s 802.3 for your 
IPX/SPX FRAME type.  This is the Netware default.  
This is a Novell limitation.

Discoverer's main window consists 
of a MDI window with a menu on top and a set of  
often used commands in a button bar.  On the 
left there is a graphical list of servers and nodes 
(Called the "List of Nodes"), the right side is 
separated by a split window bar and is the area 
reserved for SERVER and NODE information 
windows.

 
All the buttons on the button bars have a short 
informational description for the button that can 
be invoked by placing the cursor over a particular 
button and pressing (and holding down) the 
RIGHT mouse button.

To display a list of nodes attached to a particular 
server, double click on the server icon on the left 
side of the MDI window (known as the "List of 
Nodes") with the LEFT mouse button.  To close the 
graphic node list of a particular server double 
click on the server icon again (using the LEFT 
mouse button).

To display a SERVER or NODE informational 
window click on the RIGHT mouse button on a 
server or node icon in the graphical list of servers 
on the left of the MDI interface, and an 
information window will appear in the area to the 
right.

From the SERVER or NODE informational window 
you may select the information you would like to 
display.  This information includes:

The Charts menu - this shows graphical 
information in real time about the network,

The Lists menu - this shows tables of information 
that are updateable with time, 

The Info menu - this shows version information and 
statistics that do not change considerably in short 
period of time and do not need to be updated as 
often. 

Depending which selection you made you may 
use different entries in the Options menu to 
customize the display to fit your needs and 
preferences.  You can set update periods and 
colors separately for every type of chart.  The 
Color Setup dialog also can be invoked by click 
of the RIGHT mouse button anywhere on a chart.  
The vertical scale of a chart can be changed 
from Scale menu item under Options in the 
specific NODE or SERVER information window.

The NODE list's update period is settable under 
"Options" -> "Timing" from any NODE information 
window.  This sets the polling simultaneously for all 
NODE lists.  Setting this from a SERVER information 
window, sets it for all SERVER lists.  Timing set while 
displaying a chart sets timing for that chart only.

Note:  At certain moments - when Discoverer polls 
the network or collects information - new  
commands that could interfere with current 
activity will be ignored.  Do not be alarmed - this 
is a normal way Discoverer operates.
THE MAIN MDI WINDOW
Discoverer's initial main screen (the MDI window) 
consists of a menu bar, button bar, List of Nodes 
listbox (on the left) and information window area 
(on the right) divided by vertical splitbar.

 
The List of Nodes is a two level graphical 
representation of servers and nodes on the LAN.   
Discoverer fills the List of Nodes with icons of 
servers it finds on your LAN in the first few seconds 
after startup.

Note:  The first polling's success is as an indication 
of the Novell support VLMs, drivers and DLLs 
installation.  If you do not get the initial listing of 
servers, some piece of the Novell driver set was 
not properly installed.  An error message should 
appear telling you which file(s) needs to checked 
or added.

After listing of servers appears, you can display a 
list of nodes attached to any server by double 
clicking on the LEFT mouse button.  This "opens" 
the server list.  Double clicking again on the LEFT 
mouse button closes the list.

Click on RIGHT mouse button over any server or 
node icon opens a SERVER or NODE information 
window on the right side of the MDI window.
File Menu
Discoverer’s "File" menu includes the following 
items:

License - This choice only appears if Observer and 
Discoverer are not licensed.  You can license 
either program from either license dialog.

Store List of Nodes - stores the current list of nodes 
for Discoverer to recall or reuse at a later point in 
time.  (Duplicates the functionality of the button in 
the Main MDI window button bar).

This is an important concept.  The "List of Nodes" 
should be saved and added to from time to time 
as you add station to your LAN.  Think of this as 
your template from which you begin each 
Discoverer session.  When your template is 
accurate - listing all nodes and servers - you can 
see which nodes or servers are on, running and 
active.  But most importantly, you will also be able 
to see any inactive nodes or server.  If you do not 
save and update the List of Nodes, Discoverer will 
only see active stations each time it starts up, and 
thus will not show any stations or servers that may 
be down for valid or non valid reasons.

Load List of Nodes - loads saved list of nodes 
stored with "Store List of Nodes" and forces 
Discoverer to displays the saved list.

Save List of Nodes to a Text File - saves the 
complete (current) list of nodes to a text file 
(*.SAV).

Print List of Nodes - prints out the (currently 
displayed) list of nodes (prints all servers and all 
attached nodes).

Save Node Information to a File - stores List or Info 
tables to a file.  If the active information window 
(window displaying server or node information ) is 
currently displaying a chart, this menu item is 
replaced by:  

Save Chart in Spreadsheet Format - which 
allows to save the charted information in 
coma delimited text format compatible 
with Microsoft Excel and other spreadsheet 
applications.

Print Node Statistics - prints the List or Info table.  If 
the active information window (window displaying 
server or node information) is currently displaying 
a chart, this menu item is replaced by:

Copy Chart to Clipboard - which copies the 
current chart to Windows clipboard to be 
processed by any image editor including 
Windows Paintbrush.

Print Setup - lets you select and configure a printer 
from the currently installed Windows printer list.

Exit - exits Discoverer.

About Discoverer - displays version and copyright 
information.
Options Menu
Discoverer’s "Options" menu consists of three 
entries:

Preferences - the dialog to set the general 
operational parameters for Discoverer (a more 
detailed explanation of this dialog is located in 
the Preferences section later in this manual).

Observer Discovery Alias List - Discoverers 
Discovery Alias List is designed to collect hardware 
addresses used on the network, and in the same 
way as Observer aliases them with Internet 
Addresses, it aliases hardware addresses with 
Novell user names.  When saved, these aliases will 
be used by Observer for Packet Viewing.

Server exclusion List - the dialog that allows you to 
exclude/include various servers from the list of 
nodes.

Login to Server - Login to Server lets the 
administrator login to a highlighted (on the list of 
nodes) server.  To receive a list of users from the 
server, a Discoverer operator MUST HAVE 
SUPERVISOR privileges.  If he or she logged in 
earlier with different name, this option first logs you 
out, then asks you to login as supervisor (or 
equivalent).  If desired, Discoverer can autologin 
on some or all of the servers (this option must be 
enabled in Preferences dialog).
The Preferences dialog

 
Ask Confirmation on Exit - if selected, Discoverer 
displays a warning message when a user chooses 
either the Exit button or chooses "Exit" from the 
"File" menu.  It is intended to prevent accidental 
termination of Discoverer and loss of collected 
data.

Ask confirmation to save List of Nodes - if selected 
this prevents accidental overwriting of the List of 
nodes by popping up a conformation dialog.

Show Tips - this option if selected enables 
displaying a short list on the most essential tips on 
Discoverer's startup.

Statistics display mode - this gives the choice of 
the three ways information windows can be 
displayed:

Single maximized window node - in this 
mode only one maximized information 
window can be displayed at one time.  
When a user starts an information window 
for different SERVER or NODE, the current 
information window terminates.

Multiple maximized window nodes - in this 
modes an information window is maximized 
as in the previous option, but when starting 
a new window, the previous one does not 
terminate.  The new window takes place of 
the previous one.  A user can switch 
between the windows using the CTRL-TAB 
key combination.  The windows can then 
be tiled or cascaded with the appropriate 
buttons from the menu bar, or menu 
choice.

Multiple normal window nodes - in this 
mode all of the information windows are 
displayed non-maximized.  They can be 
positioned, tiled and cascaded to enable 
monitoring of multiple servers or 
workstations simultaneously.

Load saved List of Nodes on startup - 
automatically loads the current saved list of 
nodes.  Otherwise the List of Nodes starts blank 
and is gradually filled with active servers and 
nodes (as they respond to polling).  Note: this 
must be checked to use an exclusion list.  In other 
words, if this is not checked, the list of nodes fills 
with whatever servers answer and no exclusions 
are checked, or used.

Allow autologin to selected servers - When this 
option is selected, Discoverer automatically logs in 
on the servers that the Discoverer's PC was not 
attached to prior to the start of Discoverer.  If the 
login entry was not saved, a user will be asked to 
login.  If the user selects to save current login 
(from the login dialog), Discoverer will save and 
then use this login and password in future.

Note: To receive information about users 
attached, and consequently other information for 
these users from a server, you must be logged in 
as SUPERVISOR, or a user with equivalent 
privileges.  If you were not logged in as 
SUPERVISOR prior to starting Discoverer, you may 
find that all nodes are dark (if Load Saved List of 
Nodes on startup option was selected), or there 
are no nodes attached to the server.  In this case 
LOGIN TO THE SERVER by pressing on the similarly 
named line in the Options menu, and on the next 
polling session (every 20 seconds by default) 
Discoverer will autologin to the server, or you will 
be asked to enter your name and password.

Display polling cursor when minimized - this option 
toggles off and on the display of the Discover 
hourglass cursor when Discoverer itself is minimized 
but still polling servers or nodes.  This special cursor 
will help you determine whether a system delay is 
caused by Discoverer polling, or by another 
program.  When Discoverer is the active window, 
it always displays the Discoverer hourglass when 
polling.

Discoverer server polling period - This option 
allows you to adjust the polling period Discoverer 
uses to update the "List of Nodes" table on the left 
of the main MDI Discoverer Window.  Two values 
are required:

Window - this is the number of seconds that 
Discoverer waits to poll all servers/nodes 
active in the "List of Nodes" WHILE 
DISCOVERER IS ACTIVE (NOT MINIMIZED).

Minimized - this is the number of seconds 
that Discoverer waits to poll all 
servers/nodes active in the "List of Nodes" 
while Discoverer is iconified.  You may want 
to adjust this quite high if you are collecting 
statistics on a node or server.  Doing so will 
minimize the disruption of your work while 
Discoverer is running.

Addition Polling Time - this is a tuning parameter 
that should be used on large or busy LAN’s when 
the time required for the server to respond to a 
poll is so long that Discoverer believes that the 
server is down.  Typically this should be left at 0.  If 
your servers seem to go dark (i.e. Discoverer thinks 
they are down) every so often, introduce a 1 or 2 
second additional polling time, this should solve 
the problem.
Discoverer Discovery Mode

 
Discovery mode allows you to capture all of the 
hard network addresses on your LAN, store them 
in Observer's the filters table, and alias them as 
names or Novell Login names.

Press "Add New" to begin, and the discovery 
mode table will begin polling servers and 
capturing addresses.  Once captured you can:

Clear - clear the table

Add/Edit Alias - selecting one address and 
pressing this button will pop up the edit box to 
add an alias.  Make sure you click on the down 
arrow at the right when complete.

Highlight New - shows the new addresses.  These 
would be addresses that were discovered, but are 
not yet on the address list in Observer's filter 
section.

Save Highlighted - saves the highlighted address 
to Observer's filter table.

Save All - Saves all of the addresses/aliases 
(overwrighting all others).

Check the box at the bottom of the dialog to 
automatically "Fill Addresses with Novell Name"

Or check the "Load List of addresses at startup" to 
load Observer's filter table at startup to try to  
discover Novell login names for addresses without 
aliases.
Server exclusion List
Discoverer includes the ability to "exclude" 
certain servers from the list of nodes.  You may 
want to do this if you have many servers that 
cannot provide useful information in your list of 
nodes.  To exclude a server, choose "Options" -> 
"Server exclude List" and highlight the server you 
want to exclude in the "Display Servers" list and 
pressing the "Exclude" button.

 
For example, if you have many print servers, 
CDROM servers, dead servers (servers that your 
active servers can see across a wide area 
network, but are not available for your 
inspection), or servers that you are simply not 
interested in - you can exclude these, and as long 
as you have "Load saved List of Nodes on 
Startup" checked in the Preferences dialog, they 
will not appear in your list of nodes.

You can restore any server simply by going into 
the "Server exclude list" highlighting the server to 
be restored in the "Excluded Severs" box, and 
pressing the "Restore" button.

Login to Server
To be able to receive information about users 
attached, and consequently other information for 
these users, you have to be logged in as 
SUPERVISOR, or a user with equivalent privileges.  If 
you were not logged in as SUPERVISOR prior to 
starting Discoverer, you may find that all nodes 
are dark (if load saved List of Nodes on startup 
option was selected), or there are no nodes 
seemingly attached to a server.  In this case Login 
to Server by choosing this from the Options menu, 
and on the next polling session (which happens 
every 20 seconds by default) Discoverer will 
autologin to the server (if you have saved the 
servers autologin information and have Allow 
Autologin to Servers checked in preferences), or 
you will be asked to enter your name and 
password.

The Login to Server dialog has the following 
options:

 
Login name - this should be SUPERVISOR or a user 
with SUPERVISOR equivalencies.

Password - the user’s password.

Save current login - this saves the login 
information  for autologin (only used if you have 
"Allow Autologin to Selected Servers" enables in 
"Options" -> "Preferences").  This information is 
kept encrypted in the DISCOVERER.INI file.

Do not login (print server only) - this deactivates 
the autologin feature for the highlighted server.  
Use this option only if it is a server that does not 
require a login (i.e. a print server).  If you do not 
want to login to a standard server, use the Server 
exclude/include option.
The Window Menu
The Window Menu contains the following items:

Tile - tiles all information windows (both SERVER 
and NODE).

Cascade - arranges information windows in a 
standard Windows cascade.

Arrange Icons - if there are minimized information 
windows, this option lets you neatly arrange them.

Close All - closes all information windows.

In addition, if there is one or more information 
window, a list of them is appended to this menu, 
from which you can choose a window to make it 
the active window.
THE MDI WINDOW BUTTON BAR
The Main MDI Window button bar is provided for a 
quick access to some of the often used, or 
potentially often used functions of Discoverer.

Short help information for the purpose of each 
button can be seen by pressing (and holding 
down) the RIGHT mouse button on the button in 
question.

Here is the list of the buttons and their functions in 
order from left to right:

 
List of Nodes Display Options - allows you to 
configure the display of the contents of the server 
and node text in the List of Nodes.  It can be a 
node name only, node name + address, or node 
name + address + attach time.

Save List of Nodes - this is used to save the current 
list of nodes (and servers).  You might use this to 
save a list of all servers and workstations.  At a 
later date you could "Load List of Nodes" (see 
below), and Discoverer would display not only the 
active stations discovered, but also all stations in 
the saved list of nodes.  This would then display all 
active stations and all non-active stations in the 
saved list.  This is useful to get a complete listing of 
all station to determine when the network 
configuration changes, or to display which 
stations are up or down.

It is recommended that you keep "Ask 
Confirmation to Save List of Nodes" checkbox 
selected (in "Options" -> "Preferences") to 
prevent inadvertent overwrighting of the current 
list.

Load Saved List of Nodes - this loads the saved list 
of nodes.  You may want to do this prior to saving 
the list of nodes.  This way you can get all stations, 
both active and non-active in your list of nodes.

Delete entry - this deletes a highlighted entry on 
the List of Nodes.  You might want to use this to 
remove a station or server that has been stored 
on the list of nodes, but has since been removed 
from your site.

Stop Polling for Statistics - is used to completely 
stop polling.  You can start polling again by 
pressing the button again.  Stopping the polling 
will  prevent updating the List of Nodes.  Stop 
Polling can be also used to save the current state 
of a chart or list, when it is necessary to prevent it 
from updating or changing position.

Tile Node Windows and Cascade Node Windows 
can be used to arrange Information Windows in 
the view area.

Exit - closes Discoverer.
THE LIST OF NODES VIEW
The "List of Nodes" View is the actual list of SERVES 
and NODES on the left hand side of the main MDI 
window.  This is where you will see a graphical 
depiction of all of the NODES, SERVER, ROUTERS, 
BRIDGES, etc. on your LAN.

 
You can expand any server by double clicking on 
the LEFT mouse button on the server icon.  You 
can display a SERVER or NODE information 
window on any SERVER or NODE by single clicking 
on icon with your RIGHT mouse button.
INFORMATION WINDOWS (GENERAL)
The following information applies to both the 
NODE Information window and the SERVER 
information window.

An information window Options button menu 
displays the following choices:

2D - 2D charting offers choices of Lines, Columns 
and Pie charts.  Sample charts:

3D - charting offers Separate and Alternate 
Columns.  A user can choose the chart that is 
most useful for their needs.  Some menu items 
may be grayed out depending on the 
applicability to the active window. (charts only)

Colors - The Colors dialog appears when the 
Colors item is selected from the Options menu, or 
when user clicks on the RIGHT mouse button 
anywhere on a chart.  It allows you to select the 
background and foreground colors, hatch, axis, 
coordinate lines, appearance, and color or a 
specific attribute.  This is done separately for every 
type of chart (as appears in Charts menu), and 
separately for servers and nodes. (charts only)

 


Scale - The Scale submenu allows to expand or 
contract the vertical scale of a chart to 
accommodate the charts scale to the wide 
range of amplitudes of data.  This value is also 
saved separately for every type of chart.

Timing - The Timing dialog is applied to all 
updateable information window display modes 
(included in Charts and Lists menus for SERVERS 
and NODES).  It is where you set the polling period 
for the chart or list.  Reading (list refresh) period is 
the interval of time between polling a server or a 
node by Discoverer.  Values are from 10 seconds 
to 1 hour.
SERVER INFORMATION WINDOWS
A SERVER information window is displayed in the 
information area (on the left of the MDI main 
window) after a user clicks on the RIGHT mouse 
button on a server icon in the List of Nodes.  
SERVER information windows (which are very 
similar to NODE information windows) consists of a 
button bar with Charts, Lists, Info, and an Options 
popdown menu buttons and an Exit button.

Button bar buttons can be selected using mouse 
clicks, and in most cases by pressing a letter on 
the keyboard that corresponds to one displayed 
in red on the button. (Note: due to the nature of 
the MDI interface you DO NOT use ALT when 
accessing the information window buttons.  Use 
ALT-KEY combination to popdown menus on the 
Main MDI  window).

Context sensitive help is available from any 
window by pressing F1.
Charts
The SERVER information window Charts menu 
contain the following choices (sample charts are 
located in the "Information Windows (general) 
section):
Number Connections (server)
Number of Connections chart displays the 
number of active connections to a specific Novell 
server.  This is also called the number of logged in 
users.  This statistic is received directly from the 
Novell server.

This chart can be saved to a file in spreadsheet 
format ("File"-> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Open Files (server)
The Open Files chart shows number of files 
currently open on a specific Novell server. This 
statistic is received directly from the Novell server.

This chart can be saved to a file in spreadsheet 
format ("File"-> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
IPX Packet Statistics (server)
The IPX statistics chart displays the number of sent 
and received IPX packets as a function of time.  It 
shows the server's IPX packet flow activity.

Malformed packets for send and Get ECB (Event 
Control Block) for receive are a sum of several 
failure conditions, and can indicate, if significant, 
improper functioning or overload of the server.  
More detailed information can be seen in IPX 
Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
SPX Packet Statistics (server)
The SPX statistics chart displays the number of sent 
and received SPX packets as a function of time.  It 
shows the server's IPX packet flow activity.

Bad Send Packets for send and Get Bad Receive 
Packets receive are a sum of several failure 
conditions, and can indicate, if significant, 
improper functioning or overload of the server.  
More detailed information can be seen in SPX 
Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Total Packet Statistics (server)
The Total Packet Statistics display number of total 
(all protocols) sent and received packets by a 
server as a function of time.  It is an indication of 
the server's total network activity.

"Bad Send Packets" for send and "Get Bad 
Receive Packets" for receive are a sum of several 
failure conditions.

Bad Send Packets combines sum of: Send Packet 
Too Big, Send Packet Too Small and Send 
Miscellaneous Errors, and can indicate improper 
functioning of a server, or malfunctioning one of 
the NLM’s.

Get Bad Receive Packets is the sum of a set of 
error conditions, and if significant, indicate an 
overload of the server.  More detailed information 
can be can be seen in Bridge Driver Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Bridge Statistics (server)
The Bridge Statistics displays the number of 
packets routed through the bridge as a function 
of time.  Novell considers each network card 
driver in your server as a "Bridge".  Novell 
considers each instance of the driver loaded 
(usually for each frame supported) as a "board".  
So, each "Bridge" (card in your server) may have 
one or more logical "boards" loaded in it.  Each 
board is displayed and each statistic is kept for 
each board.  You can only "see" the Bridge in the 
server that you are connected to (this is a 
Netware limitation).

It includes the number of packets serviced and 
packets routed, and some the most common 
error conditions: 

Total Packets Serviced - the total number of  
packets the bridge serviced since the bridge was 
initialized.  This is the number of packets that 
arrived on the server, but not necessary were 
routed.

Total Packets Routed - the total number of 
packets the router actually routed.

Too Many Hops - this is an indication that the 
packet (that reached the current server) has 
"hopped" too many times before reaching its 
destination.  It is the number of times (since the 
bridge was initialized) the bridge received 
packets on the fifteenth hop across an 
Internetwork bridge.  These packets are 
discarded.

Hop is the transition (or hop) of a packet on its 
way to a destination server or station from another 
server or station.  This error may indicate that the 
routing scheme used on the network is 
inadequate, or possibly the server that was 
servicing a more direct connection path is 
currently down or out of order.  The situation may 
require the network administrator’s intervention.  
This error can occur only on larger sites with many 
nets and bridges, or on sites experiencing an 
"infinite loop" between routers or server.

Unknown Network - these are packets that 
reached the server and can not be routed 
because the destination network is unknown to 
the server.

This error may appear if a router that was 
transferring packets to the known destination is 
down or was shut down.  In this case the router 
sends "going down" broadcasts from which all 
routers update their routing tables to remove any 
routes that are no longer available.

No Space for the Service - this is the number of 
times (since the bridge was initialized) the bridge 
has received Internetwork packets it could not 
accommodate because the router did not have 
enough space in its DGroup area to copy the 
packets.  These packets are lost.

This condition, can be an indication of network 
overload, or the server may be too slow to 
process the amount of data on a growing 
network.  Monitoring the network bandwidth 
utilization using Observer can help clarify this 
question.  In either case, if the condition persists 
and has an adverse effect on the network 
performance, there may be a need add a server 
and split the network load between them, 
upgrade the server system with a faster CPU or 
more RAM, or reconfigure stations and servers via 
segmentation of the wire to provide a more even 
load on the bridges and servers.

No Receive Buffers - this is the number of times 
(since the bridge was initialized) the bridge could 
not receive inbound packets because of 
inadequate buffer space.  These packets are lost.

This condition is essentially similar to the previous 
one, with exception that the error occurs on the 
earlier stage of packet processing and indicates 
either too few receive buffers, or more directly the 
network (as opposed to server or bridge) is 
overloaded.  Again a more definite answer can 
be obtained monitoring long and short term 
bandwidth utilization using Observer.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Volume Usage (server)
The Volume Usage chart displays used and free 
volume space (separately by each available 
volume) on a server.  If the number of volumes is 
larger than can be fit in the information window 
area, use the scroll bar to move along the volume 
listing.  This is useful for checking remotely how 
much free disk space remains on a server volume, 
and take appropriate actions when any of the 
volumes reach critical usage.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Options
A user can customize the way charts are 
displayed by selecting the Options button in the 
SERVER information window and then choosing 2D 
or 3D, Colors, Timing and Scale options from the 
Charts menu.

Under 2D or 3D the choices are - Lines, Columns 
and Pie for 2D charts, Separate columns and 
Alternate columns for 3D charts.

The Colors dialog lets customize colors for every 
chart separately.  You can for example, have a 
different chart type and set of colors for Open File 
than you have for IPX Packet Statistics, and 
Volume usage, and so on.

The Timing dialog sets timing periods for each 
chart separately, and one common timing value 
for all Lists. 

The Scale dialog lets change the vertical scale of 
a chart to fit best your system parameters.  The 
best way to understand this dialog is to  
experiment.
Lists
Lists are updateable tables of information about 
servers. The update period is set in "Options"-> 
"Timing" menu.

The SERVER information window List menu has the 
following choices:
IPX Packet Statistics List (server)
The IPX Packet Statistics List shows a summary of  
IPX traffic since the Novell server was booted.  It 
includes:

Send Packet Count - the total number of IPX 
packets sent.

Malformed Packets - the number of times (since 
IPX was loaded) applications have passed 
malformed packets to IPX.  A packet is malformed 
if the value in its ECB's fragment count field is 0 or 
if the value of the size field within ECB's first 
fragment descriptor is less than 30 bytes.  This can 
be due to malfunctioning of one of the NLMs.

Get ECB Request Count - the number of times 
(since IPX was loaded) IPX has supplied Receive 
ECBs for incoming packets.  Event Control Blocks 
(ECB) should be provided for every incoming 
packet in order to process it.  This count does not 
indicate an error condition.

Get ECB Failure Count - the number of packets 
the driver has received, for which there was no 
available ECB.

In network or server overload condition there can 
be no ECB’s available, and packets may be lost.

AES Event Count - the number of times (since IPX 
was loaded) IPX has used the AES to schedule an 
event.

Asynchronous Event Service (AES) is called when 
the stack is not able not keep up with processing 
of network traffic and must schedule a send or 
receive event to happen in later time (usually a 
few milliseconds later).

Postponed AES Events - the number of times (since 
IPX was loaded) IPX has been unable to service 
an AES event on time.  This can be due to a MLID 
being in a critical section.  For example - IPX 
cannot send an outgoing packet to an ECB busy 
with another packet.  In this case the AES must be 
postponed (rescheduled) to happen at later time.  
If number of Postponed AES Events is high, it can 
be indication of high network or processing load 
on the server, and may indicate that it is time to 
upgrade all or parts of the server (i.e. CPU, 
memory, disk access time, etc.).

Max Configured Sockets - the maximum number 
of open sockets possible on the target server.

Max Opened Sockets - the maximum number of 
sockets open simultaneously since IPX was 
loaded.  This should be 75% or lower than the Max 
Configured Sockets.

Open Socket Failures - the number of times (since 
IPX was loaded) applications have unsuccessfully 
called IPXOpenSocket.  IPX cannot open a socket 
if the socket table is full or if the socket is already 
open.  If this number is greater than 0, you will 
need to tune your server to accommodate more 
sockets.

Listen ECB Count - the number of times (since IPX 
was loaded) applications have given IPX a Listen 
ECB.

A Listen ECB is given when a Netware application 
expects to receive a packet associated with a 
specific socket (usually a reply to a "just sent 
command" or reques).  Neither a low or high 
value is an indication of a failure condition.

ECB Cancel Failures - the number of times (since 
IPX was loaded) IPX has been unable to cancel 
an ECB.  For example, IPX cannot cancel an ECB 
if the driver and the ECB have entered a critical 
section just prior to sending a packet.  In this case, 
the cancellation is too late, and would be 
flagged as an ECB Cancel Failure.

Find Route Failures - the number of times (since 
IPX was loaded) IPX has been unable to find a 
route to a requested network address.

This error may appear if a router that was 
transferring packets to the known destination was 
shut down.  In this case the router sends "going 
down" broadcasts from which all routers update 
their routing tables and remove any routes not 
longer available.
SPX Packet Statistics List (server)
The SPX Packet Statistics List displays a summary of 
the SPX traffic since the Novell server was booted.  
It includes:

Max Connections - the maximum number of SPX 
connections possible on the target server.

Max Used Connections - the maximum number of 
SPX connections open simultaneously since IPX 
was loaded.

Establish Connection Requests - the number of 
times (since SPX was loaded) applications called 
SPXEstablishConnection.  This call attempts to 
contact a partner to establish a session.

Establish Connection Failure - the number of times 
(since SPX was loaded) SPXEstablishConnection 
calls failed because the SPX Packet Header was 
too small, the SPX Connection Table was full, no 
router was found to the target network, or the 
target node was down.

Listen Connections Requests - the number of times 
(since SPX was loaded) applications called 
SPXListenForConnection.  This call is issued by 
Netware application to instruct SPX to watch for a 
connection request from a peer system.

Listen Connection Failure - the number of times 
(since SPX was loaded) SPXListenForConnection 
calls failed because the SPX Connection Table 
was full. This is an indication that the total number 
of available SPX connections on the server is not 
adequate for current network activity.

Send Packet Count - the number of times (since 
SPX was loaded) applications tried to send a SPX 
packet.  This number is a sum of all send packet 
attempts, successful and not successful.

Window Choke Count - the number of times (since 
SPX was loaded) SPX failed to send a packet 
because the target station had not allocated a 
receive buffer.  This is an indication of high load 
on the target station.  This statistic does not show 
the station responsible; if necessary the station 
can be determined using Observer in Packet 
Capture mode or Protocol Statistics mode.

Bad Send Packets Count - the number of times 
(since SPX was loaded) 
SPXSendSequencedPacket was incorrectly called 
by passing an invalid connection ID or by passing 
the address of an ECB indicating a packet header 
size of less than 42 bytes.  This can indicate a 
malfunctioning SPX application.  In this case the 
connection to the target station is aborted.

Send Failure Count - the number of times (since 
SPX was loaded) SPX was unable to send a 
packet across a connection and receive 
acknowledgment.

This can happen when a remote peer closes a 
connection without acknowledging the SPX 
packet.  In this case there is no guarantee that 
the packet was received.  Other causes can be a 
connection closed abnormally (frozen or a 
rebooted station).

In such a case, SPX aborts the connection and 
informs the calling application.

Abort Connection Count - the number of times 
(since SPX was loaded) SPXAbortConnection was 
called.

This event is initialized when some catastrophic 
condition (from the point of view of application 
that is using this connection) occurs.  This could be 
an indication of malfunctioning NLM application.  
In this case the connection is terminated 
unilaterally by the current application without 
notifying the other machine.  The partner 
discovers the broken connection when it tries to 
send a packet to this application (getting Send 
Failure error, see above), or when the Watchdog 
checks the connection after the inactivity time 
expires.

Listen Packet Count - the number of times (since 
SPX was loaded) applications gave listen ECBs to 
SPX.  Listen ECB is given when a Netware 
application expects to receive a packet 
associated with a specific socket (usually a reply 
to a just sent command or reques).  Neither a high 
or low value is any indication of an error 
condition.  There is no limitation on the number of 
Listen ECBs, which should be provided by a 
Netware application.

Bad Listen Packet Count - the number of times 
(since SPX was loaded) applications passed SPX a 
packet whose associated ECB is malformed.  An 
ECB is malformed if the value in Fragment Count is 
0, if the value in its first Fragment Descriptor Size is 
less than 42, or if the listen socket is not open.  

Incoming Packets - the number of times (since 
SPX was loaded) the node's driver gave an 
incoming packet to SPX.

Bad Incoming Packets - the number of times 
(since SPX was loaded) SPX received and 
discarded a packet because the connection ID in 
the packet was wrong.

Suppressed Packet Count - the number of times 
(since SPX was loaded) SPX discarded inbound 
packets because they were duplicates of 
previously received packets.  This condition 
indicates the sending station has not received an 
acknowledgment for a sent packet (due to delay 
or collision).  It may indirectly indicate high 
network utilization.  Observer will help determine if 
this is the case.

No Session Listen ECB Count - the number of times 
(since SPX was loaded) SPX was forced to discard 
an inbound SPXEstablishConnection packet 
because SPX lacked a corresponding SPX Listen 
For Connection ECB.

Watchdog Destroy Sessions - the number of times 
(since SPX was loaded) WatchDog destroyed a 
connection because the connection was no 
longer valid.  WatchDog packets are sent 
periodically if no packets are received from a 
peer within 5 minutes.  If there is no WatchDog 
reply, the station repeats WatchDog request ten 
times in one minute intervals, after which the 
connection is considered invalid.
Total Packet Statistics (server)
The Total Packet Statistics List includes the 
following entries:

Driver Version, LAN driver version for the specified 
LAN board.

Statistics Version - the major and minor version 
number of the Driver Diagnostic Table.

Total Sent Packets - the number of packets the 
driver has successfully transmitted since the last 
driver reset or initialization.

Total Received Packets - the number of packets 
the driver has successfully received and passed 
into the system since the last reset or initialization.

No ECB Available Count - the number of packets 
the driver has received (since the last reset or 
initialization) for which there was no listening ECB.  
In a server overload condition, there may be no 
ECB’s available, and packets may be lost.

Packet Too Big for Send - the number of times 
(since the last reset or initialization) applications 
have asked the driver to send a packet over the 
maximum legal size.  This can indicate improper 
functioning or configuration of an application.

Packet Too Small for Send - the number of times 
(since the last reset or initialization) applications 
have asked the driver to send a packet under the 
minimum legal size.  This can indicate improper 
functioning or configuration of an application.

Receive Packet Overflow - the number of times 
(since the last reset or initialization) the driver has 
received a packet larger than the buffer space 
allocated for the packet.  When a packet is 
received, the protocol stack that accepted the 
packet provides a set of buffers into which the 
packet should be dispersed.  If there is not 
enough buffer space or for any reason the 
protocol stack allocated a smaller buffer, this error 
occurs.

Received Packet Too Big - the number of times 
(since the last reset or initialization) the driver has 
received a packet over the maximum legal size.  
It may indicate an error in the packet header due 
to a collision, or malfunctioning of the sending 
application.

Received Packet Too Small - the number of times 
(since the last reset or initialization) the driver has 
received a packet under the maximum legal size.  
This may indicate an error in the packet header 
due to a collision, or malfunctioning of the 
sending application.

Transmit Misc. Errors - the number of 
miscellaneous errors preventing the driver from 
transmitting a packet.

Receive Misc. Errors - the number of 
miscellaneous errors preventing the driver from 
receiving a packet.

Send Retry Count - the number of times (since the 
last reset or initialization) the driver resent a 
packet.  For  example, when the driver detects a 
collision or does not receive a confirmation on a 
sent packet, the driver re-sends a packet.  If 
significant, this number can indicate high network 
bandwidth utilization.  Use Observer to check this 
assumption.

Checksum Error Count - the number of checksum 
errors occurring while receiving packets (since the 
last reset or initialization).  High checksum errors 
can indicate bad cabling or a bad hub.

Receive Hardware Mismatch - the number of 
times (since the last reset or initialization) the 
hardware has received more or fewer bytes than 
expected.
Bridge Statistics List (server)
Novell refers to the "Bridge" as the physical LAN 
board in your server.

Bridge Statistics List includes the following values:

Total Packets Routed - the total number of  
packets the router actually routed.

Too Many Hops - this is too many hops for the 
packet (that reached the current server) to reach 
it's destination.  It is the number of times (since the 
bridge was initialized) the bridge received 
packets on the fifteenth hop across an 
Internetwork bridge.  These packets are 
discarded. 

Hop is the transition (or hop) of a packet on its 
way to a destination server or station from another 
server or station.  This error may indicate that the 
routing scheme used on the network is 
inadequate, or possibly the server that was 
servicing a more direct connection path is 
currently down or out of order.  The situation may 
require the network administrator’s intervention.  
This error can occur only on larger sites with many 
nets and bridges, or on sites experiencing an 
"infinite loop" between routers or server.

Unknown Network - these are packets that 
reached the server can not be routed because 
the destination network is unknown to the server.

This error may appear if a router that was 
transferring packets to the known destination was 
shut down.  In this case the router sends "going 
down" broadcasts upon which all routers update 
their routing tables and remove the no longer 
available routes.

No Space for the Service - the number of times 
(since the bridge was initialized) the bridge has 
received Internetwork packets it could not 
accommodate because the router did not have 
enough space in its DGroup area to copy the 
packets.  These packets are lost.

This condition, can be an indication of network 
overload, or the server may be too slow to 
process amount of data on a growing network.  
Monitoring the network bandwidth utilization using 
Observer can help clarify this question.  In either 
case, if the condition persists and has an adverse 
effect on the network performance, there may be 
a need add a server and split network load 
between them, upgrade the server system with a 
faster CPU or more RAM, or reconfigure stations 
and servers via segmentation of the wire to 
provide a more even load on the bridges and 
servers.

No Receive Buffers - the number of times (since 
the bridge was initialized) the bridge could not 
receive inbound packets because of inadequate 
buffer space.  These packets are lost.

This condition is essentially similar to the previous 
one, with exception that the error occurs on the 
earlier stage of packet processing and indicates 
either too small number of buffers, or more 
directly network (as opposed to server or bridge) 
overload.  Again more definite answer can be 
obtained monitoring long and short term network 
utilization using Observer.

Not My Network - the number of incoming 
packets with a destination other than LAN A.  This 
statistic shows all the packets that are routed 
through the current LAN.

NetBIOS Propagate - the number of times the 
bridge received NetBIOS broadcasts since it was 
initialized.
Volume Information List (server)
The Volume Information List provides information 
about available disk space on the server volumes.  
It includes total and free disk space, and total and 
free directory entries for each volume.  It can be 
used to check remotely how much free disk 
space remains on a server volume, and take 
appropriate actions when any of the volumes 
reaches critical usage.
Open Files List (server)
The Open Files List displays the number of currently 
open files.  This list shows the total number of files 
open on a server, and then number of files 
opened by each user attached to the server.
Info:
Info menus consist of version and other constant 
information that does not need updating on the 
server.  The Info menu consists of:
Server Version (server)
The Server version provides an extensive list of 
versions of the Novell server and miscellaneous 
utilities and services, as well as maximum number 
of connections, current connections and 
maximum number of available volumes.
IPX-SPX Versions (server)
The IPX-SPX version display contains the specific 
IPX and SPX version numbers of the server's 
IPX/SPX drivers (not of the node or operating 
system).
Bridge Driver Configuration (server)
This displays the logical LAN board driver in your 
server.  This is how Novell describes the actual 
loadable card driver for each FRAME.  With 
respect to the Bridge Driver, each value is:

Max Data Size - the maximum size of a packet's 
data portion for the target driver.  The data 
portion's maximum size is always 64 bytes less than 
the packet size advertised with the LAN board.  
(The packet header and control information 
require 64 bytes).

Transport times (ticks) - the value indicating the 
speed of the LAN associated with the target driver 
and board.  Speed is measured by the amount of 
time it takes a 576-byte packet to travel from one 
node on the LAN to another node.  Time is 
measured in units of 1/18 second and rounded to 
the next highest 1/18.

Shell Version - the major and minor versions of the 
driver release; this does not identify the installed 
NetWare version.

Description - the LAN hardware currently 
connected to the driver.

I/O Address - the I/O address block to be 
decoded by the LAN board the driver is 
associated with.  If the board uses a second I/O 
addresses, this field will be also present in the list (if 
it uses I/O).

RAM Address - the memory address block to be 
decoded by the LAN board (if it uses shared 
memory).

DMA Line - the DMA line used by the LAN board (if 
it uses DMA),

Selected Line - the value indicating which 
hardware configuration in the Hardware 
Configuration Table the driver is using,

LAN hardware ID - the value that is hard-coded 
into the Master Configuration Table.  This uniquely 
identifies the LAN hardware.  (i.e. the OEM/Driver 
Support Group Manager that Novell assigns this 
ID)

Note: Not all fields listed here may be available 
from different versions of Novell servers and 
drivers.
NODE INFORMATION WINDOWS
A NODE information window is displayed in the 
information area after a user clicks on the RIGHT 
mouse button on a node icon in the List of Nodes.  
NODE information windows (which are very similar 
to SERVER information windows) consists of a 
button bar with Charts, Lists, Info, and an Options 
popdown menu buttons and an Exit button.

Button bar buttons can be selected using mouse 
clicks, and in most cases pressing a letter on the 
keyboard that corresponds to one displayed in 
red on the button. (Note: due to the nature of the 
MDI interface you DO NOT use ALT when 
accessing the information window buttons.  Use 
ALT-KEY combination to popdown menus on the 
Main MDI  window).

Context sensitive help is available from any 
window by pressing F1.
Charts
The NODE information window Charts menu has 
the following choices (sample charts are 
displayed in the "Information Windows (general) 
section):
IPX Packet Statistics chart (node)
The IPX statistics chart displays the number of sent 
and received IPX packets as a function of time.  It 
shows the node's IPX packet flow activity.

Malformed packets for send and Get ECB (Event 
Control Block) for receive are a sum of several 
failure conditions, and can indicate, if significant, 
improper functioning or overload of the server or 
node.  More detailed information can be seen in 
the IPX Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
SPX Packet Statistics chart (node)
The SPX statistics chart displays the number of sent 
and received SPX packets as a function of time.  It 
shows the node's IPX packet flow activity.

Bad Send Packets for send and Get Bad Receive 
Packets receive are a sum of several failure 
conditions, and can indicate, if significant, 
improper functioning or overload of the server or 
node.  More detailed information can be seen in 
the SPX Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Total Node Packets chart (node)
The Total Packet Statistics chart displays the total 
number of packets (all protocols) sent and 
received by a node as a function of time.  It 
allows you to see node's total network activity.

"Bad Send Packets" for send and "Get Bad 
Receive Packets" receive are a sum of several 
failure conditions, and can indicate, if significant, 
improper functioning or overload of the node 
drivers.  More detailed information can be seen in 
Bridge Driver Statistics List.

This chart can be saved to a file in spreadsheet 
format ("File" -> "Save Chart in Spreadsheet 
Format"), or the current view of the chart can be 
copied to the clipboard to be used by an image 
editor (Paintbrush, for example).
Options
A user can customize the way charts are 
displayed by selecting the Options button in the 
NODE information window and then choosing 2D 
or 3D , Colors, Timing and Scale options from the 
Charts menu.

Under 2D or 3D there are choices of the type of 
chart - Lines, Columns and Pie for 2D charts,  
Separate columns and Alternate columns for 3D 
charts.

The Colors dialog lets customize colors for every 
chart separately (for example, Open Files can 
have a different chart type and set of colors than 
IPX Packet Statistics, and Volume usage, and so 
on.

The Timing dialog sets timing periods for each 
chart separately, and one common for all Lists. 

The Scale dialog lets you change the vertical 
scale of a chart to best fit your system 
parameters.  The best way to understand this 
dialog is to  experiment.
Lists
Lists are updateable tables of information about 
nodes or servers. The update period is set in 
"Options" -> "Timing" menu.  The NODE 
information window List menu has the following 
choices:
IPX Packet Statistics List (node)
The IPX Packet Statistics List shows a summary of 
IPX traffic since the node's IPX/SPX shell was 
loaded.  It includes:

Send Packet Count - the total number of sent IPX 
packets.

Malformed Packets - the number of times (since 
IPX was loaded) applications have passed 
malformed packets to IPX.  A packet is malformed 
if the value in its ECB's fragment count field is 0 or 
if the value of the size field within ECB's first 
fragment descriptor is less than 30 bytes.  This can 
be due to malfunctioning of one of the NLMs.

Get ECB Request Count - the number of times 
(since IPX was loaded) IPX has supplied Receive 
ECBs for incoming packets.  Event Control Block 
(ECB) should be provided for every incoming 
packet in order to process the packet.  This count 
does not indicate an error condition.

Get ECB Failure Count - the number of packets 
the driver has received for which there was no 
available ECB.

If the node’s shell does not provide enough ECBs, 
(usually in high transfer rate conditions) no ECB’s 
available will result in a failure to receive or send 
packets.

Many things can cause this count to rise, including 
the condition of a slow network card in a fast 
system, or a network card with I/O or memory 
conflicts.

AES Event Count - the number of times (since IPX 
was loaded) IPX has used the AES to schedule an 
event.

Asynchronous Event Service is called when the 
stack is not able not keep up with processing of 
network traffic and must schedule a send or 
receive event to occur at later time (usually within 
a few milliseconds).

Postponed AES Events - the number of times (since 
IPX was loaded) IPX has been unable to service 
an AES event on time.  This can be due to MLID 
being in a critical section.  For example - IPX 
cannot send an outgoing packet to a ECB busy 
with another packet.  In this case the AES must be 
postponed (rescheduled) to happen in later time.  
If number of Postponed AES Events is high, it can 
be indication of to high of network or processing 
load on the station.

Max Configured Sockets - the maximum number 
of open sockets possible on the target station.

Max Opened Sockets - the maximum number of 
sockets open simultaneously since IPX was 
loaded.

Open Socket Failures - the number of times (since 
IPX was loaded) applications have unsuccessfully 
called IPXOpenSocket.  IPX cannot open a socket 
if the socket table is full or if the specific socket is 
already open.

Listen ECB Count - the number of times (since IPX 
was loaded) applications have given IPX a Listen 
ECB.

Listen ECB is given when a Netware application 
expects to receive a packet associated with a 
specific socket (usually a reply to a "just sent 
command" or reques).  Neither a low or high 
value is an indication of a failure condition.

ECB Cancel Failures - the number of times (since 
IPX was loaded) IPX has been unable to cancel 
an ECB.  For example, IPX cannot cancel an ECB 
if the driver and the ECB have entered a critical 
section just prior to sending a packet.  In this case, 
the cancellation is too late, and the packet is lost.

Find Route Failures - the number of times (since 
IPX was loaded) IPX has been unable to find a 
route to a requested network address.

This error may appear if a router that was 
transferring packets to the known destination was 
shut down.  In this case the router sends "going 
down" broadcasts upon which all routers update 
their routing tables and remove any routes that 
are no longer available.
SPX Packet Statistics List (node)
The SPX Packet Statistics List shows a summary of 
SPX traffic since the node loaded IPX/SPX.  It 
includes:

Max Connections - the maximum number of SPX 
connections possible on the target node.

Max Used Connections - the maximum number of 
SPX connections open simultaneously since IPX 
was loaded.

Establish Connection Requests - the number of 
times (since SPX was loaded) applications called 
SPXEstablishConnection.  This call attempts to 
contact a partner to establish a communication 
session.

Establish Connection Failure - the number of times 
(since SPX was loaded) SPXEstablishConnection 
calls failed because the SPX Packet Header was 
too small, the SPX Connection Table was full, or no 
router was found to the target network, or the 
target node is down.

Listen Connections Requests - the number of times 
(since SPX was loaded) applications called 
SPXListenForConnection.  This call is issued by a 
Netware application to instruct SPX to watch for a 
connection request from a peer system.

Listen Connection Failure - the number of times 
(since SPX was loaded) SPXListenForConnection 
calls failed because the SPX Connection Table 
was full.

This is an indication that the total number of 
available SPX connections on the node is not 
adequate for current network activity.  This value 
is set in the NET.CFG file.

Send Packet Count - the number of times (since 
SPX was loaded) applications tried to send SPX 
packet.  This number is a sum of all send packet 
attempts, successful and not successful.

Window Choke Count - the number of times (since 
SPX was loaded) SPX failed to send a packet 
because the target station had not allocated a 
receive buffer.  This is an indication of high load 
on the target station.  This statistics does not show 
the station responsible; if necessary, the station 
can be determined using Observer in Packet 
Capture mode or Protocol Statistics mode.

Bad Send Packets Count - the number of times 
(since SPX was loaded) 
SPXSendSequencedPacket was incorrectly called 
by passing an invalid connection ID or bypassing 
the address of an ECB indicating a packet header 
size of less than 42 bytes.  This can indicate a 
malfunctioning SPX application.  In this case the 
connection to the target station is aborted.

Send Failure Count - the number of times (since 
SPX was loaded) SPX was unable to send a 
packet across an SPX connection and receive 
acknowledgment.  This happens when a remote 
peer closes the connection without 
acknowledging the packet.  In this case there is 
no guarantee that the packet was received.  A 
connection that closed abnormally may be 
caused by a frozen or rebooted station.

In such a case, SPX aborts the connection and 
informs the calling application.

Abort Connection Count - the number of times 
(since SPX was loaded) SPXAbortConnection was 
called.

This event is initialized when some catastrophic 
condition (from the point of view of application 
that is using this connection) occurs.  This can be 
an indication of malfunctioning NLM application.

In this case connection is terminated unilaterally 
by the current application without notifying the 
other machine.  The partner discovers the broken 
connection when it tries to send a packet to this 
application (getting Send Failure error, see 
above),  or when the Watchdog checks the 
connection after the inactivity time expires.

Listen Packet Count - the number of times (since 
SPX was loaded) applications gave listen ECBs to 
SPX.  Listen ECB is given when a Netware 
application expects to receive a packet 
associated with a specific socket (usually a reply 
to just sent command or reques).

This value is a count and does not indicate an 
error condition.  There is no limitation on the 
number of Listen ECBs, which should be provided 
by a Netware application.

Bad Listen Packet Count - the number of times 
(since SPX was loaded) applications passed SPX a 
packet whose associated ECB is malformed.  An 
ECB is malformed if the value in Fragment Count is 
0, if the value in its first Fragment Descriptor Size is 
less than 42, or if the listen socket is not open.

Incoming Packets - the number of times (since 
SPX was loaded) the node's driver gave an 
incoming packet to SPX.  This value is a count and 
does not indicate an error condition.

Bad Incoming Packets - the number of times 
(since SPX was loaded) SPX received and 
discarded a packet because the connection ID in 
the packet was wrong.

Suppressed Packet Count - the number of times 
(since SPX was loaded) SPX discarded inbound 
packets because they were duplicates of 
previously received packets.  This condition 
indicates the sending station has not received an 
acknowledgment for a sent packet (due to delay 
or collision).  It may indirectly indicate high 
network utilization.  Observer will help determine if 
this is the case.

No Session Listen ECB Count - the number of times 
(since SPX was loaded) SPX was forced to discard 
an inbound SPXEstablishConnection packet 
because SPX lacked a corresponding 
SPXListenForConnection ECB.

WatchDog Destroy Sessions - the number of times 
(since SPX was loaded) WatchDog destroyed a 
connection because the connection was no 
longer valid.  A WatchDog packet is sent 
periodically if no packets are received from a 
peer in 5 minutes.  If there is no WatchDog reply, 
the station repeats the WatchDog request ten 
times in one minute intervals, after which the 
connection is considered invalid.
Shell Driver Statistics List (node)
The Shell Driver Statistics List includes the following 
entries specific to the node:

Driver Version, LAN driver version for the specified 
LAN board.

Statistics Version - the major and minor version 
number of the Driver Diagnostic Table.

Total Sent Packets - the number of packets the 
driver has successfully transmitted since the last 
driver reset or initialization.

Total Received Packets - the number of packets 
the driver has successfully received and passed to 
the system since the last reset or initialization.

No ECB Available Count - the number of packets 
the driver has received (since the last reset or 
initialization) for which there was no listening ECB. 
In an CPU overload condition there can be no 
ECB available, and packets may be lost.

Packet Too Big for Send - the number of times 
(since the last reset or initialization) applications 
have asked the driver to send a packet over the 
maximum legal size.  This can indicate improper 
functioning or configuration of an application.

Packet Too Small for Send - the number of times 
(since the last reset or initialization) applications 
have asked the driver to send a packet under the 
minimum legal size.  This can indicate improper 
functioning or configuration of an application.

Receive Packet Overflow - the number of times 
(since the last reset or initialization) the driver has 
received a packet larger than the buffer space 
allocated for the packet.  When a packet is 
received, the protocol stack that accepted it 
provides a set of buffers into which the packet 
should be dispersed.  If there is not enough buffer 
space or for any reason, or the protocol stack 
allocated a smaller buffer, this error occurs.

Received Packet Too Big - the number of times 
(since the last reset or initialization) the driver has 
received a packet over the maximum legal size.  
It may indicate an error in the packet header due 
to a collision, or a malfunctioning sending 
application.

Received Packet Too Small - the number of times 
(since the last reset or initialization) the driver has 
received a packet under the maximum legal size.  
This may indicate an error in the packet header 
due to a collision, or a malfunctioning sending 
application.

Transmit Misc. Errors - the number of 
miscellaneous errors preventing the driver from 
transmitting a packet.

Receive Misc. Errors - the number of 
miscellaneous errors preventing the driver from 
receiving a packet.

Send Retry Count - the number of times (since the 
last reset or initialization) the driver resent a 
packet.  For  example, when the driver detects a 
collision or does not receive a confirmation on a 
sent packet, the driver re-sends a packet.  If 
significant, this number can indicate high network 
bandwidth utilization.  Use Observer to check this 
assumption.

Checksum Error Count - the number of checksum 
errors occurring while receiving packets (since the 
last reset or initialization).  If this value is high, this 
can be an indication of bad cabling or a bad 
hub port.

Receive Hardware Mismatch - the number of 
times (since the last reset or initialization) the 
hardware has received more or fewer bytes than 
expected.
Shell Statistics List (node)
Shell Statistics List includes the following values:

Shell Requests - the number of times (since the 
shell was activated) the shell has made requests 
to a file server.

Operator Aborts - the number of times (since the 
shell was activated) the user has aborted the 
shell-server connection by entering "A" in reply to 
a "Network Error" message.

Operator Retries - the number of times (since the 
shell was activated) the user has instructed the 
shell to retry an operation.

Time-outs - the number of times (since the shell 
was activated) the shell sent a request to a server 
and then timed out without receiving a reply.  
(Normally, the shell sends another request 
packet).

Write Errors - the number of times (since the shell 
was activated) the driver has been unable to 
send a request to a file server (after repeated 
retries).  In this case, the shell displays the message 
"Error writing to network" on the workstation 
screen.  The shell does not increment this counter 
if, after repeated retries, the driver is able to send 
the request.

Invalid Reply Headers - the number of times (since 
the shell was activated) the shell has received a 
reply packet header whose Checksum was -1 or 
whose PacketType indicated the packet was not 
a file server reply.

Invalid Slot Count - the number of times (since the 
shell was activated) the shell has received a file 
server reply packet specifying an incorrect 
connection ID.

Invalid Sequence Number - the number of times 
(since the shell was activated) the shell received a 
file server reply packet specifying an incorrect 
sequence number.  It usually indicates the reply 
was unnecessary.

Errors Receiving - the number of times (since the 
shell was activated) IPX has indicated an error 
even though a packet was received on the 
socket.  It usually indicates an "Overrun" error.

No Router Found - the number of times (since the 
shell was activated) the shell tried and failed to 
find a route to a destination node.  The shell 
attempts to reroute a packet when a connection 
seems to fail and the user requests a "Retry.".

Being Processed - the number of times (since the 
shell was activated) the shell received a "being 
processed" reply from a file server.  A file server 
sends this reply to a shell when the server, while 
processing the shell's request, receives duplicate 
requests from the shell for the same service.

Unknown Errors - the number of times (since the 
shell was activated) the shell received a packet 
containing an undefined error value.

Invalid Server Slot - the number of times the shell 
attempted to communicate on a particular client 
connection number, and the server indicated the 
connection number is invalid.

Network Gone Count - the number of times (since 
the shell was activated) the shell received a 
packet from a file server indicating the target 
network has gone away.  Only a 68000 file server 
can generate this kind of packet.

Allocate Can Not Find Route - the number of times 
(since the shell was activated) the shell, asked by 
an application to establish a connection with a 
file server, could not find a route to the 
destination.

Allocate No Slots Available - the number of times 
(since the shell was activated) the shell, asked by 
an application to establish a connection with a 
file server, could not establish the connection 
because the file server's connection table was 
full.

Allocate Server Is Down - the number of times 
(since the shell was activated) the shell, asked by 
an application to establish a connection with a 
file server, could not establish the connection 
because the target file server was down.
Info
Info menus consist of version and other constant 
information that does not need updating over 
time on a node.  The Info menu consists of:
OS Version Information (node)
OS Version Information of a node includes:

Machine type - type of the computer on which 
the shell is running

Operating System - for example MS DOS 6.22

Shell Version - The IPX/SPX shell version number
IPX-SPX Versions (node)
The IPX/SPX versions list shows the IPX and SPX 
version numbers of the nodes IPX/SPX driver (not 
the shell version number).
Shell Driver Configuration (node)
Information regarding the board driver on the 
node (i.e. the ODI or IPX driver):

Max Data Size - the maximum size of a packet's 
data portion for the target driver.  The data 
portion's maximum size is always 64 bytes less than 
the packet size advertised with the LAN board.  
(The packet header and control information 
require 64 bytes.).

Transport times (ticks) - the value indicating the 
speed of the LAN associated with the target driver 
and board.  Speed is measured by the amount of 
time it takes a 576-byte packet to travel from one 
node on the LAN to another node.  Time is 
measured in units of 1/18 second and rounded to 
the next highest 1/18.

Shell Version - the major and minor versions of the 
driver release; they do not identify the installed 
Netware version.

Description - displays the LAN hardware currently 
connected to the IPX/SPX driver.

I/O Address - the I/O address block to be 
decoded by the LAN board the driver.

RAM Address - the memory address to be 
decoded by the LAN board (if it uses shared 
memory).

DMA Line - the value of the DMA line used by the 
LAN board (if it uses DMA).

Interrupt Lines - value of the interrupt used by the 
LAN board.

Selected Configuration - the value indicating 
which hardware configuration in the Hardware 
Configuration Table the driver is using.  This value 
ranges from 0 to n or -1,  where n is the maximum 
number of configurations supported by the driver, 
and -1 means no value (and is not displayed by 
Discoverer).

Note: Not all fields listed here may be available 
from different versions of Novell servers and 
drivers.
User Volume Information (node)
The User Volume Information list provides 
information about space restrictions for a specific 
user, numbers of used directories, files, and bytes.

Note:  Because server has to check all volumes 
and file systems to collect this information, 
obtaining this information can take considerable 
period of time (up to a few minutes).








REFERENCE
A SHORT OVERVIEW OF TCP/IP FOR TROUBLESHOOTING
TCP/IP is a family of protocols designed to perform 
a wide set of network activities.

This overview will give a short description of TCP/IP 
from prospective of packet transfer and 
monitoring.

While TCP/IP is the name by which we refer to this 
protocol, it is really a family of protocols based 
around the IP method of addressing.  TCP is one 
of the family of protocols included in IP.

The main components of TCP/IP are (there are 
numerous less used components):

IP - Internet Protocol,
ICMP - Internet Control Message Protocol,
TCP - Transmission Control Protocol,
UDP - User Datagram Protocol,
ARP - Address Resolution Protocol.

The descriptions here are based on a model that 
uses the term "lower" to describe the starting 
point of a packet, and higher to describe deeper 
and deeper information within a packet.  The 
vegetable analogy would be an onion - it has a 
skin (the lowest level) and many possible layers 
within (each one a higher layer to the last).

TCP/IP datagrams are transferred on top of 
(inside) a network specific frame - or packet (the 
most common are Ethernet and Token Ring), and 
are used in turn to transfer a higher level 
specialized protocols that actually define what 
kind of activity is performed on the network.  
Some of these are: Telnet, FTP, NFS, SMNP, remote 
printing, and many others.  In other words, TCP/IP 
packets are really packets within packets, that is a 
TCP/IP packet is wholly contained in a Ethernet 
frame (i.e. packet or wrapper).

In order to transfer information (for example, a 
file) through the network, it must be divided in 
shorter data units which contain information 
about the source from which data originates, 
destination, length, position of the particular data 
unit in a data stream (of many units), different 
kinds of management information, routing in the 
case the datagrams have to cross one ore more 
bridges, and checksums to insure that data was 
delivered without loss or alteration due to network 
conditions like packet collisions or noise.  These 
units are called datagrams or frames.  They can 
be considered as a sequence of bytes ordered 
according to certain rules.

To make the process of managing packets 
controllable, protocol and datagrams produced 
by TCP/IP are built in a layered fashion.  On the 
lowest level (and arranged in stream of data at 
the first position) is a network specific frame 
header.  It can be different for different types of 
networks, but in general it contains a destination 
and source hardware address, and size of the 
packet and  frame type.  This layer, for example, 
may define the packet as either Token Ring or 
Ethernet.

A network card adds a network specific preamble 
and checksum to a packet and converts the 
frame into a stream of radio frequency signals 
that are transmitted through the network wire.  On 
the other end the receiving network card 
converts the radio signal back into a stream of 
characters, determines if it is to the addressee, 
and if so, transfers it to an application that 
processes it further.

According to the layered structure, everything 
that is placed after the frame header can be 
considered as a data portion of the frame.  In the 
same fashion each higher level portion can be 
considered as a data portion of the underlying 
one, making assembling before sending and then 
disassembling and extracting transferred data or 
a command portion of transmission as easy and 
as logical as possible.

In TCP/IP, the frame header that follows the IP 
header, is either TCP, UDP, ICMP, or another 
higher protocol header, followed by the data 
portion of the packet, or a still higher level 
protocol header - RPC (NFS) on top of UDP 
header, for example.

So, for example, when you look at a packet, you 
might first see the MAC portion of the packet, 
followed by the IP portion, followed by either the 
TCP, UDP, etc. portion (depending on why the 
packet was formed) and then the data portion.

Knowledge of basic structure of TCP/IP protocols 
will help to determine the possible causes of 
problems on your network and help choose the 
appropriate actions to correct them.

IMPORTANT POINT! -> Another approach to 
figuring out a problem that occurs on one of the 
stations is to try to find a good example of how 
the network communication should function.  For 
example, it may be helpful to capture a TCP 
connection or a file transfer that seems to work 
properly, and then compare it to one received 
from a malfunctioning station or host.

A detailed description of TCP/IP protocols is a 
subject for many volumes, and there are many  
books available.  Although it could be edifying for 
somebody to learn everything available on the 
subject, many problems can be detected and 
solved with basic understanding of the main 
TCP/IP protocols.  The next section gives a short 
overview of the most important packet structures 
as they are viewed by Observer and a concise 
explanation of each of the labels (in View 
Packets) and their function.
MONITORING TCP/IP SESSIONS WITH OBSERVER
The descriptions here decode each type of 
packet, starting at the beginning of the packet 
structure and moving down, layer by layer.
Ethernet Frame Header
An Ethernet frame contains a preamble and a 
frame checksum, which are added and removed 
by the Ethernet network card, and are not passed 
to the higher levels.  TCP/IP on an Ethernet 
Network uses an Ethernet II type of frame.  This 
consists of a destination and source hardware 
address and frame type field.  The hardware 
address field is six bytes long and uniquely 
identifies a network card on the network.

In Observer’s View Packets window the Ethernet 
Frame header is shown in two places.  First in the 
List of Packets (in the top portion of the screen), 
where all packet are displayed in order of arrival 
from the network.  Hardware addresses use the 
following notation (example): 80:00:00:21:D5:98,  
where every number separated by a colon is a 
byte (number from 0 to 255) represented in a 
hexadecimal form.

The next field in the List of Packets is the frame 
type. For example, ARP (0806),  IP (0800), or 
Netware Ethernet II (8137).

There is a bit of inconsistency in the type field.  If 
the frame type is smaller than 1518, this field 
actually means the length of the packet - the 
frame type for all the packets below 1518 is called 
IEEE 802.3 (real 802.3 as opposed to Novell 802.3).

Using Observer’s List of Packets options.
In addition to displaying hardware addresses and 
frame types, the List of Packets can show 
difference in time of arrival (and thus time sent) 
for the current packet and the previous packet.  
This is called the packet delta.  To enable this 
option select differential times option in "Settings" 
-> "View Configuration", and this entry will appear 
in the List of Packets.

All hardware addresses can be aliased to the 
names of users or any desirable text from the list of 
hardware addresses in Filters dialog.
Token Ring Frame Header
The Token Ring frame header is very close to an 
Ethernet header.  It consists of start and end 
delimiters (performing a similar functions as a 
preamble in Ethernet header).  There are two 
additional bit fields: Access Control field (AC) and 
Frame Control field (FC), followed by hardware 
destination and source address, which may be 
followed by a routing information field.  Because 
there is no frame type field, a Token Ring frame 
header is always followed by IEEE 802.2_SNAP, or 
IEEE 802.2 subheader specifying the higher level 
protocol used.  TCP/IP packets are formed on top 
of the 802.2_SNAP header.

An Access Control field has the following bit fields:

Priority Bits - states the priority of a frame or a 
token.  The value can be from 0 to 7.

Token Indicator - if this field is not set the packet is 
a token, not a frame.  These packets are not 
displayed by Observer.

Monitor Count Bit - this allows the Active Monitor 
to determine if the packet was not removed from 
the ring by the responsible station, and does so if 
necessary.

Priority Reservation Bit - this sets the priority of the 
packet.  Higher priority packets will be processed 
before lower priority packets.  Values are from 0-7.

The Frame Control field determines whether the 
frame is a MAC or data frame.  It consists of the 
following fields:

Frame Type - this determines whether the frame is 
MAC or data,

Control Field - which is valid only for MAC frames, 
This specifies the MAC control message or mode 
of processing the following data fields. 

Hardware destination and source addresses are 
similar to Ethernet headers, except that the 
highest bit in the first byte of the source address 
serves as a routing information indication.  When 
this bit is set, the routing information field 
immediately follows the source address.  The 
routing field has a few subfields which specify if 
the frame is a broadcast, and if it is, what type of 
broadcast, maximum size of the frame, direction 
of the routing path (either originator or 
respondent), and the path itself.
IEEE 802.2 and IEEE 802.2_SNAP subheaders
These subheaders can be used as extension of an 
Ethernet frame header (IEEE 802.2_SNAP) header, 
and is always used as an extension for the Token 
Ring frame header to specify the overlying 
protocol.

The first two fields in both subheaders are 
Destination Service Access Point (DSAP) and 
Source Service Access Point (SSAP), which denote 
the destination and the packet’s (which is the 
source) upper layer protocol.

For example:
If DSAP and SSAP are 0xE0, the subheader is IEEE 
802.2 (Novell’s Ethernet 802.2), and the protocol is 
IPX.

If DSAP and SSAP equal 0xAA, the subheader is 
IEEE 802.2_SNAP.

Both subheaders have a control field (Netware 
protocols do not rely on this field).  This field closes 
the IEEE 802.2 subheader.  The first field in IEEE 
802.2 specifies the protocol; and because the 
same field in IEEE 802.2_SNAP specifies that this 
subheader is IEEE 802.2_SNAP, there is one more  
field of this subheader which specifies the 
protocol.  Protocol numbers in 802.2_SNAP 
protocol field are the same as used in an Ethernet 
II frame header.
Internet Addresses
When systems to communicate with each other 
on Ethernet and Token Ring networks they use 48 
bit (6 byte) hardware addresses.  Hardware 
addresses are usually assigned by manufacturer 
of a network card.  Different manufacturers have 
their assigned major card numbers, and create 
unique minor card numbers for every card.  On 
most networks there are network cards of different 
makes, which creates quite wide range of 
hardware addresses.

To make internetworking routability easier and be 
able to assign some systemized set of addresses 
for the station on a local net and an Internet as a 
whole, Internet addresses use 32 bit (4 byte) 
numbers instead of 6 byte hardware addresses.

The Internet addresses are uniquely assigned by 
an Internet authority for every network (This can 
be you if you are not connected to the Internet, 
or THE Internet authority if you are).

IP addresses are usually represented by four 
numbers in range from 0 to 255 each separated 
from the next by a ".".  

For example:  200.200.200.18

Internet addresses cane be either class A, B, C or 
D - each determines how many machines can be 
on the local network.  A class A addresses can use 
3 lower bytes as a local address (9.27.6 for an 
address of 9.27.6.100, for example), B - two bytes, 
C - one byte, and D are multicast addresses.  This 
allows, for example, a class A addresses to have 
up to 65,536 machines on the network, and for 
class C only 256.  To make even finer subdivisions 
subnet address masks can be used to assign only 
a part of an address to a network address space.
Address Resolution Protocol (ARP)
Because the IP layer uses a four byte Internet 
Addresses, and frame headers contain actual 
hardware addresses of the network cards 
receiving and sending the datagrams, it is 
necessary to find out what hardware address 
corresponds to an IP address (and store this 
information in the ARP table for later use).  
Address Resolution Protocol (ARP) serves this 
purpose.

If a station needs to establish a TCP connection to 
a server or peer, there are two possible scenarios:

1. If a connection was already established to the 
destination station, the hardware -to- IP 
address mapping may already be in the local 
ARP table.  In this case the station will directly 
proceed with establishing connection using a 
hardware address from the table.

2. Otherwise an ARP broadcast packet is sent to 
the IP address that the connection needs to 
be established with, and the station waits for a 
reply from the station in question.  This ARP 
packet contains the hard network address and 
IP address of the sending station.  The 
requested station, if it is present on the 
network, sends an ARP reply with it’s hardware 
address as one of the reply fields.  The 
requesting station places the IP -to- hardware 
correspondence in the local ARP table, and is 
ready to establish connection.

An ARP message contains the following fields:

Type of Operation - this either indicates an ARP 
request or ARP reply.

Source Host address - the IP address of the 
requesting host (or replying, if the ARP message is 
a reply).

Destination Host address - the IP address of the 
requested host (or the host that send the request, 
if this is a reply).

Source Hardware address and Destination 
Hardware address - the hardware addresses of 
sending and receiving station.  If it is an ARP 
request, the destination hardware address is set to 
zeroes; an ARP reply always contains both 
addresses.
Internet Protocol (IP)
The Internet Protocol Datagram is the second 
level of encapsulation after the frame level.

Encapsulation allows IP to be completely ignorant 
concerning the type of network packets that are 
sent through.  IP headers look the same for all 
networks and frame header+subheader 
combinations.  While Internet Protocol can be 
considered as a data portion of the frame, it in 
turn has as its own data portion - TCP, UDP, ICMP 
or another higher level protocol(s).

A station can only begin to send IP packets if it 
has resolved the IP to hardware address mapping 
(see ARP section).

If the destination station is not on the local 
network, and the Datagram is transferred through 
a bridge or gateway, the layered structure allows 
the bridge to remove the frame header of the 
incoming frame, replace it with its own and send it 
in the next network destination, (which can be a 
different type of network) until it reaches the 
destination host.

The main function of IP is packet delivery (and 
routing packets through Internet bridges and 
routers).  IP itself does not contain any provision to 
make delivery of the packet reliable.  It delivers 
packets by "best effort attempt" through the 
network to their destination, but IP has no way of 
knowing if the packet was lost, underwent a 
collision, could not be received by the destination 
machine due to network congestion or 
destination machine overload.  Responsibility for 
taking care of  these kinds of problems is done by 
a higher level protocol (TCP, or by an 
application).

An overview of the IP header structure will show 
the means by which IP tries to meet its goal.  The 
IP header has the following fields:

Source host - the Internet address of the sending 
station.

Destination host - the Internet address of the 
destination station.

Version - the version of IP protocol that was used 
to create the Datagram.  It is used to see if the IP 
header format is the same on sending and 
receiving stations.  The current IP protocol version 
is 4.

IP header length - this specifies the length of the IP 
header.  Most of the fields in the IP header are 
fixed, except IP options, which can be absent, or 
be of variable length.  If IP options are not 
present, IP header length is 20 bytes (or 5 four 
byte words).

Service type - this field is split into four bit fields:

Precedence - ranging from 0 (normal 
precedence) to 7 (network control).  
Currently most hosts and gateways ignore 
precedence.

The next three fields are the mode of transport the 
Datagram requested:

Delay - normal or low, 
Throughput - normal or high, 
Reliability - normal or high.

Total IP length - the length of IP Datagram in 
bytes, including the IP header.

ID - the identification field is a unique integer that 
identifies the Datagram.  It is used to reassemble 
fragmented packets.

Fragments - this can be "Yes" or "No".  There are 
a few bit fields that give more detailed 
information about the Datagram fragmentation, 
but for practical purposes it is only important to 
know if the packet is fragmented or not.  More 
detailed information about fragmentation is rarely 
needed, and can be obtained from viewing the 
IP header in raw mode.

Time to live - this specifies how many hops the IP 
Datagram is allowed to perform on the Internet 
system.

Protocol - this specifies what higher level protocol 
is encapsulated as a IP data.

Header checksum - the checksum that ensures 
that the IP header is not corrupted during 
transmission.

The IP header contains many fields.  If you are  
interested only a few of them, use Observer’s 
post-filtering in the "Settings" -> "View 
Configuration" dialog.  This lets you select which 
fields will be displayed.  For example, you may be 
interested only in source and destination address 
and protocol type.  
Transport Control Protocol (TCP)
The same way as IP can be considered a data 
portion of network frame, the TCP portion of the 
Datagram can be looked at as IP data.  TCP adds 
one more level of complexity and functionality to 
the TCP/IP protocol set.

TCP is a data stream and connection oriented 
protocol.  In order to communicate two machines 
must first establish a connection.  A unique port 
number is assigned to each connection on both  
machines.  There can be more than one 
connection established between two machines -  
using different port numbers gives the means to 
distinguish between them.

While IP provides "best effort" in delivering a 
packet, it can not guarantee the packet delivery 
or reception.  TCP protocol provides mechanisms 
to make the overall delivery service reliable.  This is 
achieved by means of positive acknowledgment 
(ACK) and retransmition.  In TCP, the recipient of 
data must send back to the sending station 
acknowledgment about received data.  If the 
period in which the sender expects to receive an 
acknowledgment expires,  the sender will re-send 
the packet.  Sometimes for efficiencies sake, a 
station may "piggyback" an ACK along with the 
next bit of data - this is well within the TCP/IP 
specification.

When analyzing a TCP data exchange it is 
important to understand  the concept of a sliding 
receiving data window.  Let go briefly go through 
this.  If a sender was waiting for the 
acknowledgment on every packet sent, the data 
exchange rate would be quite slow.  Using a 
sliding window mechanism, the two machines 
can exchange information about how much data 
each machine can send and receive.  This is 
called the window size.  When sending a data 
stream, the sender sends packets without waiting 
for acknowledgment until it sends enough data to 
fill the known receiving station window size.  The 
other side sends back acknowledgments as it 
receives data, and the sending machine 
continuously updates the amount of data it still 
can send.  Ideally, if no packets are lost, this 
mechanism allows transmission of large amounts 
of data completely without idle periods while 
waiting for acknowledgment.  This also handles 
the common situation with a multi-tasking 
operating system where the receiving machine 
may be to busy doing something else to 
immediately send an acknowledgment.

From network traffic analysis point of view this  
means that one can not expect that every 
packet is going to be immediately 
acknowledged.  In addition, checking the stream 
of data sequence and acknowledgment number 
patterns can help in discovering a malfunctioning 
TCP interaction.  These problems are much more 
common than most people expect.  Different TCP 
implementations react differently in certain "soft 
error" conditions.  Just because Hewlett-Packard 
or IBM wrote the host TCP software, this does not 
make that TCP infallible.  It is the job of all TCP/IP’s 
(and specifically host based TCP/IPs where size, 
speed and memory limitations are few) to handle 
and try and overcome error conditions.

Observer can help to find the causes of problems 
that manifest themselves as slow transport rate or 
‘stopping and going’ during terminal sessions.  This 
knowledge can be used to tune either the host or 
station TCP software, or to request from the 
software provider more specific information about 
the solution to the displayed problem.

The TCP packet header includes the following 
fields:

The TCP label itself, which can contain, if it is 
present in the TCP header, a Code field which 
indicates the purpose of the packet.  For 
example, it shows whether  the packet is an 
acknowledgment to a received data stream.

Source port and Destination port  identify the port 
assigned to an application on both sides of the 
connection.  If the port number is one of well 
known origin, Observer displays the name of 
service the port provides (i.e. telnet for port 23).

Sequence number - this identifies the position 
where the current packet should be attached in 
the senders stream of data.  If the packet 
contains data, the next sequence number will be 
increased by the size of the transferred data 
(provided the data was acknowledged, or the 
next packet fits into the window size). 

Acknowledgment number - this indicates until 
which position the data in the receivers current 
packet stream has been received.  Or, in other 
words, starting from which position in the stream it 
expects data to be accepted.

TCP header length - this specifies the length of the 
TCP header.  Most of the fields in the TCP header 
are fixed, except TCP options, which can be 
absent, or be of variable length.  If the TCP option 
field is not present, the TCP header length is 20 
bytes (or 5 four byte words).

Window - or window size - the amount of data in 
bytes that the sender of the packet has 
advertised that it is able to receive.  Usually it is 
equal the size of the buffer assigned by the TCP 
implementation to the current connection.

TCP data length - the length of data that follows 
TCP header.  In most cases it is raw TCP data, for 
example, the case of a file transfer or terminal 
emulation.  It can also be a still higher level 
header with its own data, according to the 
general encapsulation model.

Checksum - the TCP checksum is calculated in a 
similar way as the IP header checksum.  In the 
case of TCP segments it includes in the 
calculation both the header and the data.  
Applications use the TCP checksum to ensure that 
the TCP segment (and thus the packet) arrived 
intact.

Sequence number + data length - this is not 
exactly a part of the TCP header.  It is provided by 
Observer to enable a user to conveniently 
compare sequence and acknowledgment 
numbers in the stream of data without constantly 
adding what can be quite long sequence and 
data length numbers.  Using this value one can 
immediately know what sequence number to 
expect in the next packet if the packet was 
accepted (ACKed) successfully.

TCP options - there are three TCP options. They 
are:

End of Option List, No Operation, and 
Maximum Segment Size (MSS).  The only 
one of importance is the Maximum 
Segment Size option.  The sender of the 
packet with this option informs the other 
side about the maximum size of the TCP/IP 
data buffer of the receiving system.  
Usually, the Maximum Segment Size TCP 
option appears only once during the initial 
negotiation between systems - although 
there is no restriction for this to be used 
more than once.
User Datagram Protocol (UDP)
UDP like TCP is also a higher encapsulation level 
protocol of IP protocol.

UDP uses IP to transport messages from one 
machine to another.  Unlike TCP, UDP does not 
provide a reliable mechanism for data transfer.  It 
does not require acknowledgment of received 
data and does not provide means to control data 
position in transmitted datagrams.  Datagrams 
can be lost, or arrive out of order.  However the 
same way as TCP, UDP also provides multiple port 
destinations that can support multiple 
connections from one station to another system.

Applications using UDP as a transport must 
accept a full responsibility for making UDP a 
reliable communication process.  This includes 
managing potential loss of packets, delays, 
receiving duplicates of packets, etc.

Although it may sound as if UDP is an inferior 
protocol to TCP, it has its own advantages (speed, 
block transfers, etc.), and there are many 
protocols and applications using UDP.  A couple 
of good examples are NFS and SNMP.

UDP headers include the following fields:

Source port and Destination port identify the port 
assigned to an application on both sides of the 
connection.  If a port is one of the well known 
ports, Observer displays the name of service this 
port provides.

UDP length - the length of the UDP Datagram, 
including the length of the header.

Checksum - this is checksum calculated on the 
whole UDP Datagram (including UDP header).  
This value is optional, and a zero is placed in the 
UDP header checksum if it was not calculated.  
However, using UDP checksum is the only way to 
ensure that a Datagram arrived intact, and it is 
usually calculated.
Internet Control Message Protocol (ICMP)
On an IP network, each bridge or gateway 
operates autonomously.  Sometimes datagrams 
can not be delivered to their destination - either 
because the destination machine is down or out 
of order, or the network the system is on cannot 
be reached (permanently or temporarily), or 
because a bridge or router is down or 
disconnected, or because of delays in the 
gateways and the datagram’s time to live expires, 
or a bridge network is overloaded and can not 
deliver incoming datagrams.  In any of these 
cases some mechanism is necessary for delivery 
of the error messages.  This mechanism is called 
Internet Control Message Protocol.  ICMP is 
designed to report error conditions to the original 
source of data transmission - the host or station 
that sent the failed Datagram.

ICMP messages are transferred through the 
network as data portion of IP Datagram.  This 
means that ICMP messages themselves can be 
potentially lost.  In this case to avoid generation of 
error messages about error messages, new error 
messages about ICMP errors are not generated.

ICMP contain the following messages:

Echo reply - returns exact copy of data sent by 
Echo request.  This message has Identifier and 
Sequence number fields used to match  replies 
with requests.  It can be used to test destination 
reachability and status (this is what PING uses).

Destination unreachable - this reports about an  
unreachable destination with a description of 
possible reasons for problem.

Source quench - this is sent when a Datagram 
can not be accepted by a gateway or 
destination station because of a network 
congestion or station overload.

Redirect - if gateway detects that host is not using 
an optimal route to route a Datagram through 
the network, a Redirect ICMP message is sent to 
the host.  The original Datagram is still delivered to 
the destination.

Time exceeded - sometimes a routing path has 
too many hops, or an error in the routing table 
produces a circular routing cycle.  In this case 
when time to live (hop count) reaches zero, the 
Datagram is discarded by the gateway on which 
it happened.  This gateway sends ICMP Time 
exceeded message to the source host notifying it 
about this condition.

This message is also sent when time-out for 
reassembling of a fragmented Datagram was 
reached.

Parameter problem - this ICMP message is sent to 
the source host when an error occurs in a 
Datagram, for example a gateway receives a 
Datagram with incorrect Datagram header.  A 
pointer field indicates which parameter in the 
original Datagram is considered to be incorrect.

Timestamp request and Timestamp reply are used 
to synchronize clocks between machines.

Address mask request  - this is used by a machine 
that needs to receive a subnet mask for current 
net.  If the machine knows the address of a 
requested host, it can send it directly to the host, 
otherwise the message can be broadcasted.  
Address mask reply serves to return a subnet 
mask to the requesting machine.
SHORT OVERVIEW OF NOVELL’S IPX AND SPX PROTOCOLS
Netware uses two network communication 
protocols: IPX and SPX.  SPX has two flavors: SPX 
and SPX II which is an extended version of SPX.

In the general scheme of things IPX and SPX can 
be considered as a data portion of the network  
packet frame, the same way as TCP/IP protocols 
are in relation to a packet frame.  The discussion 
of Ethernet and Token Ring packet frames are 
also applicable.  (For more information see 
sections about the packet frame headers in the 
TCP/IP protocols overview).

IPX and SPX provide different types of services for 
the applications using them.  IPX employs 
connectionless services, like TCP/IP’s UDP, while 
SPX uses a connection oriented model somewhat 
like the TCP protocol.

This means that IPX does not provide reliable data 
delivery.  Data can be lost, or be received out of 
order, and the application or protocol employing 
IPX must handle these conditions.  Being a 
connectionless protocol, IPX supports broadcast 
of packets.

On the other hand SPX and SPX II are connection 
oriented protocols.  They do not support 
broadcasts, and for two stations to send and 
receive data they must establish connection first.  
When a connection is established, all received 
data packets are acknowledged by the receiving 
station.  The next sections will give short overview 
of IPX and SPX protocols, packet headers and 
some higher level protocols used by IPX from the 
prospective of network monitoring and analysis.
Internetwork Packet Exchange (IPX) packet header
Let consider the structure of an IPX packet.  This 
will help show the ways IPX meets its goals.  

IPX packet header has 10 fields:

Checksum - this field is the first field of the IPX 
packet and is not usually used by Novell Netware.  
This field is always set to 0xFFFF in Netware before 
4.0, but starting from Netware 4.01 it can be 
optionally used.

Packet length - this is the length if IPX packet 
including IPX header and data.

Transport control - this field shows the number of 
routers a packet passed.  This number is set to 0 
by the source station, and then is increased by 
one by every bridge passed.  When the count 
reaches 16, the packet is discarded, which limits 
reachability of IPX packets to 15 routers.

Protocol type - this defines the protocol a packet 
will use.  IPX uses 0 or 4, SPX - 5, NCP - 17.

Destination Address comprises two IPX header 
fields: destination network address which is the 
four byte address of the network to which the 
node belongs, and destination node address 
which is a six byte hardware address of the 
network card in the node.  If the destination node 
is a NetWare server, hardware address is replaced 
by address 00-00-00-00-00-01;  the network frame 
address will still contain the network card 
hardware address.  The destination address can 
be a broadcast address (the largest of all possible 
addresses, namely FF-FF_FF-FF-FF-FF).

Destination Socket - this defines the destination 
process the packet is addressed to.  Some of the 
main processes will be discussed later, and 
include:

	NetWare Core Protocol (NCP),
	Service Advertising Protocol (SAP),
	Routing Information Protocol (RIP),
	NetBIOS,
	Diagnostics,
	Serialization.

Stations use a range of socket numbers from 4000 
to 8000 hexadecimal to specify the remote or 
local process entry point numbers of the process.

Source Address - this also comprises two IPX 
header fields: source network address, and 
source node address, which are similar to 
destination addresses, and define the sending 
nodes coordinates.

Source Socket - this field is similar to destination 
socket number.
Sequential Packet Exchange (SPX) packet header
The SPX header’s first ten fields are exactly the 
same as an IPX packet header’s first 10 fields.

For comparison purposes, if it was defined this 
way, the SPX part of the header could be 
considered as a higher level protocol to IPX, just 
as UDP is for IP.  However, the SPX header not only 
has the same 10 fields as IPX, but it also has its 
own additional fields.  Let’s look at the following 
seven fields additional to SPX, plus one more 
additional field of SPX II:

Connection flag - this is a one byte bit field that 
can have the following values:

System - designates a system packet (used 
internally by the server).

ACK - indicates that data was sent and 
acknowledgment is required.

End of Message - indicates that the sending 
side wants to close connection.

Datastream type - this is used for the end of 
connection request and acknowledgment.

Source connection ID - this specifies the 
connection number for the source SPX.  It is used 
to determine the difference for potential multiple 
connections from the same node and to the 
same source socket.

Destination connection ID - this is similar to Source 
connections ID except that during the initial 
establishment of the connection the Destination 
connection ID can be set to -1 (FFFF 
hexadecimal), since the destination is unknown at 
this time.

Sequence number - this is the number of packets 
transmitted from the node.  It is incremented by 
one after reception of acknowledgment from the 
destination node for the packet sent.

Acknowledgment number - this is the value of the 
sequence number expected to be received.  If  
packet is lost, and sequence number does not 
reach the acknowledgment number after the 
time-out period, a sending node assumes that the 
packet was lost.

Allocation number - this is the number of available 
receive buffers on the station.  The actual number 
of buffers is equal to the allocation number plus 
one.

A value of 0, for example, means that one buffer 
is available.  If the station receives packets and 
can not keep with the packet processing, the 
allocation number decreases, as packets are 
processed, the allocation number is increased 
with each released buffer.

SPX II is an enhancement of SPX supporting 
packet sizes up to 1518 bytes (SPX can send and 
receive maximum 576 bytes packets).  
Additionally, while SPX requires acknowledgment 
for every packet,  SPX II employs a window size 
mechanism close to that of a TCP sliding window.

To accommodate these additions, SPX II packets 
contain one more field, and in addition, new 
definitions for connection control and Datastream 
fields.  It also uses an enhanced packet 
sequencing mechanism.

The additional values in the Connection flags field 
are:

Size - this allows SPX II to negotiate the size 
of the send and received packets.

SPX II packet type - this field indicates that 
the packets are in fact SPX II.

Datastream type also contains two additional 
values:

Orderly release request, and

Orderly release acknowledgment.

The additional SPX II field is called Extended 
Acknowledgment.   This is for the situation where 
one station uses SPX and the other an SPX II 
connection.  In this case, the SPX II station 
automatically switches to SPX during initial 
connection establishment.
NetWare Core Protocol (NCP).
While IPX and SPX are the means of transfer of the 
packets, NCP is the main communication 
protocol used by Novell NetWare - as is implied by 
the word "Core".  NCP if a higher level 
encapsulation protocol to IPX and SPX.  NCP 
controls the establishment of connections, opens, 
transfer and closes files, establishment of service 
queues, and performs many other tasks.  Overall 
there are over three hundred NCP functions.

The NCP protocol is comprised of a series of 
requests and replies.  A station sends a NCP 
request with a number of a function specified in 
the NCP header, and waits for a reply - usually 
confirmation of the execution.

NCP headers are slightly different for request and 
for replies.

REQUEST HEADER contains the following fields:

Request type - this field is displayed by Observer 
next to the NCP label itself.  It specifies the type of 
NCP message, and can be one of the following:

	1111	Create service connection.
	2222	Service request.
	5555	Destroy service connection.
	7777	Burst mode transfer.

When a station connects to a server it sends a 
Create service connection request, and when 
disconnecting it sends Destroy service 
connection.  The service request is an example of 
the most common field encountered in NCP.

The fields following the NCP header specify 
precisely what kind of request the NCP packet 
carries.  These are:

Sequence - this field is a one byte field that keeps 
track of the sequence of commands between the 
station and server.  It is increased by one with 
every packet until it get to 255 and then wraps 
around to 0 at which time it begins again.

Connection - this is a service connection number 
that the server assigns to the station during the 
initial connection.

Task - this is the number of the task that is making 
a request.  It also allows the server to de-allocate 
specific resources when a task terminates.

Connection high - this is an additional connection 
number that can appear only on a 1000 user 
versions of Netware to keep track of the higher 
number connections.

These fields can be followed in the NCP request 
by the following fields:

Function code - a major number of function being 
requested.

Length - this is the length of NCP data, if present.

Sub-function code - the sub-function number of 
the major function.

For example, the function (58h) has the sub-
function codes:

Get Volume Audit Statistics (01), or
Add Audit Property (02), etc.

REPLY HEADER contains the following fields:

Reply type - this field is displayed by Observer next 
to the NCP label.  It specifies the type of NCP 
reply message, and can be one of the following:

	3333	Service reply.
	7777	Burst mode connection.
	9999	Request being processed.

Service reply - this  is the most common reply and 
used as an answer to most requests.

During the transferring of files in burst mode, the 
server uses a Burst mode connection reply.

Request being processed appears when a server 
accepts a packet and queues it for execution, 
but is not able to process it immediately.  If the 
station time-out expires and it repeats the request, 
the server may reply again with Request being 
processed.

Sequence, Connection, Task, and Connection 
high  fields are similar to NCP request fields and 
are followed by:

Completion code - which indicates whether the 
client request was successful.

Connection status - this indicates if the server is 
going down.  This field is usually set to 0, and when 
the server is going down , this value in NCP replies 
is set to 1.

The BURST MODE HEADER is different from the NCP 
request and reply header and contains the 
following fields:

Request type field, which is displayed by Observer 
next to NCP label, has the value of 7777 
hexadecimal.

Flags - this is a bit field that specifies the mode or 
condition of the connection.

Stream type - this currently has the only value of 2, 
which means burst.

Source ID - this is a unique (random) number 
created to identify a current burst connection by 
a sender.

Destination ID - this is a unique number similar to 
Source ID, but created by the receiver.

Packet sequence - this number is similar to a NCP 
non-burst sequence number and is used to track 
transmitted packets.

Send delay time - this specifies the delay time 
between packets in burst in units of 100 
microseconds.

Burst sequence number - this is the sequence 
number of the burst.  Each burst is considered as 
one unit by this count.

Acknowledgment sequence number - this is the 
sequence number the node expects to receive 
next.  This indicates whether the last burst 
transmission was received successfully.

Total burst length - this specifies the length of the 
whole burst transaction.

Burst offset  - this is the number of the packet in a 
burst.

Burst length - this is the length of a current burst.

Fragment list - this defines the number of elements 
that are missing from the transaction.

Function - this specifies if the current burst is a read 
or write.
Service Advertising Protocol (SAP).
Service Advertising Protocol (SAP) provides service 
information on all known servers throughout the  
internetwork.

SAPs are transmitted in two situations.

1. There are periodic SAPs broadcasted by a 
server on a LAN.  This periodic broadcast 
occurs at 1 minute intervals.  If a server does 
not broadcast SAP information in more than 
three minutes, all  routers and servers assume 
that the server is not available, and remove it 
from their binderies.

2. SAP packets are sent by the server (in this case 
a SAP reply) when a station loads a redirector 
(NETX or VLM).  NETX (or VLM) sends a SAP 
request to locate the nearest server.  This 
request is called the "Get Nearest Server" 
request. 

SAP messages are transferred in IPX packets with 
the Socket number set to 452h (SAP).

SAP REQUEST’s contains the following fields:

Packet type - this currently has only one value: 
nearest service request.

Server Type - this specifies the type of server 
requested.

The most common are:
	File server - (04)
	Job server - (05)
	Print server - (07)
	Job queue - (0A)
	etc. 


SAP RESPONSE contain the following fields:

Packet type and Server Type similar to those fields 
in SAP request, followed by the list of servers that 
are specified in the following fields:

Server name - the name of the server.

Network address - the 4 byte network address.

Node address - a 6 byte server node address 
(contains 00-00-00-00-00-01 for all servers).

Socket - this is the socket number that receives 
the service requests.

The fields above will be repeated as many times 
as are the number of servers that are in the list.
Routing Information Protocol (RIP).
Routing Information Protocol passes the routing 
information between servers and routers.  RIP is 
sent for the following reasons:

1. When router initializes, to inform other routers 
that it is available.

2. When router first loads it requires initial routing 
information from other routers, and thus 
requests this information via RIP.

3. For periodical update of the routing tables the 
RIPs are broadcast at one minute intervals.

4. When router changes any routing information 
in it’s tables it sends a RIP broadcast to notify 
other routers about the change.

5. When a router is going down, it notifies any 
other routers.

RIP messages are transferred by IPX packets with 
value of 453h in Socket field.

Routing information packet have the following 
format:

Packet Type - a request or reply, followed by three 
fields which are repeated as many times as there 
are routes:

Network address - this is the address of the 
network.  In a RIP request, this field can be set to 
broadcast and receive information for all 
available networks.

Hops - this specifies distance to a network in 
number of bridges that has to be crossed.

Ticks - this specifies amount of time necessary to 
reach the network. One tick is equal 1/18 of a 
second.
Serialization packets.
Serialization packets are sent periodically to 
ensure that a server with the same serial number is 
not installed twice on the same network.  Every 
NetWare server is sold with the unique serial 
number.  Loading more than one server with the 
same distribution copy is not allowed, and 
serialization packets check and notify everyone if 
a license is being broken.

Serialization packets are transferred as broadcasts 
in IPX packets with the Socket number of 457h.
WatchDog Packets
The WatchDog protocol is used to determine if a 
station that does not transmit packets for a long 
period of time is still up.  If the station is inactive for 
5 minutes (a default, which can be changed), a 
server sends a WatchDog packet to the station.  If 
the station is alive, it sends a WatchDog reply.

If the server does not receive a Watchdog reply, it 
continues to send Watchdog packets every 
minute for ten minutes (both values are defaults 
and can be set differently).  If the server does not 
receive the Watchdog reply after this period, the 
server considers the connection closed and clears 
connection from the connection table.









APPENDIX
PROGRAM DESCRIPTIONS
Observer is a Microsoft Windows based program 
that captures and analyzes packets as they are 
broadcast onto your LAN.  Observer has both DOS 
and Windows components.  Discoverer is also a 
Microsoft Windows based program, but it does 
not require any DOS based programs for function 
(from Network Instruments - it does require ODI 
and the VLM shells to be loaded at the 
workstation).

Observer’s main components are:

OBSERVER.EXE is the main program for viewing 
and capturing LAN information.

OBSERV.DLL is the Windows Dynamic Link Library 
for  OBSERVER.EXE.

VPACK.EXE is the Packet Driver interface that 
makes network packets available to the Windows 
programs.  VPACK.EXE will only work with NDIS or a 
Packet Driver.  For more information on the 
Packet Drivers, see the Installation section or this 
Appendix.

VPACKODI.EXE is the ODI interface that makes 
network packets available to the Windows 
programs.  VPACKODI.EXE will only work with 
Novell’s ODI.  For more information on the ODI, 
see the Installation section or this Appendix.

OBSERVER.HLP is the Windows help file for 
OBSERVER.EXE.

OBSERVER.INI (stored in the Windows directory) is 
where Observer stores Windows information.

OBSERVER.ADR (stored in the OBSERVER 
installation directory) stores all of the hard address 
and alias information.

OBSERVER.FLT (stored in the OBSERVER installation 
directory) stores the saved filter information.

DEMOETH.LST the DEMO data for Ethernet.

DEMOTOK.LST the DEMO data for Token Ring.

INSTALL.EXE the installation program.

INSTALL.DAT install’s data file.

OBS.DLL used by Observer and Discoverer.

DISCOVER.NIC stores information about the 
charting and display for Discoverer - this is not a 
text file.

DISCOVER.NOD stores information about the 
NODES Discoverer finds.  This is not a text file.

DISCOVER.SRV stores information about servers.  
This is not a text file.

DISCOVER.HLP the help file for Discoverer.

DISCOVER.EXE the main Discoverer program.

NICHART.DLL the charting DLL used by Discoverer.
TROUBLESHOOTING
Although most installations of Observer should 
proceed without any trouble, due to the vast 
number of network configurations and PC 
hardware/software options that Observer 
supports, sometimes trouble arises.

If you experience trouble in setting up Observer, 
keep a number of things in mind.

First and foremost, try to simplify your setup in any 
way possible.  This means if you have a screen 
saver loaded, disable it.  If you are running some 
fancy network add on peer-to-peer jet engine 
turbo stimulator, remove it.  This does not mean 
that you will not be able to use Observer with your 
other products, but if you can determine where 
the problem is, you can focus on that piece of the 
puzzle and you may be well on your way to 
solving the problem.

Second, don’t trust anyone or anything.  The only 
way to really know what your hardware settings 
are is to have the card or device in one hand and 
the manual in the other.  Programs that try and 
discover interrupts and other settings only function 
properly when everything is working correctly - 
exactly when you don’t need them.  Don't trust 
other network drivers - they may or may not be 
reporting the correct information.

Third, you can not, under any circumstances, 
share interrupts, i/o ports, or memory addresses 
between adapters.  No matter what worked 
before, or what might work in the future, sharing 
interrupts or memory settings is not a valid 
configuration.

Troubleshooting checklist:

1. Does your network work without any Observer 
programs or drivers loaded?  If not, check your 
network installation instructions.  Once your 
network appears to be running correctly, try 
and install Observer again.

2. Does Observer’s VPACK or VPACKODI driver 
load and report back that all is well?  If not, 
check the underlying network driver and verify 
that you have loaded the specific driver 
according to the Observer installation 
directions.

3. Try installing Observer on a different PC and 
see if you experience the same problem.  This 
does not mean that you will not be able to use 
Observer on the desired PC.  It may give you 
some insight into the problem you are having.
Observer Troubleshooting
Packet Driver:

Getting all 00’s or all FF’s in the Packet Driver load 
screen?

Check your card settings and verify you are giving 
the Packet Driver the correct information.

Double check that the card is not set to an 
interrupt that is being used by another adapter.  
[IRQ 3 is used by COMM 2 in most computers - this 
is a very bad choice for a network adapter if you 
have 2 COMM ports in your PC]

Packet Driver giving a usage statement (or Invalid 
PROM contents)?

Verify that you are using the correct notation in 
your Packet Driver load line.  Typically the 
following values are represented using the 
following conventions:

IRQ	number	5
I/O	hex		0x300
mem	hex		0xCC00  (note: only 4 digits 
after the "x")

NDIS:

NET START reporting an incomplete binding?

Check the [PKTDRV] section of your 
PROTOCOL.INI file and verify that the BINDINGS 
line matches your network card section’s 
heading.

ODI:

Observer is not "seeing" the packet types you are 
interested in?

Check to make sure you have included the 
correct FRAME line in your NET.CFG.

Observer not accepting packets on your LAN?

Are you licensed?  See the "Licensing" section in 
this manual for information on turning a DEMO 
version of Observer into a licensed product.  You 
can tell the state of your license by clicking on 
"File" -> "About Observer" - a license description is 
in the dialog box.

Do you have the correct filter(s) set?  Check the 
"Filter" dialog to verify the active filter set.

Note: When setting up a to/from filter you should 
set the address you are interested in the left side 
of the filter box, and ANY_ADDRESS in the right 
section.  Then select "«".  You should not put the 
desired address in both sides of the filter.

Observer can not allocate DOS packet buffer.  
Not enough contiguous DOS memory to allocate 
a DOS packet buffer.

This error is VPACK or VPACKODI telling you that 
other applications have taken all of the DOS 
memory available and have not left enough 
room for VPACK or VPACKODI to allocate a 
buffer.

VPACK and VPACKODI were designed to take 
only 3K of DOS memory while Observer is not 
running and auto allocate up to 60K of DOS buffer 
when you run Observer (the memory is returned 
when you terminate Observer).  VPACK and 
VPACKODI try to allocate 60K if they can find the 
60K contiguous.  If they can not find 60K, they try 
50K, 40K, 30K then 20K.  After that they give up 
and you see the error message.

This can be solved in two ways:

1. Unload some of the offending programs.  
Sound blasters, screen savers, clock utilities, 
and unused network protocols are the usual 
suspects.  And try running VPACK or 
VPACKODI again.

2. Run VPACK or VPACKODI with a locked 
memory buffer - explained below.
 
VPACK and VPACKODI have a flag that allow you 
to lock a capture buffer when loading.  This 
makes sure that they get their buffer no matter 
what starts in Windows.  And, since the allocation 
of the lower DOS memory under Windows is 
dynamic and often very inefficiently laid out, 
locking VPACK or VPACKODI’s memory will not 
usually result in any loss of functionality.  In other 
words, programs often take as much RAM as is 
available, and if they get less, it will not hurt them - 
WFW networking is an example of this.

The flags for VPACK and VPACKODI are:

-m=y

where y is either:

6 for a 60K buffer
5 for a 50K buffer
4 for a 40K buffer
3 for a 30K buffer
2 for a 20K buffer 

A sample command would look like:

VPACKODI  -m=3

See the Program Flags section on VPACK and 
VPACKODI for a further explanation on why this 
error occurs and what Windows is doing with the 
lower DOS memory.

Can not register MLID receive monitor, or MLID 
version to old.

This is indicating that your ODI driver for your 
network card does not support the receive 
monitor function.

Most ODI drivers developed before early 1993 do 
not support receive monitor.

Check with your card manufacturer and 
download or get a more recent driver.
Discoverer Troubleshooting
Cannot find or load NWIPXSPX.DLL or 
NWCALLS.DLL.

This is an indication that you have not updated 
your Windows PC to the latest Novell shell.

See the ODI section (1a) of the step by step 
installation instructions for a detailed description of 
what Discoverer requires.

Discoverer hangs with a "Polling Server" message 
in the status bar.

This may be an indication that you are not using 
Novell’s 802.3 frame type for IPX/SPX.  At this time 
Novell requires you to use 802.3 as your frame to 
collect statistics.

Cannot get information about a particular node or 
set of nodes.

If this condition is for some, but not all nodes, 
check to see what the nodes that do not respond 
have in common.

Maybe they are all using the same (faulty) driver?

Try updating the ODI drivers on the stations in 
question.
SAMPLE CONFIGURATION FILES:
Observer specific lines are indicated in bold.
ODI:
The following example is for a system using an 
Eagle NE2000 Ethernet adapter.

AUTOEXEC.BAT:

PROMPT $P$G
C:\DOS\SMARTDRV.EXE
C:\DOS\DOSKEY
SET MOUSE=C:\MSMOUSE
C:\MSMOUSE\MOUSE
PATH=C:\;C:\DOS;C:\WINDOWS 
SET TEMP=C:\TEMP
CD ODI
LSL
NE2000
IPXODI
VLM
C:\OBSERVER\VPACKODI
WIN


A sample NET.CFG for use with Token Ring might 
look like:


LINK DRIVER TOKEN
	INT 5
	MEM CC000
	FRAME TOKEN-RING
	FRAME TOKEN-RING_SNAP

LINK SUPPORT
	BUFFERS 15 4028
	MEMPOOL 4096

NDIS:
AUTOEXEC.BAT:

NET INIT
NET START
PROMPT $P$G
C:\DOS\SMARTDRV.EXE
C:\DOS\DOSKEY
SET MOUSE=C:\MSMOUSE
C:\MSMOUSE\MOUSE
PATH=C:\;C:\DOS;C:\WINDOWS 
SET TEMP=C:\TEMP
C:\OBSERVER\VPACK
WIN

SYSTEM.INI:

[Network Drivers]
transport=DISPKT10.DOS

PROTOCOL.INI:

[PKTDRV]
DRIVERNAME=PKTDRV$
BINDINGS=MS$NE2000		(yours may be 
different)
INTVEC=0X61

Packet Driver:
The following example is for a system using a 
SMC/WD adapter.

AUTOEXEC.BAT

PROMPT $P$G
C:\DOS\SMARTDRV.EXE
C:\DOS\DOSKEY
SET MOUSE=C:\MSMOUSE
C:\MSMOUSE\MOUSE
PATH=C:\;C:\DOS;C:\WINDOWS 
SET TEMP=C:\TEMP
C:\OBSERVER\WD_SMC 0x61 5 0x300 0xCC00
C:\OBSERVER\VPACK
WIN
PACKET DRIVER INSTALLATION INFORMATION
Note:  This is an edited version of the file INSTALL.DOC 
located in the Observer \DRIVERS directory.  If you do not 
find your network adapter listed here, check the 
INSTALL.DOC file.

Installation Instructions for the Crynwr Packet Driver 
Collection 

Document conventions

All numbers in this document are given in C-style 
representation.  Decimal is expressed as 11, hexadecimal is 
expressed as 0x0B, octal is expressed as 013.  All reference to 
network hardware addresses (source, destination and 
multicast) and demultiplexing information for the packet 
headers assumes they are represented as they would be in a 
MAC-level packet header being passed to the send_pkt() 
function.

Using the packet drivers

The packet driver must be installed prior to use.  Since each 
packet driver takes only a few thousand bytes, this is best 
done in your AUTOEXEC.BAT.  Since the Ethernet boards 
typically have jumpers on board, the packet driver must be 
informed of the values of these jumpers (auto-configure is 
possible, but can disturb other boards).  The first parameter is 
the entry point used to communicate with the packet driver.  
And again, because each board is different, the rest of the 
parameters will be different.

All parameters must be specified in C-style representation. 
The same number is expressed in decimal as 11, 
hexadecimal is expressed as 0x0B, octal is expressed as 013. 
Any numbers that the packet driver prints will be in the same 
notation.

Before installing the packet driver, you must choose an entry 
point (software interrupt) number in the range between 0x60 
and 0x7e inclusive.  Some people have reported trouble with 
dBase when using interrupts in the low 60's.  These problems 
go away when they switch to an interrupt in the high 70's 
(e.g. 0x7e).

Interrupt 0x67 is unavailable because it's used by the EMS 
interface interrupt.  Interrupts 0x70 through 0x77 are 
unavailable because the second interrupt controller uses 
them for IRQ 8 through IRQ 15.  Interrupts 0x7f and 0x80 are 
unavailable because at least one package, when locating a 
packet driver, stops searching before 0x7f.

Running a packet driver with no specifications will give a 
usage message.  The parameters for each packet driver are 
documented below.

Options

-d -- Most drivers can also be used in a PROM boot 
environment, see PROMBOOT.NOT for how to use -d and -n 
options for that purpose.  This switch delays the adapter's 
initialization until the first time the packet driver is accessed.

-n -- NetWare can use two different framing types on 
Ethernet, "IEEE 802.3" and Ethernet II.  The BYU packet driver 
shell requires Ethernet II.  However, the Crynwr packet drivers 
can convert Ethernet II into Novell's version of IEEE 802.3 (and 
back) when the -n switch is used.

-p -- A certain small level of security can be achieved by 
disabling promiscuous mode with the -p switch.  Do not 
mistake this for real security, however.

-i -- A switch used with client software that expects to find an 
IEEE 802.3 packet driver.  Many Crynwr Ethernet packet 
drivers implement both IEEE 802.3 (class 11) and Ethernet II 
aka Bluebook (class 1) framing.  The packet driver 
specification only allows a driver to report one class. The 
default is to report Ethernet II.  Using -i switches the reported 
class to IEEE 802.3.

3Com 3C501

usage: 3C501 [options] packet_int_no [hardware_irq 
[io_addr]]

The 3c501 driver requires two additional parameters -- the 
hardware interrupt number and the I/O address.  The 
defaults are 3 and 0x300.

3Com 3C503

usage: 3C503 [options] packet_int_no [int_level(2-5)[io_addr 
[cable_type]]]

The 3c503 driver requires up to three additional parameters -- 
the hardware interrupt number, the I/O address, and the 
cable type.  The 3c503 can be attached to thick or thin 
Ethernet cables, and the selection is made in software.  The 
cable type is automatically determined at start-up, but may 
be forced to external transceiver (AUI/Thickwire) by 
specifying zero or internal transceiver 
(Thinwire/10BaseT/10Base2) or one for thin. The defaults are 2, 
0x300, and 65535 (automatic).  The 3c503 can use shared 
memory, but the driver automatically determines that 
parameter from the hardware.

3Com 3c505

usage: 3c505 [options] packet_int_no [hardware_irq [io_addr 
[base_addr]]]

The 3c505 driver requires three additional parameters -- the 
hardware interrupt number, the I/O address, and the 
memory base address.  The defaults are 2 and 0x300 and 
0xd000.

3Com 3c507

usage: 3c507 [options] packet_int_no io_addr

The 3c507 will determine its parameters by reading the 
board.  The only time you would need to specify the 
parameters is when you have multiple 3c507s in the same 
machine.

The 3c507 driver will use three additional parameters -- the 
hardware interrupt number, the I/O address, and the 
memory base address.

3Com 3c509

usage: 3c509 [options] packet_int_no  (id_port] | [io_port] | 
[board_num]

The 3c509 will determine its parameters by reading the 
board.  The only time you would need to specify the 
parameters is when you have multiple 3c509s in the same 
machine, or if you have an I/O conflict with the default 
id_port (0x110).

The 3c509 driver will use three additional parameters -- the id 
port, or the I/O port, or the board number.  If the number is 
between 0 and 0xff, it is the board number.  If between 
0x100 and 0x1ff, it is an ID port.  Otherwise it is an I/O port 
number.

3Com 3c523

usage: 3c523 [options] packet_int_no [hardware_irq [io_addr 
[base_addr]]]

The 3c523 driver requires no additional parameters.  It gets 
the board's parameters out of the Microchannel POS 
registers.

HP Ethertwist

usage: hppclan [options] packet_int_no [hardware_irq 
[io_addr]]

The hppclan driver requires two additional parameters -the 
hardware interrupt number and the I/O address.  The 
defaults are 3 and 0x300.

Intel EtherExpress

usage: exp16 [options] <packet_int_no> [<io_addr>]

The Intel EtherExpress packet driver has one optional 
parameter.  The <io_addr> is only needed if there is more 
than one EtherExpress card in your system.  Otherwise, the 
driver will search for adapter and get its parameters from it.

Novell ne/2

usage: ne2 [options] <packet_int_no>
The ne/2 driver requires no additional parameters.

Novell ne1000

usage: ne1000 [options] packet_int_no [hardware_irq 
[io_addr]]

The ne1000 driver requires two additional parameters -
the hardware interrupt number and the I/O address.  The 
defaults are 3 and 0x300.

Novell ne2000

usage: ne2000 [options] packet_int_no [hardware_irq 
[io_addr]]
The ne2000 driver requires two additional parameters -the 
hardware interrupt number and the I/O address.  The 
defaults are 2 and 0x300.

Novell ne2100 and ne1500

usage: ne2100 [options] packet_int_no [hardware_irq 
[io_addr [dma_no]]]

The ne2100 Ethernet card is software compatible with the 
ne1500 card. The ne2100 driver requires three additional 
parameters -- the hardware interrupt number, the I/O 
address, and the DMA channel number.  The defaults are 3, 
0x300, and 5.

SMC (formerly Western Digital) (also IBM) SMCWD

usage: smc_wd [options] packet_int_no [-o] [int_level 
[io_addr [mem_base]]]

The SMC_WD driver runs the SMC (formerly Western Digital)E, 
EBT, EB, ET/A, and E/A Ethernet cards (but not the Ultra), and 
also on the IBM Microchannel Ethernet cards with POS ID's 
0xEFE5, 0xEFD4 and 0xEFD5. The ISA SMC_WD requires three 
additional parameters -- the hardware interrupt number, the 
I/O address, and the memory base address. The ISA defaults 
are 3 and 0x280 and 0xd000.  The MCA SMC_WD picks up its 
default parameters from the POS registers, so you only need 
specify them it you have multiple adapters. The smc_wd 
cards do not enable their memory until configuration time.  
Some 386 memory mappers will map memory into the area 
that the card intends to use. You should be able to configure 
your software to leave this area of memory alone.  Also the 
driver will refuse to map memory into occupied memory.  
The occupied memory test fails on some machines, so the 
optional switch -o allows you to disable the check for 
occupied memory.

If you get the error "PROM ADDRESS Invalid", use EZSETUP to 
set all the parameters again (to the same values).  
Occasionally wayward programs will write to locations that 
don't belong to them.  This can corrupt the EEPROM 
checksum on the card. EZSETUP will restore the correct 
checksum.

INDEX

A
Acknowledgment number, 154
address
format of entry, 44
remove, 45
alias, 8, 41, 44, 48, 49, 54, 56, 176
Aliases, 53
Alternate Columns Chart
sample, 97
Analyst/Probe, 13
ANY_ADDRESS, 41, 46, 55, 57, 180
ARP, 147
AUTOEXEC.BAT
adding VPACK, 36
adding VPACKODI, 35
Averaging time, 70
B
bandwidth utilization, 9, 39, 50, 70
long term, 9, 50
Bridge
Driver Configuration (server), 
118
Statistics (server), 102
Statistics List (server), 115
buffer
DOS memory, 73
button bar, 78, 92
C
captured packets
printing, 65
saving to a file, 66
capturing
stop from when switching, 69
charting
2D sample, 95
3D sample, 97
checksum, 141
Colors
dialog, 97
specify frame color, 62
Configuration
sample files, 183
confirmation
clearing packet buffer, 70
copyright, 15
Current Filter, 42
D
default
direcetory, 21
DEMO
install dialog, 34
mode, installation, 27
to licence, 19
version, 19
DEMOETH.LST, 176
DEMOTOK.LST, 176
direction
button, 53
DISCOVER.EXE, 176
DISCOVER.HLP, 176
DISCOVER.NIC, 176
DISCOVER.NOD, 176
DISCOVER.SRV, 176
Discoverer, 8, 10, 77
Discovery Mode, 88
File menu, 81
install dialog, 34
loggin in as supervisor, 91
Options menu, 83
polling, 79
preferences dialog, 84
required files and drivers, 29
discovery mode, 8, 39, 44, 48, 56
DOS
full screen in Windows, 27
not enough memory, 24
packet buffer, 180
TSR, 22
DRIVERS
packet driver, 31
DSAP, 145
E
Ethernet
choosing maximum bandwidth, 
51
frame header, 142
protocol sub-filters, 47
sample NET.CFG for ODI, 28, 184
F
FAX number
Network Instruments, 20
Filter
address, 42
post, 63
saving, 43
setting a filter, 46
using, 41
flags
-DEMO, 72
-i, 71
-m, 73
-TOKEN, 72
Fragments, 151
FRAME
referenced in NET.CFG, 28, 43, 
179, 184
H
hardware address
manually adding, 45
hardware addresses
adding, 44
I
i/o, 32
ICMP, 157
information window
NODE, 120
SERVER, 99
SERVER and NODE, 11
Information Windows
general, 95
Info:, 118
Lists, 106
Options, 105
INSTALL.DAT, 176
INSTALL.DOC
packet driver, 185
INSTALL.EXE, 21, 33, 176
installation
step by step, 24
Internet addresses, 146
interrupts
shared, 177
IP, 149
automatically fill in address, 49
protocol sub-filter, 47
IPX, 160
statistics chart (node), 121
statistics chart (server), 100
statistics List (node), 123
statistics List (server), 106
IPX/SPX
overview, 159
protocol sub-filter, 47
IPX/SPX Versions
node, 135
server, 118
irq, 32
K
key
number, 19
L
LANs
multiple, 15
license, 15
Licensing, 19
Line chart
sample, 96
List of Nodes, 80, 94
display options, 93
loading, 93
saving, 93
Login to Server, 90
LSL.COM, 26
LTBU, 51
number of data points, 52
M
Maximum Utilization, 51
MDI window, 77
main, 80
MLID
can not register, 182
Monitor Modes, 50
MSS, 156
multitasking, 40
N
NCP, 165
NDIS, 26
choosing, 35
install overview, 22
sample configuration, 184
troubleshooting, 179
using, 30
NET.CFG, 23, 24, 28, 29, 179
Ethernet sample, 28
Network Bandwidth, 70
network statistics, 9, 39, 53
NICHART.DLL, 176
Nodes
List of, 11
Novell
ODI, 25
Number Connections
server, 99
NWCALLS, 182
NWIPXSPX, 182
O
OBS.DLL, 176
OBSERV.DLL, 175
Observer
running, 23
using, 39
OBSERVER.ADR, 176
OBSERVER.EXE, 175
OBSERVER.FLT, 44, 49, 176
OBSERVER.HLP, 176
OBSERVER.INI, 176
ODI, 22
choosing, 35
configuring, 27
sample configuration, 183
troubleshooting, 179
Open Files
chart (server), 100
list (server), 118
OS Version Information
node, 135
P
packet
delta time stamp, 64
find, 65
serialization, 172
WatchDog, 173
packet capture, 8, 59
overview, 39
Packet Driver, 23, 26
configuring, 30
Installation Information, 185
sample configuration, 185
troubleshooting, 178
w/ Token Ring, 26
packet_int_no, 31
packets
capturing, 60
displaying raw, 62
dropped, 40, 60
viewing captured, 60, 61
Pie chart
sample, 96
polling
cursor, 86
starting/stopping, 94
polling period, 87
post-filter
IP header, 64
TCP header, 64
print captured packets
options, 65
Program Flags, 71
protocol
no fitlering, 47
sub-filter, 47
R
Received Packets
network statistics screen, 54
Right To Use, 20
license, 16
RIP, 171
S
SAP, 169
Scale, 98
search, 64
Separate Columns Chart
sample, 97
Sequence number, 154
Server exclusion List, 89
Server Version, 118
Settings
dialog, 68
Shell Driver
configuration (node), 136
list (node), 130
Shell Statistics List
node, 132
Sort, 55
SPX, 162
statistics (server), 101
statistics chart (node), 121
statistics List (node), 126
statistics list (server), 109
SPX II, 160
SSAP, 145
statistics
by protocol, 58
general screen information, 53
printing screens, 59
size distrabution, 56
Stretch time scale, 70
SUPERVISOR, 86
System Requirements, 16
T
TCP
protocol overview, 152
TCP/IP
datagrams, 140
frame header, 141
main components of, 139
overview, 139
Timing, 98
tips, 85
Token Ring, 29
choosing maximum bandwidth, 
51
Frame Header, 144
sub-filter, 47
Total Node Packets chart
node, 122
Total Packet Statistics
server, 101, 113
Troubleshooting
checklist, 178
Discoverer, 182
U
UDP, 156
V
View Configuration dialog, 62
VLM
support, 22
Volume
Information List (server), 117
Usage (server), 105
User Information (node), 137
VPACK, 23, 175
troubleshooting, 178
VPACKODI, 22, 175
troubleshooting, 178
W
WAN, 10
Warranty, 14
Window Menu, 92
Windows
buffer size, 68
lock buffer from paging, 69
network support, 23
Windows for Workgroups
w/ Novell, 25

(c) 1994 Network Instruments, LLC