WESTERN DIGITAL ETHERCARD PLUS - FAMILY LAN ADAPTER DRIVERS
      FOR USE WITH NOVELL ADVANCED NETWARE 286 VERSION 2.1X AND
      2.2.  AND FOR USE IN WORKSTATIONS WITH NETWARE 386 VERSION
      3.0 AND LATER

                          Installation Guide
                          ------------------

OVERVIEW
--------

To successfully complete the installation of the adapter driver 
you must perform the following steps:

     1.0 Hardware:
     1.1    Determine the LAN adapter hardware type.
     1.2    Determine the LAN adapter configuration.
     1.3    Install LAN adapter hardware.

     2.0 Software:
     2.1    Generate Software.
     2.2    Select Software Configuration.
             * NetWare Generation Utility.
             * Jumpers Configuration Utility.
     2.3    Install LAN software.

Specific details are provided in the following sections.


INSTALLATION PROCEDURE
----------------------

1.0 HARDWARE

    1.1   DETERMINING THE LAN ADAPTER HARDWARE TYPE

    1.1.1 Jumper Configured Adapters
               WD8003E        8K RAM
               WD8003EBT     32K RAM
               WD8003S        8K RAM
               WD8003SH       8K RAM
               WD8003WT       8K RAM
               WD8013EBT     16K RAM

           Note: Refer to JUMPERS.DOC in the root directory
                 for more information on jumpers.

    1.1.2 Micro Channel Adapters
               WD8003ET/A    16K RAM
               WD8003E/A     16K RAM
               WD8003ST/A    16K RAM
               WD8003W/A     16K RAM

    1.1.3 Software Configured Adapters
               WD8003EB       8K RAM
               WD8003W        8K RAM
               WD8003EP       8K RAM
               WD8013EP      16K RAM
               WD8013W       16K RAM
               WD8013EW      16K RAM

    1.2   DETERMINING THE LAN ADAPTER CONFIGURATION

          For information on RAM, Base I/O and IRQ, see the
          SYSMAP.DOC file furnished.

          Also refer to User Installation guide available with the
          retail packaged adapter.

    1.3   INSTALLING LAN ADAPTER HARDWARE

          Refer to User Installation guide available with the retail
          packaged adapter.
      
2.0 SOFTWARE

    2.1   Generate Software

    2.1.1 From Floppy

          When generating NetWare 286 Software from a floppy drive,
          the generation software will prompt the user to insert
          the driver diskette at the appropriate time.
           
          Note: NetWare installation procedures require the driver
                files to be located in the root directory of a
                floppy disk whose volume label is LAN_DRV_200.
                If you copy these files to another floppy disk,
                be sure that you set the volume label of the new
                disk to LAN_DRV_200.

    2.1.2 From Hard Disk

          After copying the Netware 286 floppies to the hard disk as
          described in the Netware 286 manual, a directory with the
          name 'LAN_DRV_.200' must be created at the same level as
          the 'LAN_DRV_.001' directory. Copy all the .OBJ files to
          this directory.

            - For Netware 2.1x -

          Copy the WDPLUSSH.LAN file to the directory 'SHGEN-1'.
          Copy the WDPLUS.LAN file to the directories 'AUXGEN'
          and 'BRGEN'.  Then run either 'SHGEN' for a workstation,
          'NETGEN' for a server or 'BRGEN' for a bridge.
   
            - For Netware 2.2 -

          Copy the WDPLUSSH.LAN file to the directory 'WSGEN'.
          Copy the WDPLUS.LAN file to the directories 'SYSTEM-1'
          and 'ROUTEGEN'.  Then run either 'WSGEN' for a workstation,
          'INSTALL' for a server or 'ROUTEGEN' for a router.

          For more information on using this software, refer
          to NetWare 286 Installation Manual.

    2.1.3 Running Appletalk On Your Server

          First determine whether the network is using AppleTalk
          Phase I or Phase II.  If you are not sure, read the
          APPLE.DOC file located in this directory.

          AppleTalk Phase I software is incorporated in the regular
          286 server driver.

          AppleTalk Phase II requires a special server driver called
          WDPLS2 which is located in the Network21 directory.  These
          driver files must be copied into the root of the SuperDisk
          or the LAN_DRV_200 directory.  Either the standard driver
          or AppleTalk Phase II driver, but not both, may be in the
          root directory of LAN_DRV_200 when the INSTALL or NETGEN
          programs are run.  If you are using the SuperDisk, the
          APPLE2.BAT file can be used to perform the file copying.
 
          APPLE2.BAT copies the following AppleTalk phase 2 files into
          the root directory on the SuperDisk:
          WDPLS2AD.OBJ
          WDPLS2BD.OBJ
          WDPLS2CD.OBJ
          WDPLS2DD.OBJ
          WDPLS2.LAN

          The following AppleTalk phase 1 files are copied to
          NETWARE21 directory for safe keeping.
          WDPLUSAD.OBJ
          WDPLUSBD.OBJ
          WDPLUSCD.OBJ
          WDPLUSDD.OBJ
          WDPLUS.LAN

    2.2   Select Software Configuration

          Once the proper LAN driver has been selected, the desired
          configuration parameters must be chosen from a menu.  This
          Western Digital EtherCard Plus family workstation driver has
          been designed to limit the need to reconfigure or regenerate
          the IPX.COM file, even though a variety of Western Digital
          EtherCard Plus family adapters and adapter configurations
          may be present in your workstations.  In most cases
          configuring the workstation's IPX.COM file to the default
          values will function with all adapter types.  See the
          specific adapter type for details.

    2.2.1 Jumper Configured Adapters

          When configuring a server or workstation employing a jumper
          configured adapter, one of the first four configuration
          entries must be used, the default being the first
          configuration entry. If none of these choices match the
          hardware configuration desired, then select the first/default
          configuration entry and run Novell's JUMPERS.EXE version v2.00
          configuration program. This utility allows the user to
          configure the LAN software to use any supported configuration
          parameters.  For more information on JUMPERS.EXE, refer to
          the documentation furnished with the software.  The JUMPERS
          utility is available from Novell or CompuServ.

          The RAM location for jumper configured adapters is set by
          the driver to the location specified in the configuration
          selected.

            - Selecting RAM Size -

          There are configuration selections designating RAM sizes of
          8, 16 and 32 Kbytes of RAM. 

          Adapters with 8 Kbytes of RAM can be used with configuration
          selections which specify 8, 16 or 32 Kbytes of RAM.

          Adapters with 32 Kbytes of RAM must be used with configura-
          tion selections which specify 32 Kbytes of RAM.

          The WD8003/WD8013 family AT bus 16-bit adapters can function
          in two modes,  16-bit mode and 8-bit mode.

          In 16-bit mode, the adapter performs 16-bit data transfers
          and uses the full 16 Kbytes of RAM. In 8-bit mode, the adapter
          performs 8-bit data transfers and uses only 8 Kbytes of RAM.

          To operate the 16-bit adapter in 16-bit mode, place the
          adapter in a 16-bit bus slot and configure the driver to a
          configuration selection which specifies 16 or 32 Kbytes of
          RAM.

          To operate the 16-bit adapter in 8-bit mode, configure the
          driver to a configuration selection which specifies 8 Kbytes
          of RAM, or place the adapter in an 8-bit bus slot and specify
          any driver configuration.

          NOTE:  The Default StarLAN packet type is IEEE 802.3 as of
                 release V3.07 of the 286 Server and Workstation
                 driver.  If the Novell StarLAN (AT&T StarLAN
                 compatible) packet type is required, it can be
                 changed via the JUMPERS Configuration Utility.

    2.2.2 Software Configured Adapters

            - Workstation Software -

          If one LAN adapter card is used, any of the first five
          configurations can be selected when linking a workstation.
          The shell driver automatically detects software configured
          adapters and reads the configuration information directly
          from the adapter, even if the configuration entry selected
          specified a different I/O base, IRQ and RAM base.

          If there is more than one LAN adapter, you need one of the
          'Software Configured Adapter' selections for each adapter.
          (See - Server Software - description.)

            - Server Software -

          Do NOT select the default configuration.  Select 'First
          Software Configured Adapter' for the first LAN adapter.
          Select 'Second Software Configured Adapter' for the second
          LAN adapter, etc.

          First, Second, etc., are determined by the lowest Base I/O
          address of the adapter, i.e., if there are two adapters one
          with Base I/O address 240 and the other has an address of
          280, then 240 will be the 'First Software Configured Adapter'.

    2.2.3 Micro Channel Adapters

            - Workstation Software -

          If one LAN adapter card is used, any of the first five
          configurations can be selected when linking a workstation.
          The shell driver automatically detects Micro Channel adapters
          and reads the configuration information directly from the
          adapter, even if the configuration entry selected specifies
          a different I/O base, IRQ and RAM base.

          If there is more than one LAN adapter card, one of the 'Soft
          Configured Adapter' selections is needed for each adapter.
          (See - Server Software - description.) 

            - Server Software -

          Select 'First Micro Channel Adapter' for the first LAN
          adapter.

          Select 'Second Micro Channel Adapter' for the second LAN
          adapter, etc. 

          First, Second, etc., are determined by the lowest slot number
          of the adapter, i.e., if two adapters are in the machine in
          lots 2 and 4, then the adapter in slot 2 is the 'First Micro
          Channel Adapter'.

          NOTE:  When there is more than one adapter in a machine,
                 each adapter needs to be configured so that
                 interrupts are not shared.  Do NOT use the automatic
                 configuration option when initializing the adapter
                 from the Reference Diskette.  Automatic
                 configuration assumes that interrupts are shared.
                 Instead, initialize the adapter by selecting the Set
                 Configuration option from the main menu.  Set the
                 interrupt vector to an interrupt not already in use
                 by another adapter.

    2.3   Install LAN software

          If installing an AppleTalk driver in a NetWare 286 server,
          see NetWare for Macintosh Installation Supplement.

          NOTE:  When installing a NetWare External Bridge to be used
                 with AppleTalk phase 2, the minimum requirements for
                 system memory are 5 Mbytes.













Licensed by Western Digital for use by its customers only.

Western Digital is a registered trademark of Western Digital 
Corporation. Other trademarks mentioned herein belong to 
their respective companies.

         Copyright (c) 1991 Western Digital Corporation. 
                      All Rights Reserved.