AI-LANBIOS Low-Level Driver For AMD 2100-Compatible Adapters (AM21.DOC)
	    --------------------------------------------------
		     (C) Copyright 1992 ARTISOFT, Inc.
			    (Revised 7/6/92)

INTRODUCTION
============

The AM21 low-level AI-LANBIOS driver was developed by AMD in conformance 
with the specifications outlined in the Artisoft AI-LANBIOS Driver 
Development Program.  The AM21.EXE low-level AI-LANBIOS driver allows you to 
use your Novell NE2100, NE1500T or AMD 2100 compatible adapters in a 
LANtastic network.  

In order for a Novell-compatible NE2100/1500T adapter to function with
the LANtastic Network Operating System (NOS), you must first install the
adapter as instructed in your adapter installation guide, then run the
supporting software (AM21.EXE and AILANBIO.EXE).  AM21.EXE communicates
with the adapter, while AILANBIO.EXE provides high-level communications
across the local area network.  Because of this, you cannot run any
network software until after you load AM21.EXE and AILANBIO.EXE.  For details
about the AILANBIO.exe program, please refer to your LANtastic manuals.


Compatibility Statement
=======================

Version 3.00 of AM21 is compatible with Artisoft's LANtastic/AI Network 
Operating System v4.1.  The bus-master architecture of the adapter is 
designed for use in workstations or servers where a single board is 
required.  Users should avoid even leaving more than 1 adapter inserted in
the slots in the back of the computer, as it was found to interfere with the
NE2100 card during driver testing.
In addition, users should also avoid loading the AM21 driver high since the
bus master mode of the adapter cannot access the upper memory blocks on
certain machines.


AM21.EXE V3.0
=============

There are command line switches that you can use when you run AM21.EXE
and AILANBIO.EXE.  These switches allow you greater flexibility in using
these programs.  For information on AM21.EXE command line switches, refer to 
"AM21.EXE COMMAND LINE OPTIONS" in this file.


Vendor Information
==================

AMD, 901 Thompson Place, P.O. Box 3453, Sunnyvale CA 94088-3453.  Application
support hotline: 800-222-9323 (phone).


RUNNING AM21.EXE
================

The syntax for running AM21.EXE is

     AM21[switches . . . ] [ ; comment]

where "switches" denotes any optional command line switches.  If you are
using more than one switch in a command line, use a space or a forward
slash (/) to separate the arguments.  If a switch takes a value (such as
when you designate the DOS multiplex number with the MPX= switch) the
switch must be followed by an equal sign (=) or a colon (:).  All switch
values are checked to make sure they are valid.  Illegal values produce
error messages.

These are valid switch formats:

	SWITCH
	/SWITCH
	SWITCH:VALUE
	/SWITCH=VALUE

You would use one of the first two formats for a switch that does not take
a value.  For example:

	AM21/HELP

You would use the third or fourth formats for a switch that takes a value.
Such as:

	AM21/MPX=D7


AM21.EXE COMMAND LINE OPTIONS
=============================

The valid AM21.EXE switches appear below.  The letters "ddd"  denote
that you must provide a decimal number.  The letters "hh" denote a
required hexadecimal value.  Values enclosed in brackets "[]" indicate
default values if the switch is omitted.  Values after the brackets denote
the valid range of variables for the switch.

----------
    @switch-file

This option specifies that further switches are to be taken from a
switch file.  Any switches after the @switch-file name will be used,
and the switch settings take precedence over any settings in the switch
file.  You may invoke switch files from within switch files as often as
you wish.  The file should contain valid switches and may contain comment
characters (;) at the beginning of each line or after switches.

For example,

     AM21 @setup

The file SETUP contains

     ; AM21 AI-LANBIOS driver setup file
     ;
     IOBASE=360            ; Use I/O port address 360
     IRQ=4                 ; Use interrupt request 4
     VERBOSE               ; Display verbose information

----------
     HELP or ?

This switch instructs AM21.EXE to display information about the valid
command line switches, but does not install the AM21.EXE driver.  For
example,

     AM21/help
     AM21 ?

See the messages section for a detailed description of the HELP display
output.

----------
     XEROX

This switch causes all transmitted packets to be in the XEROX format
instead of the IEEE 802.3 standard.  When using this switch AM21.EXE
will receive both XEROX and IEEE 802.3 packets.

----------
     IOBASE=hhh [300] One of the following choices:
		 300 320 340 360

This switch specifies the I/O base address configured on the adapter.  The
IOBASE switch value must match the jumper setting on the card.  The
default value is the same as the default factory setting on the cards.

The IOBASE numbers must be in multiples of 20H.  If a non-multiple is
encountered, the I/O base address is rounded down to the closest address.
For example, IOBASE=310 is the same as IOBASE=300.

Consult your adapter installation guide for more information about setting
the I/O base address on the card.

----------
     IRQ=dd [5] 3-15

This switch specifies the interrupt request (IRQ) level for the board.  If
you have more than one adapter installed, each should have its own unique
IRQ.  The IRQ switch value must match the jumper setting on the card.  The
default value is the same as the default factory setting on the card.

Consult your adapter installation guide for more information on setting
IRQ jumpers on the cards.

NOTE: If you have a 2100 compatible adapter, not all interrupts are
supported. These adapters support only interrupts 3,4,5 and 9.

----------
     DMA=d [5] 3-7 (Excluding 4)

This switch specifies the DMA channel (DREQ/DACK) for the board. If you
have more than one adapter installed, each should have it's own unique
DREQ/DACK setting. The DMA switch value should match the jumper setting
on the board.   Both the DREQ and DACK jumpers must be set to the same number.
The default number is the same as the default factory setting on the card.

Consult your adapter installation guide for more information on setting
DREQ/DACK jumpers on the cards.

NOTE: DMA level 4 is never supported on the adapter and will generate an
error message if selected.

----------
     MPX=hh [C7] C0-FF

This switch specifies the DOS multiplex (MPX) number to use for
communication with AILANBIO.EXE.  You will need to change this value only
if the default MPX number is in use by another application or NETBIOS.
Multiplex numbers 00 through BF are reserved for DOS use; therefore, you
must use a multiplex number between C0 and FF.

----------
     PACKET_SIZE=dddd [1500] 570-1500

This switch specifies the maximum size of transmitted IEEE 802.3 packets.
You may need to change this value when using certain bridges that do not
support the full 1500-byte packet size.  Even when you reduce the packet
size, the low-level driver can still receive larger packets.

----------
     RBUFS=dd [4] 2-16 (2,4,8,16)

This switch specifies the number of allocated receive buffers used by
AM21.EXE. Increasing this number can increase performance, but will also
require the use of more memory.

Receive buffers must be a power of two. Any other number will be rounded
down to the nearest power of two.
For example, RBUFS=7 is the same as RBUFS=4.

----------
     RBUF_SIZE=dddd [1518] 256-1518

This switch specifies the size of each allocated receive buffer used by
AM21.EXE. Decreasing this number will require the use of less memory, but
may impact performance.

Receive buffers are always an even number of bytes. Odd byte counts will
be rounded up to an even number.
For example, RBUF_SIZE=1001 is the same as RBUF_SIZE=1002.

The number of RBUFS will be adjusted if necessary to create a buffer
environment at least 1518 bytes in size.
For example, RBUF_SIZE=256 RBUFS=2 is the same as RBUF_SIZE=256 RBUFS=8.

----------
     TBUFS=dd [2] 2-10

This switch specifies the number of allocated transmit headers used by
AM21.EXE. Each transmit header occupies 100 bytes, so increasing this
number will increase memory usage accordingly. Increasing this number
can increase performance of the network.

----------
    REMOVE

This switch removes AM21.EXE from memory.  You must remove TSR programs
in the opposite order they were loaded.  For example, if you loaded
AM21.EXE and then AILANBIO, you must remove AILANBIO before AM21.EXE
In addition, if you have more than one invocation of AM21.EXE and
AILANBIO you must use the MPX= switch on the command line to specify which
copy of AM21.EXE but not (AILANBIO) that you want to unload.  For
example, if you load two copies of AM21.EXE and AILANBIO:

AM21.EXE/MPX=C7
AILANBIO/ADAPTER=0/MPX=C7
AM21.EXE/MPX=D7
AILANBIO/ADAPTER=1/MPX=D7

To unload these copies of AM21.EXE and AILANBIO:

AILANBIO/REMOVE
AM21.EXE/MPX=D7/REMOVE
AILANBIO/REMOVE
AM21.EXE/MPX=C7/REMOVE

The REMOVE option will remove the most recently run copy of AILANBIO.

----------
     VERBOSE

This switch causes the AM21.EXE driver to be installed and detailed
information about the configuration of the AM21.EXE driver to be
displayed.  See the messages section for a detailed description of the
VERBOSE output.

----------
     XBUS

This switch causes the AM21.EXE driver to extend the bus timing of a
PCnet-ISA based adapter, another product line designed by AMD.  This allows 
operation in certain machines that require longer bus cycles such as the 
Toshiba T5200 series laptops.  For AMD 2100-compatible adapters, this switch
has no effect.


USING MULTIPLE ADAPTERS
=======================

IMPORTANT NOTE: Multiple 2100 style adapters may not operate in some
machines due to the bus master architecture of the design in relation
to the motherboard timing.

AM21.EXE and AILANBIO.EXE communicate with each other using a DOS
multiplex (MPX) number.  Each AM21.EXE and AILANBIO.EXE pair supports
one adapter.  You will need to run an additional copy of AM21.EXE and
AILANBIO.EXE for each additional adapter installed in your computer.
Using command line switches, you must assign each AM21.EXE and
AILANBIO.EXE pair a unique multiplex and adapter number.  You must also
make sure each copy of AM21.EXE has a unique IRQ line, DMA channel and
I/O port address.  For example:

	AM21
	AILANBIO
	AM21/MPX=D7/IRQ=4/DMA=6/IOBASE=320
	AILANBIO/MPX=D7/ADAPTER=1

The first invocation of AM21.EXE and AILANBIO.EXE loads into the first
adapter using the default MPX number (C7), interrupt request number (5),
DMA channel (5), I/O port address (300) and adapter number (0).  The
command line switches in the second invocation instruct the NETBIOS to
load into the second card, (adapter number 1) using interrupt request 4,
DMA channel 6, IOBASE 320 and DOS MPX number D7.


AM21.EXE MESSAGES
===================

The AM21.EXE driver produces two types of messages: Informative and
Error.  All error messages are preceded by the text "ERROR:" and in those
cases the AM21.EXE driver is not installed.


--------
MESSAGE:

AI-LANBIOS AM21 driver Vn.nn - (C) Copyright 1992 ARTISOFT Inc.

This message is displayed each time the low-level driver is invoked.

--------
MESSAGE:
		   ---- AM21 driver installed ----

This message is displayed after the low-level driver is successfully
installed. 

--------
MESSAGE:
		 ---- AM21 driver NOT installed ----

This message is displayed if the low-level driver is not installed.  The
driver will not be installed if HELP information is displayed or an error
occurred.

--------
MESSAGE:

Command line              /verbose 
IEEE 802.3 node address  00001A188085   Network packet size      1500 
Allocated Rx buffers     4              Allocated Tx headers     2    
Rx buffer size           1518           IO base address          0300 
Interrupt request (IRQ)  5              DMA channel (DREQ/DACK)  5    
MPX interface number     C7             Packet type              IEEE 802.3
Bytes of memory used     8832  

This message is displayed if the VERBOSE switch is specified.  The values
displayed specify how the low-level driver is configured.  Some values may
not agree with switch values specified on the command line.  This will
happen when you specify an IOBASE switch value that is not a proper
multiple of the allowed value, as an example.

--------
MESSAGE:

Valid command line switches:
    HELP
    XEROX
    IOBASE= Range 0300 to 0360 hex 
    IRQ= Range 3 to 15 decimal 
    DMA= Range 3 to 7 decimal 
    MPX= Range C0 to FF hex 
    PACKET_SIZE= Range 574 to 1500 decimal 
    RBUFS= Range 2 to 16 decimal 
    RBUF_SIZE= Range 256 to 1518 decimal 
    TBUFS= Range 2 to 10 decimal 
    REMOVE
    VERBOSE
    XBUS
    ?
    @ Range 0 to 2048 byte file 

This message is displayed when the HELP or ? switch is used.  Each valid
switch is listed with the acceptable range of values (if any) and the base
(hex or decimal) that the numbers must be entered in.  The acceptable file
size range for indirect files (@) is also listed.

--------
MESSAGE:

AM21 not loaded

You have issued the AM21/REMOVE command and do not have AM21.EXE
loaded into memory.  Only issue this command after the program is loaded.

-------
MESSAGE:

		      ---- AM21 removed ----

The AM21.EXE driver has been removed from memory.

-------
ERROR:    Can't REMOVE -- AM21 interrupts re-hooked

Meaning:  You have attempted to remove AM21.EXE and the interrupts are
	  in use by another TSR, or AM21.EXE was not the last TSR
	  loaded.

Remedy:   Remove any TSRs loaded after AM21.EXE.  For example, if you
	  load AM21.EXE then AILANBIO.EXE, you must first remove
	  AILANBIO.EXE, then you can remove AM21.EXE.

-------
ERROR:    Installed AM21 is different version

Meaning:  You have loaded a version of the AM21.EXE program and
	  attempted to remove it from memory with the /REMOVE switch.  The
	  version with which you are attempting to remove AM21.EXE is
	  not the same version that was loaded.

Remedy:   Remove AM21.EXE with the same version of the program that was
	  loaded.

------
ERROR:   Cannot open indirect file - @file

Meaning: The file "file" cannot be opened as an indirect file.

Remedy:  The file must exist before it can be used as an indirect file.

------
ERROR:   Illegal character after switch name - ??????xnnnn

Meaning: The switch ?????? is followed by a character other than "=" or
	 ":" or the switch does not take a value.

Remedy:  Only use the characters "=" or ":" to specify switch values and
	 do not place characters after switches that do not take values.

------
ERROR:   Illegal digit in switch value - ??????=nnnn

Meaning: An illegal digit (character) was encountered in the numeric
	 switch value.

Remedy:  You must restrict numeric decimal values to the numbers 0-9. 
	 You must restrict hexadecimal values to the numbers 0-9 and the
	 letters A-F.

------
ERROR:   Illegal switch - ??????=nnnn

Meaning: The switch ??????=nnnn is not a recognized switch.

Remedy:  You may only specify legal switches on the command line.

------
ERROR:   MPX number hh is already in use - Try another number

Meaning: The multiplex (MPX) interrupt number hh is being used by another
	 application or low-level driver.

Remedy:  Try another MPX number.

------
ERROR:   No network hardware found at I/O base address hhhhH

Meaning: AM21.EXE did not find an adapter at the I/O port address
	 specified on the command line.

Remedy:  Make sure the adapter is correctly installed and that the IOBASE
	 command line switch corresponds to the I/O base jumper setting on
	 the board.

NOTE:    This message will also appear if the DREQ jumper is missing from
	 the adapter.

------
ERROR:   Incorrect DMA channel specified

Meaning: DMA channel 4 was specified and is illegal.

Remedy:  Make sure the proper DMA channel is selected.

------
ERROR:   Insufficient memory to load driver

Meaning: Not enough free DOS memory existed to load the driver.

Remedy:  Remove other resident programs to free conventional memory.

NOTE:    On some machines the AM21.EXE driver cannot be loaded high
	 since the bus master mode of the adapter cannot access
	 the upper memory blocks.

------
ERROR:   Adapter self test failed -- <sub message>

Meaning: The AM21 performs a self test when the driver is loaded and
	 has failed.

Remedy:  Replace the adapter or if a PCnet-ISA type card is being
	 installed, set the XBUS command line switch.

Valid sub messages:

	 Initialization timeout
	 Loopback timeout
	 Network error
	 Transmit error
	 Receive error
	 Message compare error

------
ERROR:   Incorrect DMA jumper setting

Meaning: The jumper setting of the adapter doesn't match the value
	 given on the command line.

Remedy:  Make sure the command line DMA switch matches the DREQ/DACK
	 jumper setting of the adapter.

------
ERROR:   Incorrect IRQ jumper setting

Meaning: The jumper setting of the adapter doesn't match the value
	 given on the command line.

Remedy:  Make sure the command line IRQ switch matches the IRQ jumper
	 setting of the adapter.

------
ERROR:   Switch value not in range - ??????=nnnn
	 Valid range is ssss to eeee

Meaning: The value nnnn is not in proper range.  The value "ssss"
	 represents the lowest acceptable value and the value "eeee"
	 represents the highest acceptable value.

Remedy:  Limit your range of values to the acceptable range.


TESTING AM21.EXE RETURN CODES (ERROR LEVELS)
==============================================

You may test the AM21.EXE return code or error level in a batch file by
using the IF ERRORLEVEL command.  The following error levels are returned:

     0     No error encountered.  AM21.EXE driver installed
     1     MPX number is in use
     2     Switch error
     3     No network hardware present
     4     AM21 not loaded
     5     Can't remove, different version loaded
     6     Cannot remove, interrupts re-hooked
     7     ERROR: Can't REMOVE -- AI-LANBIOS (R) still installed
     8     Incorrect DMA number specified
     9     Insufficient memory to load driver
     10    Incorrect DMA jumper setting
     11    Incorrect IRQ jumper setting
     12    Adapter failed self test

------------------
AMD is a registered trademark of Advanced Micro Devices, Inc.

PCnet-ISA is a trademark of Advanced Micro Devices, Inc.

Novell is a registered trademark of Novell, Inc.