PORT FINDER ver. 2.00 by mcTRONic Systems

     PORT  FINDER is a very versatile program.  It  will  display 
your  computer  type and bios date.  It will detect  and  display  
COM1 to COM4 and LPT1 to LPT3 ports that are responding.  You can 
swap  COM or LPT ports addresses instead of swapping cables.   If 
you are using DOS 3.3 or higher  and have COM3  and/or COM4, PORT
FINDER will  activate  both  COM3  and/or  COM4.   DOS  will then
recognize these ports and you will be able to  use the  DOS  MODE
command.   Any other  programs that  operate  through  DOS should
accept  COM3 and/or  COM4.  Your serial  port count  will also be
increased.  If you have a new IBM PS/2 computer COM3 and/or  COM4 
will already be activated.  You can use PORT FINDER to reset both
COM and LPT port addresses in  case you forget   what address  is
what.  PORT  FINDER can also be used in a BATCH  file  to  detect
which COM ports  are present.    An  Errorlevel  is  set  for all
possible  combinations.   An  example  batch file COMMTEST.BAT is
included.

     Any  program  that directly addresses the COM or  LPT  ports 
will  not be affected by PORT FINDER.  Any program that uses  DOS 
to  address  the  COM or LPT ports, will work  with  PORT FINDER, 
allowing  you to  swap any  port address you like.  Activation of
COM3 or  COM4 port does require DOS 3.3 or higher  and a  COM3 or
COM4 port.

	PORT FINDER  requires  no run time parameters, to display
responding  COM  and  LPT ports  on all  systems,  or to activate
alternate COM ports on PC/XT/AT systems.  DOS 3.3 and higher only
supports  access  to a  maximum  of 4  COM  and  3 LPT ports. The
optional  PORT FINDER  parameters  for parm1  and/or  parm2  with
descriptions are:

d:>PF [parm1] [parm2]

H   - Display this help screen       C23 - Swap COM ports 2 and 3
RC  - Reset COM port addresses       C24 - Swap COM ports 2 and 4
RL  - Reset LPT port addresses       C34 - Swap COM ports 3 and 4
C12 - Swap COM ports 1 and 2         L12 - Swap LPT ports 1 and 2
C13 - Swap COM ports 1 and 3         L13 - Swap LPT ports 1 and 3
C14 - Swap COM ports 1 and 4         L23 - Swap LPT ports 2 and 3

NOTES:

     All parameter  letters  can be upper or lower case.  The COM
and  LPT port  addresses displayed   always  indicate  the  final
location after  all  port  swaps  and resets  have been exacuted.
Enter all port numbers with low first then high.

     I highly recommend that you not leave any address holes  for 
either the COM or LPT ports.  As an example do not have only COM1 
and COM3 with no COM2.  Do not have a LPT2 and LPT3 with no LPT1.  
If you have one port it should be 1,  two ports should be 1 and 2 
and  so forth.  Swap only ports that you have.  While nothing  is 
wrong with testing out a port address you do not have by swapping 
an  address  you  have to it,  you and  your  system  may  become 
confused.   Use  the RC or RL functions to restore  all  standard 
port  address  locations.   If you have any  problems  with  your 
system after using PORT FINDER then stop using it.






TECHNICAL DATA:

	DOS assigns COM and LPT numbers, from LOW to HIGH, to all
responding  I/O  ports  in  order  as  they  are  found  and non-
responding I/O ports addresses are skipped.

MACHINE         COMx             I/O            INT.        MEM

ALL             COM1            3F8 HEX         IRQ4       40:00
ALL             COM2            2F8 HEX         IRQ3       40:02
PC/XT/AT        COM3            3E8 HEX         IRQ4       40:04
PC/XT/AT        COM4            2E8 HEX         IRQ3       40:06
PC/XT/AT        COM5            2E0 HEX         IRQ4       NONE
PC/XT/AT        COM6            3E0 HEX         IRQ3       NONE

PS/2            COM3           3220 HEX         IRQ3       40:04
PS/2            COM4           3228 HEX         IRQ3       40:06
PS/2            COM5           4220 HEX         IRQ3       NONE
PS/2            COM6           4228 HEX         IRQ3       NONE
PS/2            COM7           5220 HEX         IRQ3       NONE
PS/2            COM8           5228 HEX         IRQ3       NONE


SERIAL PORT COUNT IS AT MEM 40:11 BITS 2, 3, AND 4.

        ErrorLevel              COM1  COM2  COM3  COM4

            0                     0     0     0     0
            1                     X     0     0     0
            2                     0     X     0     0
            3                     X     X     0     0
            4                     0     0     X     0
            5                     X     0     X     0
            6                     0     X     X     0
            7                     X     X     X     0
            8                     0     0     0     X
            9                     X     0     0     X
           10                     0     X     0     X
           11                     X     X     0     X
           12                     0     0     X     X
           13                     X     0     X     X
           14                     0     X     X     X
           15                     X     X     X     X

                      (X means COMx is there)

     PORT ADDRESS     MEM

LPT1   3BC HEX       40:08 (may be included on MDA or other card)
LPT2   378 HEX       40:0A (may be addressed as LPT1 on PC,XT,AT)
LPT3   278 HEX       40:0C (may be addrresed as LPT2 on PC,XT,AT)

DISCLAIMER:

     PORT  FINDER is not guaranteed in any way.  Use at your  own 
risk!   I have made every attempt to get it right but testing  it 
on  every  machine configuration is not possible.   If  you  have 
problems with PORT FINDER then stop using it and let me know.  

     This  program is yours to use and freely copy.  You can  not 
sell  PORT FINDER or change any fee for its use.  A  distribution 
fee of not more than $5.00 can be charged with my written consent. 




                                        Thank You,


                                        James D. McDaniel
                                        Owner/Programmer

                                        mcTRONic Systems
                                        7426 Corwall Bridge Ln.
                                        Houston, TX  77041-1709
                                        (713) 462-7687


*   If  you  need  a good mail list  program  then  send  for  my 
shareware program MAILALL.   It is the best and  least exspensive
mail list program you can buy for a small company or personal use.

MAILALL  will maintain the names of up to 20 address  files  each 
with  4000 addresses on a hard disk or 1500 addresses per  floppy 
disk.   There are nine data fields and you  can sort the  address
file by any two that you wish.  MAILALL will print Labels (up  to
four across), Reports, and Envelopes.  You can edit or print  all 
functions  based on address search matches from one to  all  nine 
fields.   MAILALL  can import or export WORDSTAR  mailmerge  data 
files and can export MULTIMATE ADVANTAGE II mailmerge files.   It 
cost  just $27.50 shipped FIRST CLASS MAIL to you.  Send  for  it 
today!

PORT FINDER, COPYRIGHT (C) 1988 by mcTRONic Systems
MAILALL, COPYRIGHT (C) 1987, 1988 by mcTRONic Systems

DOCUMENT DATE:  September 7, 1988