ETHERNET REMOTE PROGRAM LOAD

Use ETHERRPL to enable remote booting of workstations (mostly diskless) that
have Ethernet network boards installed with IBM RPL style bootroms.

Command format

      LOAD [path]ETHERRPL  

Command parameters

Replace path with a full directory path to the directory containing the
module; begin with a DOS drive letter or a NetWare volume name.  If you do
not specify a path and the SYS volume is mounted, the operating system
assumes that the loadable module is located in the SYS:SYSTEM directory. 
(Use SEARCH to set up additional paths for automatic searching.)

Additional information

To remotely boot a diskless Ethernet workstation, you must complete the
following:

þ     Load ETHERRPL.

þ     Configure the workstation boot files for remote booting.  Follow the
      DOSGEN instructions in Appendix D of the NetWare 386 Installation
      manual.

þ     Bind the ETHRPL protocol to the network boards in the file server.


To load ETHERRPL, complete the following steps.

1.    Type

      LOAD ETHERRPL  <Enter>

2.    Bind the ETHRPL protocol to the driver for the Ethernet network 
      board(s) in the file server.  Type 

      BIND ETHRPL LAN_driver  <Enter>

      Replace LAN_driver with the name of the driver you are using.  If you
      have loaded the driver more than once, you will need to repeat this   
      step.

3.    Edit the AUTOEXEC.NCF file.  Add the following lines to load and bind
      ETHERRPL:  

      LOAD ETHERRPL
      BIND ETHRPL LAN_driver driver_parameters

      Replace LAN_driver with the name of the driver you used in Step 2.

      Replace driver_parameters with the parameters you used to load the LAN
      driver.