SUBPART C - SPECIAL OPERATIONS



97.201  Auxiliary operation.

     (a) Any amateur station licensed to a holder of a Technician,
General, Advanced or Amateur Extra Class operator license may be
an auxiliary station.  A holder of a Technician, General, Advanced
or Amateur Extra Class operator license may be the control operator
of an auxiliary station, subject to the privileges of the class of
operator license held.
     (b) An auxiliary station may transmit only on the 1.25 m and
shorter wavelength bands, except the 220.0-220.5 MHz segment and
the UHF 431-433 MHz and 435-438 MHz segments.
     (c) Where an auxiliary station causes harmful interference to
another auxiliary station, the two stations are equally and fully
responsible for resolving the interference unless one station's
operation is recommended by a frequency coordinator and the other
station's is not.  In that case, the licensee of the
non-coordinated auxiliary station has primary responsibility to
resolve the interference.
     (d) An auxiliary station operation may be automatically
controlled only when it is part of a system that includes a
repeater station also being automatically controlled.
     (f) An auxiliary station may transmit one-way communications.



97.203  Beacon station.

     (a) Any amateur station licensed to a holder of a Technician,
General, Advanced or Amateur Extra Class operator license may be
a beacon.  A holder of a Technician, General, Advanced or Amateur
Extra Class operator license may be the control operator of a
beacon, subject to the privileges of the class of operator license
held.
     (b) A beacon station must not concurrently transmit on more
than 1 channel in the same amateur service frequency band, from
the same station location.
     (c) The transmitter power of a beacon must not exceed 100 W.
     (d) A beacon may be automatically controlled when it is
transmitting on the 28.20-28.30 MHz, 50.06-50.08 MHz, 144.05-144.06
MHz, 220.05-220.06 MHz, 222.05-222.06 or 432.07-432.08 MHz
segments, or on the 33 cm and shorter wavelength bands.
     (e) Before establishing an automatically controlled beacon in
the National Radio Quiet Zone or before changing the transmitting
frequency, transmitter power, antenna height or directivity, the
station licensee must give written notification thereof to the
Interference Office, National Radio Astronomy Observatory, P.O.
Box 2, Green Bank, WV 24994.
          (1) The notification must include the geographical
coordinates of the antenna, antenna ground elevation above mean sea
level (AMSL), antenna center of radiation above ground level (AGL),
antenna directivity, proposed frequency, type of emission, and
transmitter power.
          (2) If an objection to the proposed operation is received
by the FCC from the National Radio Astronomy Observatory at Green
Bank, Pocahontas County, WV, for itself or on behalf of the Naval
Research Laboratory at Sugar Grove, Pendleton County, WV, within
20 days from the date of notification, the FCC will consider all
aspects of the problem and take whatever action is deemed
appropriate.
     (f) A beacon must cease transmissions upon notification by an
EIC that the station is operating improperly or causing undue
interference to other operations.  The beacon may not resume
transmitting without prior approval of the EIC.
     (g) A beacon may transmit one-way communications.



97.205  Repeater station.

     (a) Any amateur station licensed to a holder of a Technician,
General, Advanced or Amateur Extra Class operator license may be
a repeater.  A holder of a Technician, General, Advanced or Amateur
Extra Class operator license may be the control operator of a
repeater, subject to the privileges of the class of operator
license held.
     (b) A repeater may receive and retransmit only on the 10 m and
shorter wavelength frequency bands except the 28.0-29.5 MHz,
50.0-52.0 MHz, 144.0-144.5 MHz, 145.5-146.0 MHz, 220.0-220.5 MHz,
431.0-433.0 MHz and 435.0-438.0 MHz segments.
     (c) Where the transmissions of a repeater cause harmful
interference to another repeater, the two station licensees are
equally and fully responsible for resolving the interference unless
the operation of one station is recommended by a frequency
coordinator and the operation of the other station is not.  In that
case, the licensee of the non-coordinated repeater has primary
responsibility to resolve the interference.
     (d) A repeater may be automatically controlled.
     (e) Ancillary functions of a repeater that are available to
users on the input channel are not considered remotely controlled
functions of the station.  Limiting the use of a repeater to only
certain user stations is permissible.
     (f) Before establishing a repeater in the National Radio Quiet
Zone or before changing the transmitting frequency, transmitter
power, antenna height or directivity, or the location of an
existing repeater, the station licensee must give written
notification thereof to the Interference Office, National Radio
Astronomy Observatory, P.O. Box 2, Green Bank, WV 24994.
          (1) The notification must include the geographical
coordinates of the antenna, antenna ground elevation above mean sea
level (AMSL), antenna center of radiation above ground level (AGL),
antenna directivity, proposed frequency, type of emission, and
transmitter power.
          (2) If an objection to the proposed operation is received
by the FCC from the National Radio Astronomy Observatory at Green
Bank, Pocahontas County, WV, for itself or on behalf of the Naval
Research Laboratory at Sugar Grove, Pendleton County, WV, within
20 days from the date of notification, the FCC will consider all
aspects of the problem and take whatever action is deemed
appropriate.



97.207  Space station.

     (a) Any amateur station licensed to a holder of an Amateur
Extra Class operator license may be a space station.  A holder of
any class operator license may be the control operator of a space
station, subject to the privileges of the class of operator license
held by the control operator.
     (b) A space station must be capable of effecting a cessation
of transmissions by telecommand whenever such cessation is ordered
by the FCC.
     (c) The following frequency bands and segments are authorized
to space stations:
          (1) The 15 m, 12 m, 10 m, 6 mm, 4 mm, 2 mm, and 1 mm
bands; and
          (2) The 7.0-7.1 MHz, 14.00-14.25 MHz, 144-146 MHz,
2400-2450 MHz, 3.40-3.41 GHz, 5.83-5.85 GHz, 10.45-10.50 GHz and
24.00-24.05 GHz segments.
     (d) A station in space operation may automatically retransmit
the radio signals of Earth stations and other space stations.
     (e) A space station may transmit one-way communications.
     (f) Results of measurements made in the space station,
including those related to the function of the station, transmitted
by a space station may consist of specially coded messages intended
to facilitate communications.
     (g) The licensee of each space station must give two written,
pre-space station notifications to the Private Radio Bureau, FCC,
Washington, DC  20554.  Each notification must be in accord with
the provisions of Articles 11 and 13 of the Radio Regulations.
          (1) The first notification is required no less than 27
months prior to initiating space station transmissions and must
specify the information required by Appendix 4, and Resolution No.
642 of the Radio Regulations.
          (2) The second notification is required no less than 5
months prior to initiating space station transmissions and must
specify the information required by Appendix 3 and Resolution No.
642 of the Radio Regulations.
     (h) The licensee of each space station must give a written,
in-space station notification to the Private Radio Bureau, FCC,
Washington, DC  20554, no later than 7 days following initiation
of space station transmissions.  The notification must update the
information contained in the pre-space notification.
     (i) The licensee of each space station must give a written,
post-space station notification to the Private Radio Bureau, FCC,
Washington, DC  20554, no later than 3 months after termination of
the space station transmissions.  When the termination is ordered
by the FCC, notification is required no later than 24 hours after
termination.



97.209  Earth station.

     (a) Any amateur station may be an Earth station.  A holder of
any class operator license may be the control operator of an Earth
station, subject to the privileges of the class of operator license
held by the control operator.
     (b) The following frequency bands and segments are authorized
to Earth stations:
     (1) The 15 m, 12 m, 10 m, 6 mm, 4 mm, 2 mm and 1 mm bands; and
     (2) The 7.0-7.1 MHz, 14.00-14.25 MHz, 144-146 MHz, 435-438
MHz, 1260-1270 MHz, 2400-2450 MHz, 3.40-3.41 GHz, 5.65-5.67 GHz,
10.45-10.50 GHz and 24.00-24.05 GHz segments.



97.211  Telecommand station.

     (a) Any amateur station designated by the licensee of a space
station is eligible to transmit as a telecommand station, subject
to the privileges of the class of operator license held by the
control operator.
     (b) A telecommand station may transmit special codes intended
to obscure the meaning of telecommand messages to the station in
space operation.
     (c) The following frequency bands and segments are authorized
to telecommand stations:
          (1) The 15 m, 12 m and 10 m bands; 6 mm, 4 mm, 2 mm and
1 mm bands; and
          (2) The 7.0-7.1 MHz, 14.00-14.25 MHz, 144-146 MHz,
435-438 MHz, 1260-1270 MHz and 2400-2450 MHz, 3.40-3.41 GHz,
5.65-5.67 GHz, 10.45-10.50 GHz and 24.00-24.05 GHz segments.
     (d) A telecommand station may transmit one-way communications.



97.213  Remote control of a station.

     An amateur station may be remotely controlled where:
     (a) There is a radio or wireline control link between the
control point and the station sufficient for the control operator
to perform his/her duties.  If radio, the control link must use an
auxiliary station.  A control link using a fiber optic cable or
another telecommunication service is considered wireline.
     (b) Provisions are incorporated to limit transmission by the
station to a period of no more than 3 minutes in the event of
malfunction in the control link.
     (c) The station is protected against making, willfully or
negligently, unauthorized transmissions.
     (d) A photocopy of the station license and the name, address,
and telephone number of the station licensee and at least one
designated control operator is posted in a conspicuous place at
the station location.



97.215  Remote control of model craft.

     An amateur station transmitting signals to control a model
craft may be operated as follows:
     (a) The station identification procedure is not required for
transmissions directed only to the model craft, provided that a
label indicating the station call sign and the station licensee's
name and address is affixed to the station transmitter.
     (b) The control signals are not considered codes or ciphers
intended to obscure the meaning of the communication.
     (c) The transmitter power must not exceed 1 W.