American Megatrends, Inc.

                               Beep Codes


           The following beep codes would be heard on power on.


           Beep Code                    Meaning
           ______________________________________________________________
                1                       DRAM refresh failure
                2                       Parity Circuit failure
                3                       Base 64K RAM failure
                4                       System Timer failure
                5                       Processor failure
                6                       Keyboard Controller Gate A20 error
                7                       Virtual Mode Exception error
                8                       Display Memory R/W Test failure
                9                       ROM-BIOS Checksum failure

                All of these errors are codes reported by bios