MS-DOS Interrupt List
    *******************************************************************




-----------------------------------------------------------
 INT 0 - DIVIDE ERROR
    Automatically called at end of DIV or IDIV operation
 that results in error. Normally set by DOS to display an error
 message and abort the program.
 -----------------------------------------------------------
 INT 1 - SINGLE-STEP
    Generated at end of each machine instruction if
 TF bit in FLAGS is set. This is what makes the T command
 of DEBUG work for single-stepping. Is not generated after
 MOV to segment register or POP of segment register.
 -----------------------------------------------------------
 INT 2 - NMI (Non Maskable Interrupt)
    Generated by NMI signal in hardware. Used in IBM for
 memory parity error trapping.
 -----------------------------------------------------------
 INT 3 - 1-BYTE INTERRUPT
    Generated by opcode 0CCh. Similar to 8080's RST
 instruction. Generally used to set breakpoints for DEBUG.
 -----------------------------------------------------------
 INT 4 - OVERFLOW
    Generated by INTO instruction if OF flag is set. If
 flag is not set, INTO is effectively a NOP. Used to trap any
 arithmetic errors when program is ready to handle them rather
 than immediately when they occur.
 -----------------------------------------------------------
 INT 5 - Print-Screen Key
    Automatically called by keyboard scan when print-
 screen key is pressed. Normally executes routine to print
 the screen, but may call any routine that can safely be
 executed from inside the keyboard scanner.
    Status and result byte at address 0050:0000.
 -----------------------------------------------------------
 INT 6 - UNKNOWN
 -----------------------------------------------------------
 INT 7 - UNKNOWN
 -----------------------------------------------------------
 INT 8 thru 0FH - Vectored Hardware Lines (in IBM at least)
    In IBM, these 8 interrupts are generated in
 response to IRQ 0 through IRQ 7 (if enabled via port 21).
        IRQ0    -       Timer interrupt
        IRQ1    -       Keyboard interrupt
        IRQ3    -       RS232 port (com2:)
        IRQ4    -       serial controller (com1:)
        IRQ5    -       fixed disk
        IRQ6    -       diskette interrupt
        IRQ7    -       PPI interrupt
 -----------------------------------------------------------
INT 10 - VIDEO - SET VIDEO MODE
    REG AH = 0
    REG AL = 0 = 40x25 B&W
             1 = 40x25 COLOR
             2 = 80x25 BW
             3 = 80x25 COLOR
             4 = 320x200 GRAPHICS, 4 COLOR
             5 = 320x200 GRAPHICS, 4 GREY
             6 = 640x200 GRAPHICS, B&W
             7 = MONOCHROME GRAPHICS MODE
             8 = 160x200 GRAPHICS, 16 COLOR
             9 = 320x200 GRAPHICS, 16 COLOR
             A = 640x200 GRAPHICS, 4 COLOR

    Note: Modes 8-10 are only available on the PCjr (and
          Tandy 1000).
-----------------------------------------------------------
 INT 10 - VIDEO - SET CURSOR CHARACTERISTICS
     REG AH = 1
     REG CH = bit values:
                bits 5-6 = blink attribute
                             (00=normal, 01=invis., 11=fast)
                bits 0-4 = start line for cursor in char. cell
     REG CL = bit values:
                bits 0-4 = end line for cursor in char. cell
 -----------------------------------------------------------
 INT 10 - VIDEO - SET CURSOR POSITION
    REG AH = 2
    REG DH,DL = ROW,COLUMN - 0,0 = UPPER LEFT
    REG BH = PAGE NO. - 0 = GRAPHICS
 -----------------------------------------------------------
 INT 10 - VIDEO - READ CURSOR POSITION
    REG AH = 3
    REG BH = PAGE NO. - 0 = GRAPHICS
    ON EXIT:
       REG DH,DL = ROW,COLUMN
       REG CH,CL = CURSOR MODE,CURRENT SET
 -----------------------------------------------------------
 INT 10 - VIDEO - READ LIGHT PEN POSITION
    REG AH = 4
    ON EXIT:
       REG AH = 0: light pen switch not activated
           AH = 1: light pen values in registers
              DH = row of current position
              DL = column of current position
              CH = raster line (0-199)
              BX = pixel column (0-319 or 0-639)
 -----------------------------------------------------------
 INT 10 - VIDEO - SELECT DISPLAY PAGE
    REG AH = 5
    REG AL = 0 - 7: NEW PAGE VALUE FOR MODES 0 & 1
             0 - 3: NEW PAGE VALUE FOR MODES 2 & 3
             80H: READ CRT/CPU PAGE REGISTERS
             81H: SET CPU PAGE REGISTER TO VALUE IN BL
             82H: SET CRT PAGE REGISTER TO VALUE IN BH
             83H: SET BOTH DISPLAY REGISTERS
     ON EXIT:
        REG BH = CRT PAGE REGISTER
            BL = CPU PAGE REGISTER
 -----------------------------------------------------------
 INT 10 - VIDEO - SCROLL PAGE UP
    REG AH = 6
    REG AL = NO. OF LINES BLANKED AT BOTTOM OF PAGE
        0 = BLANK WINDOW
    REG BH = ATTRIBUTES TO BE USED ON BLANK LINE
    WINDOW:
       REG CH,CL = UPPER LEFT CORNER
       REG DH,DL = LOWER RIGHT CORNER
 -----------------------------------------------------------
 INT 10 - VIDEO - SCROLL PAGE DOWN
    REG AH = 7
    REG AL = NO. OF LINES BLANKED AT TOP OF PAGE
        0 = BLANK WINDOW
    REG BH = ATTRIBUTES TO BE USED ON BLANK LINE
    WINDOW:
       REG CH,CL = UPPER LEFT CORNER
       REG DH,DL = LOWER RIGHT CORNER
 -----------------------------------------------------------
 INT 10 - VIDEO - READ ATTRIBUTES/CHARACTER AT CURSOR POSITION
    REG AH = 8
    REG BH = DISPLAY PAGE
    ON EXIT:
       REG AL = CHAR
       REG AH = ATTRIBUTE OF CHAR - ALPHA MODE
 -----------------------------------------------------------
 INT 10 - VIDEO - WRITE ATTRIBUTES/CHARACTERS AT CURSOR POS
    REG AH = 9
    REG AL = CHARACTER
    REG BH = DISPLAY PAGE - ALPHA MODE
    REG BL = ATTRIBUTES OF CHAR
    REG CX = NO. OF CHAR TO WRITE
 -----------------------------------------------------------
 INT 10 - VIDEO - WRITE CHARACTERS ONLY AT CURSOR POS
    REG AH = 0AH
    REG AL = CHARACTER
    REG BH = DISPLAY PAGE - ALPHA MODE
    REG BL = COLOR OF CHARACTER (GRAPHICS MODE)
    REG CX = NO. OF CHAR TO WRITE
 -----------------------------------------------------------
 INT 10 - SET COLOR PALETTE
    REG AH = 0BH
    REG BH = PALETTE COLOR ID
    REG BL = COLOR TO BE USED W/COLOR ID
 -----------------------------------------------------------
 INT 10 - WRITE DOT ON SCREEN
    REG AH = 0CH
    REG AL = COLOR OF DOT
    REG DX = ROW (0000 - 00C7)
    REG CX = COLUMN (0000 - 027F)
    NOTE:     VIDEO MODES 6 & 7 ONLY
 -----------------------------------------------------------
 INT 10 - READ DOT ON SCREEN
    REG AH = 0DH
    REG CX = COLUMN (0000 - 027F)
    REG DX = ROW (0000 - 00C7)
    ON RETURN:
       REG AL = COLOR READ
 -----------------------------------------------------------
 INT 10 - WRITE CHARACTER - ADVANCE CURSOR (TTY WRITE)
    REG AH = 0EH
    REG AL = CHARACTER
    REG BL = FOREGROUND COLOR (VIDEO MODES 6 & 7 ONLY)
 -----------------------------------------------------------
 INT 10 - GET CURRENT VIDEO MODE
    REG AH = 0FH
    ON RETURN:
       REG AH = # OF COLUMNS ON SCREEN
       REG AL = CURRENT VIDEO MODE
       REG BH = CURRENT ACTIVE DISPLAY PAGE
 -----------------------------------------------------------
 INT 10 - SET PALETTE REGISTERS (PCjr AND TANDY 1000)
    REG AH = 10H
        AL = 0: SET PALETTE REGISTER
                BL = PALETTE REGISTER TO SET
                BH = COLOR VALUE TO STORE
        AL = 1: SET BORDER COLOR REGISTER
                BH = COLOR VALUE TO STORE
        AL = 2: SET ALL PALETTE REGISTERS
                ES:DX = POINTER TO 17-BYTE LIST
                  BYTES 0-15 = VALUES FOR PALETTE REGS. 0-15
                  BYTE 16 = VALUE FOR BORDER REGISTER
 -----------------------------------------------------------
 INT 10 - WRITE STRING, DON'T MOVE CURSOR (PC/AT ONLY)
    REG AH = 13H
        AL = 0
        BL = ATTRIBUTE
        BH = DISPLAY PAGE NUMBER
        DX = STARTING CURSOR POSITION
        CX = LENGTH OF STRING
        ES:BP = POINTER TO START OF STRING
 -----------------------------------------------------------
 INT 10 - WRITE STRING, MOVE CURSOR AFTER STRING (PC/AT ONLY)
    REG AH = 13H
        AL = 1
        BL = ATTRIBUTE
        BH = DISPLAY PAGE NUMBER
        DX = STARTING CURSOR POSITION
        CX = LENGTH OF STRING
        ES:BP = POINTER TO START OF STRING
 -----------------------------------------------------------
 INT 10 - WRITE STRING OF ALTERNATING CHARACTERS, ATTRIBUTES;
          DON'T MOVE CURSOR                      (PC/AT ONLY)
    REG AH = 13H
        AL = 2
        BH = DISPLAY PAGE NUMBER
        DX = STARTING CURSOR POSITION
        CX = LENGTH OF STRING
        ES:BP = POINTER TO START OF STRING
 -----------------------------------------------------------
 INT 10 - WRITE STRING OF ALTERNATING CHARACTERS, ATTRIBUTES;
          MOVE CURSOR                            (PC/AT ONLY)
    REG AH = 13H
        AL = 3
        BH = DISPLAY PAGE NUMBER
        DX = STARTING CURSOR POSITION
        CX = LENGTH OF STRING
        ES:BP = POINTER TO START OF STRING
 -----------------------------------------------------------
 INT 10 - GET VIDEO RAM ADDRESS
    REG AH = 70H
    ON RETURN:
       REG  AX  = SEGMENT ADDRESS OF THE FOLLOWING
    [BX] = OFFSET ADDRESS OF GREEN PLANE
    [CX] = SEGMENT ADDRESS OF GREEN PLANE
    [DX] = SEGMENT ADDRESS OF RED/BLUE PLANE
      (RED OFFSET = 0, BLUE OFFSET = 4000)
 -----------------------------------------------------------
 INT 10 - GET INCRAM ADDRESSES
    REG AH = 71H
    ON RETURN:
       REG  AX  = SEGMENT ADDRESS OF THE FOLLOWING
    [BX] = SEGMENT ADDRESS OF INCRAM
    [CX] = OFFSET ADDRESS OF INCRAM
 -----------------------------------------------------------
 INT 10 - SCROLL SCREEN RIGHT
    REG AH = 72H
    REG AL = NO. OF COLUMNS BLANKED AT LEFT OF PAGE
        0 = BLANK WINDOW
    REG BH = ATTRIBUTES TO BE USED ON BLANK COLUMNS
    WINDOW:
       REG CH,CL = UPPER LEFT CORNER
       REG DH,DL = LOWER RIGHT CORNER
 ----------------------------------------------------------
 INT 10 - SCROLL SCREEN LEFT
    REG AH = 73H
    REG AL = NO. OF COLUMNS BLANKED AT RIGHT OF PAGE
        0 = BLANK WINDOW
    REG BH = ATTRIBUTES TO BE USED ON BLANK COLUMNS
    WINDOW:
       REG CH,CL = UPPER LEFT CORNER
       REG DH,DL = LOWER RIGHT CORNER
 -----------------------------------------------------------
 INT 11 - EQUIPMENT DETERMINATION
    ON RETURN:
       REG AX = "equipment flag"
          bit 0        diskette installed
          bit 1        8087 present
          bit 2,3      always = 11
          bit 4,5      initial video mode
                       01 = 40x25 COLOR
                       10 = 80x25 COLOR
                       11 = 80X25 IBM monochrome
          bit 6,7      number of diskette drives (only if bit 0 = 1)
                       00 = 1, 01 = 2
          bit 8        0 = dma present, 1= no dma on system
          bit 9,10,11  number of RS232 cards
          bit 12       game I/O attached
          bit 13       serial printer installed (IBM-PCjr)
          bit 14,15    number of printers
 -----------------------------------------------------------
 INT 12 - MEMORY SIZE
    ON RETURN:
       REG AX = NO. OF CONTIGUOUS 1K BLOCKS
 -----------------------------------------------------------
 INT 13 - RESET DISK SYSTEM
    REG AH = 0
 -----------------------------------------------------------
 INT 13 - STATUS OF DISK SYSTEM
    REG AH = 1
    ON RETURN:
       REG AL = STATUS
                01H = BAD COMMAND
                02H = ADDRESS MARK NOT FOUND
                03H = WRITE ATTEMPTED ON WRITE-PROTECTED DISK
                04H = SECTOR NOT FOUND
                06H = DISKETTE REMOVED
                08H = DMA OVERRUN
                09H = DMA ACROSS 64K BOUNDARY
                10H = BAD CRC
                20H = CONTROLLER FAILURE
                40H = SEEK FAILED
                80H = TIME OUT
 -----------------------------------------------------------
 INT 13 - READ SECTORS INTO MEMORY
    REG AH = 2
    REG AL = NO. OF SECTORS
    REG CH = TRACK NO.
    REG CL = SECTOR NO.
    REG DH = HEAD NO.
    REG DL = DRIVE NO.
    REG ES:BX = ADDRESS OF BUFFER
    ON RETURN:
           CF = SUCCESS/FAILURE SIGNAL
       REG AH = STATUS (SEE ABOVE)
           AL = NUMBER OF SECTORS READ
 -----------------------------------------------------------
 INT 13 - WRITES SECTORS FROM MEMORY
    REG AH = 3
    REG AL = NO. OF SECTORS
    REG CH = TRACK NO.
    REG CL = SECTOR NO.
    REG DH = HEAD NO.
    REG DL = DRIVE NO.
    REG ES:BX = ADDRESS OF BUFFER
    ON RETURN:
           CF = SUCCESS/FAILURE SIGNAL
       REG AH = STATUS (SEE ABOVE)
           AL = NUMBER OF SECTORS WRITTEN
 -----------------------------------------------------------
 INT 13 - VERIFIES SECTORS
    REG AH = 4
    REG AL = NO. OF SECTORS
    REG CH = TRACK NO.
    REG CL = SECTOR NO.
    REG DH = HEAD NO.
    REG DL = DRIVE NO.
    ON RETURN:
           CF = SUCCESS/FAILURE SIGNAL
       REG AH = STATUS (SEE ABOVE)
           AL = NUMBER OF SECTORS VERIFIED
 -----------------------------------------------------------
 INT 13 - FORMAT DISKETTE TRACK
    REG AH = 5
        AL = NUMBER OF SECTORS
        CH = TRACK NUMBER
        CL = SECTOR NUMBER
        DH = HEAD NUMBER
        DL = DRIVE NUMBER
        ES:BX = POINTER TO 4-BYTE ADDRESS FIELD
                BYTE 1 = TRACK
                BYTE 2 = HEAD
                BYTE 3 = SECTOR
                BYTE 4 = BYTES/SECTOR
    ON RETURN:
           CF = SUCCESS/FAILURE SIGNAL
       REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - GET CURRENT DRIVE PARAMETERS (PC/AT ONLY)
     REG AH = 8
     ON RETURN:
            CF = SUCCESS/FAILURE FLAG
        REG AH = STATUS CODE (SEE ABOVE)
            DL = NUMBER OF DRIVES
            DH = MAX. NUMBER OF SIDES
            CL = MAX. NUMBER OF SECTORS
            CH = MAX. NUMBER OF TRACKS
 -----------------------------------------------------------
 INT 13 - INITIAL TWO FIXED DISK BASE TABLES (PC/AT ONLY)
     REG AH = 9
     ON RETURN:
            CF = SUCCESS/FAILURE FLAG
        REG AH = STATUS CODE (SEE ABOVE)
        INTERRUPT 41 POINTS TO TABLE FOR DRIVE 0
        INTERRUPT 46 POINTS TO TABLE FOR DRIVE 1
 -----------------------------------------------------------
 INT 13 - READ LONG (PC/AT ONLY)
     REG AH = 0AH
         DL = DRIVE ID
         DH = HEAD NUMBER
         CH = CYLINDER NUMBER
         CL = SECTOR NUMBER
         ES:BX = POINTER TO BUFFER
     ON RETURN:
            CF = SUCCESS/FAILURE FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - WRITE LONG (PC/AT ONLY)
     REG AH = 0BH
         DL = DRIVE ID
         DH = HEAD NUMBER
         CH = SECTOR NUMBER
         ES:BX = POINTER TO BUFFER
     ON RETURN:
            CF = SUCCESS/FAILURE FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - SEEK TO CYLINDER (PC/AT ONLY)
     REG AH = 0CH
         DL = DRIVE ID
         DH = HEAD NUMBER
         CH = SECTOR NUMBER
     ON RETURN:
            CF = SUCCESS/FAILURE FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - ATLERNATE DISK RESET (PC/AT ONLY)
     REG AH = 0DH
         DL = DRIVE ID
     ON RETURN:
            CF = SUCCESS/FAIL FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - TEST FOR DRIVE READY (PC/AT ONLY)
     REG AH = 10H
         DL = DRIVE ID
     ON RETURN:
            CF = SUCCESS/FAIL FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - RECALIBRATE DRIVE (PC/AT ONLY)
     REG AH = 11H
         DL = DRIVE ID
     ON RETURN:
            CF = SUCCESS/FAIL FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - CONTROLLER DIAGNOSTICS (PC/AT ONLY)
     REG AH = 14H
     ON RETURN:
            CF = SUCCESS/FAIL FLAG
        REG AH = STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 13 - GET DISK TYPE (PC/AT ONLY)
     REG AH = 15H
         DL = DRIVE ID
     ON RETURN:
        REG AH = DISK TYPE
                 0 = DISK NOT THERE
                 1 = DISKETTE, NO CHANGE DETECTION PRESENT
                 2 = DISKETTE, CHANGE DETECTION PRESENT
                 3 = FIXED DISK
            CX,DX = NUMBER OF 512-BYTE SECTORS WHEN AH = 3
 -----------------------------------------------------------
 INT 13 - CHANGE OF DISK STATUS (PC/AT ONLY)
     REG AH = 16H
     ON RETURN:
        REG DL = DRIVE THAT HAD DISK CHANGE
            AH = DISK CHANGE STATUS
                 00 = NO DISK CHANGE
                 01 = DISK CHANGED
 -----------------------------------------------------------
 INT 13 - SET DISK TYPE (PC/AT ONLY)
     REG AH = 17H
         AL = DISK TYPE
              00 = NO DISK
              01 = REGULAR DISKETTE IN REGULAR DRIVE
              02 = HIGH-CAP. DISK IN HIGH-CAP. DRIVE
 -----------------------------------------------------------
 INT 14 - SERIAL I/O - INITIALIZE USART
    REG AH = 0
    REG AL = INITIALIZING PARAMETERS
    BIT  7 - 6 - 5 4 - 3  2    1 - 0
   -BAUD RATE-    PARITY  STOP    WORD
            BITS  LENGTH
   000  110 BD    00 NONE 0-1   10 - 7
   001  150 BD    01 ODD 1-2   11 - 8
   010  300 BD    11 EVEN
   011  600 BD
   100 1200 BD
   101 2400 BD
   110 4800 BD
   111 9600 BD (4800 ON PCjr)
        DX = PORT NUMBER
 -----------------------------------------------------------
 INT 14 - SERIAL I/O - TRANSMIT CHARACTER
    REG AH = 1
        AL = CHARACTER
        DX = PORT NUMBER
    ON RETURN:
       REG AH = RS-232 STATUS CODE
            BIT 0 = DATA READY
                1 = OVERRUN ERROR
                2 = PARITY ERROR
                3 = FRAMING ERROR
                4 = BREAK DETECTED
                5 = TRANSMISSION BUFFER REG. EMPTY
                6 = TRANSMISSION SHIFT REG. EMPTY
                7 = TIME OUT
           AL = MODEM STATUS
            BIT 0 = DELTA CLEAR-TO-SEND
                1 = DELTA DATA-SET-READY
                2 = TRAILING EDGE RING DETECTED
                3 = CHANGE, RECEIVE LINE SIGNAL DETECTED
                4 = CLEAR-TO-SEND
                5 = DATA-SET-READY
                6 = RING DETECTED
                7 = RECEIVE LINE SIGNAL DETECTED
 -----------------------------------------------------------
 INT 14 - SERIAL I/O - RECEIVE CHARACTER
    REG AH = 2
    ON RETURN:
       REG AL = CHARACTER RECEIVED
       REG AH = RS-232 STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 14 - SERIAL I/O - GET USART STATUS
    REG AH = 3
    ON RETURN:
       REG AH = RS-232 STATUS CODE (SEE ABOVE)
       REG AL = MODEM STATUS CODE (SEE ABOVE)
 -----------------------------------------------------------
 INT 15 - TURN ON CASSETTE MOTOR
    REG AH = 0
 -----------------------------------------------------------
 INT 15 - TURN OFF CASSETTE MOTOR
    REG AH = 1
 -----------------------------------------------------------
 INT 15 - READ DATA BLOCKS FROM CASSETTE
    REG AH = 2
        CX = COUNT OF BYTES
        ES:BX = POINTER TO DATA AREA
    ON RETURN:
            CF = ERROR SIGNAL
        REG DX = COUNT OF BYTES READ
            ES:BX = POINTER PAST LAST BYTE READ
 -----------------------------------------------------------
 INT 15 - WRITE DATA BLOCKS TO CASSETTE
    REG AH = 3
        CX = COUNT OF BYTES TO WRITE
        ES:BX = POINTER TO DATA AREA
    ON RETURN:
        REG ES:BX = POINTER PAST LAST BYTE WRITTEN
 -----------------------------------------------------------
 INT 15 - DEVICE OPEN (PC/AT ONLY)
    REG AH = 80
        BX = DEVICE ID
        CX = PROCESS TYPE
 -----------------------------------------------------------
 INT 15 - DEVICE CLOSE (PC/AT ONLY)
    REG AH = 81
        BX = DEVICE ID
        CX = PROCESS TYPE
 -----------------------------------------------------------
 INT 15 - DEVICE PROGRAM TERMINATE (PC/AT ONLY)
    REG AH = 82
        BX = DEVICE ID
 -----------------------------------------------------------
 INT 15 - EVENT WAIT (PC/AT ONLY)
    REG AH = 83
        AL = SUBSERVICE
             0 = SET INTERVAL
             1 = CANCEL
        ES:BX = POINTER TO CALLER'S MEMORY
        CX,DX = NUMBER OF MICROSECONDS TO WAIT
 -----------------------------------------------------------
 INT 15 - READ JOYSTICK SWITCH SETTINGS (PC/AT ONLY)
    REG AH = 84
        DX = 0
    ON RETURN:
        REG AL = SWITCH SETTINGS
 -----------------------------------------------------------
 INT 15 - READ JOYSTICK INPUTS (PC/AT ONLY)
    REG AH = 84
        DX = 1
    ON RETURN:
        REG AX = A(x) VALUE
            BX = A(y) VALUE
            CX = B(x) VALUE
            DX = B(y) VALUE
 -----------------------------------------------------------
 INT 15 - SYSTEM REQUEST KEY PRESS (PC/AT ONLY)
    REG AH = 85
        AL = 00 PRESS
        AL = 01 BREAK
 -----------------------------------------------------------
 INT 15 - WAIT (PC/AT ONLY)
    REG AH = 86
        CX,DX = NUMBER OF MICROSECONDS TO WAIT
 -----------------------------------------------------------
 INT 15 - EXTENDED MEMORY - BLOCK MOVE  (PC/AT ONLY)
    REG AH = 87
        CX = NUMBER OF WORDS TO MOVE
        ES:SI = POINTER TO TABLE
 -----------------------------------------------------------
 INT 15 - EXTENDED MEMORY - GET MEMORY SIZE     (PC/AT ONLY)
    REG AH = 88
    ON RETURN:
       REG AX = MEMORY SIZE
 -----------------------------------------------------------
 INT 15 - SWITCH TO VIRTUAL MODE (PC/AT ONLY)
    REG AH = 89
 -----------------------------------------------------------
 INT 15 - DEVICE BUSY LOOP (PC/AT ONLY)
    REG AH = 90
        AL = TYPE CODE
 -----------------------------------------------------------
 INT 15 - SET FLAG AND COMPLETE INTERRUPT
    REG AH = 91
        AL = TYPE CODE
 -----------------------------------------------------------
 INT 16 - KEYBOARD I/O - READ CHAR FROM BUFFER - WAIT IF EMPTY
    REG AH = 0
    ON RETURN:
       REG AH = SCAN CODE
       REG AL = CHARACTER
 -----------------------------------------------------------
 INT 16 - KEYBOARD I/O - CHECK BUFFER - DO NOT CLEAR
    REG AH = 1
    ON RETURN:
       FLAG ZF = 0 = CHAR IN BUFFER
       REG AH = SCAN CODE
       REG AL = CHARACTER
       FLAG ZF = 1 = NO CHAR IN BUFFER
 -----------------------------------------------------------
 INT 16 - KEYBOARD I/O - GET SHIFT STATUS
    REG AH = 2
    ON RETURN:
        REG AL = SHIFT STATUS BITS
             BIT 0 = RIGHT SHIFT KEY DEPRESSED
                 1 = LEFT SHIFT KEY DEPRESSED
                 2 = CTRL DEPRESSED
                 3 = ALT DEPRESSED
                 4 = SCROLL LOCK ACTIVE
                 5 = NUM LOCK ACTIVE
                 6 = CAPS LOCK ACTIVE
                 7 = INSERT STATE ACTIVE
 -----------------------------------------------------------
 INT 16 - KEYBOARD - SET DELAYS (PCjr ONLY)
    REG AH = 3
        AL = 0: RESET TYPEMATIC
        AL = 1: INCREASE INITIAL DELAY
        AL = 2: INCREASE CONTINUING DELAY
        AL = 3: INCREASE BOTH DELAYS
        AL = 4: TURN OFF TYPEMATIC
 -----------------------------------------------------------
 INT 16 - KEYBOARD - KEYCLICK (PCjr ONLY)
    REG AH = 4
        AL = 0: CLICK OFF
        AL = 1: CLICK ON
 -----------------------------------------------------------
 INT 17 - CHARACTER TO PRINTER
    REG AH = 0
    REG AL = CHAR
    ON RETURN:
       REG AH = STATUS
            BIT 0 = TIME OUT
                1 = UNUSED
                2 = UNUSED
                3 = I/O ERROR
                4 = SELECTED
                5 = OUT OF PAPER
                6 = ACKNOWLEDGE
                7 = NOT BUSY
 -----------------------------------------------------------
 INT 17 - INITIALIZE PRINTER
    REG AH = 1
    ON RETURN:
       REG AH = STATUS (SEE ABOVE)
 -----------------------------------------------------------
 INT 17 - STATUS OF PRINTER
    REG AH = 2
    ON RETURN:
       REG AH = STATUS (SEE ABOVE)
 -----------------------------------------------------------
 INT 18 - TRANSFER TO ROM BASIC
    CAUSES TRANSFER TO ROM-BASED BASIC (IBM-PC)
    OFTEN REBOOTS A COMPATABLE
 -----------------------------------------------------------
 INT 19 - DISK BOOT
    CAUSES REBOOT OF DISK SYSTEM (NO MEMORY TEST PERFORMED).
 -----------------------------------------------------------
 INT 1A - GET TIME OF DAY
    REG AH = 0
    ON RETURN:
       REG CX = high (most signif.) portion of clock count
           DX = low (least signif.) portion of clock count
           AL = 0 if clock was read or written (via AH=0,1)
                withing the current 24-hour period
                Otherwise, AL > 0
 -----------------------------------------------------------
 INT 1A - SET TIME OF DAY
    REG AH = 1
        CX = high (most signif.) portion of clock count
        DX = low (least signif.) portion of clock count
 -----------------------------------------------------------
 INT 1A - READ REAL TIME CLOCK (PC/AT ONLY)
    REG AH = 2
    ON RETURN:
        REG CH = HOURS
            CL = MINUTES
            DH = SECONDS
 -----------------------------------------------------------
 INT 1A - SET REAL TIME CLOCK (PC/AT ONLY)
    REG AH = 3
        CH = HOURS
        CL = MINUTES
        DH = SECONDS
        DL = 1, IF DAYLIGHT SAVINGS; 0 IF STANDARD TIME
 -----------------------------------------------------------
 INT 1A - READ DATE FROM REAL TIME CLOCK (PC/AT ONLY)
    REG AH = 4
    ON RETURN:
        REG DL = DAY
            DH = MONTH
            CL = YEAR
            CH = CENTURY (19 OR 20)
 -----------------------------------------------------------
 INT 1A - SET DATE IN REAL TIME CLOCK (PC/AT ONLY)
    REG AH = 5
        DL = DAY
        DH = MONTH
        CL = YEAR
        CH = CENTURY (19 OR 20)
 -----------------------------------------------------------
 INT 1A - SET ALARM (PC/AT ONLY)
    REG AH = 6
        CH = HOURS
        CL = MINUTES
        DH = SECONDS
    ON RETURN:
        INT. 4A = ADDRESS OF ALARM ROUTINE
 -----------------------------------------------------------
 INT 1A - RESET ALARM (PC/AT ONLY)
    REG AH = 7
 -----------------------------------------------------------
 INT 1B - CTRL-BREAK KEY (on IBM at least)
  This interrupt is called when the keyboard scanner of
 the IBM machines detects CTRL and BREAK pressed at the same
 time. It normally points to a simple IRET so that it does
 nothing, but many programs change it to return a CTRL-C scan
 code and thus invoke INT 23.
 -----------------------------------------------------------
 INT 1C - CLOCK TICK (on IBM at least)
  This interrupt is called (in the IBM) at the end of
 each time-update operation by the real-time clock routines. It
 normally points to an IRET unless PRINT.COM has been installed.
 -----------------------------------------------------------
 INT 20 - PROGRAM TERMINATION (MSDOS generic)
    NOTE:     NO PARAMETERS - RETURNS TO DOS
 -----------------------------------------------------------
 INT 21 - PROGRAM TERMINATION (MSDOS generic)
    Reg AH = 0
    Same action as INT 20; returns to DOS.
 -----------------------------------------------------------
 INT 21 - KEYBOARD INPUT (MSDOS generic)
    REG AH = 1
    ON RETURN:
        REG AL = CHARACTER READ
 -----------------------------------------------------------
 INT 21 - DISPLAY OUTPUT (MSDOS generic)
    REG AH = 2
    REG DL = CHAR
 -----------------------------------------------------------
 INT 21 - AUX Input (MSDOS generic)
    Reg AH = 3
    Return with char in reg AL.
       NOTE - Waits for char, gives no error
          indications.
 -----------------------------------------------------------
 INT 21 - AUX Output (MSDOS generic)
    Reg AH = 4
    Reg DL = char to send to AUX
       No error indications!!
 -----------------------------------------------------------
 INT 21 - PRINTER OUTPUT (MSDOS generic)
    REG AH = 5
    REG DL = CHAR
 -----------------------------------------------------------
 INT 21 - DIRECT CONSOLE I/O - CHARACTER OUTPUT (MSDOS generic)
    REG AH = 06H
    REG DL = CHAR
 -----------------------------------------------------------
 INT 21 - DIRECT CONSOLE I/O - CHARACTER INPUT (MSDOS generic)
    REG AH = 06H
    REG DL = 0FFH
    ON RETURN:
       FLAG ZF = SET    = NO CHARACTER
     CLEAR  = CHARACTER RECIEVED
     REG AL = CHARACTER
    Character is echoed to STDOUT if received.
 -----------------------------------------------------------
 INT 21 - Direct STDIN Input, no echo (MSDOS generic)
    Reg AH = 7
    Same as Function 6 for input but char not echoed.
 -----------------------------------------------------------
 INT 21 - KEYBOARD INPUT - NO ECHO (MSDOS generic)
    REG AH = 8
    ON RETURN:
       REG AL = CHAR
 -----------------------------------------------------------
 INT 21 - PRINT STRING (MSDOS generic)
    REG AH = 9
    DS:DX  = ADDRESS OF STRING
    NOTE:      STRING TERMINATED WITH "$"
 -----------------------------------------------------------
 INT 21 - BUFFERED KEYBOARD INPUT (MSDOS generic)
    REG AH = 0AH
    DS:DX  = ADDRESS OF BUFFER
    FIRST BYTE OF BUFFER MUST HAVE MAX LENGTH
    ON RETURN SECOND BYTE HAS ACTUAL LENGTH
 -----------------------------------------------------------
 INT 21 - CHECK STANDARD INPUT STATUS (MSDOS generic)
    REG AH = 0BH
    ON RETURN:
       REG AL = FFH IF CHAR TYPED
                00H IF NOT TYPED
 -----------------------------------------------------------
 INT 21 - Clear Keyboard Buffer (MSDOS generic)
    Reg AH = 0CH
    Reg AL must be 1, 6, 7, 8, or 0aH.
       Flushes all typeahead input, then executes
 function specified by AL (by moving it to AH and repeating the
 INT 21 call).
 -----------------------------------------------------------
 INT 21 - Disk Reset (MSDOS generic)
    Reg AH = 0DH
    Flushes all disk buffers.
 -----------------------------------------------------------
 INT 21 - SELECT DISK (MSDOS generic)
    REG AH = 0EH
    REG DL = new default drive number (0 = A, 1 = B, etc.)
    ON RETURN:
       AL = number of logical drives
 -----------------------------------------------------------
 INT 21 - OPEN DISK FILE (MSDOS generic)
    REG AH = 0FH
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 00 = FILE FOUND
                FF = FILE NOT FOUND
 -----------------------------------------------------------
 INT 21 - CLOSE DISK FILE (MSDOS generic)
    REG AH = 10H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
 -----------------------------------------------------------
 INT 21 - Search First using FCB (MSDOS generic)
    REG AH = 11H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    FCB may contain wildcard chars.
    On Return:
       REG AL = 00 = FILE FOUND
                FF = FILE NOT FOUND
    If file found, FCB is created at DTA address and
    set up to OPEN or DELETE it.
 -----------------------------------------------------------
 INT 21 - Search Next using FCB (MSDOS generic)
    REG AH = 12H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    Search First must have been called earlier.
    On Return:
       Same as Search First; if AL = 0ffH, no more
 left.
 -----------------------------------------------------------
 INT 21 - Delete File via FCB (MSDOS generic)
    REG AH = 13H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    On Return:
       REG AL = 00 = FILE FOUND
                FF = FILE NOT FOUND
 -----------------------------------------------------------
 INT 21 - SEQUENTIAL DISK FILE READ (MSDOS generic)
    REG AH = 14H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 0 = SUCCESSFUL READ
                1 = END OF FILE
                2 = DATA TRANSFER AREA TOO SMALL
                3 = PARTIAL RECORD, EOF
 -----------------------------------------------------------
 INT 21 - SEQUENTIAL DISK RECORD WRITE (MSDOS generic)
    REG AH = 15H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 0 = SUCCESSFUL WRITE
                1 = DISKETTE FULL
                2 = DATA TRANSFER AREA TOO SMALL
 -----------------------------------------------------------
 INT 21 - CREATE A DISK FILE (MSDOS generic)
    REG AH = 16H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 00 = SUCCESSFUL CREATION
                FF = NO ROOM IN DIRECTORY
 -----------------------------------------------------------
 INT 21 - Rename File via FCB (MSDOS generic)
    REG AH = 17H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
       FCB contains new name starting at byte 17H.
    On Return:
       REG AL = 00 = FILE FOUND
                FF = FILE NOT FOUND
 -----------------------------------------------------------
 INT 21 - Internal - does nothing (MSDOS generic)
    REG AH = 18H
    On Return:
        AL = 0
 -----------------------------------------------------------
 INT 21 - Default Disk Number (MSDOS generic)
    REG AH = 19H
    On Return:
        AL = current drive number (letter - 'A')
 -----------------------------------------------------------
 INT 21 - SET DISK TRANSFER AREA ADDRESS (MSDOS generic)
    REG AH = 1AH
    REG DS = SEGMENT ADDRESS OF BUFFER
    REG DX = OFFSET ADDRESS OF BUFFER
    ON RETURN:
       Registers are unchanged, no error codes
 -----------------------------------------------------------
 INT 21 - Default Drive Disk Size (MSDOS generic)
    REG AH = 1BH
    On Return:
       DS:BX points to FAT ID byte
       DX = number of allocation units on disk
       AL = number of sectors per AU
       CX = number of bytes per sector
 -----------------------------------------------------------
 INT 21 - Specific Drive's Disk Size (MSDOS generic)
    REG AH = 1CH
    Reg DL = Drive Number to check
    On Return:
       DS:BX points to FAT ID byte
       DX = number of allocation units on disk
       AL = number of sectors per AU
       CX = number of bytes per sector
 -----------------------------------------------------------
 INT 21 - Internal - does nothing (MSDOS generic)
    REG AH = 1DH
    On Return:
       AL = 0
 -----------------------------------------------------------
 INT 21 - Internal - does nothing (MSDOS generic)
    REG AH = 1EH
    On Return:
       AL = 0
 -----------------------------------------------------------
 INT 21 - GET DEFAULT DRIVE PARAMETER BLOCK (MSDOS generic, undoc.)
    REG AH = 1FH
    On return:
       REG AL = 00 = No Error
                FF = Error
           (DS:BX) = ADDRESS OF DRIVE PARAMETER BLOCK.
        (THIS JUST INVOKES FUNCTION 32H WITH DL = 0)
 -----------------------------------------------------------
 INT 21 - Internal - does nothing (MSDOS generic)
    REG AH = 20H
    On Return:
       AL = 0
 -----------------------------------------------------------
 INT 21 - RANDOM DISK RECORD READ (MSDOS generic)
    REG AH = 21H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 0 = SUCCESSFUL READ
                1 = END OF FILE
                2 = DATA TRANSFER AREA TOO SMALL
                3 = PARTIAL RECORD, EOF
 -----------------------------------------------------------
 INT 21 - Random Disk Write (MSDOS generic)
    REG AH = 22H
    Same setup as Random Read, but writes to disk
 -----------------------------------------------------------
 INT 21 - FILE SIZE (MSDOS generic)
    REG AH = 23H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    ON RETURN:
       REG AL = 00 = FILE FOUND
                FF = FILE NOT FOUND
       FCB SET TO NO. OF RECORDS
 -----------------------------------------------------------
 INT 21 - Set Random Record Field (MSDOS generic)
    REG AH = 24H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    FCB must be OPEN already
    On Return:
       Random Record Field of FCB is set to be
       same as Current Block and Current Record.
    No error code is returned.
 -----------------------------------------------------------
 INT 21 - Set Interrupt Vector (MSDOS generic)
    REG AH = 25H
    Reg AL = INT number
    DS:DX = new vector to be used for specified INT
    On Return:
       Registers are unchanged; no error codes
 -----------------------------------------------------------
 INT 21 - Create PSP (MSDOS generic)
    REG AH = 26H
    Reg DX = Segment number to set up PSP at
    On Return:
       Current PSP is copied to specified segment
 -----------------------------------------------------------
 INT 21 - RANDOM BLOCK READ (MSDOS generic)
    REG AH = 27H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    REG CX = NO. OF RECORDS TO BE READ
    ON RETURN:
       REG AL = 0 = SUCCESSFUL READ
                1 = END OF FILE
                2 = DATA TRANSFER AREA TOO SMALL
                3 = PARTIAL RECORD, EOF
 -----------------------------------------------------------
 INT 21 - RANDOM BLOCK WRITE (MSDOS generic)
    REG AH = 28H
    REG DS = SEGMENT ADDRESS OF FCB
    REG DX = OFFSET ADDRESS OF FCB
    REG CX = NO. OF RECORDS TO BE WRITTEN
    ON RETURN:
       REG AL = 0 = SUCCESSFUL WRITE
                1 = DISKETTE FULL
                2 = DATA TRANSFER AREA TOO SMALL
 -----------------------------------------------------------
 INT 21 - Parse Filename (MSDOS generic)
    REG AH = 29H
        DS:SI = POINTER TO STRING TO PARSE
        ES:DI = POINTER TO MEMORY TO FILL WITH UNOPENED FCB
        AL = BIT MASK TO CONTROL PARSING
            BIT 0 = 0: PARSING STOPS IF FILE SEPERATOR FOUND
                    1: LEADING SEPERATOR IGNORED
                1 = 0: DRIVE NUMNER IN FCB SET TO DEFAULT IF
                        STRING CONTAINS NO DRIVE NUMBER
                    1: DRIVE NUMBER IN FCB NOT CHANGED
                2 = 0: FILENAME IN FCB SET TO BLANKS IF NO
                        FILENAME IN STRING
                    1: FILENAME IN FCB NOT CHANGED IF STRING
                        DOES NOT CONTAIN A FILENAME
                3 = 0: EXTENSION IN FCB SET TO BLANKS IF NO
                        EXTENSION IN STRING
                    1: EXTENSION LEFT UNCHANGED
    ON RETURN:
        REG AL = 00: NO WILDCARDS IN NAME OR EXTENSION
                 01: WILDCARDS APPEARED IN NAME OR EXTENSION
            DS:SI = POINTER TO FIRST BYTE AFTER PARSED STRING
            ES:DI = UNOPENED FCB
 -----------------------------------------------------------
 INT 21 - GET CURRENT DATE (MSDOS generic)
    REG AH = 2AH
    ON RETURN:
       REG DL = DAY
       REG DH = MONTH
       REG CX = YEAR
       REG AL = DAY OF THE WEEK (0=SUNDAY, 1=MONDAY, ETC.)
 -----------------------------------------------------------
 INT 21 - Set CURRENT DATE (MSDOS generic)
    REG AH = 2bH
    REG DL = DAY
    REG DH = MONTH
    REG CX = YEAR
    On Return:
       AL = 0 if no error
       AL = 0ffH if bad value sent to routine
 -----------------------------------------------------------
 INT 21 - GET CURRENT TIME (MSDOS generic)
    REG AH = 2CH
    ON RETURN:
       REG CH = HOURS
       REG CL = MINUTES
       REG DH = SEC
       REG DL = SEC/100
    NOTE: TIME IS UPDATED EVERY 5/100 SECOND
 -----------------------------------------------------------
 INT 21 - Set CURRENT TIME (MSDOS generic)
    REG AH = 2DH
    REG CH = HOURS
    REG CL = MINUTES
    REG DH = SEC
    REG DL = SEC/100
    On Return:
       AL = 0 if no error
       AL = 0ffH if bad value sent to routine
 -----------------------------------------------------------
 INT 21 - Set Verify Flag (MSDOS generic)
    REG AH = 2EH
        DL = 0
        AL = 1 if VERIFY on
        AL = 0 if VERIFY off
 -----------------------------------------------------------
 INT 21 - Get Disk Transfer Area Address (MSDOS generic)
    REG AH = 2FH
    On Return:
       Reg ES = SEGMENT address of DTA
       Reg BX = OFFSET address of DTA
 -----------------------------------------------------------
 INT 21 - Get DOS Version (MSDOS generic)
    REG AH = 30H
    On Return:
       Reg AL = Major Version number
       Reg AH = Minor Version number
                (i.e., DOS 2.10 returns AX = 0A02H)
       Reg BH = OEM number
       Reg BL:CX = 24-bit user number
 -----------------------------------------------------------
 INT 21 - TERMINATE BUT STAY RESIDENT (MSDOS generic)
    REG AH = 31H
    REG AL = EXIT CODE
    REG DX = PROGRAM SIZE, IN PARAGRAPHS
        ADDRESS IN HEX - XX XX 0 -
    ON RETURN:
        REG AX = RETURN CODE (RETRIEVEABLE BY FUNCTION 4DH)
 -----------------------------------------------------------
 INT 21 - GET DRIVE PARAMETER BLOCK (MSDOS generic, undocumented)
    REG AH = 32H
        DL = DRIVE NUMBER
                0 = DEFAULT, 1 = A, ETC.
    ON RETURN:
        REG AL = 0FFH IF INVALID DRIVE NUMBER, ELSE
            DS:BX = ADDRESS OF DRIVE PARAMETER BLOCK.

                STRUCTURE OF DOS DRIVE PARAMETER BLOCK:

DPBLOCK         STRUCT          ;OFFSET
DISK_OFFSET     DB      ?       ;  0.  DRIVE NUMBER (0 = A, ETC.)
UNIT_OFFSET     DB      ?       ;  1.  UNIT NUMBER WITHIN DEVICE DRIVER
SECTOR_SIZE     DW      ?       ;  2.  NUMBER OF BYTES PER SECTOR
MAX_CLUSTER     DB      ?       ;  4.  LARGEST SECTOR NUMBER IN CLUSTER
                                ;      ADD ONE FOR NUMBER OF SECTORS/CLUSTER
LOG2_SECTORS    DB      ?       ;  5.  LOG BASE TWO OF THE CLUSTER SIZE
RESERVED        DW      ?       ;  6.  NUMBER OF RESERVED (BOOT) SECTORS
FAT_COUNT       DB      ?       ;  8.  NUMBER OF COPIES OF THE FAT
ROOT_COUNT      DW      ?       ;  9.  NUMBER OF ROOT DIRECTORY ENTRIES
DATA_START      DW      ?       ; 11.  FIRST SECTOR OF DATA ON MEDIUM
MAX_NUMBER      DW      ?       ; 13.  LARGEST POSSIBLE CLUSTER NUMBER
                                ;      SUBTRACT ONE FOR NUMBER OF CLUSTERS
FAT_SECTORS     DB      ?       ; 15.  NUMBER OF SECTORS IN ONE FAT COPY
ROOT_START      DW      ?       ; 16.  FIRST SECTOR OF ROOT DIRECTORY
DEVICE_ADDR     DD      ?       ; 18.  CORRESPONDING DEVICE DRIVER ADDRESS
DESCRIPTOR      DB      ?       ; 22.  MEDIA DESCRIPTOR BYTE FOR MEDIUM
VALID_BYTE      DB      ?       ; 23.  0FFH INDICATES BLOCK MUST BE REBUILT
NEXT_BLOCK      DD      ?       ; 24.  ADDRESS OF NEXT DEVICE BLOCK IN LIST

;       FROM THIS POINT ON, DOS 3 DIFFERS FROM 2:

                IF      DOS2
DIR_START       DW      ?       ; 28.  STARTING CLUSTER OF CURRENT DIRECTORY
                                ;      ZERO INDICATES THE ROOT DIRECTORY
PATH_NAME       DB      64 DUP (?)
                                ; 30.  ASCIIZ CURRENT DIRECTORY PATH STRING
                ELSE    DOS3
;               ON MY XT, THIS WAS ALWAYS:
                DW      0
                DW      0FFFFH
                ENDIF
DPBLOCK         ENDS
 -----------------------------------------------------------
 INT 21 - Get or Set CONTROL-BREAK (MSDOS generic)
    REG AH = 33H
    Reg AL = 0 for Get or 1 for Put
    Reg DL = 0 for OFF or 1 for ON
    On Return:
        DL = 0 if BREAK=OFF or 1 if BREAK=ON
        AL = FFH IF ERROR
 -----------------------------------------------------------
 INT 21 - Internal - Return CritSectFlag Pointer (MSDOS generic)
    REG AH = 34H
    On Return:
       ES:BX points to DOS "Critical Section Flag"
    When byte pointed to is zero, DOS is supposed to be
    safe to interrupt. NOT RELIABLE according to Chris
    Dunford.
       Examination of DOS 2.10 code in this area
    indicates that the byte immediately FOLLOWING this
    "Critical Section Flag" must be 00 to permit the
    PRINT.COM interrupt to be called. This suggests that
    checking the WORD pointed to, rather than the BYTE,
    might increase reliability of the test greatly.
 -----------------------------------------------------------
 INT 21 - Get Interrupt Vector (MSDOS generic)
    REG AH = 35H
    Reg AL = INT number
    On Return:
       Reg ES = Segment address of INT vector
       Reg BX = Offset address of INT vector
 -----------------------------------------------------------
 INT 21 - DISK SPACE (MSDOS generic)
    REG AH = 36H
    REG DL = DRIVE NUMBER (1-4)
    ON RETURN:
       REG AX = ? (SIDES)
       REG BX = ? (BLOCKS FREE)
       REG CX = ? (BLOCK SIZE)
       REG DX = ? (TOTAL BLOCKS)
    NOTE: MULT AX x CX x BX for FREE SPACE ON DISK
   MULT AX x CX x DX for TOTAL DISK SPACE
 -----------------------------------------------------------
 INT 21 - Internal - multifunction (MSDOS generic)
        AH=37h
        AL=0    Read switch character (returns current character in DL)
           1    Set switch character (specify new character in DL)
           2    Read device availability (as set by function AL=3)
           3    Set device availability, where:
                DL=0 means /DEV/ must preceed device names
                DL#0 means /DEV/ need not preceed device names

        Returns:

        DL =    Switch character (if AL=0 or 1)
                Device availability flag (if AL=2 or 3)

        Error return:

        AL=0FFh means the value in AL was not in the range 0-3.

        Note:

        Functions 2 & 3 appear not to be implemented for dos 3.x
 -----------------------------------------------------------
 INT 21 - Get Country-Dependent Information (MSDOS generic)
    REG AH = 38H
    Complex and differs between Dos 2.x and Dos 3.x
    See Peter Norton "Programmer's Guide to the IBM PC", p. 305
 -----------------------------------------------------------
 INT 21 - CREATE A SUBDIRECTORY (MSDOS generic)
    REG AH = 39H
    Reg DS = SEGMENT address of ASCIIZ pathname
    Reg DX = OFFSET address of ASCIIZ pathname
    On Return:
       Flag CF = 0 = SUCCESSFUL
                 1 = ERROR
       Reg AX = Error Code if any
 -----------------------------------------------------------
 INT 21 - REMOVE A DIRECTORY ENTRY (MSDOS generic)
    REG AH = 3AH
    Reg DS = SEGMENT address of ASCIIZ pathname
    Reg DX = OFFSET address of ASCIIZ pathname
    On Return:
       Flag CF = 0 = SUCCESSFUL
                 1 = ERROR
       Reg AX = Error Code if any
 -----------------------------------------------------------
 INT 21 - CHANGE THE CURRENT DIRECTORY (MSDOS generic)
    REG AH = 3BH
    Reg DS = SEGMENT address of ASCIIZ
    Reg DX = OFFSET address of ASCIIZ
    On Return:
       Flag CF = 0 = SUCCESSFUL
                 1 = ERROR
       Reg AX = Error Code if any
 -----------------------------------------------------------
 INT 21 - CREATE A FILE WITH HANDLE (MSDOS generic)
    REG AH = 3CH
    REG CX = ATTRIBUTES FOR FILE
    REG DS = SEGMENT ADDRESS OF ASCIIZ
    REG DX = OFFSET ADDRESS OF ASCIIZ
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL CREATION
                 1 = ERROR
       REG AX = FILE HANDLE
         OR ERROR CODE
 -----------------------------------------------------------
 INT 21 - OPEN DISK FILE WITH HANDLE (MSDOS generic)
    REG AH = 3DH
    REG AL = ACCESS CODE
       0 = Read Only
       1 = Write Only
       2 = Read/Write
    REG DS = SEGMENT ADDRESS OF ASCIIZ
    REG DX = OFFSET ADDRESS OF ASCIIZ
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL OPENING
                 1 = ERROR
       REG AX  = FILE HANDLE
     OR ERROR CODE
 -----------------------------------------------------------
 INT 21 - CLOSE A FILE WITH HANDLE (MSDOS generic)
    REG AH = 3EH
    REG BX = FILE HANDLE
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL CLOSE
                 1 = ERROR
       REG AX  = ERROR CODE IF ERROR
 -----------------------------------------------------------
 INT 21 - READ FROM FILE WITH HANDLE (MSDOS generic)
    REG AH = 3FH
    REG BX = FILE HANDLE
    REG CX = NO. OF BYTES TO READ
    REG DS = SEGMENT ADDRESS OF BUFFER
    REG DX = OFFSET ADDRESS OF BUFFER
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL READ
                 1 = ERROR
       REG AX = 0 = END OF FILE
        OR NO. OF BYTES READ
        OR ERROR CODE
 -----------------------------------------------------------
 INT 21 - WRITE TO FILE WITH HANDLE (MSDOS generic)
    REG AH = 40H
    REG BX = FILE HANDLE
    REG CX = NO. OF BYTES TO Write
    REG DS = SEGMENT ADDRESS OF BUFFER
    REG DX = OFFSET ADDRESS OF BUFFER
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL WRITE
                 1 = ERROR
       REG AX =  NO. OF BYTES Writtten
     OR ERROR CODE
 -----------------------------------------------------------
 INT 21 - DELETE A FILE (MSDOS generic)
    REG AH = 41H
    REG DS = SEGMENT OF ASCIIZ TO DELETE
    REG DX = OFFSET OF ASCIIZ TO DELETE
    On Return:
       Flag CF = 0 = SUCCESSFUL
                 1 = ERROR
       Reg AX = Error Code if any
 -----------------------------------------------------------
 INT 21 - MOVE FILE READ/WRITE POINTER (MSDOS generic)
    REG AH = 42H
    REG AL = METHOD VALUE
       0 = offset from beginning of file
       1 = offset from present location
       2 = offset from end of file
    REG BX = FILE HANDLE
    REG CX = BYTES OFFSET HIGH
    REG DX = BYTES OFFSET LOW
    ON RETURN:
       FLAG CF = 0 = SUCCESSFUL MOVE
                 1 = ERROR
       REG DX = NEW LOC. OF R/W POINTER HIGH
       REG AX = NEW LOC. OF R/W POINTER LOW
           ERROR CODE IF ERROR
 -----------------------------------------------------------
 INT 21 - GET/PUT FILE ATTRIBUTES (MSDOS generic)
    REG AH = 43H
    REG AL = 0 = GET FILE ATTRIBUTES
             1 = PUT FILE ATTRIBUTES
    REG CX = FILE ATTRIBUTES ON PUT
            BIT 0 = READ ONLY
                1 = HIDDEN FILE
                2 = SYSTEM FILE
                3 = VOLUME LABEL
                4 = SUBDIRECTORY
                5 = WRITTEN SINCE BACKUP
    REG DX = POINTER TO FILE ASCIIZ FILE NAME
    ON RETURN:
       FLAG CF = SET IF ERROR
       REG AX = Error Code 1, 3, or 5
       REG CX = FILE ATTRIBUTES ON GET
 -----------------------------------------------------------
 INT 21 - IOCTL (MSDOS generic)
    REG AH = 44H
    Complex. See T2K manual pages 121-124
 -----------------------------------------------------------
 INT 21 - Create Duplicate Handle (MSDOS generic)
    REG AH = 45H
    Reg BX = file handle to duplicate
    On Return:
       If carry set, AX = Error Code
       If carry clear, AX = duplicate handle
 -----------------------------------------------------------
 INT 21 - Force Duplicate Handle (MSDOS generic)
    REG AH = 46H
    Reg BX = Existing file handle
    Reg CX = new file handle
    On Return:
       If CF set, AX = Error Code
       If clear, both handles now refer to
          Existing file
 -----------------------------------------------------------
 INT 21 - Get Current Directory (MSDOS generic)
    REG AH = 47H
    Reg DL = drive (0=default, 1=A, etc.)
    DS:SI points to 64-byte buffer area
    On Return:
       If CY set, AX = Error Code
       Else DS:DI points to ASCIIZ name of
    current directory (not including drive ID)
 -----------------------------------------------------------
 INT 21 - Allocate Memory (MSDOS generic)
    REG AH = 48H
    Reg BX = number of 16-byte paragraphs desired
    On Return:
       If CF set:
          BX = Maximum number available
       If CF clear:
          AX = Segment address of allocated space
 -----------------------------------------------------------
 INT 21 - Free Memory (MSDOS generic)
    REG AH = 49H
    Reg ES = Segment address of area to be freed
    On Return:
       If CF set, AX = Error Code
 -----------------------------------------------------------
 INT 21 - Adjust Block Size (MSDOS generic)
    REG AH = 4AH
    Reg ES = Segment address of block to change
    Reg BX = New size in paragraphs
    On Return:
       If CF set, BX = max number available
       Else operation was successful
 -----------------------------------------------------------
 INT 21 - Load or Execute (MSDOS generic)
    REG AH = 4BH
    Complex. See T2K manual pages 131-133
 -----------------------------------------------------------
 INT 21 - Quit With Exit Code (MSDOS generic)
    REG AH = 4CH
    Reg AL = exit code
    Does not return. Control passes to DOS
 -----------------------------------------------------------
 INT 21 - GET EXIT CODE OF SUBPROGRAM (MSDOS generic)
    REG AH = 4DH
    On Return:
        AL = exit code of subprogram (FNs 31H or 4cH)
        AH = circumstance which caused termination
                0 = Terminate/abort
                1 = Control-C
                2 = Hard error
                3 = Terminate and stay resident
 -----------------------------------------------------------
 INT 21 - Find First ASCIIZ (MSDOS generic)
    REG AH = 4EH
        CX = SEARCH ATTRIBUTES
        DS:DX = POINTER TO ASCIIZ FILENAME (WITH ATTRIBUTES)
    ON RETURN:
        IF CF SET, REG AX = ERROR CODE
             ELSE, DATA BLOCK WRITTEN AT CURRENT DTA
 -----------------------------------------------------------
 INT 21 - Find Next ASCIIZ (MSDOS generic)
    REG AH = 4FH
    ON RETURN:
        IF CF SET, AX = ERROR CODE
             ELSE, DATA BLOCK WRITTEN AT CURRENT DTA
 -----------------------------------------------------------
 INT 21 - Internal - Set PSP Segment (MSDOS generic)
    REG AH = 50H
    Reg BX = Segment address of new PSP
    On Return:
       No return codes
 -----------------------------------------------------------
 INT 21 - Internal - Get PSP Segment (MSDOS generic)
    REG AH = 51H
    On Return:
       BX = Current PSP Segment
 -----------------------------------------------------------
 INT 21 - Internal - Unknown (MSDOS generic)
    REG AH = 52H
    On Return:
       Unknown pointer in ES:BX
 -----------------------------------------------------------
 INT 21 - Internal - Unknown (MSDOS generic)
    REG AH = 53H
    On Return:
       Unknown
 -----------------------------------------------------------
 INT 21 - Get Verify Flag (MSDOS generic)
    REG AH = 54H
    On Return:
       AL = 0 if flag OFF
       AL = 1 if flag ON
 -----------------------------------------------------------
 INT 21 - Internal - Create PSP (MSDOS generic)
    REG AH = 55H
    Like FN 26H but creates "child" PSP rather
    than copying existing one.
 -----------------------------------------------------------
 INT 21 - RENAME A FILE (MSDOS generic)
    REG AH = 56H
    REG DS = SEGMENT OF ASCIIZ OLD NAME
    REG DX = OFFSET OF ASCIIZ OLD NAME
    REG ES = SEGMENT OF ASCIIZ NEW NAME
    REG DI = OFFSET OF ASCIIZ NEW NAME
    ON RETURN:
       FLAG CF = CLEARED = SUCCESSFULL RENAME
     SET = ERROR &
     REG AX = ERROR CODE
 -----------------------------------------------------------
 INT 21 - Get/Put Date/Time (MSDOS generic)
    REG AH = 57H
        AL = FUNCTION CODE
                0 = GET DATE AND TIME
                1 = SET DATE AND TIME
        BX = FILE HANDLE
        CX = TIME TO BE SET (IF AL = 1)
        DX = DATE TO BE SET (IF AL = 1)
    ON RETURN:
        IF CF SET:
                REG AX = ERROR CODE
        IF CF NOT SET:
                REG CX = TIME OF LAST WRITE (IF AL = 0)
                    DX = DATE OF LAST WRITE (IF AL = 0)
 -----------------------------------------------------------
 INT 21 - GET EXTENDED ERROR CODE (DOS 3.X generic)
    REG AH = 59H
        BX = VERSION CODE (0000 FOR DOS 3.0)
    ON RETURN:
        REG AX = EXTENDED ERROR CODE
            BH = CLASS OF ERROR
            BL = SUGGESTED ACTION CODE
            CH = LOCUS (WHERE ERROR OCCURRED)
 -----------------------------------------------------------
 INT 21 - CREATE TMEPORARY FILE (DOS 3.x generic)
    REG AH = 5AH
        DS:DX = POINTER TO DIRECTORY PATH NAME
        CX = FILE ATTRIBUTE
    ON RETURN:
        REG AX = ERROR CODE (IF CF SET)
            DS:DX = PATH NAME (IF CF NOT SET)

 NOTE: THE FILE CREATED IS NOT TRULY "TEMPORARY". IT MUST BE
 REMOVED BY THE USER.
 -----------------------------------------------------------
 INT 21 - CREATE NEW FILE (DOS 3.x generic)
   REG AH = 5BH
        DS:DX = POINTER TO DIRECTORY PATH NAME
        CX = FILE ATTRIBUTE
    ON RETURN:
        REG AX = ERROR CODE (IF CF SET)
            DS:DX = PATH NAME (IF CF NOT SET)

 NOTE: UNLIKE FUNCTION 3CH, FUNCTION 5BH WILL FAIL IF THE
 ALREADY EXISTS.
 -----------------------------------------------------------
 INT 21 - LOCK/UNLOCK FILE ACCESS (DOS 3.x generic)
    REG AH = 5CH
        AL = 0 IF LOCK
             1 IF UNLOCK
        BX = FILE HANDLE
        CX:DX = OFFSET TO LOCK
        SI:DI = AMOUNT TO LOCK
    ON RETURN:
        REG AX = ERROR CODE (IF CF SET)
 -----------------------------------------------------------
 INT 21 - GET PSP ADDRESS (DOS 3.x generic)
    REG AH = 62H
    ON RETURN:
        REG BX = SEGMENT ADDRESS OF PSP
 -----------------------------------------------------------
 INT 22 - TERMINATE ADDRESS (MSDOS generic)
    FAR (DWORD) address of routine to be executed
 when program "returns to DOS". Should NOT ever be called.
 -----------------------------------------------------------
 INT 23 - CONTROL "C" EXIT ADDRESS (MSDOS generic)
    Automatically called from keyboard scanner when
 CTRL-C or CTRL-BREAK is detected. Normally aborts program
 and returns to DOS, but may be changed.
 -----------------------------------------------------------
 INT 24 - FATAL ERROR ABORT ADDRESS (MSDOS generic)
    Automatically called upon detection of unrecoverable
 disk error. Normally prints "Abort, Retry, or Ignore?" message
 and takes the reply, but may be changed if desired.
 -----------------------------------------------------------
 INT 25 - ABSOLUTE DISK READ (MSDOS generic)
    Similar to INT 13 function, but this one is generic
 for all MSDOS rather than being machine specific.
    ENTRY CONDITIONS:
    AL = Drive number (0=A, 1=B, etc)
    DS:BX = Disk Transfer Address (buffer)
    CX = Number of sectors to read
    DX = First relative sector to read. 0 reads boot
         sector, 1 reads FAT, etc.
    EXIT:
    If carry set, AL=error code.
    If carry not set, operation successful.
    NOTE:  This routine PUSHes the flags onto the stack when it
    is called, and does NOT remove them at exit. Be sure
    to POP the stack immediately after returning, to
    prevent overflow. All of the registers, not just
    those listed, are changed by the routine.
 -----------------------------------------------------------
 INT 26 - ABSOLUTE DISK WRITE (MSDOS generic)
    All parameters and conditions are the same as for
    INT 25, except that this routine WRITES to the disk
    rather than READing from it. Note that it does NOT
    update the FAT, directories, etc., and can easily
    destroy a disk unless carefully used.
 -----------------------------------------------------------
 INT 27 - TERMINATE BUT STAY RESIDENT (MSDOS generic)
    REG CS = CURRENT PROGRAM SEGMENT
    REG DX = LAST PROGRAM BYTE + 1
    NOTE:     RETURN IS TO DOS
 -----------------------------------------------------------
 INT 28 - Internal routine for MSDOS
    This interrupt is called from inside the "get input
 from keyboard" routine in DOS, if and only if it is safe to use
 INT 21 to access the disk at that time. It is used primarily by
 the PRINT.COM routines, but any number of other routines could
 be chained to it by saving the original vector, and calling it
 with a FAR call (or just JMPing to it) at the end of the new
 routine.
    Until PRINT.COM installs its own routine, this
 interrupt vector simply points to an IRET opcode.
 -----------------------------------------------------------
 INT 29 - Internal routine for MSDOS
    This interrupt is called from the DOS output routines
 if output is going to a device rather than a file, and the
 device driver's attribute word has bit 3 (04H) set to "1".
 Nothing more is known about it at this time.
 -----------------------------------------------------------
 INT 2E - UNKNOWN
 -----------------------------------------------------------
 INT 30 - UNKNOWN
 -----------------------------------------------------------
 INT 31 - UNKNOWN
 -----------------------------------------------------------
 INT 33 - USED BY MICROSOFT MOUSE
    FUNCTIONS AND PARAMETERS UNKNOWN
 -----------------------------------------------------------
 INT F8 - INTERVAL TIMER (10 MSEC)
    PARAMETERS UNKNOWN
 -----------------------------------------------------------
 INT FA - USART READY (RS-232C)
    PARAMETERS UNKNOWN
 -----------------------------------------------------------
 INT FB - USART Rx READY (keyboard)
    PARAMETERS UNKNOWN
 -----------------------------------------------------------


               -------------------- END -------------------