RESIDENT COMMAND INTERPRETER

				  John Chapman
			       844 S. Madison St.
			    Hinsdale, Illinois 60521

			     COMPUSERV ID 70205,1217

	DISCLAIMER

	This  modification is provided without warranty of any kind.  The
	author	assumes no liability for failure of this code to  perform
	in  any  environment.  The  user is  completely  responsible  for
	determining   the  applicability  of  this  modification   to	a
	particular environment.

	LIMITATIONS

	This modification causes the transient portion of COMMAND.COM  to
	be  made resident at system IPL.   Re-booting the system with  an
	unmodified   COMMAND.COM   is  the  only  way  to   remove   this
	modification.  This  modification  alters  the	starting  segment
	[paragraph] address available to programs, lowering the amount of
	storage  available  by 4288 bytes [for PC/DOS 1.1 with	a  normal
	load   segment	address  of  02C1].    The  starting  segment  of
	COMMAND.COM can be found at location 0000:9E,  and should display
	[debug] as	 0000:009E 2C 01

	CONTENTS

	This   modification,   supplied  as  a	BASIC	program    called
	"RESCMD.COM"  (Or  RESCMDCK.BAS  for realtime clock users)  which
	will read in an UNMODIFIED DOS 1.1 COMMAND.COM and produce a  new
	file, "COMMAND.CMD" which has all the mods installed. This set of
	modifications  alters  the  IBM  Personal  Computer  DOS  command
	interpreter  (COMMAND.COM)  to remain entirely	resident,  rather
	than  be half resident and half transient.  The whole purpose  of
	this  modification is to suppress 99% of the occurrances  of  the
	refresh   of  the  transient  portion.	 This  will  remove   the
	requirement  to  ALWAYS have a disk with a valid  COMMAND.COM  in
	drive  A.  This  change has been especially useful with  multiple
	DISKCOPY  type activities,  and with those  application  packages
	which  use all of memory,  including the top 4880 bytes where the
	transient COMMAND.COM resides.

	The  modification  merely omits the relocation of  the	transient
	portion of COMMAND.COM, and sets the first free paragraph address
	to  be	the area behind the transient routines,  rather than  the
	small "resident" portion.







					1



	PC/DOS Initialization Overview

	The  IBM  Personal  Computer DOS is brought in from disk  by  the
	bootstrap loader read from track 0 of drive A by the ROM routines
	after the initial hardware tests are performed at  power-on,  and
	subsequently  when  ALT-CTRL-DEL re-boot is  requested.  In  both
	cases, the following sequence occurs:

	     1) The "boot" program is read from track 0.

	     2) It reads IBMBIO.COM  from  a  specific location

	     3) IBMBIO is given control and builds the environmental
		control blocks, initializes peripherals, and then
		reads IBMDOS.COM from its specific location on disk

	     4) IBMDOS is passed control. After initializing the
		remainder of the operating system, IBMDOS loads
		the COMMAND.COM file [the command interpreter], and
		passes it control

	     5) The command interpreter immediately relocates all of the
		main line code for command prompting,  parsing,  and  the
		code which supports the resident commands to the high end
		of memory, where it can be more easily destroyed by
		wandering programs.

	     6) Resident COMMAND.COM will now [pretend to] detect a
		checksum error in the transient portion of itself,
		immediately causing a Re-load from disk, thus setting
		the tone for a long and tedious interaction, interrupted
		frequently by disk I/O and requests for a DOS disk
		in the default drive.



	REAL-TIME CLOCK VERSION

	An   alternate	version  of  the  modification	is  supplied   as
	"RESCMDCK.BAS".   This version REQUIRES THE PRESENCE OF A  CLOCK.
	The  DOS  DATE	and TIME commands ARE DISABLED by  this  version,
	requiring the user to employ the software provided with the clock
	card  to access date and time.	 The space formerly used by  DATE
	and TIME is reused for three new RESIDENT commands,  BEEP,  PAGE,
	and CLS.  PAGE causes the printer (LPT1:) to skip to top-of form.
	CLS clears the active display.	BEEP causes a warbling tone to be
	produced.

	[The DOS 1.10 command  DEL  will  not  be  recognized however the
	function remains implemented under the ERASE command.]








					2