DRIVECHK
                 Version 4.4 for IBM Personal Computers
                          Program 05/30/89
                   Minor document update 01/28/90

(c) Copyright John L. Dickinson 1983, 1987, 1989, 1990.  All rights reserved.

DISCLAIMER

   This program is provided "as-is" without warranty of any kind,
   either expressed or implied, including, but not limited to the
   implied warranties of merchantability and fitness for a particular
   purpose.  The entire risk as to the quality and performance of the
   program is with you.

   In no event will I be liable to you for any damages, including any
   lost profits, lost savings or other incidental or consequential
   damages arising out of the use or inability to use this program
   even if I have been advised of the possibility of such damages, or
   for any claim by any other party.


COPYING PROVISIONS

   This program and documentation may be freely copied and shared
   provided it is not modified in any manner and this notice is not
   bypassed or removed.  Please register by sending your name,
   address and any comments to the author.  There is no charge.

                        John L. Dickinson
                        2470 N. Tierra Verde Pl.
                        Tucson, Arizona 85749-9315


CHANGE HISTORY

   11/26/87 Version 4.3
    - Initial shareware release.

   05/30/89 Version 4.4
    - Reset diskette subsystem after drive timeout.  This prevents
      hangs when no diskette is inserted.
    - Add NOZAP and ZAP commands.
    - Minor updates to STATUS messages.

   01/28/90
    - Document update only.  Updated supplier addresses and phone
      numbers.

OVERVIEW

   DRIVECHK is a diskette drive diagnostic program that graphically
   displays alignment and other drive characteristics of 48, 96 and
   135 tracks per inch (TPI) diskette drives without the need for an
   oscilloscope.  These include 40 and 80 track 5 1/4 inch drives as
   well as 80 track 3 1/2 inch drives.  The PC-AT High Capacity drive
   and Personal System/2 High Density drive can also be tested.  A
   drive can be checked in just a few minutes without removing the
   PC's cover.

   You may also be interested in a companion program called ALIGN
   which uses the Xidex/Dysan Analog Alignment Disk (AAD) and an
   oscilloscope.  It is more suited to drive repair than diagnosis.

   DRIVECHK can be used to check a drive's operation periodically,
   prove a suspected defective drive is bad, or as a final check
   after repairs or adjustments.  DRIVECHK is not designed for making
   drive adjustments, although it can be used to set the radial head
   alignment which is only one of several diskette drive adjustments.

   DRIVECHK works with a XIDEX/DYSAN Digital Diagnostic Disk (DDD).
   The Digital Diagnostic Disk is specially formatted and precisely
   recorded with varying degrees of intentionally misaligned
   information.  The Xidex/Dysan DDD disk has no programs on it and
   cannot be copied since it is made on special equipment that
   records "between the grooves."  It is not a PC-DOS formatted disk
   and its tracks have 16 sectors (except the 96 TPI High Capacity
   DDD for the PC-AT which has 26 sectors).  You select a different
   DDD depending on the size and track density of the drive you want
   to test.  You can also select a High Capacity diskette to test the
   PC-AT high capacity drive.

                            Xidex/       Xidex/   Price
   Size     TPI   Tracks  Dysan Model  Dysan P/N  Each
   ------   ---   ------  -----------  ---------  ------
   5 1/4"    48     40      508-400     802045    $40.00
   5 1/4"    96     80      506-400     802010    $40.00  (normal media)
   5 1/4"    96     80      516-400     810253    $40.00  (high capacity)
   3 1/2"   135     80      305-400     810244    $40.00  (normal media)
   3 1/2"   135     80 -Use 305-400 normal media version- (high density)


   All of the above disks are double density and double-sided.
   508-400 is used for the majority of PC drives which are 40 track.
   506-400 can be used either to test the PC-AT's High Capacity drive
   or a user attached 80 track drive.  It tests the PC-AT High
   Capacity at a 300 KBS data rate.  516-400 tests the PC-AT High
   Capacity drive in it's high capacity mode at a 500 KBS data rate.
   305-400 is for normal media 3 1/2 inch drives and is also used to
   test the Personal System/2 High Density (1.44M) drive at its lower
   capacity data rate.

   Xidex/Dysan also makes DDD's for other sizes and densities, but
   they aren't supported by DRIVECHK.

   Using DRIVECHK and a DDD disk you can observe:

       * Radial head alignment of each head
       * Operating Margin  (How much error can the drive
         tolerate?)
       * Head positioner hysteresis (backlash)
       * Seek variation or head positioner linearity  (How does the
         radial head alignment vary at different tracks?)
       * Margin variation: Relative performance at different tracks
       * Head azimuth
       * Diskette eccentricity (clamping error or spindle wobble)
       * Drive spindle speed
       * Instantaneous speed variation

   The program does NOT display:

       * Index timing
       * Track 0 stop adjustment
       * Track 0 switch adjustment

   I don't think there is any program that can test these last items
   with the PC's covers in place.  Index timing is not a usual cause
   of drive failure unless the drive has been disassembled (such as
   removing the cone lever assembly to fix a door latch!)

   DRIVECHK runs under IBM PC-DOS version 2.0 or later on a PC,
   PC-XT, PC-AT, PCjr, PC Convertible, Personal System/2 or
   compatibles with at least 128K.  An 80 column display, either
   monochrome or color is required.

   DRIVECHK works with standard IBM drives any many others.  However,
   DRIVECHK has no provisions for changing the BIOS diskette
   parameter tables - step time, settle time, etc.


USING THE DRIVECHK PROGRAM

   The DRIVECHK program consists of the single file DRIVECHK.EXE.
   There is no installation other than copying it to your program
   diskette.

   It is possible that other memory resident DOS programs could
   interfere with DRIVECHK or cause DRIVECHK to give incorrect
   results.  If you suspect improper operation, boot DOS from your
   master DOS diskette without loading other programs or options
   before running DRIVECHK.  This is not a likely cause of problems,
   but is something to keep in mind.

   The DRIVECHK program reads the Digital Diagnostic Disk and
   produces three graphic displays on a monochrome (or color) display
   using character graphics.  Personal System/2 users with monochrome
   displays may need to adjust display controls to make the display
   brighter than normal to see everything.

   There are no pass-fail answers and the results are subject to
   interpretation.  While every drive appears different, defective
   drives are usually rather obvious.

   In the discussions that follow, all three displays use the same
   notation to indicate success or failure to read various data
   sectors on the DDD.

        *  An asterisk indicates that the sector was successfully
           read after seeking to the track from both directions.

        +  A plus sign indicates that the sector was successfully
           read after seeking from one direction only.  (From track
           0)

        -  A minus sign indicates a successful sector read after
           seeking from one direction only.  (Opposite of +, a
           successful seek from the center out.)

    blank  A blank space indicates an unsuccessful read operation
           after a seek from either direction.

        X  An X is like the "Free" space in Bingo.  It shows up in
           the displays for a couple of sectors that DRIVECHK isn't
           equipped to retrieve.  (Either they are not recorded on
           the DDD disk or else DRIVECHK simply can't handle them.
           I'm not sure which.)

   Since the purpose of DRIVECHK and the DDD disk is to test the
   drive to the limits of it's capability, many blanks (read
   failures) are to be expected even on the best drives in perfect
   adjustment.  An occasional + or - is normal too, but usually at
   only at the limit of a drive's capability.  That is, you might
   see a + or - at the end of a row of asterisks.

   During the tests, the status returned from each read attempt is
   displayed on the left of the screen.  You can generally ignore it.
   Status messages here may appear to be "errors" when DRIVECHK tests
   your drive beyond its capability.  This is normal and occurs when
   a blank will displayed instead of an asterisk, + or -.

   No printing capability in built into the program, so the PrtSc
   (Print Screen) key is used to get hard copy.  Graphic characters
   are used, making the IBM Graphics Printer or equivalent helpful,
   although the results should be readable on any printer.


DRIVECHK COMMAND OVERVIEW

   Commands are entered in DRIVECHK's command area to specify the
   drive, choose a diagnostic display, reset the diskette subsystem
   or quit the program.  Only enough letters to define the command
   uniquely must be entered.  Any command that starts a diagnostic
   test can be stopped by pressing any key during the test.

   Command summary:

    Drive specification -

      DRIVE   <0,1,2,3>     Selects a drive number           (default 0)
      TPI     48            Specifies  48 TPI DDD            (default)
              96            Specifies  96 TPI DDD on regular media
              96HC          Specifies  96 TPI DDD on high capacity media
              135           Specifies 135 TPI DDD
      TYPE    REG           Specifies a "regular" drive      (default)
              HC            Specifies a PC-AT High Capacity drive
      SIDES   <SS,DS>       Specifies single or double-sided (default DS)
      LIMIT   END           Limits seeks to mfr's specified last track (dflt)
              PLUS          Allows a seek one track past the "end"

    Choosing a diagnostic display -

      CENTERING             Display eccentricity (misclamp or wobble)
      CHART                 Display alignment and several other factors
      AZIMUTH               Display head azimuth (rotation)
      SPEED                 Display spindle speed
      ALIGN                 Repeating display for alignment

    Other -

      HELP or ?             Display this command summary
      RESET                 Reset the diskette subsystem
      NOZAP                 Rarely needed.  See command description.
      ZAP                   Rarely needed.  See command description.
      QUIT                  Exit DRIVECHK and return to DOS


TYPICAL OPERATION OVERVIEW

   Boot DOS and insert the DRIVECHK program disk in any working
   drive.

   After the DOS prompt, enter DRIVECHK (preceded by a drive
   specifier, if necessary) and press Enter.  Once DRIVECHK is
   loaded, the program disk is no longer needed in the system.

   Press any key to get past the initial screen to the main command
   menu.

   If you are testing the "A" drive, DRIVECHK's default of DRIVE 0 is
   correct.  If you are testing the "B" drive enter DRIVE 1 to select
   it.  See the DRIVE command description for more information or if
   you are testing an external diskette drive.

   If necessary, specify drive and Digital Diagnostic Disk
   characteristics using the TPI, TYPE, SIDES and LIMIT commands as
   needed.

   Insert the Xidex/Dysan Digital Diagnostic Disk in the drive to be
   tested.

   The next three commands take a little time to do the analysis.
   The results are displayed when the commands complete.  If hard
   copy is needed, use the PrtSc key.

     Enter the CENTERING command.  If the display indicates off
     center operation, then reclamp the diskette.

     Enter the CHART command.

     If testing with a 48 TPI DDD or a PC-AT High Capacity drive
     with the high capacity 515-400 DDD, enter the AZIMUTH command.

     Enter the SPEED command.  After a few seconds, press any key
     to stop the drive and display.

   If desired, select another drive with the DRIVE command.

   When finished, enter Q or QUIT to return to DOS.


DETAILED COMMAND DESCRIPTIONS (in alphabetical order)

  ALIGN command

   The ALIGN command can assist adjusting the radial head alignment.
   DRIVECHK really isn't intended for doing any adjustments, but
   ALIGN is provided to get radial track alignment done in a pinch.

   The CHART command gives a much better overall picture of
   alignment, but takes a minute or two, making adjustments tedious,
   if not impossible.  ALIGN shows less information, but is much
   faster and repeats until stopped by pressing any key.

   ALIGN produces the same diagnostic display as the CHART command,
   but only for one track.  This is track 16 for 48 TPI, track 32 for
   96 TPI and track 32 for 135 TPI.  These tracks are the same ones
   used with the "cat's eye" pattern on the analog alignment
   diskettes for 48 and 96 TPI.  For 135 TPI, ALIGN uses track 32,
   not track 40 as on the 135 TPI analog alignment disk.

   The ALIGN command seeks to the track from both directions as do
   CHART and the other diagnostic displays.  ALIGN takes about 10
   seconds to refresh the display as you make adjustments.

   There's more to a complete alignment job than just radial head
   alignment.  Realize that making this one adjustment is no
   substitute for a complete checkup with an oscilloscope and analog
   alignment disk.


  AZIMUTH command

   AZIMUTH measures the amount of head rotation around a vertical
   axis.  Azimuth can be measured when using 48 TPI or High Capacity
   96 TPI DDDs.  Azimuth tracks are not recorded on all DDDs since
   azimuth is much less critical on the narrower tracks of 96 and 135
   TPI diskettes.

   The DDD tracks for measuring azimuth are all too "easy" in my
   opinion.  Therefore, small azimuth errors cannot be detected.
   Fortunately, small azimuth errors are of little consequence.  An
   Analog Alignment Disk and an oscilloscope provide a much more
   critical azimuth test.

                            Azimuth in minutes

                            --------  ++++++++
                            43333222  22233334
                            29630741  14703692
                           |--------||--------|
                           |********||X*******|   Head 1 (Upper)
                           |--------||--------|
                           |********||X*******|   Head 0 (Lower)
                           |--------||--------|

   If the display shows anything but all asterisks, then the drive
   definitely has a problem.  Note, however, that inability to read
   the azimuth data can also be caused by incorrect radial head
   alignment.  When using the High Capacity 96 TPI DDD, the display
   is wider and has more resolution due to the greater number of
   sectors.


  CENTERING command

   The CENTERING command displays information on diskette
   eccentricity.  This could be caused by clamping error or spindle
   wobble.  To get a better idea of the effect being measured, think
   how a record would rotate with its hole punched off center.  If
   the display shows eccentricity, remove the DDD disk, inspect the
   center hole, and reclamp it.

   48 TPI example:           Head 0     Head 1

                            Sector->   Sector->
                           |--------| |--------|
                   27 +9.0 |**-*****| |***-****|
                   27 -9.0 |********| |********|
                           |--------| |--------|
             Track 24 +8.0 |********| |********|
                   24 -8.0 |********| |********|
                           |--------| |--------|
                   21 +7.0 |********| |********|
                   21 -7.0 |********| |********|
                           |--------| |--------|

   The CENTERING display shows three sets of data for each head.  The
   top set is the hardest to read and the bottom set is the easiest
   to read.  The actual offsets differ depending on the track density
   (TPI) of the DDD you are using.  When using the High Capacity 96
   TPI DDD, the display is wider and has more resolution due to the
   greater number of sectors.

   To help understand what's happening in this test, picture the head
   traveling between the two rails of a circular railroad track.  If
   it can "see" both the rails, then an asterisk is displayed for
   each "rail."  If the head strays from a point halfway between the
   "rails" then it may not be able to "see" one of the rails and a +,
   - or blank is displayed.  The circular tracks are straightened out
   for this display and 8 data points (13 for High Capacity 96 TPI
   DDD) are shown for one revolution of each "rail."  If your
   CENTERING display shows successful reads and read failures
   alternating from one side of center to the other, then it
   indicates bad disk centering or spindle wobble.

   An occasional read failure such as the two "-" characters in the
   example, are not necessarily an indication of a problem.  In the
   example above, the read failures were on the most severe test, and
   there the other "rail" was read perfectly.

   Here's an example of what a centering problem might look like:

                           |--------|
                           |*-  -***|
                           |****+  +|
                           |--------|

   The CENTERING command should be used first to check the DDD
   diskette's clamping.  Incorrect clamping invalidates the results
   of other displays.  If poor results are obtained repeatedly, then
   continue with other tests.  Radial alignment errors may be
   affecting the CENTERING results.

   Hopefully, you will never clamp your DDD disk off-center since
   such damage no doubt affects its accuracy.


  CHART command

   CHART displays the most interesting and useful of the three
   displays which looks about like this for a fairly normal drive:

   96 TPI example:
-------------------------------------------------------------------------------

                                 Radial          Hyste-   Seek   Margin
          Out     In        Track Align.  Margin  resis    Vari.   Vari.
      |--------|--------|   ----- ------  ------  ------  ------  ------
      |  ******|***     |     79   -1.5     9.5     0.0
      |  ******|**+     |     71   -2.0     9.0     0.3
Head 1| *******|****    |     41   -1.5    10.5     0.0
Upper | *******|****    |     32   -1.5    10.5     0.0
      |+*******|****    |      6   -1.5    10.5     0.3
      |********|X***-   |      0   -2.0    11.0     0.3
      |--------|--------|    Hd.1  -1.7    10.2     0.1     0.2     0.6
      | *******|X****+  |      0   -1.0    11.0     0.3
      | +******|*****-  |      6   -0.5    10.5     0.5
Head 0| +******|******  |     32   +0.0    11.0     0.3
Lower | *******|*****   |     41   -1.0    11.0     0.0
      |  ******|****-   |     71   -1.0    10.0     0.3
      |  ******|X****   |     79   -0.5    10.5     0.0
      |--------|--------|    Hd.0  -0.7    10.7     0.2     0.3     0.3
            Drive 0       Overall  -1.2    10.4     0.2     0.3     0.5

-------------------------------------------------------------------------------

   This chart shows the results of reading "Progressive Offset"
   tracks on the DDD disk.  Each horizontal line indicates the
   results of reading one track.  Each head attempts to read 6
   progressive offset tracks spread across the disk.  There are 16
   sectors on each track (26 for High Capacity 96 TPI DDD).  Half are
   displaced from the track center line in increasing amounts toward
   the hub and are shown on the right half of the display.  The other
   half are displaced in increasing amounts toward the outside of the
   disk and are shown on the left half of the display.  The small
   (easy) displacements are adjacent to the vertical centerline of
   the display.  The larger (difficult) displacements are at the left
   and right edges of the display.

   The displacements depend on the DDD you are using.

   TPI  Displacements in milli-inches                               Increment
   ---  ----------------------------------------------------------  ---------
   48   6.0  7.0  8.0  9.0 10.0 11.0 12.0 13.0                       1.0 mil.
   96   3.0  3.5  4.0  4.5  5.0  5.5  6.0  6.5                        .5 mil.
   96HC 1.0  1.5  2.0  2.5  3.0  3.5  4.0  4.5 5.0 5.5 6.0 6.5 7.0    .5 mil.
   135  1.0  1.5  2.0  2.5  3.0  3.5  4.0  4.5                        .5 mil.

   The displayed numeric results are all in milli-inches, regardless
   of the track density (TPI) of the drive under test.  Generally,
   the higher the track density, the smaller the numbers for normal
   drives.  The CHART command's "picture" is scaled so it's image
   size is about the same, regardless of the track density.

   There are no Pass/Fail limits built into DRIVECHK.  You can
   establish your own thresholds based on experience.

   Note: The CHART command generally displays all the progressive
   offset tracks available on the DDD.  However at 135 TPI, there are
   7 progressive offset tracks available, not 6 as at 48 and 96 TPI.
   In this case, the CHART command ignores track 69 (but it does
   track 67 which is pretty close).  Displaying track 69 would not
   add much value to the display.

   Confused?  Never mind, it's still easy to read the display.

   The chart indicates:

   * Radial head alignment of each head

     In general, the pattern should be centered from left to right.
     That is, it should be centered about the vertical centerline of
     the chart.  The ideal numeric result is 0.  When most people
     talk about a drive's "alignment," this is usually what they are
     talking about.

     Positive values indicate a head adjusted towards the drive
     spindle.  Negative values indicate away from the spindle.

     The top half of the chart is the upper head and its pattern
     should be directly over that of the lower head.  If not, then
     the two heads are not aligned relative to each other.  You can
     check this visually even if the overall pattern is off to the
     left or right.  Numerically, it's the difference between the
     "Radial Align." for "Hd.0" and "Hd.1".

     The results with a 96 TPI High Capacity DDD appear wider than
     the other's results since it has more sectors.  The 96 TPI High
     Capacity CHART display adds four "easy" offsets (columns) on
     both sides of the vertical center line and one more difficult
     offset (column) at the outer edges.  Keep this in mind when
     comparing the High Capacity CHART display with others.  The
     equivalent offsets (columns) are shown with a double line over
     them.

   * Operating Margin

     Operating Margin is a term for a measurement of the drive's
     ability to read weak signals.  Weak signals can be caused by a
     faulty or weak disk, poor head to media contact, bad electronics
     or many other factors..  Operating Margin answers the question
     "How much cumulative error can the drive tolerate?"  This may
     also be called "Read Sensitivity."

     The wider the pattern and the larger the number, the better.

     Since results with a 96 TPI High Capacity DDD appear wider than
     the others, keep this in mind when comparing CHART displays from
     other DDDs.

   * Head positioner hysteresis (backlash)

     Play in the head positioner mechanism shows up as + signs down
     one edge of the pattern and - signs down the other.  A few here
     and there at the edges are of no consequence.  An ideal numeric
     result is 0.

     You won't see significant hysteresis in most modern drives
     because they use a split band positioner that is very effective
     at keeping backlash to a minimum.  Occasionally a head stepper
     motor can contribute to this effect if it doesn't step with
     precision.

   * Seek variation or head positioner linearity

     The test for seek variation answers the question "How does the
     radial head alignment vary at different tracks?"  While the
     horizontal pattern lines for each track may have different
     widths, they should all be about a common vertical center line.
     That is, they shouldn't wander, from left to right.  A drive
     only has one radial alignment adjustment and it is set near the
     middle of the disk.  This measurement shows the radial alignment
     at other track locations.

     The numeric result is the average radial alignment difference
     from the nominal radial alignment for all tracks.  An ideal
     result is 0.

   * Margin variation: Relative performance at different tracks

     The width of the pattern lines shouldn't vary too much from
     track to track, although it's common for the Operating Margin to
     be somewhat worse toward the inner tracks where the linear
     recording density is actually higher.  This can give the overall
     display a somewhat rounded appearance much like two parenthesis:
     ().

     Be sure, however, not to accept too much of this rounded
     appearance.  In general, any good drive should show at least one
     asterisk on either side of the vertical line at the inner
     (highest) track.  Note that if it doesn't, it may still be able
     to read a good disk since those "easy" points adjacent to the
     centerline are already recorded somewhat off track center.

     The numeric result is the average margin difference from the
     nominal margin for all tracks.  An ideal result is 0.


  DRIVE  <0,1,2,3>

   The DRIVE command specifies which physical drive is to be tested
   using a drive address number of 0, 1, 2 or 3.  The default is
   drive 0, the first internal diskette drive.  Examples:

                    DRIVE 0         (Set drive 0)
                    D 2             (Set drive 2)

   The drive number designates a physical drive address and not a DOS
   drive letter or a drive letter associated with a special device
   driver such as DOS 3.2's DRIVER.SYS.  (DRIVER.SYS may be installed
   for any diskette drive, but it is not used or needed by the
   DRIVECHK program.)

   Drive address numbers are:

    0  First internal diskette drive.  Identified by DOS as
       "A" (or "A" and "B" when only one internal diskette
       drive is installed.)

    1  Second internal diskette drive.  Identified by DOS as "B".

    2  First external diskette drive.

    3  Second external diskette drive.

   The drive letter that DOS assigns to external drives varies and
   depends on the number of fixed disks, system board switch settings
   and device drivers.  DRIVECHK doesn't care what letter DOS uses.


  HELP command

   The HELP command causes another screen to be displayed with a
   brief DRIVECHK command summary.  Pressing any key returns you to
   the main DRIVECHK screen.

   A question mark in the command line or pressing function key F1
   also displays the help screen.  Examples:

                    HELP
                    H
                    ?


  LIMIT command

   LIMIT END         Limits seeks to mfr's specified last track (default)
   LIMIT PLUS        Allows a seek one track past the "end"

   The limit command specifies the highest track number that will be
   used for directional seeks from the center (near the hub) out.
   Most drives don't have a high track stop and can handle one or
   more tracks past the end of the advertised track capacity.

   DRIVECHK can take advantage of this capability so tests can
   perform a seek from both directions to the normal "last" track.
   For instance, on a 40 track drive which has tracks numbered from 0
   to 39, DRIVECHK seeks to track 39 both from a lower track and
   track 40, the ENDing track PLUS one.  This is LIMIT PLUS and must
   be specified if you want this feature.  LIMIT END is the default.

   Some drives have upper track limit stops and can't go past track
   39 (or 79).  With these drives it is impossible to seek to the
   ENDing track from both directions.  If you are testing one of
   these drives, specify LIMIT END or use the default.  On a 40 track
   drive with tracks from 0 to 39, DRIVECHK will then seek to track
   39 only from a lower track, avoiding the track limiter.

   This LIMITing only affects the results for the last track in the
   CHART display.  However, the LIMIT command also controls the last
   track used for directional seeks for all data points on all
   diagnostic displays.  If your drive can't handle the extra track,
   and you have specified LIMIT PLUS, then the head mechanism will
   hit the stop.  This probably won't hurt anything, but it's likely
   to rattle your nerves, destroy the displayed results and require a
   RESET command or re-boot to get back on track.

   If you test a drive with LIMIT PLUS and the drive limits seeks to
   the ending track, then the DRIVECHK displays may appear with all
   plus signs (+) instead of the usual asterisks.

   You can ignore the LIMIT command if you wish.


  NOZAP

   NOZAP is an obscure command that you can probably ignore.  It
   doesn't even appear on the DRIVECHK help screen.

   If:

     - You specify TPI 96   (regular media DDD, not high capacity)
             and
     - You specify TYPE HC  (high capacity drive)
             and
     - You do not have an IBM PC-AT (i.e. you have a clone
       or a non-IBM high capacity controller and drive in a
       PC or XT etc.)

   then, you may need to enter the NOZAP command.  Otherwise, ignore
   it.  If NOZAP is needed, enter it before any commands that run the
   drive, otherwise the zap is applied the first time the drive is
   run.  If this happens, then re-boot.

   NOZAP avoids a fixup "zap" of the BIOS data area required by a
   regular media, 96 TPI (80 track) disk in the IBM PC-AT's high
   capacity drive.  The zap is correct for the IBM PC-AT.  If you
   don't have an IBM brand PC-AT, then the zap may be harmful as the
   BIOS data area may not be exactly like IBM's.  Enter NOZAP before
   any commands that run the drive to bypass the normal IBM PC-AT
   fixup.

   If you have this combination and enter NOZAP, then DRIVECHK
   attempts to run.  It's not supported as DRIVECHK can't possibly
   tell how to program your particular hardware for what would
   otherwise be a nonsupported 720K diskette in a high capacity
   drive.

   When NOZAP is in effect, "NOZAP" appears in the lower left of the
   screen while the disk is running.


  QUIT command

   The QUIT command ends the program and returns to DOS.


  RESET command

   The RESET command causes a reset of the diskette system (via BIOS
   INT 13 with AH=0).  You probably won't need to use RESET except
   possibly if you are doing radial head alignment or the head has
   hit a limit stop.  (See the LIMIT command.)

   After entering RESET, the next time any drive is accessed, it will
   then be "recalibrated."  This means that the diskette controller
   makes no assumptions about which track the head is on, moves the
   head until track 0 is located as indicated by the drive, and then
   proceeds with the requested operation.  Once this recalibration
   process is complete, the diskette controller keeps it's own head
   position register and merely pulses the head forward or back, one
   step at a time to get to a desired track.  If one pulse is missed
   or the head is moved manually with power-on, then the controller's
   track register won't agree with the physical position of the head.

   "Recalibration" is not an adjustment.  It is a normal operation
   done by the diskette controller so it can get in sync with the
   physical head position.  Every drive is "calibrated" by the
   controller the first time you use it after power-on or boot.

   The RESET command allows you to recalibrate during drive
   adjustment or test.  For instance, assume you are using the ALIGN
   command to display track 16 results (or what you think is track
   16).  If you believe the drive is actually on a different
   track, then issue RESET before ALIGN.

   It is also a good idea to use the RESET command just before the
   final checks on radial head alignment to be sure you're not
   exactly 1 or 2 tracks off.

   Without the RESET command, it would otherwise be necessary to
   re-boot or turn the machine off-and-on to force a recalibrate
   operation.


  SIDES command

   SIDES   <SS,DS>

   The SIDES command specifies either single or double-sided testing.
   Double-sided is the default.  If a single-sided drive is tested
   while DRIVECHK thinks it is a double-sided drive, no harm is done.
   It just takes more than twice as long as it needs to.  Since
   specifying SIDES SS cuts the testing in half, it speeds up all
   diagnostic displays, but gives no results for the second head.
   You may want to use SIDES SS to make the ALIGN display even
   faster.  Examples:

                    SIDES SS              (Set single-sided)
                    S DS                  (Set double-sided)


  SPEED command

   The SPEED command measures diskette drive spindle speed which is
   the speed the diskette rotates.  It also gives and indication of
   the Instantaneous Speed Variation or ISV.  ISV is a short term
   speed variation which doesn't show in the average speed.  Possible
   causes of high ISV include incorrect belt adjustment, binding,
   motor cogging or poor brush contact.

   The SPEED command has no operands, but the drive should be
   properly specified with the DRIVE, TPI and TYPE commands first, if
   necessary.  SPEED requires a DDD diskette and does not work with
   standard DOS diskettes.  (If you don't have a DDD, use the ALIGN
   program and a standard DOS diskette to measure the speed.)

   To use the SPEED command, enter SPEED and let it run for a few
   seconds, stopping it with any key.  It you don't stop it, it stops
   on its own after testing 150 revolutions.

   Nearly all diskette drives have a nominal speed of 300 RPM.  The
   only IBM exception now is the PC-AT's High Capacity drive which
   has a nominal speed of 360 RPM.  The PC-AT High Capacity drive
   runs at 360 RPM regardless of the type of media it is using.

   Spindle speed accuracy is not as critical as the displayed numbers
   might suggest.  Most drives allow a speed tolerance of 1 or 1.5
   percent which is about plus or minus 3 or 4 RPM.  The actual speed
   also varies a bit due to the drag of different diskettes.  Some
   people over-emphasize spindle speed because it's about the only
   adjustment they can adjust without extra equipment.  The SPEED
   command dumps out all those numbers more for entertainment than
   necessity.

   The measured speed is always within the displayed range of
   approximately 280 to 320 RPM for 300 RPM drives and 330 to 390 RPM
   for 360 RPM drives.  This is true even if the actual speed is
   outside that range and is the result of the measurement method
   used by the program.  In practice, a drive whose speed is outside
   that range probably won't be working anyhow and may also show an
   erratic speed.  If there's any question, a look at the strobe on
   most drives will tell you very quickly if the drive is anywhere
   near the correct speed.

   SPEED example:

           Current  Average  Maximum  Minimum  Percent  Measurement
             RPM      RPM      RPM      RPM      ISV      Number
            298.40   298.40   298.40   298.40    0.00       1
            298.37   298.38   298.40   298.37    0.01       2
            298.38   298.38   298.40   298.37    0.01       3
            298.40   298.39   298.40   298.37    0.01       4
            298.37   298.39   298.40   298.37    0.01       5
            298.38   298.38   298.40   298.37    0.01       6
            298.40   298.39   298.40   298.37    0.01       7
            298.37   298.38   298.40   298.37    0.01       8
            298.39   298.39   298.40   298.37    0.01       9
            298.41   298.39   298.41   298.37    0.01      10

            298.39   298.39   298.44   298.34    0.03      38

               280  285  290  295  300  305  310  315  320
     ÀÄÄÄÄÄÄÄÄÄ |....|....|....|....|....|....|....|....| ÄÄÄÄÄÄÄÄÄÙ
                                  ^

   The easiest part of the display to read is the speed meter on the
   bottom.  It indicates the current RPM and changes whenever the
   actual drive speed changes.  (It is not the average drive speed.
   However, if it doesn't move much, then the current and average
   will be the same.)  The arrow on the meter moves in one RPM
   increments, displaying the "Current RPM" rounded to the nearest
   whole RPM value, which is close enough.

   You can probably ignore the rest of the SPEED display.  The first
   10 lines show individual statistics for the first 10 measured
   revolutions.  (SPEED lets the drive come up to operating speed and
   stabilize before starting measurement.) "Current RPM" is for just
   one revolution.  All the other statistics are cumulative.  The
   last line of statistics, separated with a blank line, is the data
   for the last revolution measured.  It is updated every revolution
   until the SPEED command is stopped or "times out" at 150
   revolutions.  As all the values except "Current RPM" are
   cumulative, they tend to stabilize as the test progresses.

   "Current RPM" is the measured spindle speed for one revolution.

   "Average RPM" is the average of the spindle speed RPM measurements
   so far and is the best overall indication of spindle speed.

   "Maximum RPM" and "Minimum RPM" are the highest and lowest spindle
   speeds encountered during the test.

   "Percent ISV" is an indication of Instantaneous Speed Variation.
   It is calculated by taking the difference between the maximum and
   minimum speeds, dividing by the average speed and multiplying by
   100 to get a percentage value.

   The "Measurement Number" is the revolution number since the drive
   came up to speed and measurements started.


  TPI command

   TPI     <48,96,96HC,135>

   The TPI command specifies the track density (tracks per inch) of
   the DDD you are using.  For 96 TPI, the TPI command also indicates
   whether the DDD is on regular media or high capacity media for the
   PC-AT High Capacity drive.  48 is the default.  You may prefer to
   think in terms of the number of tracks instead.

                     TPI    Size    Tracks
                    -----   ------   ------
                     48     5 1/4"     40
                     96     5 1/4"     80 (regular media)
                     96HC   5 1/4"     80 (high capacity media)
                    135     3 1/2"     80 (regular media)

   Normally, you set TPI to match the physical drive to be tested.

   You can test the High Capacity drive on the PC-AT with one of
   three DDDs:

                PC-AT High Capacity Drive test options

                                         TPI         TYPE
        Digital Diagnostic Disk         command     command
        ----------------------------    --------    -------
        48 TPI                          TPI 48      TYPE HC
        96 TPI (regular media)          TPI 96      TYPE HC
        96 TPI (high capacity media)    TPI 96HC    TYPE HC

   Testing it at 80 tracks with the model 506-400 96 TPI or 516-400
   96 TPI High Capacity DDD certainly gives the best results.  But,
   if you only have the model 508-400 DDD for 48 TPI drives, you can
   still get useful diagnostic displays by using it and specifying
   TPI 48 and TYPE HC.  The PC-AT then double-steps the High Capacity
   drive as it always does with 40 track diskettes.  Note that the
   CHART pattern is about half as wide and the resolution half of
   what it would be with the correct 96 TPI DDD.  The CENTERING
   display is also much more critical.

   If you are specifying TPI 96 and TYPE HC (a regular 96 TPI DDD and
   a high capacity drive) and you do not have an IBM PC-AT (i.e. you
   have a clone or a non-IBM high capacity controller and drive in a
   PC or XT), then you may need to specify NOZAP.  See the NOZAP
   command.

   Don't specify TPI 96, 96HC or 135 on a 40 track drive.  DRIVECHK
   tries to use tracks that aren't there and bangs the head assembly
   against its travel limit.

   Examples:
                    TPI 48               (Set 48 tracks per inch DDD)
                    TP 96                (Set 96 tracks per inch DDD)
                    TPI 96HC             (Set 96 tracks per inch DDD
                                          on High Capacity media.)


  TYPE command

   TYPE     <REG,HC>

   The TYPE command specifies a "regular" diskette drive or the
   PC-AT's High Capacity drive.  TYPE REG is the default.  The
   Personal System/2 High Density (1.44M) drive is tested with TYPE
   REG.

         REG           Specifies a "regular" drive      (default)
         HC            Specifies a PC-AT High Capacity drive

   High Capacity support in DRIVECHK has only been tested on a PC-AT.
   Operation with other machines and non-IBM hardware may not be
   successful.  TYPE HC tests the drive at a 300 KBS data transfer
   rate with TPI 48 or TPI 96.  It tests at the 500 KBS rate when
   used with the special high capacity DDD and TPI 96HC.  Results
   with the 300 KBS test are probably a good indication of
   performance at 500 KBS as well as the 40 track compatibility mode.

   While it's best to test the High Capacity drive as TYPE HC and TPI
   96 or TPI 96HC, if you only have a 48 TPI DDD diskette, you can
   use TYPE HC and TPI 48.  See the TPI command description.

   If you are specifying TPI 96 and TYPE HC (a regular 96 TPI DDD and
   a high capacity drive) and you do not have an IBM PC-AT (i.e. you
   have a clone or a non-IBM high capacity controller and drive in a
   PC or XT), then you may need to specify NOZAP.  See the NOZAP
   command.

   Examples:
                   TYPE REG           (Specify "regular" drive)
                   TY HC              (Specify High Capacity drive)


  ZAP

   ZAP is an obscure command that you can probably ignore.  It
   doesn't even appear on the DRIVECHK help screen.

   ZAP reverses a prior NOZAP command.  It restores the default for
   the special case IBM PC-AT, TPI 96, TYPE HC operation.  See the
   NOZAP command for an explanation.


REPEATABILITY

   If you run DRIVECHK more than once on the same drive, chances are
   you will not get exactly the same result.  Close, but not exact.

   The reason is that the drive is tested to the point of read
   failure and this point may not be exactly the same from trial to
   trial.  Variations in clamping, temperature, head contact and
   chance effects all contribute to minor variations in results.  No
   two Digital Diagnostic Disks are exactly equal either.  (Remember,
   the extent of intentional misalignment on the disk is an ANALOG
   quantity.)

   Take extra care when handling and storing your Digital Diagnostic
   Diskettes.  They are precision tools.  Handling and damage that
   would not cause read or write failures on your data diskettes
   could cause DDD's to give different results.  DDD's do not
   come with hub reinforcing rings.  Don't put them on as it may
   affect accuracy.  Also, don't insert a DDD in a drive that has
   known mechanical or electrical problems that could cause damage.
   One "Oops!" and you can kiss it good-bye.  While your DDD's can
   last a long time, you may want to order extras, just in case....



MESSAGES

   (operand name) operand is too large.  Range=(min)...(max)

     Explanation:  The value you specified as a parameter is too
     large for the command you entered.

     Action:  Choose a value within the specified range and retry the
     command.

   (operand name) operand is too small.  Range=(min)...(max)

     Explanation:  The value you specified as a parameter is too
     small for the command you entered.

     Action:  Choose a value within the specified range and retry the
     command.

   (operand name) operand must be a numeric integer

     Explanation:  The value you specified as a parameter is not a
     valid numeric constant.

     Action:  Check the characters you entered and retry the command
     using numeric characters only for the operand value.  Decimal
     points, plus and minus signs are not permitted.

   Azimuth can only be checked with TPI 48 or 96HC

     Explanation:  You requested an azimuth display with the AZIMUTH
     command, but the TPI (tracks per inch) is not set at 48 or 96HC.
     The 48 TPI and 96 TPI High Capacity DDD are the only ones with
     azimuth information recorded on it.  96 TPI regular media and
     135 TPI DDDs do not have azimuth tracks.

     Action:  If TPI is set wrong and you are using a 48 TPI DDD or
     96 TPI High Capacity DDD, then enter TPI 48 or TPI 96HC as
     appropriate and then retry the AZIMUTH command.  Otherwise,
     azimuth cannot be checked.

   Can't process.  HC is not valid with TPI 135

     Explanation: A High Capacity drive has been specified with the
     TYPE command, but the current TPI (tracks per inch) is incorrect
     for a High Capacity drive.

     Action:  Either change the drive type with the TYPE command to a
     type other than HC or change the TPI with the TPI command to 48,
     96 or 96HC as appropriate.

   Can't process.  96HC is only correct with TYPE HC

     Explanation:  A TPI (tracks per inch) of 96 with a High Capacity
     media DDD has been specified with the TPI command, but the
     current drive type is incorrect for a High Capacity media DDD.

     Action:  Either change the drive type with the TYPE command to
     type HC or change the TPI with the TPI command to something
     other than 96HC.

   Diskette system has been reset

     Explanation:  This is an informational message displayed every
     time the RESET command is executed.  It indicates that the next
     time the drive is started, the diskette controller will
     re-calibrate the drive by seeking to track 0 before seeking to
     the current track.

     Action: None.

   Drive operand is not 0, 1, 2 or 3

     Explanation:  The specified diskette drive number must be 0, 1,
     2, or 3.

     Action:  Retry the command using the correct drive number.

   Error reading diskette

     Explanation:  The program encountered a disk error while reading
     the diskette for spindle speed testing.  Testing and measurement
     continues, although some of the calculated results may lose
     accuracy.  If you just get a single error, you can restart the
     speed test.  If you get this error continuously, then you are
     either using the wrong diskette or may have a solid diskette
     drive failure.

     Action:  Make sure you are using the correct Digital Diagnostic
     Diskette and that the DRIVE, TYPE and TPI values are properly
     set.  The DRIVECHK speed test does not work with ordinary DOS
     formatted diskettes.  If you don't have a Digital Diagnostic
     Diskette, use the ALIGN program and any DOS formatted diskette
     to check the drive speed.

   LIMIT operand is not PLUS or END

     Explanation:  The specified LIMIT operand must be PLUS or
     END.

     Action:  Retry the command using a correct LIMIT parameter.

   Missing operand(s)

     Explanation:  Not enough operands were entered on the command
     line for the specified command.

     Action:  Re-enter the command with the proper number of operands
     as indicated in the command description.

   Read error verifying DDD diskette

     Explanation:  DRIVECHK was unable to read the DDD model number
     that is recorded on every DDD diskette.  Either you do not have
     a DDD in the drive under test or the identifying sector cannot
     be read.

     Action:  DRIVECHK continues with the requested diagnostic test
     on the assumption that the drive is out of adjustment and some
     useful results may be obtained.  If you do not have a DDD in the
     drive under test, then press any key to stop the test.

   SIDES operand is not DS or SS

     Explanation:  The specified SIDES operand must be DS or SS.

     Action:  Retry the command using a correct SIDES parameter.

   Test ended

     Explanation:  You have stopped a diagnostic test by pressing any
     key during the test.  No results will be displayed.

     Action:  If you still want to run the test, then re-enter the
     command to run it.

   Too many operands

     Explanation:  More operands were entered on the command line
     than the specified command can accept.

     Action:  Re-enter the command with the proper number of operands
     as indicated in the command description.  Many commands do not
     have any operands.

   TPI operand is not 48, 96, 96HC or 135

     Explanation:  The specified TPI (tracks per inch) must be
     48, 96, 96HC or 135.

     Action:  Retry the command using the correct track density
     specification.

   TYPE operand is not REG or HC

     Explanation:  The specified TYPE value must be REG or HC.
     See the TYPE command description for an explanation.

     Action:  Retry the command using the correct TYPE value.

   Unknown command

     Explanation:  The specified command is not recognized by
     DRIVECHK.

     Action:  Check the command spelling and re-enter it.

   Warning: TYPE HC is intended for PC-AT

     Explanation:  You specified a High Capacity drive and DRIVECHK
     is not running on a PC-AT which is the only IBM Personal
     Computer that supports a High Capacity drive.

     Action:  If you are not testing a High Capacity drive, then
     re-enter the TYPE command specifying a type that is appropriate
     for your Personal Computer model and diskette drive type.  If
     you are testing a High Capacity drive on a machine other than a
     PC-AT, then you may continue.  However, High Capacity support in
     DRIVECHK has only been tested on a PC-AT.  Operation with other
     machines and non-IBM hardware may not be successful.

   Your model (model) DDD is not for (tpi) TPI

     Explanation:  DRIVECHK read the DDD diskette and found it was
     for a different TPI (tracks per inch) than that specified with
     the TPI command.  The track density of the DDD you use must
     match the value entered with the TPI command.  Furthermore, if
     you have a 96 TPI High Capacity DDD, you must use TPI 96HC.

     Action:  Either insert the correct DDD or use the TPI command so
     it agrees with the DDD you are using.



COMPETITIVE PROGRAMS

   There are several diskette drive diagnostic programs and disks on
   the market.  While I have never used any of them and have only
   seen sales literature for some, I'd say that DRIVECHK has the
   following advantages:

        - Graphic results with a somewhat unique presentation that
          lets you judge the drive's performance for yourself.
          (Like a gauge in a car compared to "idiot lights.")
        - Packs more information into each display, making it
          easier to see the overall results and easier to use
          the program.  The user doesn't have to do much to
          see all the data.
        - Supports 96 and 135 TPI drives as well as 48 TPI
        - Supports the PC-AT High Capacity drive with 3 different
          types of DDDs.
        - Allows testing the PC-AT High Capacity drive with a
          48 TPI DDD (which gives reduced resolution).
        - Displays an indication of instantaneous speed variation.

   And disadvantages:

        - Slower
        - No pass-fail results.

   You may wish to investigate other programs on the market that have
   a similar purpose.  The first three listed here use the some of
   the same Xidex/Dysan DDD diskettes that DRIVECHK uses.  (I don't
   know what disk Cross-Chex uses.)

        - Interrogator (Xidex/Dysan)
        - Memory Minder / Disk Drive Analyzer (J&M Systems)
        - ReadiScope (ReadiWare Systems)
        - Cross-Chex (Award Software)
        - Datalife Disk Drive Analyzer (Verbatim)
        - Recording Interchange Diagnostic (Dymek)

ORDERING DIGITAL DIAGNOSTIC DISKETTES

   Digital Diagnostic Disks (DDD's) are not available directly from
   Xidex/Dysan Corporation in small quantities.  Their regional sales
   offices or main office can give you the name of a dealer who
   stocks them or can get them for you.  Any Xidex/Dysan dealer can
   order them.

           Xidex/Dysan Corporation, CE Division
           5100 Patrick Henry Drive
           Santa Clara, CA 95050
           Telephone (800) 233-5099 Xidex
                     (408) 988-3472
                     (800) 422-3455 Xidex CE Division

   One mail order dealer with a range of Xidex/Dysan products is

           Supply Line, Inc.
           1420 N. Claremont Blvd. Suite 205B
           Claremont, California 91711
           Telephone (800) 422-3392  outside of California
                     (800) 648-7376  inside California
                     (714) 621-1984