DRIVECHK 4.4, 5/30/89  and  ALIGN 3.0, 6/2/89
        (c) Copyright John L. Dickinson 1983, 1987, 1989
        See complete documentation for copying provisions.

   DRIVECHK (Drive Check) tests and diagnoses diskette drives.
   ALIGN helps service personnel adjust and repair diskette drives.

   Each program works in conjunction with a separately purchased
   Xidex/Dysan diskette that is specially formatted and contains no
   programs.

DRIVECHK Overview

   DRIVECHK graphically displays alignment and other diskette drive
   characteristics without the need for an oscilloscope.  A drive can
   be checked in just a few minutes without removing the PC's cover.

   DRIVECHK can be used to periodically check a drive's operation,
   prove a suspected defective drive is bad, or as a final check
   after repairs or adjustments.  The program is easy to use, but the
   results are more suitable for technical hobbyists and service
   personnel than casual PC users.

   DRIVECHK requires a Xidex/Dysan Digital Diagnostic Disk (DDD).
   The Digital Diagnostic Disk is specially formatted and precisely
   recorded, but doesn't contain any programs.

   DRIVECHK runs under IBM PC-DOS version 2.0 or later on any IBM
   Personal Computer with at least 128K and an 80 character display.

   See DRIVECHK.DOC for complete documentation.

ALIGN Overview

   ALIGN allows you to move a diskette drive head to absolute track
   locations and operate the drive while checks and adjustments are
   made.

   ALIGN is one of several tools needed to adjust and service
   diskette drives.  ALIGN does not attempt to teach you how to do an
   alignment, but it isn't difficult if you have what you need.

   In addition to this program, you need service information, an
   oscilloscope and a Xidex/Dysan Analog Alignment Diskette (AAD) for
   the drive to be serviced.  Extension or external diskette drive
   signal and power cables are very helpful.  An Analog Alignment
   Diskette (AAD) contains NO data, just special waveforms and can't
   be copied.  You can try the program using any diskette.

   ALIGN runs under IBM PC-DOS version 2.0 or later on any IBM
   Personal Computer with 128K and an 80 character display except
   the PCjr.  The diskette drives to be adjusted are connected to the
   PC in the usual manner.

   See ALIGN.DOC for complete documentation.

File Descriptions:

   OVERVIEW.DOC    (This document) Short overview of DRIVECHK and ALIGN.
   DRIVECHK.DOC    Documentation for DRIVECHK.EXE
   DRIVECHK.EXE    Diskette drive diagnostic program.
   ALIGN.DOC       Documentation for ALIGN.EXE
   ALIGN.EXE       Diskette drive alignment program.