Info-IBMPC Digest	Wednesday, 11 January 1984	Volume 3 : Issue 6

This Week's Editor: Randy Cole

    SPECIAL ISSUE for those writing code for the IBM asynch port.  Thanks
     is due to Billy Brackenridge for editing the messages which follow,
       and of course, to the people who participated in the discussion.

----------------------------------------------------------------------

Date: 10 Jan 1984 1244-PST
Subject: Edge Triggered Messages
From: Billy <BRACKENRIDGE@USC-ISIB>

Here is an edited version of the edge triggered interrupt debate.  It also
should shed some light on some of the design decisions taken in the two MIT
communications packages in the INFO-IBMPC library:


Date: 30 Nov 1983
From: Craig Milo Rogers	 <ROGERS@USC-ISIB>

I've been using a version of your interrupt-driven COM: package for the IBM
PC.  I think that I've discovered a timing bug in it, as follows:

1)	The IBM PC uses the 8259 interrupt controller in edge-triggered mode.

2)	The COM interrupt routine checks for interrupts from the 8250 before
	clearing the interrupt flag in the 8259 with a specific
	end-of-interrupt.

3)	Between the time that the interrupt code checks for interrupt sources,
	and the time that it clears the interrupt flag, a new interrupt source
	could appear on the 8250.  The resulting edge to the 8259 would be
	lost when the EOI is issued.

My conclusion is that the end-of-interrupt should be issued to the 8259 BEFORE
the 8250 is checked for interrupt sources.  How does this sound to you?


------------------------------
Date:  16 December 1983
From:  Jerry Saltzer at MIT-MULTICS

I finally had a chance to look into the 8250-8259 interrupt interaction
question that you raised.  The documentation on the 8259 is a little vague on
this point, but I believe that it is actually quite clever in edge-triggered
mode.  If an edge comes along, it latches the fact, and ignores more edges
till the signal goes back down again AND the interrupt gets forwarded to the
8088.  Then it begins watching for more edges.	For the case of an 8250, the
8250 brings up its interrupt line, the 8259 latches and, unless there is other
activity, notifies the 8088.  The 8088 accepts the interrupt and begins
running the COM interrupt handler, which knocks down the interrupt line when
it reads the IIR of the 8250.  That dropping of the interrupt line in turn
causes the 8259 to start watching for another edge.

The EOI has as its only function allowing the 8259 to coordinate interrupts
among various levels.	 Until the EOI is issued, not recognized by the 8259. 
After the EOI, they will be. The EOI has nothing to do with whether or not
edges are noticed and latched for later handling.

Thus the EOI should be set as the last thing on the way out. If you set it
early in the routine, the manipulation of the registers in the 8250 will cycle
the interrupt line and generate a COM interrupt on top of the COM interrupt. 
The result is a series of nested COM interrupts until you get deep enough that
the IIR seems empty and no further COM interrupts get generated.

That is how I read the manual, though I am the first to admit that any
interpretation of the manual seems to require a leap or two of the imagination
to fill in some of the gaps.  In any case, this model of how it works is
consistent with all the external observations we have been able to make of the
two chips and with the bugs we have tripped over when we tried different
models (such as yours.)


------------------------------
Date: 19 Dec 1983
From: Craig Milo Rogers

Thank you for your analysis of the problem.  That must explain the "LATCH
ARMED" indications on the "IR Trigerring Timing Requirements" diagram in the
8259A specs from Intel.	 Your empirical experiences certainly outweigh my
theoretical speculations.

However, I would like to speculate some more based on the new data. Assume
that the receiver were to request an interrupt.	 The 8250 would request an
interrupt.  IRR would be set active in the 8259A.  Eventually, the 8088
interrupts.  IRR is set inactive, ISR is set active.  The interrupt routine
checks the receive condition, and clears it.  The 8250 drops its interrupt
request line.  The 8259A latch is reenabled.  Suppose that the transmit
section were now to request an interrupt.  The 8250 would raise its interrupt
line.  The 8259A would latch it, and set IRR again. The 8088 is still in the
interrupt service routine, which now repolls the 8250 for transmit interrupts. 
Seeing one, it clears it.  The 8250 drops its interrupt line.  The interrupt
service routine issues the EOI, clearing the ISR bit.  The 8088 returns from
the interrupt routine, reenabling its interrupts.  The 8259A has been waiting
for the 8088 to process the interrupt cycle caused by the IRR bit activated by
the transmit request. However, since the 8250's interrupt line was dropped
before the 8088 acknowleged the interrupt to the 8259A, the 8259A should
perform a "Default IR7" interrupt cycle, instead of a normal interrupt.	 If
the line printer (IR7) is enabled at the same time, this will cause a false
line printer interrupt.	 Any objections to this scenario?

In any case, I fail to see how nested COM interrupts could result. 8088
interrupts are disabled throughout execution of the interrupt routine (no STI
or POPF).  At least, this is true of the version the Dick Gillmann gave me to
start with.


------------------------------
Date:  20 December 1983
From:  Saltzer at MIT-MULTICS

Your scenario is one I hadn't thought about before, but it sounds correct.  It
also explains one mystery.  Our serial line interrupt handler has a counter to
pick up interrupts for which no condition code is set; that counter has never
registered anything but zero.  Yet the repoll sequence ought to cause some
conditions to be serviced in advance of the interrupt that they cause, so that
counter ought to occasionally record something.	 (We are certain that such
early conditions actually occur because the handler loses characters if you
don't repoll.)	Your scenario calls for such early-serviced conditions to lead
to level-7 interrupts rather than serial line interrupts, so this handler
never sees them.  I suppose that whatever level-7 handler is available is
smart enough to ignore interrupts that don't have serviceable conditions to
back them up so it doesn't matter.  And I don't suppose it counts these cases
so I can't verify that the com line is giving it extra things to ignore.

I forgot that the CPU remains masked through the handler--the nested interrupt
thing can't happen.

It would help if INTEL would publish wiring diagrams of the 8259 and 8250. 
The English descriptions leave a lot to the imagination.


------------------------------
Date: 20 Dec 1983
From: Craig Milo Rogers

Interesting.  I expect that your repoll sequence is necessary to prevent lost
characters because the 8250 is presenting an interrupt *level* condition,
rather than an interrupt *edge* condition.  Thus, if more than one interrupt
source is present withing the chip (say, receive and transmit), the interrupt
request will remain active until all sources have been serviced.  If the
interrupt service routine were to service only one source before returning,
the 8250 would not generate another edge for the 8259A.	 At least, this is how
I read the 8250 documentation in the IBM Technical Reference manual.

Thus, if you don't repoll to verify that all possible interrupt sources on the
8250 are clear before returning from the current interrupt, I would expect you
to eventually reach a state where no more characters get through.  This is
somewhat different from your description of "losing characters" when repolling
isn't present.	I am concerned about the discrepancy.  Does your application
code perhaps time out and reset the 8250?

So, even if you were to instrument the IRQ7 (line printer) service routine, I
would expect to find few fake interrupts due to the 8250 ports.	 Considering
the various windows involved, missing interrupt request edges should be far
more common than delayed interrupt request edges, up to the point where the
interrupt service routine itself is consuming 50% or so of the 8088 CPU.

By the way, I believe that there is a wiring error in the IBM Line Printer
interface circuit, so that all line printer interrupts are treated by the
8259A as fake IRQ7 interrupts rather than real ones. If you have time, you
might review my analysis at the start of the line printer interrupt handler in
LPT_PKG.ASM.  I am interested in any comments you have.


------------------------------
Date:  20 December 1983
From:  Saltzer at MIT-MULTICS

You are certainly correct in your analysis of why one must repoll for further
conditions after servicing the first one found.	 However I am unconvinced by
the argument that suggests that early handling of conditions will be rare.  If
the line is operating full-duplex, a transmit holding register empty condition
can occur at any time.	If it occurs before the receive condition is read (but
after the receive condition is registered) the interrupt line out of the 8250
will stay high, causing the "lost interrupt" effect.  And that small window
definitely does get hit, at least at 9600 baud and 19.2K, in our experience. 
If the THRE condition occurs after the receive condtion is read, then there
should be a fake interrupt at level 7.	If this window is at least as large as
the previous one (and it is in this code) then unneeded interrupts should be
at least as frequent as lost interrupts without repolling.


------------------------------
From: Craig Milo Rogers

By the way, the repoll code in the COM routines doesn't check for line/modem
status transition interrupts.  It seems to me that this is an error.  A
line/modem status transition could take place while a transmit or receive
interrupt is being processed;  the interrupt request line will not drop;  the
interrupt routine will dismiss;	 no more COM interrupts.


------------------------------
Date:  22 December 1983
From:  Saltzer at MIT-MULTICS

Good try, but no cigar.	 The COM code doesn't enable line/modem status
transition conditions, so they don't affect the interrupt request line. If
they were enabled, they would have to be polled, agreed.  There is a place in
the code to go to in case the conditions appear in the IIR, but that path was
provided as a safety net, not because I expected it ever to be followed.

I ran into a subtle interaction in the polling for transmit interrupts, which
led me look for every possible excuse to avoid enabling for lower priority
interrupts.  The reading of the IIR (which you have to do to find out whether
or not the lower priority interrupts are there) resets the THRE condition.  So
I couldn't figure out any way to repoll without taking a chance on losing a
THRE condition.	 Repolling again for an empty transmitter register would work,
but then one would have to repoll yet again for a modem/line interrupt, etc.,
forever.  So I just ducked the issue and left it for someone to sort out who
really needed those conditions monitored.


End of Info-IBMPC Digest
************************