-------------------------------  SORT.DOC  ----------------------------------

                        Documentation for SORT.BLD
                           (C) 1983 Lee M. Buck 
                               Arlington, VA.

This file provides a brief description of the machine language subroutine
SORT.BLD.  The subroutine is written in assembly language and has been
linked and is set up to use directly in a BASIC program.  The sort algorithm
used in the routine is a Shell-Metzner sort.  The demonstration program
SORTEST.BAS shows how to use the subroutine and also includes an interpreter
BASIC version of a Shell-Metzner sort.  This routine will only sort strings
but it can be used to sort numbers if they are properly converted to a string.
They should be the same length and have the same number of decimal places, if 
any.  Dates can be sorted if they are stored YY/MM/DD. Several strings can be 
concatenated from multiple fields of a record in data base applications to 
provide fast multi-field sorts in BASIC programs.

The machine language sort routine must be set up using the program SORTBLD.BAS
before running the test program.  SORTBLD.BAS will create the file SORT.BLD.
This file is the relocatable machine language sort which is 'BLOADed' into
memory for use with a BASIC program.  The demonstration program SORTEST.BAS
uses SORT.BLD to sort random strings into ascending order and then descending
order.  SORTEST.BAS is set up to run on a 64K memory machine using BASIC
(NOT BASICA ! - unless the CLEAR stmt argument is reduced).  The program gives
guidelines for running on a machine with 96K memory or more if you want to test
larger problems.  If you have less than 64K, the program must be modified to
reflect less memory (on the same two lines as for more memory - see the listing
for details - and your BASIC manual).

The demonstration program generates a specified number of varaible length
strings.  The strings are first sorted into ascending order by an INTERPRETER
BASIC Shell-Metzner sort algorithm.  The original array is then sorted using
the machine language subroutine; first ascending and then descending order.
The results of the sorts and the original array can then be displayed on the
screen or on a printer.

The subroutine will sort up to 10000 strings --  more than a BASIC program is
likely to be able to hold in memory.  The strings can be of equal or unequal
length.

A note on performance:  A comparison to interpreter BASIC is silly for this
routine, but compared to the BASIC compiler this routine is about 30% faster
than the compiler when using the BASRUN.EXE module to compile the BASIC code
for a Shell-Metzner sort.  It is about equal in speed (marginally faster)
than the compiler when compiled without the BASRUN.EXE module (using the /O 
option).  This routine will sort 2000 strings (from 1 to 10 characters) in
about 11 seconds. This is probably SLOWER than will be experienced in 'real'
problems since the strings that are sorted in the demo are made by repeating
a randomly generated character 'N' times.  It takes longer to determine that
JJJJJJJ is less than JJJJJJJJ than to determine that Johnson is less than Jones
since a difference occurs at the third character for the latter example rather
than at the eighth character.


COMMENT* THIS SUBROUTINE IS A 'FAR' PROCEDURE FOR USE WITH BASIC PROGRAMS. THE
        MODULE SORTS A STRING ARRAY INTO ASCENDING OR DESCENDING ORDER USING AN
        ASCII COLLATING SEQUENCE.  THE PARAMETERS THAT MUST BE PASSED TO THE
        PROCEDURE INCLUDE THE FIRST ELEMENT IN THE ARRAY, THE FIRST ELEMENT IN
        A POINTER ARRAY AND THE NUMBER OF ELEMENTS TO SORT.

        THE POINTER ARRAY IS AN ARRAY OF INTEGERS THAT ARE USED TO INDICATE THE
        ORDER OF THE STRING ARRAY.  FOR EXAMPLE, THE VALUE OF POINTER(10)
        INDICATES THE POSITION OF ARRAY$(10).  INITIALLY, POINTER(10) WOULD
        HAVE A VALUE OF 10, BUT FOLLOWING THE SORT POINTER(10) WOULD HAVE A
        VALUE EQUAL TO THE POSITION ARRAY$(10) SHOULD HAVE IN THE ORDERED ARRAY

        THE POINTER METHOD IS USED FOR TWO REASONS.  ONE IS THAT IT IS SLOW TO
        MOVE STRINGS AROUND, SECONDLY, BASIC DOES NOT WANT YOU MESSING WITH THE
        'STRING DESCRIPTOR'.  IF YOU SWAP STRINGS OF UNEQUAL LENGTH, THE STRING
        DESCRIPTORS WILL BE WRONG AND WOULD REQUIRE SOME MESSY ADJUSTMENTS.
        USING POINTERS IS FASTER AND EASIER.

        THE BASIC CALL IS:
                           CALL SORT(ARRAY$(1),PTR%(1),N%)

        'SORT' MUST BE SET BY THE CALLING PROGRAM TO THE CORRECT 'ENTRY POINT'
        IN THE PROCEDURE TO DETERMINE WHETHER AN ASCENDING OR DESCENDING SORT
        IS PERFORMED.

                ASCENDING SORT  --  SORT = 0 

                DESCENDING SORT --  SORT = 2 

                SET THE CORRECT SEGMENT LOCATION WITH 'DEF SEG...', THEN
                CALL SORT(ARRAY$(1),PTR%(1),N%)

        UPON RETURN FROM THE ROUTINE, THE PTR% ARRAY IS ADJUSTED TO REFLECT THE
        CORRECT ORDER OF THE ARRAY$ ELEMENTS.

        NOTE:  THIS ROUTINE IS FOR SORTING ASCII STRINGS, NOT NUMBERS. YOU CAN
        SORT NUMBERS WITH IT ONLY IF THEY ARE 'PROPERLY' CONVERTED TO STRINGS
        FIRST. IT WILL NOT WORK WITH COMPILED BASIC PROGRAMS BECAUSE THE STRING
        DESCRIPTORS USED IN COMP. BASIC ARE 4 BYTES NOT 3 AS IN INTERP. BASIC.

        PROGRAM BY:  LEE M. BUCK
                     4830 N. 24th STREET
                     ARLINGTON, VA 22207
                     703-527-5813

        DATE: 3-27-83           REVISED: 4-23-83

        THIS PROGRAM MAY NOT BE DISTRIBUTED FOR A FEE WITHOUT WRITTEN CONSENT
        OF THE AUTHOR.  IT IS INTENDED FOR FREE USE BY THE IBM PC USER 
        COMMUNITY.
*