X A S M


				  Revision 1.04


		       A macro configured cross assembler






	    Copyright 1986 by Stuart Venters  ALL RIGHTS RESERVED.
			      804 Watts Drive.
			      Huntsville, Alabama  35801








	THIS SOFTWARE MAY NOT BE USED FOR PROFIT WITHOUT PRIOR WRITTEN
	AUTHORIZATION FROM THE AUTHOR.	The price is $50 and includes
	the latest version release disk and your choice of target machine
	definition file.





		      History and available targets

     XASM is a cross assembler written for single chip computers.  It was not
     written for a specific target machine.  It contains no built in machine
     opcodes like JMP or LOAD.	Instead these are provided by a macro definition
     file for the particular target machine.

     XASM is a personal tool which I think may be of general interest.	I wrote
     this assembler after working on several single chip projects with available
     cross assemblers.	This assembler eliminates problems I had with those
     assemblers in areas of cost, speed, error checking, listing format, macro
     implementation, and portability.  It is 4 times faster than the last
     assembler I bought or about 1500 LPM on a PC-AT.  The listing is clean
     showing all of the code bytes and none of the internal macro expansions.

     XASM was written in C under CPM80.  It currently runs on MS-DOS. The port
     from CPM to MS-DOS took about two hours.  This speaks well of both C and
     the portability of XASM to other machines.

     Plans are to enhance XASM in two directions:  adding a relocating loader
     and creating a microcode assembler for custom projects.  I have made every
     effort to ensure that XASM is a reliable tool.  However, if you find a bug
     or are interested in the enhancements please drop me a note.

     XASM can be configured for a variety of targets.  The current list of
     macro files available for XASM is as follows:

	   1102MACS	   (Requires object code scrambler program.)
			   Seiko 1102 1112
			   SMC 1102

	   1650MACS	   General Instrument PIC-1650 series

	   6301MACS	   Hitachi 6301 6303 63701 6801 6803
			   Motorola 6800 6801 6803

	   6805MACS	   Hitachi 6305 6805
			   Motorola 6805 68705

	   8048MACS	   INTEL 8048 8041 series

	   Z8MACS	   ZILOG Z8 family

     It is my intention to extend this list if there is demand.  To this end
     I will construct the required macro files for other targets as they are
     ordered.



			    Operation

     The assembler is invoked by a command line as follows:

	XASM {debug} {filenames} mainfile

	    Files are read in order from left to right.
	    Filenames have ".ASM" appended to them.
	    Mainfile.ASM is the last source file.
	    Mainfile.LST is the list file.
	    Mainfile.HEX is the object file in INTEL hex format.

	    Example:
		XASM 6805MACS UTIL TEST
			Reads the macro definitions from 6805MACS.ASM
			Reads the utilities file UTIL.ASM
			Reads the test file TEST.ASM
			Writes the object file TEST.HEX
			Writes the listing file TEST.LST

	    Debug sets the internal debug level from 0 to 9.
	       -d1 is useful for watching assembler progress.
	       -d4 is useful for debugging macro definitions.

     The source file is a text file of source lines.  A source line consists of
     a possible label field, an opcode field, and possibly some operand fields
     separated by commas.  The label field, if present, starts in column 1 and
     may end with a colon.  The opcode field is a single legal variable name
     surrounded on both sides with spaces or tabs.

     A real source file follows:



;define a macro SUM which puts out 1 byte which is the sum or it's arguments
sum	  macro
	   db	  $1+($2)
	  endm

a	  equ	  16
b:	  set	  7	  ;

;now use the macro
LABEL:	  SUM	  a,b	  ;set LABEL equal to current pc,
			  ; calls macro SUM with $1="A" and $2="B"
;
b	  set	  8	  ;
;
label	  sum	  A,b	  ;same, colon and case are not significant
	  sum	  a,b	  ;same, except no label (leading space is delimiter)




			    Assembler built in functions


    SET  sets the label to the left of the SET to the expression value
	to the right.  Can be done more than once in a pass.  Value is not
	recalculated in pass 2 but is saved from pass 1.

    EQU  sets the label to the left of the EQU to the expression value
	to the right.  Label can not have a previous value. Value is not
	recalculated in pass 2 but is saved from pass 1.

    ORG  sets the program counter to the value of the expression to the
	right of the ORG.   Value is not recalculated in pass 2 but is saved
	from pass 1.

    DB	 outputs a byte or series of bytes according to the expression(s) to
	the right of the DB. Legal byte values are from -128 to 255.

    DW	 outputs a word or series of bytes according to the
	expression(s) to the right of the DW.

    PACKING sets the output mode for DW.  PACKING 0 sets MSB first and is the
	default.  PACKING 1 sets LSB FIRST.  PACKING 2 sets word mode.

    ERROR marks the current line as being in error.  The argument is a string
	with the error code.

    IFERR has two arguments.  The second is evaluated and if non-zero
	an error is caused using the first argument as the error value.
	The evaluation occurs in both pass 1 and 2.  If the expression is
	undefined, no error occurs.

    IF	 tests the expression to the right of the IF.  If the expression is
	non-zero, the if part is executed.  If the expression is zero or
	undefined, the else part is executed.  The expression is not
	recalculated in pass 2 but is saved from pass 1.  Hence if's always
	execute the same way in pass 1 and 2.

    ELSE separates the true part from the false part of an IF sequence.  Is
	optional.

    ENDIF terminates an IF sequence.  Is not optional.

    TITLE sets the current title string to the string to the right of TITLE.

    PAGE causes printing to start on a new page

    END  causes assembly to stop.  May be inside an IF statement.

    MACRO causes all lines following until an ENDM to be stored as a macro
	definition.  The macro name is the label to the left of MACRO.

    ENDM  terminates a macro definition.

    INCLUDE causes the file named in the quoted string to the right of INCLUDE
	to be included in the source stream.  Nesting is permitted.




			    Expressions
	Expressions are evaluated from left to right with no hierarchy but
	with parentheses. There are two types of operations.  These are
	numeric and string. All operations are dyadic.	They take a left
	and right value or expression in parens and put out an expression
	value.

		The numeric operations work on numeric values.	If they
		are given a string, they will use the character code of
		the first string element as the numeric value.	Arithmetic
		is 16 bit unsigned. The list of operations is as follows:

			+   addition
			-   subtraction
			*   multiply
			/   divide
			&   bitwise and
			|   bitwise or
			<   relation less than. (0 if false, 1 if true)
			>   relation greater than. (0 if false, 1 if true)
			=   relation equal to. (0 if false, 1 if true)
			!   relation not equal to. (0 if false, 1 if true)


		The string operations are included to make programming target
		machine opcode macros easier.  They operate on two strings.
		The operations are as follows:

			=  Returns 1 if the strings are equal. 0 otherwise.

			!  Returns 0 if the strings are equal. 1 otherwise.

			?  Returns 1 if the characters in the first string
			     match the first characters in the second string.
			     Else returns 0.

			^  Called with a string on the left and an expression
			     on the right.  First removes the leading characters
			     in the expression which match the string. Next
			     evaluates the rest of the expression and returns
			     result.



			    Values
     Values are the simplest form of an expression.  There are three types
     of values.  These are constants, variables, and pseudo constants.

	String constants are formed by a string of characters enclosed in
	double quotes.	A backslash is an escape character in a string.  A
	double quote can be entered by preceeding it with a backslash.	Watch
	backslashes in filenames of INCLUDE statements.  (DOS takes forward
	slashes just fine.)

	Numeric constants always begin with "0" thru "9".  Examples of
	the possible numeric constants are as follows:

		123	a simple base 10 number
		123d	the same base 10 number
		10X123	the same base 10 number

		16XABC	the base 16 number ABC
		ABCh	the same base 16 number
		0XABC	the same base 16 number (base 0 --> base 16)

		777q	the base 8 number 777
		8x777	same

		101b	the base 2 number 101
		2x101	same

		36x10Q	the base 36 number 10Q

	Variables always begin with "A" thru "Z".  The following characters
	may be "A"-"Z", "0"-"9", or  "_".  Examples of legal variables are:

		A
		A923
		a923   (The same as case does not count.)
		FIRST_ONE
		FIRST_ONE_1 (Symbol size is not limited.)

	Pseudo constants always begin with "$".

		$ means the program counter value at the beginning of the
			current source file line. (Not macro line.)

		$1 means the first macro argument
		 .
		 .
		$9 means the ninth macro argument

     Values may be preceeded by a minus sign.