PRINTING GRAPHICS SCREENS FROM THE PC
     
     This document discusses methods of printing graphics for a variety of
     printers.  Several printer programs are on disk to help you print
     graphics for particular printers and monitor combinations. These
     programs come from a variety of sources and have been gathered from
     public domain and shareware distributors.
     
     
     GRAPHICS.COM
     =============================
     
     This routine comes with PC-DOS, and allows you to be able to use
     printscreen to print a graphics screen to a standard Epson type dot
     matrix printer.  Simply enter the command GRAPHICS before you initiate
     a printscreen. However, it is only useful for printing CGA type
     graphics to the printer.  If you are using Hercules type (monochrome
     graphics) graphics see other options below.
     
     EPSON.COM
     =============================
     
     This is a replacement for GRAPHICS.COM, and may be used with a variety
     of dot matrix printers.  Some people like the way EPSON.COM prints out
     graphics better than GRAPHICS.COM. Try them both and decide which to
     use.
     
     Note that many printers emulate Epson type graphics, so even if your
     printer is not an Epson, this routine may still work.
     
     SCRNDUMP.COM
     =============================
     
     SCRNDUMP v 1.02 will install an enhancement to the PrtSc key which
     adds graphics printing support for Hercules Mono, Color Graphics
     Adapter (mono mode) and Enhanced Graphics Adapter (6430x350 Color).
     Printers supported are Okidata 92, Okidata 192, Epson/IBM, and C.Itoh
     Prowriter. Only the selected driver remains resident. Copyrighted by
     Hardwood Software Associates. Entered into public domain for
     non-commercial use only. Version 1.02 corrects page selection on EGA.
     
     Instructions for using SCRNDUMP
     
     Usage:  SCRNDU /g /p
     
     Where:  g = E[GA] for Enhanced Graphics(640x350 Color)
               = C[GA] for Color Graphics(640x200 Mono only)
               = H[ercules] for Herc Mono Graphics (720x348 Mono)
             p = E[PSON] for EPSON/IBM printer
               = C[ITOH] for CITOH PROWRITER/PROWRITER II printer
               = 1[92] for OKIDATA 192 printer
               = 9[2] for OKIDATA 92 printer
     
     EXAMPLE:Suppose you had a Hercules type monitor setup, and an Epson
     printer.  You would enter the following command at the DOS prompt:
     
     C>SCRNDUMP /h/e
                                        1

          

     
     The screen printing program is now resident.  Once a screen you wish
     to print is displayed on the monitor, you press the 'Shift/PrtSc' (or
     PrintScreen on Enhanced Keyboard) to activate the screen print
     program. Then...
     
     1)If the screen is a text screen, press the spacebar.
     
     2)If the screen is a graphics screen, press the number 1 on the upper
     row of number keys.
     
     If no key is pressed within 10 seconds the regular text print screen
     routine is used. Graphics printing in progress can be canceled by
     pressing 'ESC'.
     
     LASERJET.EXE and THINKJET.EXE
     =============================
     
     The LASETJET/THINKJET PRINT SCREEN utility allows you to print the
     contents of your IBM PC or PC/XT display screen using the LaserJet or
     ThinkJet printers.
     
     These instructions explain how to install and use this utility. Notice
     that there are two sets of installation instructions--one for LaserJet
     printers and one for ThinkJet printers.
     
     Now proceed to the installation instructions for your printer.
     
     
     *************************
     **LASERJET INSTALLATION**
     *************************
     
     The LaserJet printer is configured at the factory to communicate at
     9600 baud.
     
     a.  Copy the LASERJET.EXE file from to the operating system (DOS)
     disk, or to your hard disk.
     
     b.  Now, to initiate the LASERJET print screen program, you would
     enter the following command at the DOS prompt:
     
     C>LASERJET A
     
     You may want to include this command in your AUTOEXEC.BAT file or in
     the file that begins the program that creates the graphs you wish to
     print.  For example, in the KWIKSTAT program, you may want to change
     the file KS.BAT to have the following lines:
     
     LASERJET A
     KS20DTAT
     
     (The LASERJET command replaces the GRAPHICS command)
     
     If there are any commands in the AUTOEXEC.BAT file for other screen
     dump programs (such as IBM "GRAPHICS"), remove them from the file.
                                        2

          

     
     USING THE PRINT SCREEN UTILITY
     
     Once you have performed the installation procedure, to print the
     contents of the PC display, read and then perform the following
     two-step procedure:
     
     a.  Press "SHIFT-PrtSc"  (or the PrintScreen key on the enhanced
     keyboard). After a 5-second delay, your display screen will be dumped
     to the printer. Note that if the display is in Alpha mode, an "A" will
     flash in the upper left corner of the screen.  If the screen is in
     Graphics mode, a short horizontal line will appear in the upper left
     corner of the screen.
     
     b.  You may select any of the options from the list below by pressing
     the key of the desired option within 5 seconds of pressing the
     "SHIFT-PrtSc".  One option from each group (orientation, print
     positioning, or page ejection) may be selected.  Printing will begin 5
     seconds after the last key is pressed.  The Enter key may be pressed
     to terminate the 5-second delay.  NOTE:  If you select any of the
     options listed below, you do not have to select one from each
     group--those that are not specified will default automatically.
     
                             KEY              OPTION
     
     ORIENTATION            * P -- PORTRAIT ORIENTATION
                              L -- LANDSCAPE ORIENTATION
     
     PRINT POSITIONING      * T -- TOP OF PAGE (PORTRAIT MODE ONLY)
                              M -- MIDDLE OF PAGE (PORTRAIT MODE ONLY)
                              B -- BOTTOM OF PAGE (PORTRAIT MODE ONLY)
     
     PAPER EJECTION         * Y -- AUTO FORM FEED AT END OF PAGE
                              N -- NO AUTO FORM FEED AT END OF PAGE
     
                ENTER KEY -- TERMINATES 5-SECOND TIME-OUT PERIOD
     
          *  Default values
     
     EXAMPLE:  To print a page of graphics, centered on the page, press the
     "SHIFT" key and "PrtSc" key, immediately followed by pressing the "M"
     key. Your graphics will be dumped from the display and printed at the
     center of the page.
     
     NOTE: The PRINT SCREEN utility can print one graphics screen and one
     alphanumeric screen on the same page, but cannot print two graphics
     screens on the same page because of limited LaserJet memory. However,
     two graphs may be printed on the same page by printing one graph using
     the form feed option (to eject the page) and then manually feeding the
     same page through the printer to print the second page.
     
     When using some software packages, the screen will not print as
     desired.  In these cases, try the following options to enable you to
     print the screen.  Use these options only after you have already tried
     the PRINT SCREEN utility unsuccessfully.  These options are accessed
     the same way as the other options (by pressing the key associated with
                                        3

          

     the option within 5 seconds of pressing the "SHIFT", "PrtSc" keys).
     
     
            KEY             OPTION
     
             A    -- ALPHA SCREEN DUMP
             G    -- GRAPHICS SCREEN DUMP
     
             C    -- COLOR GRAPHICS
             W    -- BLACK & WHITE GRAPHICS
     
             4    -- 40 CHARACTERS/LINE ALPHA
             8    -- 80 CHARACTERS/LINE ALPHA
     
     For example, when printing a color bar chart using LOTUS 1-2-3, you
     must first press "SHIFT", "PrtSc", and then "G" and "C" (for color
     graphics).
     
     If you have difficulty printing your display screen with a particular
     software package, try the above options until the screen prints
     correctly.
     
     

































                                        4